CS/ECE 252: INTRODUCTION TO COMPUTER ENGINEERING

UNIVERSITY OF WISCONSIN—MADISON

Instructor: Andy Phelps

TAs: Newsha Ardalani, Peter Ohmann and Jai Menon

Midterm Examination 1

In Class (50 minutes)

Friday, Feb 11

Weight: 15%

NO: BOOK(S), NOTE(S), CALCULATORS OF ANY SORT.

This exam has 8 pages, including a blank page at the end. Plan your time carefully, since some problems are longer than others. You must turn in pages 8 to 6.

LAST NAME:  ___________________________________________________________

FIRST NAME:___________________________________________________________

SECTION: 	 ___________________________________________________________

ID# 		 ___________________________________________________________

| Question | Maximum Point | Points |
| --- | --- | --- |
| 1 | 6 |  |
| 2 | 8 |  |
| 3 | 4 |  |
| 4 | 8 |  |
| 5 | 4 |  |
| 6 | 10 |  |
| Total | 40 |  |

Q1. (6 points)

The value -32,149 can be represented as a 2’s complement integer with 16 bits as shown below:

| 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

- Represent -32,151 as a 2’s complement integer with 16 bits in the box provided. (2 points)

| 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

- Represent -32,149 as a 2’s complement integer with 32 bits in the box provided. (4 points)

| 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Q2. (8 points)

The value “-6 5/8” can be represented by the strings of 0s and 1s according to the following data types. Please show them below.

| ASCII (Only represent the characters between the quotation marks and assume it as a null terminated string, show your result in hexadecimal) | 2D 36 20 35 2F 38 00 |
| --- | --- |
| 32 Bit IEEE Floating Point | 1 10000001 10101000000000000000000 |

The bits for an IEEE floating point number are allocated as follows:

| Sign (1 bit) | Exponent (8 bits) | Fraction (23 bits) |
| --- | --- | --- |

where N = (-1)S × 1.fraction × 2exponent-127

Q3. (4 points)

Give an example of an integer that can be represented in floating point format (32-bit IEEE format), but cannot be represented as a 32-bit two’s complement integer. Show its hexadecimal representation.

Q4. (8 points)

Fill in the following boxes with appropriate values. If there are more than one values possible, write all the possible values. Mark in “NA” if something is not possible.

| Number | 7-bit Unsigned binary | 7-bit Sign-magnitude | 7-bit 1's-complement | 7-bit 2's-complement |
| --- | --- | --- | --- | --- |
| -64 | N/A | N/A | N/A | 1000000 |
| -34 | N/A | 1100010 | 1011101 | 1011110 |
| 64 | 1000000 | N/A | N/A | N/A |
| 63 | 0111111 | 0111111 | 0111111 | 0111111 |

Q5. (4 points)

Add the following 8-bit numbers in 2's-complement notation. For each set, provide the sum (in 8-bit 2's-complement) and indicate whether or not an overflow has occurred.

- 0010 1011 + 0110 0000

1000 1011

Overflow?: Yes

- 1110 0101 + 0001 1010

1111 1111

Overflow?: No

Q6. (2 points each)

- A Turing machine is an abstract idea that helps us to define:

a. How to make an infinite tape

b. How to do binary arithmetic

- The shortcomings of digital computers compared to analog

- What it means to compute

Answer : d

II.When referring to an algorithm, definiteness means:

a. The number of unknowns and equations is the same

b. Each step must be precisely defined

c. The algorithm’s variables must not overflow a fixed number of bits

- All of the above

Answer : b

III. Two computers, A and B, are identical except for the fact that A has a divide instruction and B does not. Both have subtract instructions. Which of the following is true?

a. A can compute more types of problems than B.

b. B can compute all the same problems as A, in the same amount of time, given enough memory.

c. B can compute all the same problems as A, in the same amount of time.

- B can compute all the same problems as A, but might take longer.

Answer : both b and d are acceptable

- A collection of n bits can have how many states?

a. 2n

- 2n

- 2n-127

- n

Answer : b

- Put the following in order of their levels of abstraction.  "1" represents the lowest level, and "4" represents the highest level.

a. Algorithm

b. Instruction Set Architecture

c. Circuits

d. Transistors and other such devices

| 1 | 2 | 3 | 4 |
| --- | --- | --- | --- |
| D | C | B | A |