## Slide 1: Address Translation with Paging
Case studies for X86, SPARC, and PowerPC

## Slide 2: Overview
Page tables
  What are they? (review)
  What does a page table entry (PTE) contain?
  How are page tables organized?
Making page table access fast
  Caching entries
  Translation lookaside buffer (TLB)
  TLB management

## Slide 3: Generic Page Table
Memory divided into pages
Page table is a collection of PTEs that maps a virtual page number to a PTE
Organization and content vary with architecture
If no virtual to physical mapping => page fault
Virtual page #
PTE (or page fault)
?
…
Page Table

## Slide 4: Generic PTE
PTE maps virtual page to physical page
Includes some page properties
  Valid?, writable?, dirty?, cacheable?
Physical Page #
Property bits
Virtual Page #
Some acronyms used in this lecture:
PTE = page table entry
PDE = page directory entry
VA = virtual address
PA = physical address
VPN = virtual page number
{R,P}PN = {real, physical} page number

## Slide 5: Real Page Tables
Design requirements
  Minimize memory use (PT are pure overhead)
  Fast (logically accessed on every memory ref)
Requirements lead to
  Compact data structures
  O(1) access (e.g. indexed lookup, hashtable)
Examples: X86 and PowerPC

## Slide 6: X86-32 Address Translation
Page tables organized as a two-level tree
Efficient because address space is sparse
Each level of the tree indexed using a piece of the virtual page number for fast lookups
One set of page tables per process
Current set of page tables pointed to by CR3
CPU walks the page tables to find translations
Accessed and dirty bits updated by CPU
4K or 4M (sometimes 2M) pages

## Slide 7: X86-32 PDE and PTE Details
Available
Available
Available
Global
PAT
Dirty
Accessed
Cache Disabled
Write-through
User/Supervisor
Read/Write
Present
IA-32 Intel Architecture Software Developer’s Manual, Volume 3, pg. 3-24
20 bit page number of a physical memory page
12 bit properties
Where is the virtual page number?
If a page is not present, all but bit 0 are available for OS
Available
Available
Available
Global
4K or 4M Page
Reserved
Accessed
Cache Disabled
Write-through
User/Supervisor
Read/Write
Present
20 bit page number of a PTE
12 bit properties
Page Directory Entry (PDE)
Page Table Entry (PDE)

## Slide 8: X86-32 Page Table Lookup
Top 10 address bits index page directory and return a page directory entry that points to a page table
Middle 10 bits index the page table that points to a physical memory page
Bottom 12 bits are an offset to a single byte in the physical page
Checks made at each step to ensure desired page is available in memory and that the process making the request has sufficient rights to access the page
0
1
2
.
.
.
1024
0
1
2
.
.
.
1024
0
1
2
.
.
.
1024
0
1
2
.
.
.
1024
Page
Directory
Page
Tables
Physical
Memory
32-bit virtual address
10-bit page dir index
10-bit page tbl index
12-bit offset of byte in page

## Slide 9: X86-32 and PAE
Intel added support for up to 64GB of physical memory in the Pentium Pro - called Physical Address Extensions (PAE)
Introduced a new CPU mode and another layer in the page tables
In PAE mode, 32-bit VAs map to 36-bit PAs
Single-process address space is still 32 bits
4-entry page-directory-pointer-table (PDPT) points to a page directory and then translation proceeds as normal
Page directory and page table entries expanded to 64 bits to hold 36 bit physical addresses
Only 512 entries per 4K page
4K or 2M page sizes
Notes: 2 bits, 9-bits, 9-bits, 12-bits

## Slide 10: What about 64-bit X86?
X86-64 (AMD64 or EM64T) supports a 64-bit virtual address (only 48 bits effective)
Three modes
  Legacy 32-bit (32-bit VA, 32-bit PA)
  Legacy PAE (32-bit VA, up to 52-bit PA)
  Long PAE mode (64-bit VA, 52-bit PA)
Long mode requires four levels of page tables to map 48-bit VA to 52-bit PA
AMD64 Architecture Programmer’s Manual Volume 2: System Programming, Ch. 5

## Slide 11: PowerPC Address Translation
80-bit virtual address obtained via PowerPC segmentation mechanism
62-bit physical (“real”) address
PTEs organized in a hash table (HTAB)
Each HTAB entry is a page table entry group (PTEG)
Each PTEG has (8) 16-byte PTEs
Hash function on VPN gives the index of two PTEGs (Primary and secondary PTEGs)
Resulting 16 PTEs searched for a VPN match
No match => page fault

## Slide 12: PowerPC Segmentation
SLB is an “associative memory”
Top 36 bits of a program-generated “effective address used as a tag called the effective segment id (ESID)
Search for tag value in SLB
If a match exists, property bits validated for access
A failed match causes segment fault
Associated 52-bit virtual segment id (VSID) is concatenated with the remaining address bits to form an 80-bit virtual address
Segmentation used to separate processes within the large virtual address space
Segment Lookaside Buffer (SLB)
36-bit ESID
28 address bits
ESID
52-bit VSID
Property bits (U/S, X, V)
Associative Lookup
52-bit VSID
64-bit “effective” address generated by a program
28 address bits
80-bit “virtual” address used for page table lookup
Matching entry

## Slide 13: PowerPC Page Table Lookup
Variable size hash table
Processor register points to hash table base and gives table’s size
Architecture-defined hash function on virtual address returns two possible hash table entries
Each of the 16 possible PTEs is checked for a VA match
If no match then page fault
Possibility that a translation exists but that it can’t fit in the hash table – OS must handle
Hash Table (HTAB)
80-bit virtual address
Primary hash index
Secondary hash index
Hash function
Secondary PTEG
Primary PTEG
16-byte PTE
Match?
No Match?
Page Fault

## Slide 14: PowerPC PTE Details
16-byte PTE
Both VPN and RPN
Why only 57 bit VPN?
0
56
62
60
0
63
2
51
54
55
56
57
60
61
62
63
Abbreviated Virtual Page Number
SW
/
H
V
/
/
Real Page Number
/
/
AC
R
C
WIMG
N
PP
Key
SW=Available for OS use
H=Hash function ID
V=Valid bit
AC=Address compare bit
R=Referenced bit
C=Changed bit
WIMG=Storage control bits
N=No execute bit
PP=Page protection bits
PowerPC Operating Environment Architecture, Book III, Version 2.01, Sections 4.3-4.5

## Slide 15: Making Translation Fast
Page table logically accessed on every instruction
Paging has turned each memory reference into at least three memory references
Page table access has temporal locality
Use a cache to speed up access
Translation Lookaside Buffer (TLB)

## Slide 16: Generic TLB
Cache of recently used PTEs
Small – usually about 64 entries
Huge impact on performance
Various organizations, search strategies, and levels of OS involvement possible
Consider X86 and SPARC
TLB
Virtual Address
Physical Address or
TLB Miss or
Access fault

## Slide 17: TLB Organization
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
A
0
1
2
3
4
5
6
7
A
B
0
1
2
3
A
B
C
D
A
B
C
D
E
L
M
N
O
P
Direct mapped
Fully associative
Two-way set associative
Four-way set associative
Tag (virtual page number)
Value (page table entry)
TLB Entry
Various ways to organize a 16-entry TLB
Lookup
Calculate index (index = tag % num_sets)
Search for tag within the resulting set
Why not use upper bits of tag value for index?
Set
Index

## Slide 18: Associativity Trade-offs
Higher associativity
  Better utilization, fewer collisions
  Slower
  More hardware
Lower associativity
  Fast
  Simple, less hardware
  Greater chance of collisions
How does page size affect TLB performance?

## Slide 19: X86 TLB
TLB management shared by processor and OS
CPU fills TLB on demand from page table (the OS is unaware of TLB misses)
CPU evicts entries when a new entry must be added and no free slots exist
Operating system ensures TLB/page table consistency by flushing entries as needed when the page tables are updated or switched (e.g. during a context switch)
TLB entries can be removed by the OS one at a time using the INVLPG instruction or the entire TLB can be flushed at once by writing a new entry into CR3

## Slide 20: Example: Pentium-M TLBs
Four different TLBs
  Instruction TLB for 4K pages
    128 entries, 4-way set associative
  Instruction TLB for large pages
    2 entries, fully associative
  Data TLB for 4K pages
    128 entries, 4-way set associative
  Data TLB for large pages
    8 entries, 4-way set associative
All TLBs use LRU replacement policy
Why different TLBs for instruction, data, and page sizes?

## Slide 21: SPARC TLB
SPARC is RISC (simpler is better) CPU
Example of a “software-managed” TLB
TLB miss causes a fault, handled by OS
OS explicitly adds entries to TLB
OS is free to organize its page tables in any way it wants because the CPU does not use them
E.g. Linux uses a tree like X86, Solaris uses a hash table

## Slide 22: Minimizing Flushes
On SPARC, TLB misses trap to OS (SLOW)
We want to avoid TLB misses
Retain TLB contents across context switch
SPARC TLB entries enhanced with a context id
Context id allows entries with the same VPN to coexist in the TLB (e.g. entries from different process address spaces)
When a process is switched back onto a processor, chances are that some of its TLB state has been retained from the last time it ran
Some TLB entries shared (OS kernel memory)
  Mark as global
  Context id ignored during matching

## Slide 23: Example:UltraSPARC III TLBs
Five different TLBs
Instruction TLBs
  16 entries, fully associative (supports all page sizes)
  128 entries, 2-way set associative (8K pages only)
Data TLBs
  16 entries, fully associative (supports all page sizes)
  2 x 512 entries, 2-way set associative (each supports one page size per process)
Valid page sizes – 8K (default), 64K, 512K, and 4M
13-bit context id – 8192 different concurrent address spaces
What happens if you have > 8192 processes?

## Slide 24: Speeding Up TLB Miss Handling
In some cases a huge amount of time can be spent handling TLB misses (2-50% in one study of SuperSPARC and SunOS)
Many architectures that use software managed TLBs have hardware assisted TLB miss handling
SPARC uses a large, virtually-indexed, direct-mapped, physically contiguous table of recently used TLB entries called the Translation Storage Buffer (TSB)
The location of the TSB is loaded into the processor on context switch (implies one TSB per process)
On TLB miss, hardware calculates the offset of the matching entry into the TSB and supplies it to the software TLB miss handler
In most cases, the software TLB miss handler only needs to make a tag comparison to the TSB entry, load it into the TLB, and return
If an access misses in the TSB then a slow software search of page tables is required
Notes: http://www.phptr.com/articles/article/asp?p=174103&seqNum=1