## Slide 1: I/O System: Disks
Questions answered in this lecture:
  What are the layers of the I/O systems?
  How does a device driver interact with device controllers?
  What are the characteristics of modern disk drives?
  How do disks schedule requests?
UNIVERSITY of WISCONSIN-MADISON Computer Sciences Department
CS 537 Introduction to Operating Systems
Andrea C. Arpaci-Dusseau Remzi H. Arpaci-Dusseau

## Slide 2: I/O System
user process
file system
I/O system
device driver
user process
user process
OS
device controller
disk

## Slide 3: Device Drivers
Mechanism: Encapsulate details of device
  File system not aware of device details
  Much of OS code is in device drivers
    Responsible for many of the errors as well!
Device driver interacts with device controller
  Read status registers, read data
  Write control registers, provide data for write operations
How does device driver access controller?
  Special instructions
    Valid only in kernel mode, No longer popular
  Memory-mapped
    Read and write to special memory addresses
    Protect by placing in kernel address space only
      May map part of device in user address space for fast access

## Slide 4: Device Drivers: Starting I/O
Programmed I/O (PIO)
  Must initiate and watch every byte
  Disadvantage: Large overhead for large transfers
Direct Memory Access (DMA)
  Offload work from CPU to to special-purpose processor responsible for large transfers
  CPU: Write DMA command block into main memory
    Pointer to source and destination address
    Size of transfer
  CPU: Inform DMA controller of address of command block
  DMA controller: Handles transfer with I/O device controller
  Can use physical or virtual addresses (DVMA)
    Disadvantages of each approach??

## Slide 5: Device Drivers: When is I/O complete?
Polling
  Handshake by setting and clearing flags
    Controller sets flag when done
    CPU repeatedly checks flag
  Disadvantage: Busy-waiting
    CPU wastes cycles when I/O device is slow
    Must be attentive to device, or could lose data
Interrupts: Handle asynchronous events
  Controller asserts interrupt request line when done
  CPU jumps to appropriate interrupt service routine (ISR)
    Interrupt vector: Table of ISR addresses
    Index by interrupt number
  Low priority interrupts postponed until higher priority finished
  Combine with DMA: Do not interrupt CPU for every byte

## Slide 6: Disk Controller
Responsible for interface between OS and disk drive
  Common interfaces: ATA/IDE vs. SCSI
    ATA/IDE used for personal storage
    SCSI for enterprise-class storage
Basic operations
  Read block
  Write block
OS does not know of internal complexity of disk
  Disk exports array of Logical Block Numbers (LBNs)
  Disks map internal sectors to LBNs
Implicit contract:
  Large sequential accesses to contiguous LBNs achieve much better performance than small transfers or random accesses

## Slide 7: Disk Terminology
spindle
platter
surface
track
cylinder
sector
read/write head
ZBR (Zoned bit recording): More sectors on outer tracks

## Slide 8: Disk Performance
How long to read or write n sectors?
  Positioning time + Transfer time (n)
  Positioning time: Seek time + Rotational Delay
  Transfer time: n / (RPM * bytes/track)
Seek: Time to position head over destination cylinder
Rotation: Wait for sector to rotate underneath head

## Slide 9: Disk Calculations
Example disk:
  #surfaces: 4
  #tracks/surface: 64K
  #sectors/track: 1K (assumption??)
  #bytes/sector: 512
  RPM: 7200 = 120 tracks/sec
  Seek cost: 1.3ms - 16ms
Questions
  How many disk heads? How many cylinders?
  How many sectors/cylinder? Capacity?
  What is the maximum transfer rate (bandwidth)?
  Average positioning time for random request?
  Time and bandwidth for random request of size:
    4KB?
    128 KB?
    1 MB?

## Slide 10: Disk Abstraction
How should disk map internal sectors to LBNs?
Goal: Sequential accesses (or contiguous LBNs) should achieve best performance
Approaches:
  Traditional ordering
  Serpentine ordering

## Slide 11: Positioning
Drive servo system keeps head on track
  How does the disk head know where it is?
  Platters not perfectly aligned, tracks not perfectly concentric (runout) -- difficult to stay on track
  More difficult as density of disk increase
    More bits per inch (BPI), more tracks per inch (TPI)
Use servo burst:
  Record placement information every few (3-5) sectors
  When head cross servo burst, figure out location and adjust as needed

## Slide 12: Reliability
Disks fail more often....
  When continuously powered-on
  With heavy workloads
  Under high temperatures
How do disks fail?
  Whole disk can stop working (e.g., motor dies)
  Transient problem (cable disconnected)
  Individual sectors can fail (e.g., head crash or scratch)
    Data can be corrupted or block not readable/writable
Disks can internally fix some sector problems
  ECC (error correction code): Detect/correct bit flips
  Retry sector reads and writes: Try 20-30 different offset and timing combinations for heads
  Remap sectors: Do not use bad sectors in future
    How does this impact performance contract??

## Slide 13: Buffering
Disks contain internal memory (2MB-16MB) used as cache
Read-ahead: “Track buffer”
  Read contents of entire track into memory during rotational delay
Write caching with volatile memory
  Immediate reporting: Claim written to disk when not
  Data could be lost on power failure
    Use only for user data, not file system meta-data
Command queueing
  Have multiple outstanding requests to the disk
  Disk can reorder (schedule) requests for better performance

## Slide 14: Disk Scheduling
Goal: Minimize positioning time
  Performed by both OS and disk itself; Why?
FCFS: Schedule requests in order received
  Advantage: Fair
  Disadvantage: High seek cost and rotation
Shortest seek time first (SSTF):
  Handle nearest cylinder next
  Advantage: Reduces arm movement (seek time)
  Disadvantage: Unfair, can starve some requests

## Slide 15: Disk Scheduling
SCAN (elevator): Move from outer cylinder in, then back out again
  Advantage: More fair to requests, similar performance as SSTF
  Variation: Circular-Scan (C-Scan)
    Move head only from outer cylinder inward (then start over)
    Why??? (Two reasons)
LOOK: SCAN, except stop at last request
Calculate seek distance for workload with cylinder #s: 10, 2, 0, 85, 50, 40, 1, 37, 41; Start at #43, moving up

## Slide 16: Disk Scheduling
Real goal: Minimize positioning time
  Trend: Rotation time dominating positioning time
    Very difficult for OS to predict
      ZBR, track and cylinder skew, serpertine layout, bad block remapping, caching, ...
    Disk controller can calculate positioning time
  Shortest positioning time first (SPTF)
Technique to prevent starvation
  Two queues
  Handle requests in current queue
  Add newly arriving requests added to other queue