## Slide 1: Storage System: RAID
Questions answered in this lecture:
  What is RAID?
  How does one trade-off between: performance, capacity, and reliability?
  What is RAID-0, RAID-1, RAID-4, and RAID-5?
UNIVERSITY of WISCONSIN-MADISON Computer Sciences Department
CS 537 Introduction to Operating Systems
Andrea C. Arpaci-Dusseau Remzi H. Arpaci-Dusseau

## Slide 2: Motivation: Why use multiple disks?
Capacity
  More disks allows us to store more data
Performance
  Access multiple disks in parallel
  Each disk can be working on independent read or write
  Overlap seek and rotational positioning time for all
Reliability
  Recover from disk (or single sector) failures
  Will need to store multiple copies of data to recover
RAID: Redundant Array of Inexpensive/Independent Disks

## Slide 3: Hardware vs. Software RAID
Hardware RAID
  Storage box you attach to computer
  Same interface as single disk, but internally much more
    Multiple disks
    More complex controller
    NVRAM (holding parity blocks)
Software RAID
  OS (device driver layer) treats multiple disks like a single disk
  Software does all extra work
Interface for both
  Linear array of bytes, just like a single disk (but larger)

## Slide 4: RAID-0: Striping
Stripe blocks across disks in a “chunk” size
  How to pick a reasonable chunk size?
0
4
8
12
1
5
9
13
2
6
10
14
3
7
11
15
How to calculate where chunk # lives?
Disk:
Offset within disk:

## Slide 5: RAID-0: Striping
Evaluate for D disks
Capacity: How much space is wasted?
Performance: How much faster than 1 disk?
Reliability: More or less reliable than 1 disk?
0
4
8
12
1
5
9
13
2
6
10
14
3
7
11
15

## Slide 6: RAID-1: Mirroring
Motivation: Handle disk failures
Put copy (mirror or replica) of each chunk on another disk
0
2
4
6
0
2
4
6
1
3
5
7
1
3
5
7
Capacity:
Reliability:
Performance:

## Slide 7: RAID-4: Parity
Motivation: Improve capacity
Idea: Allocate parity block to encode info about blocks
  Parity checks all other blocks in stripe across other disks
Parity block = XOR over others (gives “even” parity)
  Example: 0 1 0 --> Parity value?
How do you recover from a failed disk?
  Example: x 0 0 and parity of 1
  What is the failed value?
0
3
6
9
1
4
7
10
2
5
8
11
P0
P1
P2
P3

## Slide 8: RAID-4: Parity
Capacity:
Reliability:
Performance:
  Reads
  Writes: How to update parity block?
    Two different approaches
      Small number of disks (or large write):
      Large number of disks (or small write):
    Parity disk is the bottleneck
0
3
6
9
1
4
7
10
2
5
8
11
P0
P1
P2
P3

## Slide 9: RAID-5: Rotated Parity
Capacity:
Reliability:
Performance:
  Reads:
  Writes:
  Still requires 4 I/Os per write, but not always to same parity disk
0
3
6
P3
1
4
P2
9
2
P1
7
10
P0
5
8
11
Rotate location of parity across all disks

## Slide 10: Advanced Issues
What happens if more than one fault?
  Example: One disk fails plus “latent sector error” on another
  RAID-5 cannot handle two faults
  Solution: RAID-6 (e.g., RDP) Add multiple parity blocks
Why is NVRAM useful?
  Example: What if update 2, don’t update P0 before power failure (or crash), and then disk 1 fails?
  NVRAM solution: Use to store blocks updated in same stripe
    If power failure, can replay all writes in NVRAM
  Software RAID solution: Perform parity scrub over entire disk
0
3
6
9
1
4
7
10
2’
5
8
11
P0
P1
P2
P3

## Slide 11: Conclusions
RAID turns multiple disks into a larger, faster, more reliable disk
RAID-0: Striping Good when performance and capacity really matter, but reliability doesn’t
RAID-1: Mirroring Good when reliability and write performance matter, but capacity (cost) doesn’t
RAID-5: Rotating Parity Good when capacity and cost matter or workload is read-mostly
Good compromise choice