## Slide 1
WOOF : The World’s First Opensource Out-of-order Processor
Raghu Balasubramanian, Jaikrishnan Menon, Karu Sankaralingam
Why build a processor?
A Research tool
Fast and more accurate measurements.
Building a new branch predictor ? in addition to miss-prediction rates, get the area, power and timing hit.
Technology constrains of unreliable hardware and energy efficiency becoming more significant today!
A Teaching tool
Create real hardware
We used a version of this processor in CS 758. Student teams had 2 weeks to improve processor performance. Student teams designed branch predictors, played with the caching schemes etc.,
It’s cool
We will have the worlds first free and open-source out of order superscalar processor capable of running Linux standalone.
Our Out of Order Implementation
Links and References
[1] OpenRISC official website http://opencores.org/or1k
[2] GNU toolchain http://openrisc.net/toolchain-build.html
[3] Xilinx FPGA port http://chokladfabriken.org/projects/orpsoc-atlys
[4] Julius Baxter, “Open Source Hardware Development and the OpenRISC Project” Master’s Thesis at IMIT
[5] M. de Kruijf, and K. Sankaralingam, “Idempotent Processor Architecture”
MICRO '11: International Symposium on Microarchitecture, 2011.
[6] S. Nomura, M. Sinclair, C. Ho, V. Govindaraju, M. de Kruijf, and K. Sankaralingam ”Sampling + DMR: Practical and Low-overhead Permanent Fault Detection.” ISCA '11
Dual issue out of order design pin compatible with ORPSoC
Configurable micro-architectural parameters include
Number of physical registers
Number of functional units
Instruction queue depths
Register write back ports
Activelist depth
Initial Results
Case studies
Idempotent Processing
Exception handling takes up significant resources in-terms of chip area and energy efficiency (check-pointing logic, recovery logic etc.,).
Also complicates design and verification efforts.
Idempotence: Regions of code that may be executed multiple times producing the same result.
Exception? restarting execution from the start of this region would suffice[5].
Area, power and design effort reduction.
Sampling-DMR
A fault detection mechanism that guarantees 100% detection of permanent faults[6]
< 1% performance overhead
Need controllable fault injection models
Applications + full system required
Speedups compared to In-Order processor
Evaluation methodology
Micro-benchmarks compiled on gcc (linked with newlibc)
Single issue as golden model
VCS for simulation
Perfect branch predictor
Offline memory disambiguation
Performance limiters (as seen from the issue side)
Chart: 
| parser_1 | gzip_1 | equake_1 | sieve | ammp_1 | gzip_2 | bzip2_2 | ammp_2 | bzip2_1 | bzip2_3 | fft | forward_GMTI | doppler_GMTI | vadd | dhry | twolf_3 | fft2_GMTI | fft4_GMTI | Geometric Mean
In-order | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Pred : Always taken, LSU : inorder | 1.026 | 1.3521 | 1.2491 | 1.0543 | 1.0812 | 1.0308 | 0.96928 | 0.98622 | 0.97518 | 0.96141 | 0.84903 | 0.79549 | 0.79855 | 0.8595 | 0.87426 | 0.80126 | 0.76884 | 0.80626 | 0.93542
Pred : Perfect, LSU : inorder | 1.239 | 1.4181 | 1.585 | 1.1489 | 1.304 | 1.1554 | 1.211 | 1.2763 | 1.1939 | 1.1838 | 1.1036 | 1.0843 | 1.0799 | 1.0865 | 1.0117 | 1.0206 | 1.0351 | 0.97581 | 1.2001
Pred : Perfect, LSU : Perfect | 1.6717 | 1.6684 | 1.5553 | 1.3296 | 1.2955 | 1.2705 | 1.2672 | 1.2712 | 1.212 | 1.2174 | 1.0582 | 1.0605 | 1.0602 | 1.0387 | 1.0273 | 1.0214 | 1.009 | 0.95965 | 1.2497
Chart: 
| parser_1 | gzip_1 | sieve | ammp_2 | gzip_2 | ammp_1 | bzip2_3 | matrix_1 | bzip2_2 | bzip2_1 | twolf_3 | fft | dct8x8 | forward_GMTI | dhry | vadd | transpose_GMTI | doppler_GMTI | fft2_GMTI | fft4_GMTI
2 insn issued | 69.36 | 79.81 | 49.33 | 75.0335 | 59.51 | 73.7659 | 69.4285 | 58.45 | 66.8862 | 68.3205 | 62.06 | 42.13 | 46.23 | 46.03 | 43.55 | 38.21 | 33.803 | 41.8 | 42.02 | 43.99
Structural hazard | 7.38 | 9.26 | 8.61 | 10.6594 | 6.62 | 5.9822 | 9.5568 | 6.7 | 10.0889 | 6.3785 | 10.83 | 10.28 | 12.27 | 10.31 | 8.68 | 9.06 | 8.89 | 10.1 | 11.1 | 10.6
IQ backpressure | 23.21 | 10.84 | 41.75 | 11.007 | 29.8 | 15.3953 | 15.237 | 23.89 | 7.928 | 5.3959 | 3.68 | 13.8 | 4.84 | 6.19 | 9.9 | 14.8 | 19.2 | 8.09 | 6.87 | 4.4
Single Step | 0.05 | 0.09 | 0.31 | 3.3001 | 4.07 | 4.8566 | 5.7777 | 10.96 | 15.0968 | 19.9052 | 23.43 | 33.79 | 36.66 | 37.47 | 37.87 | 37.93 | 38.107 | 38.87 | 40.01 | 41.01
Results
20% increase in performance on average
JAL and JR instructions : performance killers, they are single stepped to avoid data hazards
Next steps
Statistics  Analysis  Balanced design
Better exception handling support
Synthesize and run linux
Opensource code:
Available in Spring 2013
The OpenRISC platform
What’s new?
An Out-of-Order Processor
A super-scalar processor implementation
Synthesizable
Able to run a full system standalone
Easy to add instructions, customize on micro-architectural parameters
Support for statistics gathering
LLVM Compiler support
Advantages : easier extendibility, faster compile times, target independent optimizations, diagnostics.
or32 Target support : skeleton backend  or1k assembly generator  binutils  or32 binary
Status : compiles micro-benchmarks and SPEC2000 benchmarks
The Design
9 man month effort
Functional units and decode logic reused from single issue in-order core
Modular: Easy to add functional units, instructions, stat counters
Current status : Runs binaries that do not require MMU support
A 32-bit RISC load store architecture[1]
A full system software simulator
Toolchains
GNU[2]
LLVM
Operating system support
Linux kernel 3.0
eCos, RTEMS, uCOS-II and FreeRTOS
Bootloaders like U-Boot
System on Chip reference platforms : ORPSoC
Xilinx[3], Altera ports
Support for a number of peripherals including
a debug I/F, Ethernet, VGA, UART, AC97 audio etc.,
On the core is the or1200 : A 5 stage commercially proven RTL implementation