CS/ECE 252: INTRODUCTION TO COMPUTER ENGINEERING

UNIVERSITY OF WISCONSIN—MADISON

Prof. Mikko Lipasti & Prof. Gurinder S. Sohi

TAs: Daniel Chang, Felix Loh, Philip Garcia, Sean Franey, Vignyan Kothinti Naresh, Raghu Raman and Newsha Ardalani

Midterm Examination 4

In Class (50 minutes)

Friday, December 17, 2010

Weight: 17.5%

NO: BOOK(S), NOTE(S), CALCULATORS OF ANY SORT.

This exam has 11 pages, including one page for the LC3 Instruction Set and two blank pages at the end. Plan your time carefully, since some problems are longer than others. You must turn in pages 1 to 7.

LAST NAME:  ___________________________________________________________

FIRST NAME:___________________________________________________________

SECTION: 	 ___________________________________________________________

ID# 		 ___________________________________________________________

| Question | Maximum Point | Points |
| --- | --- | --- |
| 1 | 3 |  |
| 2 | 5 |  |
| 3 | 4 |  |
| 4 | 6 |  |
| 5 | 7 |  |
| Total | 25 |  |

1. Assembly Errors (3 Points)

Consider the following assembly code.

.ORIG x3000

.START

LD R0, ASCII

LD R1, NEG

LOOP    	TRAP x22

BRzp LOOP

TRAP x23

ADD R0, R0, ONELESS

ADD R3, R0, R1

BRp LOOP

HALT  	HALT

ASCII 	.FILL 	x0047

NEG   	.FILL 	xFFBD

ONELESS 	.FILL 	#-1

.END

Briefly explain three assembly errors in the above program (3 points)

2. Two-Pass Assembly Process (5 points)

An assembly language LC-3 program is given below :

.ORIG x3000

AND R2, R2, #0

AND R3, R3, #0

LD R0, INP0

LD R5, INP1

LOOP 	  BRz QUIT

ADD R3, R3, #1

ADD R2, R2, R0

ADD R5, R5, #-1

BR LOOP

QUIT    ST R2, ANSWER

HALT

ANSWER  .FILL x0000

INP1      .FILL x0007

INP0      .FILL x0010

.END

(a). Fill in the symbol table created by the assembler on the first pass of the above program. (3 points)

| Symbol Name | Address |
| --- | --- |

(b) Once the symbol table is created, the assembler then creates a binary version (.obj) of the program as listed below (with 2 missing lines). (2 points)

0101 0100 1010 0000 ;AND R2, R2, #0

0101 0110 1110 0000 ;AND R3, R3, #0

0010 0000 0000 1001 ;LD R0, M0

0010 0010 0000 1001 ;LD R5, M1

0000 0100 0000 0100 ;BRz DONE

0001 0110 1110 0001 ;ADD R3, R3, #1

0001 0100 1000 0000 ;ADD R2, R2, R0

____ ____ ____ ____ ;ADD R5, R5, #-1

0000 1111 1111 1011 ;BR LOOP

0011 0100 0000 0001 ;ST R2, RESULT

____ ____ ____ ____ ;HALT (TRAP x25)

0000 0000 0000 0000 ;.FILL x0000

0000 0000 0000 0111 ;.FILL x0007

0000 0000 0001 0000 ;.FILL x0010

3. I/O in LC-3 (4 Points)

An LC-3 program is provided below:

.ORIG x3000

LD   R0, ASCII

LD   R1, NEG

AGAIN    	LDI  R2, DSR

BRzp AGAIN

STI  R0, DDR

ADD  R0, R0, #1

ADD  R3, R0, R1

BRn  AGAIN

HALT

ASCII    	.FILL x0044

NEG      	.FILL xFFB6

DSR      	.FILL xFE04              ; Address of DSR

DDR      	.FILL xFE06              ; Address of DDR

.END

a)      What does this program do? (3 points)

b)      What is the purpose of the Display Status Register (DSR)? (1 points)

4. Subroutines (6 Points)

1 	;CODE TO INPUT AND PRINT 6 CHARACTERS

2

3        	 .ORIG x3000

4          AND R0, R0, #0          	; Initialise R0, our counter

5 LOOP

6        	 LEA R1, INPSTRING       	; R1 now has base of INPSTRING

7        	 ADD R1, R1, R0          	; R1 now has base + offset = R0

8        	 ST R0, SAVEREG1         	; SAVE R0

9        	 JSR ONECHAR             	; Call Subroutine

10          LD __, SAVEREG1         	; Restore ??

11        	 ADD R0, R0, #1          	; Increment R0

12        	 LD R1, LENGTH           	; Load R1 with minus length

13        	 ADD R1, R1, R0          	;

14        	 BRn LOOP                	; loop till 6 characters are reached

15        	 LEA R0, INPSTRING       	; Get ready to print

16        	 PUTS                    	; TRAP X22 And print

17        	 HALT                   	; We're done

18

19 ONECHAR

20        	 ST __, SAVEREG2         	; SAVE ??

21        	 GETC                    	; TRAP X20 Get a character from 								; Keyboard input.

22        	 LD __, SAVEREG2         	; Restore ??

23        	 STR R0, R1, #0          	; Save keyboard inp(R0 contains input)

24        	 RET

25

26 LENGTH  .FILL xFFFA             	; minus Length (-6)

27 KBSR    .FILL xFE00

28 KBDR    .FILL xFE02

29 SAVEREG1  .FILL x0

30 SAVEREG2  .FILL x0

31 INPSTRING .BLKW 7

32         .END

In the code above the Subroutine ONECHAR takes 1 character from the user (keyboard) and saves it into the memory. The assembly code uses ONECHAR in a loop 6 times to input 6 characters and saves it to the memory. Finally it prints the string to the screen.

(a) 	Line 8 saves R0 before calling the subroutine ONECHAR. Briefly explain why this is necessary. (2 points)

(b)	What other register needs to be stored and restored inside the subroutine [Fill in lines 20, 22].

(c)	Once the subroutine is done, we will have to restore the registers. Fill in the register restored in line 10 (1 point)

5. General Questions(7 points)

Circle the best answer.

1. A new service routine is defined starting in memory location x3700. After loading a program that calls this subroutine, the user sets memory location x0062 to x3700. Which of the following can be used to call this subroutine?

a. 	TRAP x3700

b.  TRAP x0037

c.	TRAP x63

d.  TRAP x62

2. JSRR R3 is equivalent to

a.	LEA R3, #1

JMP R7, #0

b. 	LEA R7, #1

JMP R3, #0

c. 	LEA R3, #1

JMP R3, #0

d. All of the above are equivalent

3. Which of the following pseudo-op tells the assembler where the program ends

a. END

b. .END

c. HALT

d. END

4. Assembling the instruction ADD R1, R1, #45 causes which of the following errors

a. ADD instruction takes only 3 register sources (2 sources + 1 destination)

b. Immediate value (45) is out of range

c. R1 is not initialised

d. The instruction does not cause an error.

5. How many memory locations are used by the following assembly directive :

PALINDROME .STRINGZ "radar"

a. 5

b. 4

c. 7

d. 6

6. In the PennSim simulator, the lc3os.asm is assembled and lc3os.obj is loaded. At what address location is the operating system code start?

a. x0000

b. x0200

c. x3000

d. x2000

7. Which of the following combinations best describes the way input/output service routines work in the LC-3 processor

a. 	Memory mapped I/O and interupt driven

b. 	Memory mapped I/O and polling

c. 	Special opcode for I/O and polling

d. 	Special opcode for I/O and interupt driven

Scratch Sheet 1

(in case you need additional space for some of your answers)

Scratch Sheet 2

(in case you need additional space for some of your answers)

LC-3 Instruction Set (Entered by Mark D. Hill on 03/14/2007; last update 03/15/2007)

PC’: incremented PC. setcc(): set condition codes N, Z, and P. mem[A]:memory contents at address A.
SEXT(immediate): sign-extend immediate to 16 bits. ZEXT(immediate): zero-extend immediate to 16 bits.

15  14  13  12  11  10   9   8   7   6   5   4   3   2   1   0

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ ADD DR, SR1, SR2 ; Addition

| 0   0   0   1 |    DR     |    SR1    | 0 | 0   0 |    SR2    |

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ DR  SR1 + SR2 also setcc()

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ ADD DR, SR1, imm5 ; Addition with Immediate

| 0   0   0   1 |    DR     |    SR1    | 1 |       imm5        |

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ DR  SR1 + SEXT(imm5) also setcc()

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ AND  DR, SR1, SR2 ; Bit-wise AND

| 0   1   0   1 |    DR     |    SR1    | 0 | 0   0 |    SR2    |

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ DR  SR1 AND SR2 also setcc()

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ AND DR,SR1,imm5 ; Bit-wise AND with Immediate

| 0   1   0   1 |    DR     |    SR1    | 1 |       imm5        |

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ DR  SR1 AND SEXT(imm5) also setcc()

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ BRx,label (where x={n,z,p,zp,np,nz,nzp}); Branch

| 0   0   0   0 | n | z | p |              PCoffset9            | GO  ((n and N) OR (z AND Z) OR (p AND P))

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ if(GO is true) then PCPC’+ SEXT(PCoffset9)

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ JMP BaseR ; Jump

| 1   1   0   0 | 0   0   0 |   BaseR   | 0   0   0   0   0   0 |

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ PC  BaseR

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ JSR label ; Jump to Subroutine

| 0   1   0   0 | 1 |                  PCoffset11               |

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ R7  PC’, PC  PC’ + SEXT(PCoffset11)

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ JSRR BaseR ; Jump to Subroutine in Register

| 0   1   0   0 | 0 | 0   0 |   BaseR   | 0   0   0   0   0   0 |

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ temp  PC’, PC  BaseR, R7  temp

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ LD DR, label ; Load PC-Relative

| 0   0   1   0 |    DR     |              PCoffset9            |

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ DR  mem[PC’ + SEXT(PCoffset9)] also setcc()

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ LDI DR, label ; Load Indirect

| 1   0   1   0 |    DR     |              PCoffset9            |

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ DRmem[mem[PC’+SEXT(PCoffset9)]] also setcc()

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ LDR DR, BaseR, offset6 ; Load Base+Offset

| 0   1   1   0 |    DR     |   BaseR   |        offset6        |

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ DR  mem[BaseR + SEXT(offset6)] also setcc()

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ LEA, DR, label ; Load Effective Address

| 1   1   1   0 |    DR     |              PCoffset9            |

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ DR  PC’ + SEXT(PCoffset9) also setcc()

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ NOT DR, SR ; Bit-wise Complement

| 1   0   0   1 |    DR     |     SR    | 1 | 1   1   1   1   1 |

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ DR  NOT(SR) also setcc()

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ RET ; Return from Subroutine

| 1   1   0   0 | 0   0   0 | 1   1   1 | 0   0   0   0   0   0 |

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ PC  R7

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ RTI ; Return from Interrupt

| 1   0   0   0 | 0   0   0   0   0   0   0   0   0   0   0   0 |

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ See textbook (2nd Ed. page 537).

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ ST SR, label ; Store PC-Relative

| 0   0   1   1 |    SR     |              PCoffset9            |

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ mem[PC’ + SEXT(PCoffset9)]  SR

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ STI, SR, label ; Store Indirect

| 1   0   1   1 |    SR     |              PCoffset9            |

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ mem[mem[PC’ + SEXT(PCoffset9)]]  SR

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ STR SR, BaseR, offset6 ; Store Base+Offset

| 0   1   1   1 |    SR     |   BaseR   |        offset6        |

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ mem[BaseR + SEXT(offset6)]  SR

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ TRAP ; System Call

| 1   1   1   1 | 0   0   0   0 |           trapvect8           |

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ R7  PC’, PC  mem[ZEXT(trapvect8)]

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ ; Unused Opcode

| 1   1   0   1 |                                               |

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+ Initiate illegal opcode exception

15  14  13  12  11  10   9   8   7   6   5   4   3   2   1   0