CS/ECE 252: INTRODUCTION TO COMPUTER ENGINEERING

UNIVERSITY OF WISCONSIN—MADISON

Instructor: Andy Phelps

TAs: Peter Ohmann, Newsha Ardalani and Jai Menon

Midterm Examination 4

In Class (50 minutes)

Friday, May 6

Weight: 15%

This exam has 12 pages, including a blank page.

You must turn in all pages.

For your convenience, a listing of the LC-3 instruction set is given at the end of this booklet, as well as a listing of the ASCII code.

NO: BOOK(S), NOTE(S), CALCULATORS OF ANY SORT.

LAST NAME:  ___________________________________________________________

FIRST NAME:___________________________________________________________

SECTION: 	 ___________________________________________________________

ID# 		 ___________________________________________________________

| Question | Maximum Points | Points |
| --- | --- | --- |
| 1 | 4 |  |
| 2 | 7 |  |
| 3 | 7 |  |
| 4 | 7 |  |
| 5 | 10 |  |
| Total | 35 |  |

1. Assembly Errors (4 Points)

In the following template for an assembly program, circle any labels where the first pass of the assembler would report an error (if any).

.ORIG x3000

Main		...

...

Loop		...

...

End		...

...

Add		...

...

Sum	 	...

...

Loop		...

...

And		...

...

Or		...

...

X10		...

...

.END

2. Two-Pass Assembly Process (7 points)

An assembly language LC-3 program is given below:

.ORIG 		x3000

AND		R2, R2, #0

AND 		R3, R3, #0

LD  		R0, M0

LD  		R4, M1

LOOP 	     	BRz      	DONE

JSR		INCR3

ADD    		R2, R2, R0

JSR		DECR4

BR       		LOOP

DONE       	ST        		R2, ANSWER

HALT

INCR3		ADD     	R3, R3, #1

RET

DECR4		ADD 		R4, R4, #-1

RET

; Storage area for variables below:

ANSWER  	.BLKW	 	#4

M0      		.FILL 		x0007

M1      		.FILL 		x0010

.END

a) Fill in the symbol table created by the assembler on the first pass of the above program. (4 points)

| Symbol Name | Address |
| --- | --- |

Once the symbol table is created, the assembler then creates a binary version (.obj) of the program.  A portion is listed below.  Three lines are missing the binary.

0101 0100 1010 0000 ;AND R2, R2, #0

0101 0110 1110 0000 ;AND R3, R3, #0

0010 0000 0001 0000 ;LD R0, M0

0010 0010 0001 0000 ;LD R4, M1

0000 0100 0000 0100 ;BRz DONE

____ ____ ____ ____ ;JSR INCR3

0001 0100 1000 0000 ;ADD R2, R2, R0

____ ____ ____ ____ ;JSR DECR4

0000 1111 1111 1011 ;BR LOOP

0011 0100 0000 0001 ;ST R2, RESULT

____ ____ ____ ____ ;HALT (TRAP x25)

0001 0110 1110 0001 ;ADD R3, R3, #1

1100 0001 1100 0000 ;RET

0001 1001 0011 1111;ADD R4, R4, #-1

1100 0001 1100 0000 ;RET

b) For each of the above missing lines, circle the correct binary value: (3 points)

Missing Line #1

1) 0100 1000 0000 0100

2) 0100 1000 0000 0101

3) 0100 1000 0000 1011

Missing Line #2

1) 0100 1000 0000 0100

2) 0100 1000 0000 0101

3) 0100 1000 0000 1101

Missing Line #3

1) 1111 0000 0010 0101

2) 1111 0000 0001 1001

3) 1111 0000 0000 1101

3. I/O in LC-3 (7 Points)

An LC-3 program is provided below:

.ORIG x3000

LD   	R0, ASCII

LD   	R1, NEG

AGAIN 		LDI  	R2, DSR

BRzp 	AGAIN

STI  	R0, DDR

ADD  	R0, R0, #1

ADD  	R3, R0, R1

BRn  	AGAIN

HALT

ASCII   		.FILL 	x0043

NEG     		.FILL 	xFFB6

DSR      		.FILL 	xFE04              ; Address of DSR

DDR     		.FILL 	xFE06              ; Address of DDR

.END

a)      What is the purpose of  "STI  R0, DDR"?  (1 points)

b)      What is the purpose of reading the Display Status Register (DSR)? (2 point)

c)      What is in DSR bit 14, but we are not using in this program? (1 point)

d)      What does this program do? (3 point)

4. Subroutines (7 Points)

In the code below, the Subroutine ONECHAR takes 1 character from the user (keyboard) and saves it into memory. The assembly code uses ONECHAR in a loop 6 times to input 6 characters and save them to memory. Finally, it prints the string to the screen.

1 	;CODE TO INPUT AND PRINT 6 CHARACTERS

2

3        			.ORIG 	x3000

4          			AND 	R0, R0, #0          		; Initialize R0, our counter

5 	LOOP

6        	 		LEA 	R1, INPSTRING    	; R1 now has base of INPSTRING

7        	 		ADD 	R1, R1, R0          		; R1 now has base + offset = R0

8        	 		ST 	R0, SAVEREG1         	; SAVE R0

9        	 		JSR 	ONECHAR             	; Call Subroutine

10          		LD 	R0, SAVEREG1         	; Restore R0

11        	 		ADD 	R0, R0, #1          		; Increment R0

12        	 		LD 	R1, LENGTH           	; Load R1 with minus length

13        	 		ADD 	R1, R1, R0          		;

14        	 		BRn 	LOOP                		; loop till 6 characters are reached

15        	 		LEA 	R0, INPSTRING       	; Get ready to print

16        	 		PUTS                    		; TRAP x22: Print string

17        			HALT                   		; We're done

18

19 	ONECHAR	ST 	 ____, SAVEREG2         	; SAVE ?? upon entering the subroutine

20        			GETC                    		; TRAP x20: Get a character from keyboard.

21        	 		STR 	 R0, R1, #0          		; Save keyboard input (R0 contains input)

22        		 	LD 	 ____, SAVEREG2         	; Restore ?? before leaving

23        	 		RET

24

25 	LENGTH	.FILL	0xFFFA       		; minus Length (-6)

26 	KBSR		.FILL 	0xFE00

27 	KBDR		.FILL 	0xFE02

28 	SAVEREG1	.FILL 	0x0

29 	SAVEREG2	.FILL 	0x0

30 	INPSTRING	.BLKW 	7

31         			.END

(a) 	Line 8 saves R0 before calling the subroutine ONECHAR. Briefly explain why this is necessary. (2 points)

(b)	What other register needs to be stored and restored inside the subroutine?  Fill in lines 19 and 22 above. (2 points)

(c)	In the program we save and restore registers two places, in lines 8 and 10 and again in lines 19 and 22.  For lines 8 and 10, indicate whether it illustrates Caller-save or Callee-save. (1 point)

(d)       How many times will each character appear on the screen?  Why? (2 point)

5. General Questions (10 points)

Circle the best answer.

I.  A new service routine is defined starting in memory location x3700. After loading a program that calls this subroutine, the user sets memory location x0067 to x3700. Which of the following can be used to call this subroutine?

a.	TRAP x3767

b.  TRAP x67

c. 	TRAP x3700

d.  TRAP x0037

II.  JSR <label> is equivalent to

a.	LEA R7, #0		[that is, 1110 111 000000000]

BRnzp <label>

b. LEA R7, #1

BRnzp <label>

c. LEA R7, <label>

JMP R7

d. All of the above are equivalent

III.  JSRR R3 is equivalent to

a.	LEA R3, #0

JMP R7

b. LEA R7, #1

JMP R3

c. LEA R3, #0

JMP R3

d. LEA R3, #1

JMP R7

IV.  Into what phase of the control state machine is the logic to test for an interrupt signal usually added?

- just before Decode

- just after Decode

- just after Evaluate Address

- just before Execute

- just after Store Result

V.  Which of the following can be used only once in the program?

- .END

- .HALT

- .FILL

- .BLKW

VI.  Assembling the instruction ADD R1, R1, #45 causes which of the following errors?

a. Immediate value is out of range

b. ADD instruction takes only 3 register sources (2 sources + 1 destination)

c. R1 is not initialized

d. The instruction does not cause an error.

VII.  How many memory locations are used by the following assembly directive?:

MYFAVORITE  .STRINGZ  "Exam 4"

a. 3

b. 4

c. 6

d. 7

e. 8

VIII.  Which one of the following is correct about "Caller-save"? (circle the correct answer)

a)  It is better than Callee-save, since the caller knows exactly which registers

the subroutine will overwrite.

b)  It is used primarily in ISAs that have very wide registers.

c)  It might end up saving registers that didn't really need to be saved.

d)  It's particularly useful when entering interrupt handlers, to save the user's registers.

IX.  Comments are:

a) Unimportant because they are only for people, not the assembler.

b) Useful, but only if someone else takes over working on your program.

c) So important that you should have a comment on every line, e.g.

ADD R0,R0,R1	; Adds R1 into R0

d) Important for the author, as well as for reviewers, maintainers, and users of the software.

X.  If you execute a RET instruction in memory location x4231, what is the possible range of values for the PC afterwards?  [PCinc indicates PC after it is incremented.]

- x0000 -- xFFFF

- (PCinc - 2048) -- (PCinc + 2047)

- (PCinc - 256) -- (PCinc + 255)

- (PCinc - 16) -- (PCinc + 15)

Scratch Paper

ASCII Table

Char  Dec  Oct  Hex | Char  Dec  Oct  Hex | Char  Dec  Oct  Hex | Char Dec  Oct   Hex

-------------------------------------------------------------------------------------

(nul)   0 0000 0x00 | (sp)   32 0040 0x20 | @      64 0100 0x40 | `      96 0140 0x60

(soh)   1 0001 0x01 | !      33 0041 0x21 | A      65 0101 0x41 | a      97 0141 0x61

(stx)   2 0002 0x02 | "      34 0042 0x22 | B      66 0102 0x42 | b      98 0142 0x62

(etx)   3 0003 0x03 | #      35 0043 0x23 | C      67 0103 0x43 | c      99 0143 0x63

(eot)   4 0004 0x04 | $      36 0044 0x24 | D      68 0104 0x44 | d     100 0144 0x64

(enq)   5 0005 0x05 | %      37 0045 0x25 | E      69 0105 0x45 | e     101 0145 0x65

(ack)   6 0006 0x06 | &      38 0046 0x26 | F      70 0106 0x46 | f     102 0146 0x66

(bel)   7 0007 0x07 | '      39 0047 0x27 | G      71 0107 0x47 | g     103 0147 0x67

(bs)    8 0010 0x08 | (      40 0050 0x28 | H      72 0110 0x48 | h     104 0150 0x68

(ht)    9 0011 0x09 | )      41 0051 0x29 | I      73 0111 0x49 | i     105 0151 0x69

(nl)   10 0012 0x0a | *      42 0052 0x2a | J      74 0112 0x4a | j     106 0152 0x6a

(vt)   11 0013 0x0b | +      43 0053 0x2b | K      75 0113 0x4b | k     107 0153 0x6b

(np)   12 0014 0x0c | ,      44 0054 0x2c | L      76 0114 0x4c | l     108 0154 0x6c

(cr)   13 0015 0x0d | -      45 0055 0x2d | M      77 0115 0x4d | m     109 0155 0x6d

(so)   14 0016 0x0e | .      46 0056 0x2e | N      78 0116 0x4e | n     110 0156 0x6e

(si)   15 0017 0x0f | /      47 0057 0x2f | O      79 0117 0x4f | o     111 0157 0x6f

(dle)  16 0020 0x10 | 0      48 0060 0x30 | P      80 0120 0x50 | p     112 0160 0x70

(dc1)  17 0021 0x11 | 1      49 0061 0x31 | Q      81 0121 0x51 | q     113 0161 0x71

(dc2)  18 0022 0x12 | 2      50 0062 0x32 | R      82 0122 0x52 | r     114 0162 0x72

(dc3)  19 0023 0x13 | 3      51 0063 0x33 | S      83 0123 0x53 | s     115 0163 0x73

(dc4)  20 0024 0x14 | 4      52 0064 0x34 | T      84 0124 0x54 | t     116 0164 0x74

(nak)  21 0025 0x15 | 5      53 0065 0x35 | U      85 0125 0x55 | u     117 0165 0x75

(syn)  22 0026 0x16 | 6      54 0066 0x36 | V      86 0126 0x56 | v     118 0166 0x76

(etb)  23 0027 0x17 | 7      55 0067 0x37 | W      87 0127 0x57 | w     119 0167 0x77

(can)  24 0030 0x18 | 8      56 0070 0x38 | X      88 0130 0x58 | x     120 0170 0x78

(em)   25 0031 0x19 | 9      57 0071 0x39 | Y      89 0131 0x59 | y     121 0171 0x79

(sub)  26 0032 0x1a | :      58 0072 0x3a | Z      90 0132 0x5a | z     122 0172 0x7a

(esc)  27 0033 0x1b | ;      59 0073 0x3b | [      91 0133 0x5b | {     123 0173 0x7b

(fs)   28 0034 0x1c | <      60 0074 0x3c | \      92 0134 0x5c | |     124 0174 0x7c

(gs)   29 0035 0x1d | =      61 0075 0x3d | ]      93 0135 0x5d | }     125 0175 0x7d

(rs)   30 0036 0x1e | >      62 0076 0x3e | ^      94 0136 0x5e | ~     126 0176 0x7e

(us)   31 0037 0x1f | ?      63 0077 0x3f | _      95 0137 0x5f | (del) 127 0177 0x7f