## Slide 1: GPU Architectures A CPU Perspective
Derek Hower AMD Research 5/21/2013

## Slide 2: Goals
Data Parallelism: What is it, and how to exploit it?
  Workload characteristics
Execution Models / GPU Architectures
  MIMD (SPMD), SIMD, SIMT
GPU Programming Models
  Terminology translations: CPU  AMD GPU  Nvidia GPU
  Intro to OpenCL
Modern GPU Microarchitectures
  i.e., programmable GPU pipelines, not their fixed-function predecessors
Advanced Topics: (Time permitting)
  The Limits of GPUs: What they can and cannot do
  The Future of GPUs: Where do we go from here?

## Slide 3: Data Parallel Execution on GPUs
Data Parallelism, Programming Models, SIMT

## Slide 4: Graphics Workloads
Streaming computation
GPU

## Slide 5: Graphics Workloads
Streaming computation on pixels
GPU

## Slide 6: Graphics Workloads
Identical, Streaming computation on pixels
GPU

## Slide 7: Graphics Workloads
Identical, Independent, Streaming computation on pixels
GPU

## Slide 8: Architecture Spelling Bee
Spell ‘Independent’
P-A-R-A-L-L-E-L

## Slide 9: Generalize: Data Parallel Workloads
Identical, Independent computation on multiple data inputs
3,7
4,0
2,7
5,0
1,7
6,0
0,7
7,0

## Slide 10: Naïve Approach
Split independent work over multiple processors
7,0
6,0
5,0
4,0
CPU0
CPU1
CPU2
CPU3
2,7
3,7
1,7
0,7

## Slide 11: Data Parallelism: A MIMD Approach
Multiple Instruction Multiple Data
Split independent work over multiple processors
7,0
6,0
5,0
4,0
CPU0
Fetch
Decode
Execute
Memory
Writeback
CPU1
Fetch
Decode
Execute
Memory
Writeback
CPU2
Fetch
Decode
Execute
Memory
Writeback
CPU3
Fetch
Decode
Execute
Memory
Writeback
2,7
3,7
1,7
0,7
Program
Program
Program
Program

## Slide 12: Data Parallelism: A MIMD Approach
Multiple Instruction Multiple Data
Split independent work over multiple processors
7,0
6,0
5,0
4,0
CPU0
Fetch
Decode
Execute
Memory
Writeback
CPU1
Fetch
Decode
Execute
Memory
Writeback
CPU2
Fetch
Decode
Execute
Memory
Writeback
CPU3
Fetch
Decode
Execute
Memory
Writeback
2,7
3,7
1,7
0,7
Program
Program
Program
Program
When work is identical (same program):
Single Program Multiple Data (SPMD)
(Subcategory of MIMD)

## Slide 13: Data Parallelism: An SPMD Approach
Single Program Multiple Data
Split identical, independent work over multiple processors
7,0
6,0
5,0
4,0
CPU0
Fetch
Decode
Execute
Memory
Writeback
CPU1
Fetch
Decode
Execute
Memory
Writeback
CPU2
Fetch
Decode
Execute
Memory
Writeback
CPU3
Fetch
Decode
Execute
Memory
Writeback
2,7
3,7
1,7
0,7
Program
Program
Program
Program

## Slide 14: Data Parallelism: A SIMD Approach
Single Instruction Multiple Data
Split identical, independent work over multiple execution units (lanes)
More efficient: Eliminate redundant fetch/decode
7,0
6,0
5,0
4,0
CPU0
Fetch
Decode
Execute
Memory
Writeback
Execute
Execute
Execute
Memory
Memory
Memory
Writeback
Writeback
Writeback
Program
0,7
1,7
2,7
3,7

## Slide 15: SIMD: A Closer Look
One Thread + Data Parallel Ops  Single PC, single register file
7,0
6,0
5,0
4,0
CPU0
Fetch
Decode
Execute
Memory
Writeback
Execute
Execute
Execute
Memory
Memory
Memory
Writeback
Writeback
Writeback
Program
0,7
1,7
2,7
3,7
Register File

## Slide 16: Data Parallelism: A SIMT Approach
Single Instruction Multiple Thread
Split identical, independent work over multiple lockstep threads
Multiple Threads + Scalar Ops  One PC, Multiple register files
7,0
6,0
5,0
4,0
WF0
Fetch
Decode
Execute
Memory
Writeback
Execute
Execute
Execute
Memory
Memory
Memory
Writeback
Writeback
Writeback
Program
0,7
1,7
2,7
3,7

## Slide 17: Terminology Headache #1
It’s common to interchange
‘SIMD’ and ‘SIMT’

## Slide 18: Data Parallel Execution Models
MIMD/SPMD
SIMD/Vector
SIMT
Multiple independent
threads
Multiple lockstep threads
One thread with wide execution datapath

## Slide 19: Execution Model Comparison
MIMD/SPMD
SIMD/Vector
SIMT
Example Architecture | Multicore CPUs | x86 SSE/AVX | GPUs
Pros | More general: supports TLP | Can mix sequential & parallel code | Easier to program Gather/Scatter operations
Cons | Inefficient for data parallelism | Gather/Scatter can be awkward | Divergence kills performance
Notes: Will explain pros/cons in depth later…this is a preview. End slide with: “Calling GPUs SIMT is a simplification. There is more to the story…”

## Slide 20: GPUs and Memory
GPU
Recall: GPUs perform Streaming computation 
Streaming memory access
DRAM latency: 100s of GPU cycles
How do we keep the GPU busy (hide memory latency)?

## Slide 21: Hiding Memory Latency
Options from the CPU world:
Caches
  Need spatial/temporal locality
OoO/Dynamic Scheduling
  Need ILP
Multicore/Multithreading/SMT
  Need independent threads




## Slide 22: Multicore Multithreaded SIMT
Many SIMT “threads” grouped together into GPU “Core”
SIMT threads in a group ≈ SMT threads in a CPU core
  Unlike CPU, groups are exposed to programmers
Multiple GPU “Cores”
GPU “Core”
GPU “Core”
GPU

## Slide 23: Multicore Multithreaded SIMT
Many SIMT “threads” grouped together into GPU “Core”
SIMT threads in a group ≈ SMT threads in a CPU core
  Unlike CPU, groups are exposed to programmers
Multiple GPU “Cores”
GPU “Core”
GPU “Core”
GPU
This is a GPU Architecture (Whew!)
Notes: What do we call these things…?

## Slide 24: GPU Component Names
GPU “Core”
Processing Element
SIMD Unit
Compute Unit
GPU Device
AMD/OpenCL
Derek’s CPU Analogy
Lane
Pipeline
Core
Device
Notes: “Derek” heavily influenced by Henn&Patt

## Slide 25: GPU Programming Models
OpenCL

## Slide 26: GPU Programming Models
CUDA – Compute Unified Device Architecture
  Developed by Nvidia -- proprietary
  First serious GPGPU language/environment
OpenCL – Open Computing Language
  From makers of OpenGL
  Wide industry support: AMD, Apple, Qualcomm, Nvidia (begrudgingly), etc.
C++ AMP – C++ Accelerated Massive Parallelism
  Microsoft
  Much higher abstraction that CUDA/OpenCL
OpenACC – Open Accelerator
  Like OpenMP for GPUs (semi-auto-parallelize serial code)
  Much higher abstraction than CUDA/OpenCL
Notes: Will focus on OpenCL, but will compare to CUDA with terminology translation

## Slide 27: GPU Programming Models
CUDA – Compute Unified Device Architecture
  Developed by Nvidia -- proprietary
  First serious GPGPU language/environment
OpenCL – Open Computing Language
  From makers of OpenGL
  Wide industry support: AMD, Apple, Qualcomm, Nvidia (begrudgingly), etc.
C++ AMP – C++ Accelerated Massive Parallelism
  Microsoft
  Much higher abstraction that CUDA/OpenCL
OpenACC – Open Accelerator
  Like OpenMP for GPUs (semi-auto-parallelize serial code)
  Much higher abstraction than CUDA/OpenCL
Notes: Will focus on OpenCL, but will compare to CUDA with terminology translation

## Slide 28: OpenCL
Early CPU languages were light abstractions of physical hardware
  E.g., C
Early GPU languages are light abstractions of physical hardware
  OpenCL + CUDA

## Slide 29: OpenCL
Early CPU languages were light abstractions of physical hardware
  E.g., C
Early GPU languages are light abstractions of physical hardware
  OpenCL + CUDA
GPU “Core”
GPU “Core”
GPU
GPU Architecture

## Slide 30: OpenCL
Early CPU languages were light abstractions of physical hardware
  E.g., C
Early GPU languages are light abstractions of physical hardware
  OpenCL + CUDA
GPU “Core”
GPU “Core”
GPU
Workgroup
Workgroup
NDRange
GPU Architecture
OpenCL Model
Wavefront
Work-item

## Slide 31: NDRange
N-Dimensional (N = 1, 2, or 3) index space
  Partitioned into workgroups, wavefronts, and work-items
NDRange
Workgroup
Workgroup

## Slide 32: Kernel
Run an NDRange on a kernel (i.e., a function)
Same kernel executes for each work-item
  Smells like MIMD/SPMD
3,7
4,0
2,7
5,0
1,7
6,0
0,7
7,0
Kernel

## Slide 33: Kernel
3,7
4,0
2,7
5,0
1,7
6,0
0,7
7,0
Kernel
Run an NDRange on a kernel (i.e., a function)
Same kernel executes for each work-item
  Smells like MIMD/SPMD…but beware, it’s not!
Workgroup

## Slide 34: OpenCL Code
__kernel
void flip_and_recolor(__global float3 **in_image,
__global float3 **out_image,
int img_dim_x, int img_dim_y)
{
int x = get_global_id(1); // get work-item id in dim 1
int y = get_global_id(2); // get work-item id in dim 2
out_image[img_dim_x - x][img_dim_y - y] =
recolor(in_image[x][y]);
}

## Slide 35: GPU Microarchitecture
AMD Graphics Core Next

## Slide 36: GPU Hardware Overview
GPU “Core”
GPU
GPU
L2 Cache
GDDR5
L1 Cache
Local Memory
SIMT
SIMT
SIMT
SIMT
Registers
L1 Cache
Local Memory
SIMT
SIMT
SIMT
SIMT
Registers
GPU “Core”

## Slide 37: Compute Unit – A GPU Core
Compute Unit (CU) – Runs Workgroups
  Contains 4 SIMT Units
  Picks one SIMT Unit per cycle for scheduling
SIMT Unit – Runs Wavefronts
  Each SIMT Unit has 10 wavefront instruction buffer
  Takes 4 cycles to execute one wavefront
L1 Cache
Local Memory
SIMT
SIMT
SIMT
SIMT
Registers
10 Wavefront x 4 SIMT Units =
40 Active Wavefronts / CU
64 work-items / wavefront x 40 active wavefronts =
2560 Active Work-items / CU
Workgroup

## Slide 38: Compute Unit Timing Diagram
On average: fetch & commit one wavefront / cycle
Time
SIMT0
SIMT1
SIMT2
SIMT3
WF1_0
WF1_1
WF1_2
WF1_3
WF2_0
WF2_1
WF2_2
WF2_3
WF3_0
WF3_1
WF3_2
WF3_3
WF4_0
WF4_1
WF4_2
WF4_3
WF5_0
WF5_1
WF5_2
WF5_3
WF6_0
WF6_1
WF6_2
WF6_3
WF7_0
WF7_1
WF7_2
WF7_3
WF8_0
WF8_1
WF8_2
WF8_3
WF9_0
WF9_1
WF9_2
WF9_3
WF10_0
WF10_1
WF10_2
WF11_0
WF11_1
WF12_0
1
2
3
4
5
6
7
8
9
10
11
12

## Slide 39: SIMT Unit – A GPU Pipeline
Like a wide CPU pipeline – except one fetch for entire width
16-wide physical ALU
  Executes 64-wavefront over 4 cycles. Why??
64KB register state / SIMT Unit
  Compare to x86 (Bulldozer): ~1KB of physical register file state (~1/64 size)
Address Coalescing Unit
  A key to good memory performance
Registers
Registers
Registers
Registers
Registers
Registers
Registers
Registers
Registers
Registers
Registers
Registers
Registers
Registers
Registers
Registers
Address Coalescing Unit
Notes: 16x4 execution – greater instruction mix across CU + 32 bit work-item load = 64 byte coalesced load

## Slide 40: Address Coalescing
Wavefront: Issue 64 memory requests
NDRange
Workgroup
Workgroup

## Slide 41: Address Coalescing
Wavefront: Issue 64 memory requests
Common case:
  work-items in same wavefront touch same cache block
Coalescing:
  Merge many work-items requests into single cache block request
Important for performance:
  Reduces bandwidth to DRAM

## Slide 42: GPU Memory
GPUs have caches.

## Slide 43: Not Your CPU’s Cache
By the numbers: Bulldozer – FX-8170 vs. GCN – Radeon HD 7970
 | CPU (Bulldozer) | GPU (GCN)
L1 data cache capacity | 16KB | 16 KB
Active threads (work-items) sharing L1 D Cache | 1 | 2560
L1 dcache capacity / thread | 16KB | 6.4 bytes
Last level cache (LLC) capacity | 8MB | 768KB
Active threads (work-items) sharing LLC | 8 | 81,920
LLC capacity / thread | 1MB | 9.6 bytes

## Slide 44: GPU Caches
Maximize throughput, not hide latency
  Not there for either spatial or temporal locality
L1 Cache: Coalesce requests to same cache block by different work-items
  i.e., streaming thread locality?
  Keep block around just long enough for each work-item to hit once
  Ultimate goal: Reduce bandwidth to DRAM
L2 Cache: DRAM staging buffer + some instruction reuse
  Ultimate goal: Tolerate spikes in DRAM bandwidth
If there is any spatial/temporal locality:
  Use local memory (scratchpad)

## Slide 45: Scratchpad Memory
GPUs have scratchpads (Local Memory)
  Separate address space
  Managed by software:
    Rename address
    Manage capacity – manual fill/eviction
Allocated to a workgroup
  i.e., shared by wavefronts in workgroup
L1 Cache
Local Memory
SIMT
SIMT
SIMT
SIMT
Registers

## Slide 46: Example System: Radeon HD 7970
High-end part
32 Compute Units:
  81,920 Active work-items
  32 CUs * 4 SIMT Units * 16 ALUs = 2048 Max FP ops/cycle
  264 GB/s Max memory bandwidth
925 MHz engine clock
  3.79 TFLOPS single precision (accounting trickery: FMA)
210W Max Power (Chip)
  >350W Max Power (card)
  100W idle power (card)

## Slide 47: Radeon HD 7990 - Cooking
Two 7970s on one card:
375W (AMD Official) – 450W (OEM)
Notes: Comparing GPU performance to CPU performance: Apples and Oranges

## Slide 48: A Rose by Any Other Name…

## Slide 49: Terminology Headaches #2-5
GPU “Core”
CUDA Processor
Processing Element
CUDA Core
SIMD Unit
Streaming
Multiprocessor
Compute Unit
GPU Device
GPU Device
Nvidia/CUDA
AMD/OpenCL
Derek’s CPU Analogy
Lane
Pipeline
Core
Device
Notes: “Derek” heavily influenced by Henn&Patt

## Slide 50: Terminology Headaches #6-9
Group
Thread
Work-item
Warp
Wavefront
Block
Workgroup
NDRange
Grid
CUDA/Nvidia
OpenCL/AMD
Henn&Patt
Sequence of SIMD Lane Operations
Thread of SIMD Instructions
Body of vectorized loop
Vectorized loop

## Slide 51: Terminology Headache #10
GPUs have scratchpads (Local Memory)
  Separate address space
  Managed by software:
    Rename address
    Manage capacity – manual fill/eviction
Allocated to a workgroup
  i.e., shared by wavefronts in workgroup
L1 Cache
Local Memory
SIMT
SIMT
SIMT
SIMT
Registers
Nvidia calls ‘Local Memory’
‘Shared Memory’.
AMD sometimes calls it ‘Group Memory’.

## Slide 52: Recap
Data Parallelism: Identical, Independent work over multiple data inputs
  GPU version: Add streaming access pattern
Data Parallel Execution Models: MIMD, SIMD, SIMT
GPU Execution Model: Multicore Multithreaded SIMT
OpenCL Programming Model
  NDRange over workgroup/wavefront
Modern GPU Microarchitecture: AMD Graphics Core Next (GCN)
  Compute Unit (“GPU Core”): 4 SIMT Units
  SIMT Unit (“GPU Pipeline”): 16-wide ALU pipe (16x4 execution)
  Memory: designed to stream
GPUs: Great for data parallelism. Bad for everything else.

## Slide 53: Advanced Topics
GPU Limitations, Future of GPGPU

## Slide 54: Choose Your Own Adventure!
SIMT Control Flow & Branch Divergence
Memory Divergence
When GPUs talk
  Wavefront communication
  GPU “coherence”
  GPU consistency
Future of GPUs: What’s next?

## Slide 55: SIMT Control Flow
Consider SIMT conditional branch:
  One PC
  Multiple data (i.e., multiple conditions)
if (x <= 0)
y = 0;
else
y = x;
?

## Slide 56: SIMT Control Flow
Work-items in wavefront run in lockstep
  Don’t all have to commit
Branching through predication
if (x <= 0)
y = 0;
else
y = x;
Branch  set execution mask: 1000
Else  invert execution mask: 0111
Converge  Reset execution mask: 1111
Active lane: commit result
Inactive lane: throw away result
All lanes active at start: 1111

## Slide 57: SIMT Control Flow
Work-items in wavefront run in lockstep
  Don’t all have to commit
Branching through predication
if (x <= 0)
y = 0;
else
y = x;
Branch  set execution mask: 1000
Else  invert execution mask: 0111
Converge  Reset execution mask: 1111
Active lane: commit result
Inactive lane: throw away result
All lanes active at start: 1111
Branch divergence

## Slide 58: Branch Divergence
When control flow diverges, all lanes take all paths
Divergence Kills Performance

## Slide 59: Beware!
Divergence isn’t just a performance problem:
__global int lock = 0;
void mutex_lock(…)
{
…
// acquire lock
while (test&set(lock, 1) == false) {
// spin
}
return;
}
Notes: Consider: one wavefront executes this code. One work-item will get the lock. The rest will not. The work-item that gets the lock can’t proceed because it is in lockstep with the work-items that failed to get the lock. No one makes progress.

## Slide 60: Beware!
Divergence isn’t just a performance problem:
__global int lock = 0;
void mutex_lock(…)
{
…
// acquire lock
while (test&set(lock, 1) == false) {
// spin
}
return;
}
Deadlock: work-items can’t enter mutex together!

## Slide 61: Memory Bandwidth
Bank 0
Bank 1
Bank 2
Bank 3
Lane 0
Lane 1
Lane 2
Lane 3
DRAM
SIMT
 -- Parallel Access

## Slide 62: Memory Bandwidth
Bank 0
Bank 1
Bank 2
Bank 3
Lane 0
Lane 1
Lane 2
Lane 3
DRAM
SIMT
 -- Sequential Access

## Slide 63: Memory Bandwidth
Bank 0
Bank 1
Bank 2
Bank 3
Lane 0
Lane 1
Lane 2
Lane 3
DRAM
SIMT
 -- Sequential Access
Memory divergence

## Slide 64: Memory Divergence
One work-item stalls  entire wavefront must stall
  Cause: Bank conflicts, cache misses
Data layout & partitioning is important

## Slide 65: Memory Divergence
One work-item stalls  entire wavefront must stall
  Cause: Bank conflicts, cache misses
Data layout & partitioning is important
Divergence Kills Performance

## Slide 66: Communication and Synchronization
Work-items can communicate with:
  Work-items in same wavefront
    No special sync needed…they are lockstep!
  Work-items in different wavefront, same workgroup (local)
    Local barrier
  Work-items in different wavefront, different workgroup (global)
    OpenCL 1.x: Nope
    CUDA 4.x: Yes, but complicated

## Slide 67: GPU Consistency Models
Very weak guarantee:
  Program order respected within single work-item
  All other bets are off
Safety net:
  Fence – “make sure all previous accesses are visible before proceeding”
  Built-in barriers are also fences
A wrench:
  GPU fences are scoped – only apply to subset of work-items in system
    E.g., local barrier
Take-away: confusion abounds

## Slide 68: GPU Coherence?
Notice: GPU consistency model does not require coherence
  i.e., Single Writer, Multiple Reader
Marketing claims they are coherent…
GPU “Coherence”:
  Nvidia: disable private caches
  AMD: flush/invalidate entire cache at fences

## Slide 69: GPU Architecture Research
Blending with CPU architecture:
  Dynamic scheduling / dynamic wavefront re-org
  Work-items have more locality than we think
Tighter integration with CPU on SOC:
  Fast kernel launch
    Exploit fine-grained parallel region: Remember Amdahl’s law
  Common shared memory
Reliability:
  Historically: Who notices a bad pixel?
  Future: GPU compute demands correctness
Power:
  Mobile, mobile mobile!!!

## Slide 70: Computer Economics 101
GPU Compute is cool + gaining steam, but…
  Is a 0 billion dollar industry (to quote Mark Hill)
GPU design priorities:
  1. Graphics
  2. Graphics
  …
  N-1. Graphics
  N. GPU Compute
Moral of the story:
  GPU won’t become a CPU (nor should it)