## Slide 1: Monte Carlo Localization for Mobile Robots
Frank Dellaert1, Dieter Fox2, Wolfram Burgard3, Sebastian Thrun4
1Georgia Institute of Technology
2University of Washington
3University of Bonn
4Carnegie Mellon University

## Slide 2: Take Home Message
Representing uncertainty using samples is powerful, fast, and simple !
Notes: Eeverybody in this is room is convinced of the importance of robot localization, and there has been a large body of work in both localizing a robot within a map, and/or when located, keeping track of its location over time.
To do this, a robot relies on on knowledge about how motor commands affect its position, and on sensors to provide information about where it is in the environment. Since on real robots, both this motion and sensory information is inherently noisy, some of the most successful localization approaches have been those that take this uncertainty explicitly into account.
By far the most succesful paradigm for representing uncertainty is by means of probablity distributions over a state space, where each state corresponds to a certain location and/or configuration of the robot. (Bayesian framework)

## Slide 3: Outline
Robot Localization
Sensor ?
Density Representation ?
Monte Carlo Localization
Results

## Slide 4: Outline
Robot Localization
Sensor ?
Density Representation ?
Monte Carlo Localization
Results

## Slide 5: Minerva

## Slide 6: Motivation
Crowded public spaces
Unmodified environments

## Slide 7: Museum Application
Exhibit
Desired Location

## Slide 8: Global Localization
Where in the world is Minerva the Robot ?
Vague initial estimate
Noisy and ambiguous sensors

## Slide 9: Local Tracking
Sharp initial estimate
Noisy and ambiguous sensors

## Slide 10: The Bayesian Paradigm
Knowledge as a probability distribution
60% Rain
40% dry
Notes: Representing knowledge using a probability distribution
Goal: convince it’s useful
Problem: two types of knowledge:
Knowledge about a certain quantity in the world, e.g. where are we ?
  by conditioning on data
  Obtaining this type of knowledge is called inference
World models in the form of joint or conditional probabilities
  by observing many instances
  obtaining this type of knowledge is called ‘learning’
Maybe we need examples
location, orientation, color, class, identity, labeling in segmentation, calibration (take a look at proceedings)
Sensor model, priors e.g. MRF as prior
Hmm. 3 different types: variables, likelihood models, priors

## Slide 11: Probability of Robot Location
P(Robot Location)
X
Y
State space = 2D, infinite #states

## Slide 12: Bayesian Filtering
Two phases: 1. Prediction Phase 2. Measurement Phase

## Slide 13: 1. Prediction Phase
P(xt) =  P(xt|xt-1,u) P(xt-1)
u
xt-1
xt
Motion Model

## Slide 14: 2. Measurement Phase
P(xt|z) = k P(z|xt) P(xt)
z
xt
Sensor Model

## Slide 15: Outline
Robot Localization
Sensor ?
Density Representation ?
Monte Carlo Localization
Results

## Slide 16: What sensor ?
Sonar ?
Laser ?
Vision ?

## Slide 17: Problem: Large Open Spaces
Walls and obstacles out of range
Sonar and laser have problems
One solution: Coastal Navigation

## Slide 18: Problem: Large Crowds
Horizontally mounted sensors have problems
One solution: Robust filtering

## Slide 19: Solution: Ceiling Camera
Upward looking camera
Model of the world = Ceiling Mosaic

## Slide 20: Global Alignment (other talk)

## Slide 21: Ceiling Mosaic

## Slide 22: Large FOV Problems
3D ceiling -> 3D Model ?
Matching whole images slow

## Slide 23: Small FOV Solution
Model = orthographic mosaic
No 3D Effects
Very fast

## Slide 24: Vision based Sensor
P(z|x)
h(x)
z

## Slide 25: Outline
Robot Localization
Sensor ?
Density Representation ?
Monte Carlo Localization
Results

## Slide 26: Hidden Markov Models
A
B
C
D
E
A B C D E
Notes: For example, one approach has been to divide the environment of the robot into discrete states, e.g. one for each room or part of a room. To estimate the current state, a Hidden Markov Model can be used. This necessitates either specifying or learning both a motion model (transition probabilities) and a sensor model (emission probabilities).

## Slide 27: Kalman Filter
motion
motion
Very powerful
Gaussian, unimodal
sensor

## Slide 28: Under Light

## Slide 29: Next to Light

## Slide 30: Elsewhere

## Slide 31: Markov Localization
Fine discretization over {x,y,theta}
Very successful: Rhino, Minerva, Xavier…

## Slide 32: Dynamic Markov Localization
Burgard et al., IROS 98
Idea: use Oct-trees

## Slide 33: Sampling as Representation
P(Robot Location)
X
Y

## Slide 34: Samples <=> Densities
Density => samples Obvious
Samples => density Histogram, Kernel Density Estimation

## Slide 35: Sampling Advantages
Arbitrary densities
Memory = O(#samples)
Only in “Typical Set”
Great visualization tool !
minus: Approximate
Notes: Arbitrary distribution over robot location.
Maybe show map and say white is equally likely

## Slide 36: Outline
Robot Localization
Sensor ?
Density Representation ?
Monte Carlo Localization
Results

## Slide 37: Disclaimer
Handschin 1970 (!) lacked computing power
Bootstrap filter 1993 Gordon et al.
Monte Carlo filter 1996 Kitagawa
Condensation 1996 Isard & Blake

## Slide 38: Added Twists
Camera moves, not object
Global localization

## Slide 39: Monte Carlo Localization
weighted S’k
Sk
S’k
Sk-1
Predict
Weight
Resample

## Slide 40: 1. Prediction Phase
u
Motion Model
P(xt| ,u)

## Slide 41: 2. Measurement Phase
Sensor Model
P(z|xt)

## Slide 42: 3. Resampling Step
O(N)

## Slide 43: A more in depth look

## Slide 44: Bayes Law, new look
Densities: update prior p(x) to p(x|z) via l(x;z)
Samples update a sample from p(x) to a sample from the posterior p(x|z) through l(x;z)

## Slide 45: Bayes Law Problem
We really want p(x|z) samples
But we only have p(x) samples !
How can we upgrade p(x) to p(x|z) ?

## Slide 46: More General Problem
We really want h(x) samples
But we only have g(x) samples !
How can we upgrade g(x) to h(x) ?

## Slide 47: Solution = Importance Sampling
1. generate xi from g(x)
2. calculate wi = h(xi)/g(xi)
3. assign weight qi = wi/ wi
Still works if h(x) only known up to normalization factor

## Slide 48: Mean and Weighted Mean
Fair sample: obtain samples xi from p(x|z) E[m(x)|z] ~  m(xi)/N
Weighted sample: obtain weighted samples (xi,qi) from p(x|z) E[m(x)|z] ~  qi m(xi)

## Slide 49: Bayes Law using Samples
1. generate xi from p(x)
2. calculate wi = l(xi;z)
3. assign weight qi = wi/  wi
Indeed: wi=p(x|z)/p(x) = l(x;z) p(x) /p(x) = l(x;z)
4. if you want, resample from (xi,qi)

## Slide 50: Monte Carlo Localization
weighted S’k
Sk
S’k
Sk-1
Predict
Weight
Resample

## Slide 51: Outline
Robot Localization
Sensor ?
Density Representation ?
Monte Carlo Localization
Results

## Slide 52: Video A
Office Environment
Sonar Sensors
Global Localization
Symmetry confusion

## Slide 53: Global Localization

## Slide 54: Global Localization (2)

## Slide 55: Global Localization (3)

## Slide 56: Reference Path

## Slide 57: Accuracy

## Slide 58: Video B
Smithsonian Museum of American History
Ceiling Camera, Global Localization

## Slide 59: Odometry Only

## Slide 60: Using Vision

## Slide 61: Fast Internet Morning

## Slide 62: Fast Internet Morning
Odometry only
Vision
Laser

## Slide 63: Video C
UW Sieg Hall
Laser

## Slide 64: Conclusions
Monte Carlo Localization: Powerful yet efficient Significantly less memory and CPU Very simple to implement
Future: discrete states, rate information, distributed

## Slide 65: Take Home Message
Representing uncertainty using samples is powerful, fast, and simple !
Notes: Eeverybody in this is room is convinced of the importance of robot localization, and there has been a large body of work in both localizing a robot within a map, and/or when located, keeping track of its location over time.
To do this, a robot relies on on knowledge about how motor commands affect its position, and on sensors to provide information about where it is in the environment. Since on real robots, both this motion and sensory information is inherently noisy, some of the most successful localization approaches have been those that take this uncertainty explicitly into account.
By far the most succesful paradigm for representing uncertainty is by means of probablity distributions over a state space, where each state corresponds to a certain location and/or configuration of the robot. (Bayesian framework)