## Slide 1: Compiling for the Intel® Itanium™ Architecture
Steve Skedzielewski
Intel Corporation
Compiler Tricks

## Slide 2: Agenda
Architecture Principles
Compiler Bag of Tricks
  Speculation
  Predication
  Branching
  Loop Generation

## Slide 3: Traditional Architectures: Limited Parallelism
Today’s Processors are often 60% Idle
parallelized
code
parallelized
code
Hardware
Compiler
multiple
functional units
Original Source
Code
Sequential Machine
Code
.
.
.
.
.
.
.
.
.
.
.
.
Execution Units Available-
Used Inefficiently
Notes: In traditional architectures, the compiler rearranges the source code to increase parallelism- the level of parallel execution enabled by the code- thereby increasing performance. The compiler then creates sequential machine code that “implies” parallelism to the hardware; the hardware is forced to reinterpret what the compiler meant. The result is a limited ability to extract the full potential of parallelism in the code.

## Slide 4: Itanium™ Architecture: Explicit Parallelism
Increases Parallel Execution
Compiler
Itanium™
Compiler Views Wider
Scope
Original Source
Code
Compile
Parallel Machine
Code
Hardware
multiple functional units
.
.
.
.
.
.
.
.
.
.
.
.
More efficient use of
execution resources
Notes: The Itanium™ architecture uses a better strategy to maximize parallel execution. The Itanium™ architecture compiler can create parallel machine code that eliminates the need for a hardware decoder, which relieves a significant burden from the hardware. The communication between the compiler and the processor is precise, in fact, its “explicit”. This allows the compiler greater freedom to schedule instructions, which results in increased parallel execution.
Not only is Intel developing its own compilers, its also enabling companies like Microsoft, HP, Edinburgh Portable Compilers, and others to develop their own Itanium™ architecture compilers.

## Slide 5: Itanium™ Architecture Principles
Explicit parallelism:
  Instruction level parallelism (ILP) in machine code
  Compiler schedules across a wide scope
Enhanced ILP :
  Predication, Speculation, Software pipelining, ...
Compatibility:
  Across all Itanium™ processor family members
  IA-32 in hardware and PA-RISC through instruction mapping
Massive resources:
  Many registers
  Many functional units

## Slide 6: Speculation Review
ld.s
instr 1
instr 2
br
chk.s
use
Itanium™ Architecture
instr 1
instr 2
. . .
br
Load
use
Traditional Architectures
Advances a load,
even above a branch
Memory latency is a major performance bottleneck in today’s systems
  CPU to memory gap increasing
Barrier

## Slide 7: Speculating Uses
Enables Further Parallelism
Uses of speculative data can also be executed speculatively
  distinguishes speculation from simple prefetch
ld.s
instr 1
instr 2
br
chk.s
use
Itanium™ Architecture

## Slide 8: Introducing the NaT (“Not a Thing”)
ld.s
instr 1
instr 2
br
chk.s
use
Propagate
Exception
;Exception Detection
;Exception Delivery
Itanium™ Architecture
NaT is the GR’s 65th bit that indicates:
  whether or not an exception has occurred
  when a branch to recovery code is required
NaT set during ld.s, tested by Chk.s

## Slide 9: Propagation
All computations propagate NaTs, which reduces the number of checks
Cmp propagates “false” when writing predicates
chk.s r5
sub r7 = r5,r2
ld8.s r3 = (r9)
ld8.s r4 = (r10)
shladd r6 = r3, 3, r4
ld8.s r5 = (r6)
p1,p2 = cmp(...)
Needs only one chk on result

## Slide 10: Exception Deferral: More Than Skin Deep
ld.s
instr 1
instr 2
uses
br
chk.s
(Home Block)
ld
uses
br home
Recovery code
Costly exceptions can be deferred
OS can control deferral of:
  Page faults
  Protection violations
  …
NaTs enable deferral with recovery
Enables aggressive code motion at compile time
Notes: Sparc has very limited support for speculation. A load can ignore exceptions but
- every load must be checked (no propagation)
- every exception must be fielded by the OS for filtering
- every recovery is entered after OS interruption.
- needs to include recovery table for dispatch

## Slide 11: Store Barrier
Traditional architectures limited by the store barrier
instr 1
instr 2
. . .
Store(*)
Load (*)
use
Barrier
Traditional Architectures

## Slide 12: Introducing Data Speculation
Compiler can issue a load prior to a preceding, possibly-conflicting store
Unique to Itanium™ Architecture
instr 1
instr 2
. . .
st8
ld8
use
Barrier
Traditional Architectures
ld8.a
instr 1
instr 2
st8
ld.c
use
Itanium™ Architecture

## Slide 13: Data Speculation
Uses can be speculated
Synergy with control speculation increases performance
ld8.a
instr 1
instr 2
st8
ld.c
use
ld8.a
instr 1
use
instr 2
st8
chk.a
ld8
uses
br home
Recovery code

## Slide 14: Architectural Support for Data Speculation
Instructions
  ld.a - advanced loads
  ld.c - check loads
  chk.a - advanced load checks
Speculative Advanced loads - ld.sa - is an advanced load with deferral
ALAT - HW structure containing outstanding advanced loads

## Slide 15: Advanced Load Address Table - ALAT
ld.a inserts entries.
Conflicting stores remove entries
  Also: ld.c.clr, chk.a.clr,
Presence of entry indicates success
  chk.a branches when no entry is found
reg #
Address
reg #
Address
reg #
Address
...
ld.a reg# =...
st
chk.a reg#
?

## Slide 16: Speculation Benefits
Reduces impact of memory latency
Improves code with many cache accesses
  Large databases
  Operating systems
Gives scheduling flexibility

## Slide 17: Agenda
Architecture Principles
Compiler Bag of Tricks
  Speculation
  Predication
  Branching
  Loop Generation

## Slide 18: Predication
cmp
p1
p1
p1
p2
p2
p2
Traditional Architectures
Itanium™ Architecture
Converts branches to conditional execution
  Executes multiple paths simultaneously
Exposes parallelism and reduces critical path
  Better utilizes wider machines
  Reduces mispredicted branches
else
then
cmp
Notes: The figure above demonstrates how traditional architectures would view a particular segment of code. The jumps represent branches. If the condition in the first block is true, “then” instructions 3 and 4 should be executed or “else” instructions 5 and 6 should be executed. Architectures try to predict the correct flow resulting in significant performance penalties for mispredicted branches.

## Slide 19: Complex Transformations
Not your simple if-then-else
Mark from SPEC CPU95 130.li
Low ILP in each block
Highly mispredicted branch

## Slide 20: Complex Transformations
set p1 or p2 based upon next path
Global control flow reduction
p1
p1
p1
p1
p2
p2
p2
One loop back branch
  - always taken
Set p1 = true
Utilizes machine width

## Slide 21: Upward Code Movement
cmp.unc.eq p1,p2 = r1,r2
:
(p1) br --> label
:
ld r4 = [r3]
add r5 = r4,1
cmp.unc.eq p1,p2 = r1,r2
:
ld.s r4 = [r3]
add r5 = r4,1
:
(p1) br --> label
chk.s r4, rec
Depending upon deferral mode, the add could cause cache miss
Speculate both the load and the use

## Slide 22: Upward Code Movement
cmp.unc.eq p1,p2 = r1,r2
:
(p1) br --> label
:
ld r4 = [r3]
add r5 = r4,1
cmp.unc.eq p1,p2 = r1,r2
:
(p2) ld r4 = [r3]
(p2) add r5 = r4,1
:
(p1) br --> label
Predication can avoid speculative side effects
Predicate with fall-thru predicate
Motion bounded by compare

## Slide 23: Downward Code Movement
A
B
C
Predication enables downward code movement from A to C without compensation code in B
A
C
Compensation Block
Merge Block
Main Trace
Use predication to
merge sparse code in
compensation block with
code in merge block

## Slide 24: Code Motion Tradeoffs
A
D
C
B
Slots available in hot path
Predicate region formation
occurs before scheduling
Predication can pull instructions
from lower weight path
Downward
Code Motion
Upward
Code Motion
Scheduler can move instructions
from above and below
Solutions
Heuristic formation
Preschedule information
Reverse if-conversion

## Slide 25: Introducing Parallel Compares
Reduces Critical Path
B
A
C
D
B
A
C
D
Three new types of compares:
  AND: both target predicates set FALSE if compare is false
  OR: both target predicates set TRUE if compare is true
  ANDOR: if true, sets one TRUE, sets other FALSE

## Slide 26: Method of Use
0
0
1
1
Or Predicate
Initially clear predicate
All true compares will set
All false compares do nothing
And Predicate
Initially set predicate
All true compares do nothing
All false compares will clear
cmp.unc.ne p1 = r0,r0
cmp.or.eq p1 = 40,r7
cmp.or.eq p1 = 9,r7
cmp.unc.eq p1 = r0,r0
cmp.and.ge p1 = 48,r6
cmp.and.lt p1 = 58,r6

## Slide 27: Parallel Compare Example
cmp.unc.eq p1,p2 = r0,0
cmp.and.orcm p1,p2 = c1
cmp.and.orcm p1,p2 = c2
cmp.and.orcm p1,p2 = c3
cmp.and.orcm p1,p2 = c4
(p1) then_code
(p2) else_code
c1
c2
c3
else
c4
then
Itanium™ Architecture Code
1
2
Significant control height reduction
0
if (c1 && c2 && c3 && c4)
then then_code
else else_code

## Slide 28: Predication Benefits
Reduces branches and mispredict penalties
Parallel compares further reduce critical paths
Greatly improves code with hard to predict branches
Works in tandem with speculation
Traditional architectures’ “bolt-on” approach can’t efficiently approximate predication
  Cmove: 39% more instructions, 23% slower performance*
  All instructions need predication
* Source: S. Mahlke, 1995

## Slide 29: Agenda
Architecture Principles
Compiler Bag of Tricks
  Speculation
  Predication
  Branching
  Loop Generation

## Slide 30: Branch Instruction
Instruction 1
Instruction 0
Template
128-bit bundle
0
127
QP
IP-Offset
Branch
21-bits
Two basic branch formats
  Relative: IP := IP + Offset21
  Indirect: IP := BR[I]
    8 branch registers for efficient branch execution
    Call/Return linking through branch registers
Loop branches with 64-bit loopcount register (LC)
  Enables perfect branch prediction of counted loops
  Traditional architectures always mispredict last iteration
    Important for low trip count loops
41-bits

## Slide 31: Branch Predicates
cmp p1 = cond
(p1) br target;
Conditional branches
(p0) br target;
Unconditional branch
Compare and branch can be in same cycle
Compiler-directed static prediction augments dynamic prediction
  Reduced false mispredicts due to aliasing
  Frees space in H/W predictor
  Can give hint for dynamic predictor

## Slide 32: 8 Queens Example
R1=&b[j]
R3=&a[i+j]
R5=&c[i-j+7]
ld R2=[R1]
ld.s R4=[R3]
ld.s R6=[R5]
P1,P2 <-cmp.unc(R2==true)
(p1) chk.s R4
(p1) P3,P4 <-cmp.unc(R4==true)
(p3) chk.s R6
(p3) P5,P6 <-cmp.unc(R5==true)
(P5) br then
else
1
2
4
5
6
7
Then
Else
P1
P2
P5
P3
P4
P6
8 queens control flow
Unconditional Compares
if ((b[j] == true) && (a[i+j] == true) && (c[i-j+7] == true))

## Slide 33: Eight Queens Example
R1=&b[j]
R3=&a[i+j]
R5=&c[i-j+7]
p1 <- true
ld R2=[R1]
ld R4=[R3]
ld R6=[R5]
p1,p2 <- cmp.and(R2==true)
p1,p2 <- cmp.and(R4==true)
p1,p2 <- cmp.and(R6==true)
(p1) br then
else
1
2
4
Major reduction in control flow
if ((b[j] == true) && (a[i+j] == true) && (c[i-j+7] == true))

## Slide 34: Multi-way Branch
3 branch cycles
1 branch cycle
w/o Speculation
Hoisting Loads
ld8 r6 = (ra)
(p1) br exit1
ld8 r7 = (rb)
(p3) br exit2
ld8 r8 = (rc)
(p5) br exit3
chk r6, rec0
(p1) br exit1
Chk r7, rec1
(p3) br exit2
Chk r8, rec2
(p5) br exit3
ld8.s r6 = (ra)
ld8.s r7 = (rb)
ld8.s r8 = (rc)
ld8.s r6 = (ra)
ld8.s r7 = (rb)
ld8.s r8 = (rc)
chk r6, rec0
(p2) chk r7, rec1
(p4) chk r8, rec2 }{
(p1) br exit1
(p3) br exit2
(p5) br exit3
}
P1
P6
P5
P2
P4
P3
Multi-way branches: more than 1 branch in a single cycle
  Allows n-way branching
Supports Aggressive Speculation

## Slide 35: Multi-way Branch
cmp p1, p2 = c1
cmp p3, p4 = c2
cmp p5, p6 = c3
:
:
st [r10] =
(p1) br exit1
st [r11] =
(p3) br exit2
st [r12] =
(p5) br exit3
cmp p1, p2 = c1
cmp p3, p4 = c2
cmp p5, p6 = c3
:
:
st [r10] =
(p2) st [r11] =
(p4) st [r12] =
(p1) br exit1
(p3) br exit2
(p5) br exit3
w/o Predication
Predication
Predication and Multi-way increase ILP

## Slide 36: Agenda
Architecture Principles
Compiler Bag of Tricks
  Speculation
  Predication
  Branching
  Loop Generation

## Slide 37: Loop Example
for (i=0, i< len, i++) {
if (IS_LOWERCASE(line[i]))
newline[i] = CNVT_TO_UPPERCASE(line[i]);
else
newline[i] = line[i];
}
for (i=0, i< len, i++) {
if (line[i] >= ‘a’ && line[i] <= ‘z’)
newline[i] = line[i]-32;
else
newline[i] = line[i];
}
Convert string to uppercase
After macro expansion
Typical integer-type loop

## Slide 38: Loop Assembly Code
loop:
ld c = [ra], 1
cmp p1 = true
cmp.and p1 = (c > 96)
cmp.and p1 = (c < 123)
(p1) sub c = c,32
st [rb] = c, 1
br.cloop loop
loop:
ld c = [ra], 1
bgt c, 96 bottom
blt c, 123 bottom
sub c = c,32
bottom:
st [rb] = c, 1
blt ra, end loop
Traditional Arch
Itanium™ Architecture
Fewer branches and no mispredictions. Still low ILP.
1
2
3
5
1
2
3
4
40 cycles for 8 iterations
32 cycles for 8 iterations
4

## Slide 39: Unroll for ILP
ld c = [ra],1
loop:
ld d = [ra],1
bgt c,115,b1
blt c,96, b1
sub c=c,36
b1:
st [rb] = c,1
beq rb,end, exit
ld c = [ra],1
bgt d,115,b2
blt d,96, b2
sub d=d,36
b2:
st [rb] = d,1
blt rb,end, loop
ld d
ld c
sub
st c
beq
ld c
bgt d
blt d
sub
bgt c
blt c
st d
blt
b1:
b2:
loop:
Unroll twice
8 iterations in
33 cycles
1.2x perf. inprov.
Code size: 2x
Won’t gain by
unrolling more

## Slide 40: Software Pipelining
Overlapping execution of different loop iterations
vs.
More iterations in same amount of time
Whole loop computation in one cycle
Notes: 31
95
66
48

## Slide 41: Software Pipelining
1 ld
2 ld cmps
3 ld cmps ?sub
4 ld cmps ?sub st
Cycle
Kernel
Data transferred from one
functional unit to the next
Input
ld
cmps
?sub
st
Output

## Slide 42: Introducing Rotating Registers
GR 32-127, FR32-127 can rotate
Separate Rotating Register Base for each: GRs, FRs
Loop branches decrement all register rotating bases (RRB)
Instructions contain a “virtual” register number
  RRB + virtual register number = physical register number.
References
  “Overlapped Loop Support in the Cydra 5” - Dehnert et. al, 1989
  “Code Generation Schemas for Modulo-Scheduled Loops” - Rau et. al, MICRO-25, 1992
Allows painless transfer of
data between stages

## Slide 43: Pipelined Loop
s1
s2
s3
s4
r36 = xx
r34 = xx
ld
r37 = xx
cmp<
cmp>
sub
st
Kernel code
loop:
ld r34 = [ra], 1
cmp p1 = true
cmp.and p1 = (r35>96)
cmp.and p1 = (r35<123)
(p1) sub r36 = r36, 32
st [rb] = r37, 1
br.ctop loop
Physical
register file
Virtual
register
RRB = 0
r35 = xx
+
r34 = xx
r35 = xx
r36 = xx
r37 = xx

## Slide 44: Fill the pipe ...
r35 = xx
r36 = xx
r34 = G
ld
r37 = xx
cmp<
cmp>
sub
st
Execute prologue stage
Kernel code
loop:
ld r34 = [ra], 1
cmp p1 = true
cmp.and p1 = (r35>96)
cmp.and p1 = (r35<123)
(p1) sub r36 = r36, 32
st [rb] = r37, 1
br.ctop loop
Physical
register file
Virtual
register
RRB = 0
+
r34 = G
r35 = xx
r36 = xx
r37 = xx
G
o
_
G
r
e
y
h

## Slide 45: Fill the pipe ...
r35 = xx
r36 = xx
r34 = G
ld
r37 = xx
cmp<
cmp>
sub
st
Perform a loop branch
Decrement lc
Rotate registers by
  decrementing RRB
Physical
register file
Virtual
register
RRB = 0
+
r34 = G
r35 = xx
r36 = xx
r37 = xx

## Slide 46: Fill the pipe ...
r34 = G
r35 = xx
r33 = o
ld
r36 = xx
cmp<
cmp>
sub
st
Execute prologue stage
Kernel code
loop:
ld r34 = [ra], 1
cmp p1 = true
cmp.and p1 = (r35>96)
cmp.and p1 = (r35<123)
(p1) sub r36 = r36, 32
st [rb] = r37, 1
br.ctop loop
Physical
register file
Virtual
register
RRB = -1
+
r34 = o
r35 = G
r36 = xx
r37 = xx

## Slide 47: Fill the pipe ...
r33 = o
r34 = G
r32 = _
ld
r35 = xx
cmp<
cmp>
sub
st
Execute prologue stage
Kernel code
loop:
ld r34 = [ra], 1
cmp p16 = true
cmp.and p16 = (r35>96)
cmp.and p16 = (r35<123)
(p17) sub r36 = r36, 32
st [rb] = r37, 1
br.ctop loop
Physical
register file
Virtual
register
RRB = -2
+
r34 = _
r35 = o
r36 = G
r37 = xx
G
o
_
G
r
e
y
h

## Slide 48: Execute the Kernel
r32 = _
r33 = o
r37 = G
ld
r34 = G
cmp<
cmp>
sub
st
Execute kernel
Whole iteration per cycle
G
Kernel code
loop:
ld r34 = [ra], 1
cmp p16 = true
cmp.and p16 = (r35>96)
cmp.and p16 = (r35<123)
(p17) sub r36 = r36, 32
st [rb] = r37, 1
br.ctop loop
Physical
register file
Virtual
register
RRB = -3
+
r34 = G
r35 = _
r36 = o
r37 = G
G
o
_
G
r
e
y
h

## Slide 49: Execute the Kernel
r37 = G
r32 = _
r36 = r
ld
r33 = O
cmp<
cmp>
sub
st
Execute kernel
Whole iteration per cycle
G
O
Kernel code
loop:
ld r34 = [ra], 1
cmp p16 = true
cmp.and p16 = (r35>96)
cmp.and p16 = (r35<123)
(p17) sub r36 = r36, 32
st [rb] = r37, 1
br.ctop loop
Physical
register file
Virtual
register
RRB = -4
+
r34 = r
r35 = G
r36 = _
r37 = O
G
o
_
G
r
e
y
h

## Slide 50: Execute the Kernel
r36 = r
r37 = G
r35 = e
ld
r32 = _
cmp<
cmp>
sub
st
Execute kernel
Whole iteration per cycle
G
O
Kernel code
loop:
ld r34 = [ra], 1
cmp p16 = true
cmp.and p16 = (r35>96)
cmp.and p16 = (r35<123)
(p17) sub r36 = r36, 32
st [rb] = r37, 1
br.ctop loop
Physical
register file
Virtual
register
RRB = -5
+
r34 = e
r35 = r
r36 = G
r37 = _
G
o
_
G
r
e
y
h

## Slide 51: Pipelining Overhead
Prologue
Kernel
Epilogue
Prologue and Epilogue are bad
Code size expansion
Overhead not good for low trip count loops - cache performance
Can we avoid prologue and epilogue?

## Slide 52: Prologue Code
1 ld
2 ld cmps
3 ld cmps ?sub
4 ld cmps ?sub st
Cycle
Kernel
Incrementally turn on functional units

## Slide 53: Avoid Pro and Epilogues
r35 = xx
r36 = xx
r34 = xx
ld
r37 = xx
cmp<
cmp>
sub
st
Physical
register file
Unit Enabler
Have enable bit on each functional unit
Enablers are initialized to off
Feed through a sequence of bits of
length dependent upon loop count and
pipe depth
Kernel (loop count)
Epilogue

## Slide 54: Revisiting Rotating Predicate Registers
s1
s2
s3
s4
PR16-63 can rotate, with separate Rotating Register Base
Loop branches decrement all register rotating base (RRB)
Instructions contain a “virtual” predicate register number
  RRB + virtual register number = physical register number.
Some predicates control pipeline stages, Stage Predicates
Qualifying Predicates can still be in the loop
Complete Loop Code
loop:
(p16) ld r34 = [ra], 1
(p16) cmp.unc p20 = true
(p17) cmp.and p21 = (r35>96)
(p17) cmp.and p21 = (r35<123)
(p22) sub r36 = r36, 32
(p19) st [rb] = r37, 1
br.ctop loop

## Slide 55: How does this work
r35 = xx
r36 = xx
r34 = G
ld
r37 = xx
cmp<
cmp>
sub
st
Physical
register file
Complete Loop Code
loop:
(p16) ld r34 = [ra], 1
(p16) cmp p20 = true
(p17) cmp.and p21 = (r35>96)
(p17) cmp.and p21 = (r35<123)
(p22) sub r36 = r36, 32
(p19) st [rb] = r37, 1
br.ctop loop
RRB = 0
Stage Predicates
Kernel
Epilogue
Qualifying Predicate

## Slide 56: Auto Predicate Generation
Predicate
Generator
Initalize
lc to trip count
ec to epilogue count
p16 to true
Loop branches
Rotate predicates by decrementing RRB
When lc > 0
  - Decr. lc, set p16=true
When lc = 0
  - Decr. ec, set p16=false
Fall through when ec=0
lc
ec
RRB
p16

## Slide 57: Fill the pipe again ...
r35 = xx
r36 = xx
r34 = G
ld
r37 = xx
cmp<
cmp>
sub
st
Physical
register file
Complete Loop Code
Kernel
Epilogue
loop:
(p16) ld r34 = [ra], 1
(p16) cmp.unc p20 = true
(p17) cmp.and p21 = (r35>96)
(p17) cmp.and p21 = (r35<123)
(p22) sub r36 = r36, 32
(p19) st [rb] = r37, 1
br.ctop loop
RRB = 0
Stage Predicates

## Slide 58: Fill the pipe again ...
r34 = G
r35 = xx
r33 = o
ld
r36 = xx
cmp<
cmp>
sub
st
Physical
register file
Complete Loop Code
Kernel
Epilogue
loop:
(p16) ld r34 = [ra], 1
(p16) cmp.unc p20 = true
(p17) cmp.and p21 = (r35>96)
(p17) cmp.and p21 = (r35<123)
(p22) sub r36 = r36, 32
(p19) st [rb] = r37, 1
br.ctop loop
RRB = -1
Stage Predicates

## Slide 59: Fill the pipe again ...
r33 = o
r34 = G
r32 = _
ld
r35 = xx
cmp<
cmp>
sub
st
Physical
register file
Complete Loop Code
Kernel
Epilogue
loop:
(p16) ld r34 = [ra], 1
(p16) cmp.unc p20 = true
(p17) cmp.and p21 = (r35>96)
(p17) cmp.and p21 = (r35<123)
(p22) sub r36 = r36, 32
(p19) st [rb] = r37, 1
br.ctop loop
RRB = -2
Stage Predicates

## Slide 60: Chunking thru kernel
r32 = _
r33 = o
r37 = G
ld
r34 = G
cmp<
cmp>
sub
st
Physical
register file
Complete Loop Code
loop:
(p16) ld r34 = [ra], 1
(p16) cmp.unc p20 = true
(p17) cmp.and p21 = (r35>96)
(p17) cmp.and p21 = (r35<123)
(p22) sub r36 = r36, 32
(p19) st [rb] = r37, 1
br.ctop loop
RRB = -3
Kernel
Epilogue

## Slide 61: Chunking thru kernel
r37 = G
r32 = _
r36 = r
ld
r33 = O
cmp<
cmp>
sub
st
Physical
register file
Complete Loop Code
loop:
(p16) ld r34 = [ra], 1
(p16) cmp.unc p20 = true
(p17) cmp.and p21 = (r35>96)
(p17) cmp.and p21 = (r35<123)
(p22) sub r36 = r36, 32
(p19) st [rb] = r37, 1
br.ctop loop
RRB = -4
G
Kernel
Epilogue

## Slide 62: Chunking thru kernel
r36 = r
r37 = G
r35 = e
ld
r32 = _
cmp<
cmp>
sub
st
Physical
register file
Complete Loop Code
Epilogue
loop:
(p16) ld r34 = [ra], 1
(p16) cmp.unc p20 = true
(p17) cmp.and p21 = (r35>96)
(p17) cmp.and p21 = (r35<123)
(p22) sub r36 = r36, 32
(p19) st [rb] = r37, 1
br.ctop loop
RRB = -5
G
O

## Slide 63: Chunking thru kernel
r35 = e
r36 = r
r34 = y
ld
r37 = G
cmp<
cmp>
sub
st
Physical
register file
Complete Loop Code
Epilogue
loop:
(p16) ld r34 = [ra], 1
(p16) cmp.unc p20 = true
(p17) cmp.and p21 = (r35>96)
(p17) cmp.and p21 = (r35<123)
(p22) sub r36 = r36, 32
(p19) st [rb] = r37, 1
br.ctop loop
RRB = -6
G
O

## Slide 64: Chunking thru kernel
r34 = y
r35 = e
r33 = h
ld
r36 = r
cmp<
cmp>
sub
st
Physical
register file
Complete Loop Code
Epilogue
loop:
(p16) ld r34 = [ra], 1
(p16) cmp.unc p20 = true
(p17) cmp.and p21 = (r35>96)
(p17) cmp.and p21 = (r35<123)
(p22) sub r36 = r36, 32
(p19) st [rb] = r37, 1
br.ctop loop
RRB = -7
G
O
G

## Slide 65: Draining the pipe
r33 = h
r34 = Y
r32 = xx
ld
r35 = E
cmp<
cmp>
sub
st
Physical
register file
Complete Loop Code
loop:
(p16) ld r34 = [ra], 1
(p16) cmp.unc p20 = true
(p17) cmp.and p21 = (r35>96)
(p17) cmp.and p21 = (r35<123)
(p22) sub r36 = r36, 32
(p19) st [rb] = r37, 1
br.ctop loop
RRB = -8
G
O
G
R

## Slide 66: Draining the pipe
r34 = xx
r35 = H
r33 = xx
ld
r36 = Y
cmp<
cmp>
sub
st
Physical
register file
Complete Loop Code
loop:
(p16) ld r34 = [ra], 1
(p16) cmp.unc p20 = true
(p17) cmp.and p21 = (r35>96)
(p17) cmp.and p21 = (r35<123)
(p22) sub r36 = r36, 32
(p19) st [rb] = r37, 1
br.ctop loop
RRB = -9
G
O
G
R
E

## Slide 67: Draining the pipe
r33 = xx
r34 = xx
r32 = xx
ld
r35 = H
cmp<
cmp>
sub
st
Physical
register file
Complete Loop Code
loop:
(p16) ld r34 = [ra], 1
(p16) cmp.unc p20 = true
(p17) cmp.and p21 = (r35>96)
(p17) cmp.and p21 = (r35<123)
(p22) sub r36 = r36, 32
(p19) st [rb] = r37, 1
br.ctop loop
RRB = -10
G
O
G
R
E
Y
Fall through the loop
Don’t rotate

## Slide 68: Example Summary
r33 = xx
r34 = xx
r32 = xx
ld
r35 = H
cmp<
cmp>
sub
st
Physical
register file
loop:
(p16) ld r34 = [ra], 1
(p16) cmp.unc p20 = true
(p17) cmp.and p21 = (r35>96)
(p17) cmp.and p21 = (r35<123)
(p22) sub r36 = r36, 32
(p19) st [rb] = r37, 1
br.ctop loop
RRB = -10
G
O
G
R
E
Y
H
8 iterations in 12 cycles
2.6x speedup of initial code
2.75x over unrolled traditional
No code expansion
No mispredicts (4x, 1 10 cycle miss)
Minimal register usage

## Slide 69: Software Pipelining
Especially Useful for Integer Code with Small Number of Loop Iterations
Itanium™ architecture features support SWP
  Full Predication
  Special branch handling features
  Register rotation: removes loop copy overhead
  Predicate rotation/generation: removes prologue & epilogue
Traditional architectures use loop unrolling
  High overhead: extra code for loop body, prologue, and epilogue
Notes: 31
95
66
48

## Slide 70: Compiler Bag of Tricks
Predication
  Removes branches and mispredictions
  Enables aggressive code motion
  Parallel compares increase parallelism
Speculation
  Hides memory latency
  Enables aggressive code motion
  Control speculation over branches
  Data speculation over stores
  Compiler-controlled recovery code

## Slide 71: Compiler Bag of Tricks
Rich branch architecture
  Multi-way branches increase ILP
  Loop branches
  Static direction hints assist prediction
S/W pipelining support with minimal overhead encourages broad usage
  Performance for small integer loops with unknown trip counts as well as monster FP loops

## Slide 72: BACKUP

## Slide 73: 8 Queens Example
if ((b[j] == true) && (a[i+j] == true) && (c[i-j+7] == true))
Then
Else
P1
P2
P5
P3
P4
P6
Parallel Compares
R1=&b[j]
R3=&a[i+j]
R5=&c[i-j+7]
p1 <- true
ld R2=[R1]
ld R4=[R3]
ld R6=[R5]
p1,p2 <- cmp.and(R2==true)
p1,p2 <- cmp.and(R4==true)
p1,p2 <- cmp.and(R6==true)
(p1) br then
else
1
2
4
5
Reduced from 7 cycles to 5
8 queens control flow
Then
Else
P1= true
P1=False

## Slide 74: Five Predicate Compare Types
(qp) p1,p2 <- cmp.relation
  if(qp) {p1 = relation; p2 = !relation};
(qp) p1,p2 <- cmp.relation.unc
  p1 = qp&relation; p2 = qp&!relation;
(qp) p1,p2 <- cmp.relation.and
  if(qp & (relation==FALSE)) { p1=0; p2=0; }
(qp) p1,p2 <- cmp.relation.or
  if(qp & (relation==TRUE)) { p1=1; p2=1; }
(qp) p1,p2 <- cmp.relation.or.andcm
  if(qp & (relation==TRUE)) { p1=1; p2=0; }
Notes: Conditional move is bad since it can add a cycle to the critical path.
It introduces more instructions.
Multiple predicate writers appear in the same cycle.
This is the whole story on predication.

## Slide 75: Control Speculation Summary
All loads have a speculative form that sets the NaT bit when deferring exceptions
Computational instructions propagate NaTs
OS controls deferral of faults but supported directly in HW - “no-fault speculation”
  Minimizes overhead of data that is not used
Chk more effective than non-faulting load

## Slide 76: More complex example
Killtime loop in m88ksim
for (i=0, i<32, i++)
comptime[i] -= MIN(comptime[i], time)
Pipelined Loop
Loop:
(p16) ld r36 = [r10],4
(p18) cmp p21,p23 = r38,r32
(p22) sub r37 = r0,0
(p24) sub r38 = r38,r32
(p20) st [r11] = r40,4
br.ctop loop
Initial Loop
loop:
ld r5=[r10],4
cmp p1,p2 = r5,r32
(p1) br side
sub r5=r5,r32
st [addr]=r5,4
br cloop
side:
add t=0,r0
st4 [addr]=t,4
br cloop

## Slide 77: Software Pipelining Benefits
Loop pipelining maximizes performance; minimizes overhead
  High applicability
  Minimum code size - fewer cache misses
  Reduced register usage
  Greater performance improvements in higher latency conditions
Reduced overhead allows S/W pipelining of small loops with unknown trip counts
  Good for integer scalar codes

## Slide 78: Memory Address Modes
Register Indirect is only address mode
  Memory address comes from a General Register
  no add in critical memory access path
Post-Increment provided for efficient address arithmetic
  can add 9-bit signed immediate value, or a value from a general register
  uses idle ALU resources
  avoid extra add instructions
Benefits vector Floating Point Code

## Slide 79: Memory Address Modes
Load Instructions
  (qp) ld{1,2,4,8} r1 = [r3] no post-inc
  (qp) ld{1,2,4,8} r1 = [r3] , imm9
  (qp) ld{1,2,4,8} r1 = [r3] , r2
Store Instructions
  (qp) st{1,2,4,8} [r3] = r2 no post-inc
  (qp) st{1,2,4,8} [r3] = r2, imm9