## Slide 1
We construct an analytical model using a LPDDR data sheet to understand the power savings from mercurial cache. We model for standard server hardware with with 32GB DIMMs. We model the cost of copy and assume hardware checksum support.
Mercurial Caches: Operating System Support for Energy Proportional DRAM
Asim Kadav, Rathijit Sen and Michael M. Swift, University of Wisconsin-Madison
DRAM Power-saving Technologies
Mercurial Caches
Mercurial Caches provides OS abstractions to use low power DRAM. It occupies portions of DRAM and puts them in low power state (turned off or cache clean data). It uses software checksums to ensure correctness in the absence of reliable hardware. Its goal is to save power with little performance loss during low memory utilization
Preliminary Evaluation
References
[1] L.A. Barroso and U. Ho ̈lzle. The datacenter as a computer: An introduction to the design of warehouse-scale machines. Synthesis Lectures on Computer Architecture, 2009.
[2] D.H. Yoon, J. Chang, N. Muralimanohar, and P. Ranganathan. BOOM: Enabling mobile memory based low-power server DIMMs. In ISCA, June 2012.
How can we make DRAM power consumption energy proportional ?
Problem: DRAM is one of the significant consumer of power in modern systems. Unlike CPUs which provide voltage and frequency scaling techniques, DRAM techniques to save power upon partial memory use are limited.
Goal: Provide abstractions in existing operating systems to utilize low power memory technologies using mercurial caches.
DRAM Technology | Data Retention | Granularity | Latency | Power Savings
ACPI S4 | No | All DRAM | >1s | 100%
Self-refresh (SR) | Yes | All DRAM | 100ns | 33%
Clock stop | Yes | All DRAM | 200µs | 83%
Temperature Controlled SR | Yes | All DRAM | 100ns | 60%
Partial Array Self Refresh (PASR) | Yes | 1/16th DIMM | 100ns | ~25-30%
Lower refresh rates | Partial | Any | Clock | ~42%
Deep power down (DPD) | No | Per module | 200µs | 95%
Low power mode in LPDDR/DDR3 DRAM systems. Many technologies in the figure co-exist. TCSR savings are for 40C drop for 64MB DIMM. Mercurial caches use the techniques enclosed in the box.
OS bottlenecks to adopting low power techniques
Physical memory block (DIIMM sized)
Physical memory block (DIMM sized)
DIMM
1. A cache interface to get/put 4K pages reliably
2. OS modifications to make mercurial caches
transparent to virtual memory subsystem:
3. OS support to facilitate low power granularity allocations: Pre-reserve and migrate pages
mcache_get_page()/mcache_put_page()
OS Behavior | Solution
Fragmentation of physical address space | Energy-aware migration of movable pages
Migration of pages not possible due to pinned pages | Mark specific segment boundaries dedicated to movable pages
Mercurial cache interface manages low power memory with checksum support
shrink()/grow() memory pools
OS Behavior | Policy Rationale | Problem
Use all idle memory as page cache | OS uses all available memory to improve system performance | There is never any “free” space to be put to low power state
Fragments physical address space since address space is virtualized. | Contiguous memory requirement is limited (few MBs), keeping address space defragmented is only an overhead. | Memory needs to be put in low powered state in contiguous segments to save power
DRAMs contribute significantly to system power
“Free memory is bad memory” philosophy and physical memory fragmentation hurt any memory consolidation for power savings
Chart: 
| CPU | DRAM | Other | Disks | Networking
Power | 33 | 30 | 22 | 10 | 5
Google 2009[1]
Servers are provisioned with 10s of GBS of memory and consume 30-57% of total power for a system provisioned with 128 GB DDR3 memory[2]
Mercurial caches use reservation policies for movable data and migration mechanisms to switch contiguous memory into low power state
Result 1: Mercurial caches provide energy savings proportional to the DRAM usage, across different low power technologies
Result 2: Comparing power cost of copyout against savings from low power, we find mercurial caches can sustain a reference rate up to the row cycle time (~200K references)
Result 3: a) In experiments, completely turning off memory results in swapping and reduces performance by 5x as compared to mercurial caches b) It is also better than swapping out to a low power SSD, where the reference rate that can be sustained is low (upto 10K pages), due to access latency
mcache
mcache (full DIMM)
Low power mercurial cache pool per DIMM
Problem | Solution
How to dynamically grow and shrink mercurial caches w/o affecting running applications? | Predict the working set using free page information to quickly satisfy memory demands and slowly reclaim unused memory
How to ensure that mercurial caches do not appear as missing memory to VM system? | Account for mercurial caches when performing VM actions such as prefetching, allocations etc.
What data to store in mercurial caches if they are not turned off completely? | Register as slab cache and use them as a third level eviction cache for page cache
Using low power memory technologies inside OS
We assume 10K ref/sec to low power memory and 1 million ref./sec to regular memory. DPD turns off low memory and hence data is read from the disk and memory references are 0.
Comparing memory power savings as copy costs from low power memory begin to dominate. DPD can sustain zero references since memory is turned off.