digraph G
 {
	 ratio="fill";
	 size="8,10";
	 MICRODRIVERS__DUMMY [label="MICRODRIVERS__DUMMY (LOC=2)"];
	 MICRODRIVERS__MODIF___mutex_init [label="MICRODRIVERS__MODIF___mutex_init (LOC=2)"];
	 MICRODRIVERS__MODIF___pci_register_driver [label="MICRODRIVERS__MODIF___pci_register_driver (LOC=12)"];
	 MICRODRIVERS__MODIF___release_region [label="MICRODRIVERS__MODIF___release_region (LOC=4)"];
	 MICRODRIVERS__MODIF___request_region [label="MICRODRIVERS__MODIF___request_region (LOC=4)"];
	 MICRODRIVERS__MODIF___spin_lock_init [label="MICRODRIVERS__MODIF___spin_lock_init (LOC=3)"];
	 MICRODRIVERS__MODIF___wake_up [label="MICRODRIVERS__MODIF___wake_up (LOC=3)"];
	 MICRODRIVERS__MODIF__spin_lock [label="MICRODRIVERS__MODIF__spin_lock (LOC=3)"];
	 MICRODRIVERS__MODIF__spin_lock_bh [label="MICRODRIVERS__MODIF__spin_lock_bh (LOC=3)"];
	 MICRODRIVERS__MODIF__spin_lock_irq [label="MICRODRIVERS__MODIF__spin_lock_irq (LOC=2)"];
	 MICRODRIVERS__MODIF__spin_lock_irqsave [label="MICRODRIVERS__MODIF__spin_lock_irqsave (LOC=3)"];
	 MICRODRIVERS__MODIF__spin_unlock [label="MICRODRIVERS__MODIF__spin_unlock (LOC=3)"];
	 MICRODRIVERS__MODIF__spin_unlock_bh [label="MICRODRIVERS__MODIF__spin_unlock_bh (LOC=3)"];
	 MICRODRIVERS__MODIF__spin_unlock_irq [label="MICRODRIVERS__MODIF__spin_unlock_irq (LOC=2)"];
	 MICRODRIVERS__MODIF__spin_unlock_irqrestore [label="MICRODRIVERS__MODIF__spin_unlock_irqrestore (LOC=3)"];
	 MICRODRIVERS__MODIF_create_proc_entry [label="MICRODRIVERS__MODIF_create_proc_entry (LOC=6)"];
	 MICRODRIVERS__MODIF_device_create_file [label="MICRODRIVERS__MODIF_device_create_file (LOC=5)"];
	 MICRODRIVERS__MODIF_free_irq [label="MICRODRIVERS__MODIF_free_irq (LOC=2)"];
	 MICRODRIVERS__MODIF_hrtimer_get_res [label="MICRODRIVERS__MODIF_hrtimer_get_res (LOC=4)"];
	 MICRODRIVERS__MODIF_kmem_cache_zalloc [label="MICRODRIVERS__MODIF_kmem_cache_zalloc (LOC=3)"];
	 MICRODRIVERS__MODIF_logAlloc [label="MICRODRIVERS__MODIF_logAlloc (LOC=2)"];
	 MICRODRIVERS__MODIF_logRead [label="MICRODRIVERS__MODIF_logRead (LOC=2)"];
	 MICRODRIVERS__MODIF_logStackFrame [label="MICRODRIVERS__MODIF_logStackFrame (LOC=2)"];
	 MICRODRIVERS__MODIF_logWrite [label="MICRODRIVERS__MODIF_logWrite (LOC=2)"];
	 MICRODRIVERS__MODIF_mutex_lock [label="MICRODRIVERS__MODIF_mutex_lock (LOC=2)"];
	 MICRODRIVERS__MODIF_mutex_unlock [label="MICRODRIVERS__MODIF_mutex_unlock (LOC=2)"];
	 MICRODRIVERS__MODIF_pci_bus_read_config_byte [label="MICRODRIVERS__MODIF_pci_bus_read_config_byte (LOC=5)"];
	 MICRODRIVERS__MODIF_pci_bus_read_config_word [label="MICRODRIVERS__MODIF_pci_bus_read_config_word (LOC=5)"];
	 MICRODRIVERS__MODIF_pci_disable_device [label="MICRODRIVERS__MODIF_pci_disable_device (LOC=5)"];
	 MICRODRIVERS__MODIF_pci_enable_device [label="MICRODRIVERS__MODIF_pci_enable_device (LOC=4)"];
	 MICRODRIVERS__MODIF_pci_release_regions [label="MICRODRIVERS__MODIF_pci_release_regions (LOC=2)"];
	 MICRODRIVERS__MODIF_pci_request_regions [label="MICRODRIVERS__MODIF_pci_request_regions (LOC=3)"];
	 MICRODRIVERS__MODIF_pci_restore_state [label="MICRODRIVERS__MODIF_pci_restore_state (LOC=2)"];
	 MICRODRIVERS__MODIF_pci_save_state [label="MICRODRIVERS__MODIF_pci_save_state (LOC=2)"];
	 MICRODRIVERS__MODIF_pci_set_master [label="MICRODRIVERS__MODIF_pci_set_master (LOC=6)"];
	 MICRODRIVERS__MODIF_pci_set_power_state [label="MICRODRIVERS__MODIF_pci_set_power_state (LOC=2)"];
	 MICRODRIVERS__MODIF_pci_unregister_driver [label="MICRODRIVERS__MODIF_pci_unregister_driver (LOC=4)"];
	 MICRODRIVERS__MODIF_proc_symlink [label="MICRODRIVERS__MODIF_proc_symlink (LOC=4)"];
	 MICRODRIVERS__MODIF_request_irq [label="MICRODRIVERS__MODIF_request_irq (LOC=5)"];
	 __raw_spin_unlock [label="__raw_spin_unlock (LOC=4)"];
	 __snd_bug_on [label="__snd_bug_on (LOC=3)"];
	 __ticket_spin_unlock [label="__ticket_spin_unlock (LOC=7)"];
	 _snd_cmipci_uswitch_get [label="_snd_cmipci_uswitch_get (LOC=20)"];
	 _snd_cmipci_uswitch_put [label="_snd_cmipci_uswitch_put (LOC=33)"];
	 alsa_card_cmipci_exit [label="alsa_card_cmipci_exit (LOC=4)"];
	 alsa_card_cmipci_init [label="alsa_card_cmipci_init (LOC=3)"];
	 cleanup_module [label="cleanup_module (LOC=1)"];
	 close_device_check [label="close_device_check (LOC=22)"];
	 cmipci_sb_reg_decode [label="cmipci_sb_reg_decode (LOC=10)"];
	 dev_get_drvdata [label="dev_get_drvdata (LOC=3)"];
	 dev_name [label="dev_name (LOC=4)"];
	 dev_set_drvdata [label="dev_set_drvdata (LOC=4)"];
	 gameport_allocate_port [label="gameport_allocate_port (LOC=5)"];
	 gameport_register_port [label="gameport_register_port (LOC=4)"];
	 gameport_set_name [label="gameport_set_name (LOC=4)"];
	 get_line_in_mode [label="get_line_in_mode (LOC=12)"];
	 hw_param_interval [label="hw_param_interval (LOC=4)"];
	 inb [label="inb (LOC=1)"];
	 init_module [label="init_module (LOC=1)"];
	 inl [label="inl (LOC=1)"];
	 inw [label="inw (LOC=1)"];
	 kmalloc [label="kmalloc (LOC=16)"];
	 kzalloc [label="kzalloc (LOC=3)"];
	 native_irq_enable [label="native_irq_enable (LOC=4)"];
	 open_device_check [label="open_device_check (LOC=25)"];
	 outb [label="outb (LOC=1)"];
	 outl [label="outl (LOC=1)"];
	 outw [label="outw (LOC=1)"];
	 pci_get_drvdata [label="pci_get_drvdata (LOC=3)"];
	 pci_name [label="pci_name (LOC=3)"];
	 pci_set_drvdata [label="pci_set_drvdata (LOC=4)"];
	 query_chip [label="query_chip (LOC=47)"];
	 raw_local_irq_enable [label="raw_local_irq_enable (LOC=4)"];
	 restore_mixer_state [label="restore_mixer_state (LOC=31)"];
	 save_mixer_state [label="save_mixer_state (LOC=30)"];
	 set_dac_channels [label="set_dac_channels (LOC=36)"];
	 setup_ac3 [label="setup_ac3 (LOC=46)"];
	 setup_spdif_playback [label="setup_spdif_playback (LOC=38)"];
	 snd_cmipci_capture_close [label="snd_cmipci_capture_close (LOC=5)"];
	 snd_cmipci_capture_open [label="snd_cmipci_capture_open (LOC=22)"];
	 snd_cmipci_capture_pointer [label="snd_cmipci_capture_pointer (LOC=4)"];
	 snd_cmipci_capture_prepare [label="snd_cmipci_capture_prepare (LOC=4)"];
	 snd_cmipci_capture_spdif_close [label="snd_cmipci_capture_spdif_close (LOC=5)"];
	 snd_cmipci_capture_spdif_hw_free [label="snd_cmipci_capture_spdif_hw_free (LOC=10)"];
	 snd_cmipci_capture_spdif_open [label="snd_cmipci_capture_spdif_open (LOC=16)"];
	 snd_cmipci_capture_spdif_prepare [label="snd_cmipci_capture_spdif_prepare (LOC=20)"];
	 snd_cmipci_capture_trigger [label="snd_cmipci_capture_trigger (LOC=5)"];
	 snd_cmipci_ch_reset [label="snd_cmipci_ch_reset (LOC=7)"];
	 snd_cmipci_clear_bit [label="snd_cmipci_clear_bit (LOC=9)"];
	 snd_cmipci_clear_bit_b [label="snd_cmipci_clear_bit_b (LOC=9)"];
	 snd_cmipci_create [label="snd_cmipci_create (LOC=246)"];
	 snd_cmipci_create_fm [label="snd_cmipci_create_fm (LOC=51)"];
	 snd_cmipci_create_gameport [label="snd_cmipci_create_gameport (LOC=44)"];
	 snd_cmipci_dev_free [label="snd_cmipci_dev_free (LOC=4)"];
	 snd_cmipci_free [label="snd_cmipci_free (LOC=22)"];
	 snd_cmipci_free_gameport [label="snd_cmipci_free_gameport (LOC=12)"];
	 snd_cmipci_get_input_sw [label="snd_cmipci_get_input_sw (LOC=17)"];
	 snd_cmipci_get_native_mixer [label="snd_cmipci_get_native_mixer (LOC=22)"];
	 snd_cmipci_get_native_mixer_sensitive [label="snd_cmipci_get_native_mixer_sensitive (LOC=5)"];
	 snd_cmipci_get_volume [label="snd_cmipci_get_volume (LOC=21)"];
	 snd_cmipci_hw_free [label="snd_cmipci_hw_free (LOC=3)"];
	 snd_cmipci_hw_params [label="snd_cmipci_hw_params (LOC=4)"];
	 snd_cmipci_info_input_sw [label="snd_cmipci_info_input_sw (LOC=8)"];
	 snd_cmipci_info_native_mixer [label="snd_cmipci_info_native_mixer (LOC=11)"];
	 snd_cmipci_info_volume [label="snd_cmipci_info_volume (LOC=11)"];
	 snd_cmipci_interrupt [label="snd_cmipci_interrupt (LOC=30)"];
	 snd_cmipci_line_in_mode_get [label="snd_cmipci_line_in_mode_get (LOC=9)"];
	 snd_cmipci_line_in_mode_info [label="snd_cmipci_line_in_mode_info (LOC=12)"];
	 snd_cmipci_line_in_mode_put [label="snd_cmipci_line_in_mode_put (LOC=17)"];
	 snd_cmipci_mic_in_mode_get [label="snd_cmipci_mic_in_mode_get (LOC=10)"];
	 snd_cmipci_mic_in_mode_info [label="snd_cmipci_mic_in_mode_info (LOC=11)"];
	 snd_cmipci_mic_in_mode_put [label="snd_cmipci_mic_in_mode_put (LOC=13)"];
	 snd_cmipci_mixer_new [label="snd_cmipci_mixer_new (LOC=102)"];
	 snd_cmipci_mixer_read [label="snd_cmipci_mixer_read (LOC=7)"];
	 snd_cmipci_mixer_write [label="snd_cmipci_mixer_write (LOC=5)"];
	 snd_cmipci_pcm2_new [label="snd_cmipci_pcm2_new (LOC=20)"];
	 snd_cmipci_pcm_new [label="snd_cmipci_pcm_new (LOC=21)"];
	 snd_cmipci_pcm_pointer [label="snd_cmipci_pcm_pointer (LOC=19)"];
	 snd_cmipci_pcm_prepare [label="snd_cmipci_pcm_prepare (LOC=100)"];
	 snd_cmipci_pcm_spdif_new [label="snd_cmipci_pcm_spdif_new (LOC=21)"];
	 snd_cmipci_pcm_trigger [label="snd_cmipci_pcm_trigger (LOC=48)"];
	 snd_cmipci_playback2_close [label="snd_cmipci_playback2_close (LOC=6)"];
	 snd_cmipci_playback2_hw_free [label="snd_cmipci_playback2_hw_free (LOC=5)"];
	 snd_cmipci_playback2_hw_params [label="snd_cmipci_playback2_hw_params (LOC=15)"];
	 snd_cmipci_playback2_open [label="snd_cmipci_playback2_open (LOC=36)"];
	 snd_cmipci_playback_close [label="snd_cmipci_playback_close (LOC=5)"];
	 snd_cmipci_playback_hw_free [label="snd_cmipci_playback_hw_free (LOC=7)"];
	 snd_cmipci_playback_open [label="snd_cmipci_playback_open (LOC=24)"];
	 snd_cmipci_playback_pointer [label="snd_cmipci_playback_pointer (LOC=4)"];
	 snd_cmipci_playback_prepare [label="snd_cmipci_playback_prepare (LOC=14)"];
	 snd_cmipci_playback_spdif_close [label="snd_cmipci_playback_spdif_close (LOC=5)"];
	 snd_cmipci_playback_spdif_open [label="snd_cmipci_playback_spdif_open (LOC=25)"];
	 snd_cmipci_playback_spdif_prepare [label="snd_cmipci_playback_spdif_prepare (LOC=12)"];
	 snd_cmipci_playback_trigger [label="snd_cmipci_playback_trigger (LOC=5)"];
	 snd_cmipci_probe [label="snd_cmipci_probe (LOC=48)"];
	 snd_cmipci_proc_init [label="snd_cmipci_proc_init (LOC=7)"];
	 snd_cmipci_proc_read [label="snd_cmipci_proc_read (LOC=17)"];
	 snd_cmipci_put_input_sw [label="snd_cmipci_put_input_sw (LOC=23)"];
	 snd_cmipci_put_native_mixer [label="snd_cmipci_put_native_mixer (LOC=25)"];
	 snd_cmipci_put_native_mixer_sensitive [label="snd_cmipci_put_native_mixer_sensitive (LOC=9)"];
	 snd_cmipci_put_volume [label="snd_cmipci_put_volume (LOC=37)"];
	 snd_cmipci_rate_freq [label="snd_cmipci_rate_freq (LOC=10)"];
	 snd_cmipci_read [label="snd_cmipci_read (LOC=3)"];
	 snd_cmipci_read_b [label="snd_cmipci_read_b (LOC=3)"];
	 snd_cmipci_read_w [label="snd_cmipci_read_w (LOC=3)"];
	 snd_cmipci_remove [label="snd_cmipci_remove (LOC=5)"];
	 snd_cmipci_resume [label="snd_cmipci_resume (LOC=30)"];
	 snd_cmipci_set_bit [label="snd_cmipci_set_bit (LOC=9)"];
	 snd_cmipci_set_bit_b [label="snd_cmipci_set_bit_b (LOC=9)"];
	 snd_cmipci_silence_hack [label="snd_cmipci_silence_hack (LOC=45)"];
	 snd_cmipci_spdif_default_get [label="snd_cmipci_spdif_default_get (LOC=11)"];
	 snd_cmipci_spdif_default_info [label="snd_cmipci_spdif_default_info (LOC=6)"];
	 snd_cmipci_spdif_default_put [label="snd_cmipci_spdif_default_put (LOC=15)"];
	 snd_cmipci_spdif_mask_get [label="snd_cmipci_spdif_mask_get (LOC=8)"];
	 snd_cmipci_spdif_mask_info [label="snd_cmipci_spdif_mask_info (LOC=6)"];
	 snd_cmipci_spdif_stream_get [label="snd_cmipci_spdif_stream_get (LOC=11)"];
	 snd_cmipci_spdif_stream_info [label="snd_cmipci_spdif_stream_info (LOC=6)"];
	 snd_cmipci_spdif_stream_put [label="snd_cmipci_spdif_stream_put (LOC=15)"];
	 snd_cmipci_spdout_enable_get [label="snd_cmipci_spdout_enable_get (LOC=7)"];
	 snd_cmipci_spdout_enable_put [label="snd_cmipci_spdout_enable_put (LOC=18)"];
	 snd_cmipci_suspend [label="snd_cmipci_suspend (LOC=25)"];
	 snd_cmipci_uswitch_get [label="snd_cmipci_uswitch_get (LOC=8)"];
	 snd_cmipci_uswitch_put [label="snd_cmipci_uswitch_put (LOC=8)"];
	 snd_cmipci_write [label="snd_cmipci_write (LOC=4)"];
	 snd_cmipci_write_b [label="snd_cmipci_write_b (LOC=4)"];
	 snd_cmipci_write_w [label="snd_cmipci_write_w (LOC=4)"];
	 snd_info_set_text_ops [label="snd_info_set_text_ops (LOC=7)"];
	 snd_power_change_state [label="snd_power_change_state (LOC=5)"];
	 MICRODRIVERS__MODIF___pci_register_driver -> MICRODRIVERS__DUMMY;
	 MICRODRIVERS__MODIF_create_proc_entry -> MICRODRIVERS__DUMMY;
	 MICRODRIVERS__MODIF_device_create_file -> MICRODRIVERS__DUMMY;
	 MICRODRIVERS__MODIF_hrtimer_get_res -> MICRODRIVERS__DUMMY;
	 MICRODRIVERS__MODIF_pci_disable_device -> MICRODRIVERS__DUMMY;
	 MICRODRIVERS__MODIF_pci_set_master -> MICRODRIVERS__DUMMY;
	 MICRODRIVERS__MODIF_pci_unregister_driver -> MICRODRIVERS__DUMMY;
	 MICRODRIVERS__MODIF_proc_symlink -> MICRODRIVERS__DUMMY;
	 __raw_spin_unlock -> __ticket_spin_unlock;
	 _snd_cmipci_uswitch_get -> __raw_spin_unlock;
	 _snd_cmipci_uswitch_get -> inb;
	 _snd_cmipci_uswitch_get -> raw_local_irq_enable;
	 _snd_cmipci_uswitch_get -> snd_cmipci_read;
	 _snd_cmipci_uswitch_put -> __raw_spin_unlock;
	 _snd_cmipci_uswitch_put -> inb;
	 _snd_cmipci_uswitch_put -> outb;
	 _snd_cmipci_uswitch_put -> raw_local_irq_enable;
	 _snd_cmipci_uswitch_put -> snd_cmipci_read;
	 _snd_cmipci_uswitch_put -> snd_cmipci_write;
	 cleanup_module -> alsa_card_cmipci_exit;
	 close_device_check -> __raw_spin_unlock;
	 close_device_check -> raw_local_irq_enable;
	 close_device_check -> snd_cmipci_ch_reset;
	 close_device_check -> snd_cmipci_set_bit;
	 gameport_allocate_port -> kzalloc;
	 get_line_in_mode -> snd_cmipci_read;
	 get_line_in_mode -> snd_cmipci_read_b;
	 init_module -> alsa_card_cmipci_init;
	 kzalloc -> kmalloc;
	 open_device_check -> __raw_spin_unlock;
	 open_device_check -> raw_local_irq_enable;
	 open_device_check -> snd_cmipci_clear_bit;
	 pci_get_drvdata -> dev_get_drvdata;
	 pci_name -> dev_name;
	 pci_set_drvdata -> dev_set_drvdata;
	 query_chip -> snd_cmipci_read;
	 raw_local_irq_enable -> native_irq_enable;
	 restore_mixer_state -> kmalloc;
	 save_mixer_state -> kmalloc;
	 set_dac_channels -> __raw_spin_unlock;
	 set_dac_channels -> raw_local_irq_enable;
	 set_dac_channels -> snd_cmipci_clear_bit;
	 set_dac_channels -> snd_cmipci_set_bit;
	 setup_ac3 -> snd_cmipci_clear_bit;
	 setup_ac3 -> snd_cmipci_set_bit;
	 setup_spdif_playback -> __raw_spin_unlock;
	 setup_spdif_playback -> raw_local_irq_enable;
	 setup_spdif_playback -> save_mixer_state;
	 setup_spdif_playback -> setup_ac3;
	 setup_spdif_playback -> snd_cmipci_clear_bit;
	 setup_spdif_playback -> snd_cmipci_set_bit;
	 snd_cmipci_capture_close -> close_device_check;
	 snd_cmipci_capture_open -> open_device_check;
	 snd_cmipci_capture_pointer -> snd_cmipci_pcm_pointer;
	 snd_cmipci_capture_prepare -> snd_cmipci_pcm_prepare;
	 snd_cmipci_capture_spdif_close -> close_device_check;
	 snd_cmipci_capture_spdif_hw_free -> __raw_spin_unlock;
	 snd_cmipci_capture_spdif_hw_free -> raw_local_irq_enable;
	 snd_cmipci_capture_spdif_hw_free -> snd_cmipci_clear_bit;
	 snd_cmipci_capture_spdif_hw_free -> snd_cmipci_hw_free;
	 snd_cmipci_capture_spdif_open -> open_device_check;
	 snd_cmipci_capture_spdif_prepare -> __raw_spin_unlock;
	 snd_cmipci_capture_spdif_prepare -> raw_local_irq_enable;
	 snd_cmipci_capture_spdif_prepare -> snd_cmipci_clear_bit;
	 snd_cmipci_capture_spdif_prepare -> snd_cmipci_pcm_prepare;
	 snd_cmipci_capture_spdif_prepare -> snd_cmipci_set_bit;
	 snd_cmipci_capture_trigger -> snd_cmipci_pcm_trigger;
	 snd_cmipci_ch_reset -> snd_cmipci_write;
	 snd_cmipci_clear_bit -> inl;
	 snd_cmipci_clear_bit -> outl;
	 snd_cmipci_clear_bit_b -> inb;
	 snd_cmipci_clear_bit_b -> outb;
	 snd_cmipci_create -> inb;
	 snd_cmipci_create -> kzalloc;
	 snd_cmipci_create -> query_chip;
	 snd_cmipci_create -> snd_cmipci_ch_reset;
	 snd_cmipci_create -> snd_cmipci_clear_bit;
	 snd_cmipci_create -> snd_cmipci_create_fm;
	 snd_cmipci_create -> snd_cmipci_create_gameport;
	 snd_cmipci_create -> snd_cmipci_free;
	 snd_cmipci_create -> snd_cmipci_mixer_new;
	 snd_cmipci_create -> snd_cmipci_mixer_write;
	 snd_cmipci_create -> snd_cmipci_pcm2_new;
	 snd_cmipci_create -> snd_cmipci_pcm_new;
	 snd_cmipci_create -> snd_cmipci_pcm_spdif_new;
	 snd_cmipci_create -> snd_cmipci_proc_init;
	 snd_cmipci_create -> snd_cmipci_read_b;
	 snd_cmipci_create -> snd_cmipci_set_bit;
	 snd_cmipci_create -> snd_cmipci_write;
	 snd_cmipci_create -> snd_cmipci_write_b;
	 snd_cmipci_create_fm -> snd_cmipci_clear_bit;
	 snd_cmipci_create_fm -> snd_cmipci_read;
	 snd_cmipci_create_fm -> snd_cmipci_set_bit;
	 snd_cmipci_create_fm -> snd_cmipci_write;
	 snd_cmipci_create_gameport -> gameport_allocate_port;
	 snd_cmipci_create_gameport -> gameport_register_port;
	 snd_cmipci_create_gameport -> gameport_set_name;
	 snd_cmipci_create_gameport -> pci_name;
	 snd_cmipci_create_gameport -> snd_cmipci_set_bit;
	 snd_cmipci_dev_free -> snd_cmipci_free;
	 snd_cmipci_free -> snd_cmipci_ch_reset;
	 snd_cmipci_free -> snd_cmipci_clear_bit;
	 snd_cmipci_free -> snd_cmipci_free_gameport;
	 snd_cmipci_free -> snd_cmipci_mixer_write;
	 snd_cmipci_free -> snd_cmipci_write;
	 snd_cmipci_free_gameport -> snd_cmipci_clear_bit;
	 snd_cmipci_get_input_sw -> __raw_spin_unlock;
	 snd_cmipci_get_input_sw -> cmipci_sb_reg_decode;
	 snd_cmipci_get_input_sw -> raw_local_irq_enable;
	 snd_cmipci_get_input_sw -> snd_cmipci_mixer_read;
	 snd_cmipci_get_native_mixer -> __raw_spin_unlock;
	 snd_cmipci_get_native_mixer -> cmipci_sb_reg_decode;
	 snd_cmipci_get_native_mixer -> inb;
	 snd_cmipci_get_native_mixer -> raw_local_irq_enable;
	 snd_cmipci_get_native_mixer_sensitive -> snd_cmipci_get_native_mixer;
	 snd_cmipci_get_volume -> __raw_spin_unlock;
	 snd_cmipci_get_volume -> cmipci_sb_reg_decode;
	 snd_cmipci_get_volume -> raw_local_irq_enable;
	 snd_cmipci_get_volume -> snd_cmipci_mixer_read;
	 snd_cmipci_hw_params -> hw_param_interval;
	 snd_cmipci_info_native_mixer -> cmipci_sb_reg_decode;
	 snd_cmipci_info_volume -> cmipci_sb_reg_decode;
	 snd_cmipci_interrupt -> __raw_spin_unlock;
	 snd_cmipci_interrupt -> snd_cmipci_clear_bit;
	 snd_cmipci_interrupt -> snd_cmipci_read;
	 snd_cmipci_interrupt -> snd_cmipci_set_bit;
	 snd_cmipci_line_in_mode_get -> __raw_spin_unlock;
	 snd_cmipci_line_in_mode_get -> get_line_in_mode;
	 snd_cmipci_line_in_mode_get -> raw_local_irq_enable;
	 snd_cmipci_line_in_mode_put -> __raw_spin_unlock;
	 snd_cmipci_line_in_mode_put -> raw_local_irq_enable;
	 snd_cmipci_line_in_mode_put -> snd_cmipci_clear_bit;
	 snd_cmipci_line_in_mode_put -> snd_cmipci_clear_bit_b;
	 snd_cmipci_line_in_mode_put -> snd_cmipci_set_bit;
	 snd_cmipci_line_in_mode_put -> snd_cmipci_set_bit_b;
	 snd_cmipci_mic_in_mode_get -> __raw_spin_unlock;
	 snd_cmipci_mic_in_mode_get -> raw_local_irq_enable;
	 snd_cmipci_mic_in_mode_get -> snd_cmipci_read_b;
	 snd_cmipci_mic_in_mode_put -> __raw_spin_unlock;
	 snd_cmipci_mic_in_mode_put -> raw_local_irq_enable;
	 snd_cmipci_mic_in_mode_put -> snd_cmipci_clear_bit_b;
	 snd_cmipci_mic_in_mode_put -> snd_cmipci_set_bit_b;
	 snd_cmipci_mixer_new -> __raw_spin_unlock;
	 snd_cmipci_mixer_new -> __snd_bug_on;
	 snd_cmipci_mixer_new -> raw_local_irq_enable;
	 snd_cmipci_mixer_new -> snd_cmipci_mixer_write;
	 snd_cmipci_mixer_read -> inb;
	 snd_cmipci_mixer_read -> outb;
	 snd_cmipci_mixer_write -> outb;
	 snd_cmipci_pcm_pointer -> snd_cmipci_read_w;
	 snd_cmipci_pcm_prepare -> __raw_spin_unlock;
	 snd_cmipci_pcm_prepare -> raw_local_irq_enable;
	 snd_cmipci_pcm_prepare -> set_dac_channels;
	 snd_cmipci_pcm_prepare -> snd_cmipci_clear_bit;
	 snd_cmipci_pcm_prepare -> snd_cmipci_rate_freq;
	 snd_cmipci_pcm_prepare -> snd_cmipci_read;
	 snd_cmipci_pcm_prepare -> snd_cmipci_set_bit;
	 snd_cmipci_pcm_prepare -> snd_cmipci_write;
	 snd_cmipci_pcm_prepare -> snd_cmipci_write_w;
	 snd_cmipci_pcm_trigger -> __raw_spin_unlock;
	 snd_cmipci_pcm_trigger -> snd_cmipci_clear_bit;
	 snd_cmipci_pcm_trigger -> snd_cmipci_set_bit;
	 snd_cmipci_pcm_trigger -> snd_cmipci_write;
	 snd_cmipci_playback2_close -> close_device_check;
	 snd_cmipci_playback2_hw_free -> snd_cmipci_hw_free;
	 snd_cmipci_playback2_hw_free -> snd_cmipci_silence_hack;
	 snd_cmipci_playback2_hw_params -> hw_param_interval;
	 snd_cmipci_playback2_open -> open_device_check;
	 snd_cmipci_playback_close -> close_device_check;
	 snd_cmipci_playback_hw_free -> restore_mixer_state;
	 snd_cmipci_playback_hw_free -> setup_spdif_playback;
	 snd_cmipci_playback_hw_free -> snd_cmipci_hw_free;
	 snd_cmipci_playback_hw_free -> snd_cmipci_silence_hack;
	 snd_cmipci_playback_open -> open_device_check;
	 snd_cmipci_playback_pointer -> snd_cmipci_pcm_pointer;
	 snd_cmipci_playback_prepare -> setup_spdif_playback;
	 snd_cmipci_playback_prepare -> snd_cmipci_pcm_prepare;
	 snd_cmipci_playback_spdif_close -> close_device_check;
	 snd_cmipci_playback_spdif_open -> open_device_check;
	 snd_cmipci_playback_spdif_prepare -> setup_spdif_playback;
	 snd_cmipci_playback_spdif_prepare -> snd_cmipci_pcm_prepare;
	 snd_cmipci_playback_trigger -> snd_cmipci_pcm_trigger;
	 snd_cmipci_probe -> pci_set_drvdata;
	 snd_cmipci_probe -> snd_cmipci_create;
	 snd_cmipci_proc_init -> snd_info_set_text_ops;
	 snd_cmipci_proc_read -> inb;
	 snd_cmipci_put_input_sw -> __raw_spin_unlock;
	 snd_cmipci_put_input_sw -> cmipci_sb_reg_decode;
	 snd_cmipci_put_input_sw -> raw_local_irq_enable;
	 snd_cmipci_put_input_sw -> snd_cmipci_mixer_read;
	 snd_cmipci_put_input_sw -> snd_cmipci_mixer_write;
	 snd_cmipci_put_native_mixer -> __raw_spin_unlock;
	 snd_cmipci_put_native_mixer -> cmipci_sb_reg_decode;
	 snd_cmipci_put_native_mixer -> inb;
	 snd_cmipci_put_native_mixer -> outb;
	 snd_cmipci_put_native_mixer -> raw_local_irq_enable;
	 snd_cmipci_put_native_mixer_sensitive -> snd_cmipci_put_native_mixer;
	 snd_cmipci_put_volume -> __raw_spin_unlock;
	 snd_cmipci_put_volume -> cmipci_sb_reg_decode;
	 snd_cmipci_put_volume -> raw_local_irq_enable;
	 snd_cmipci_put_volume -> snd_cmipci_mixer_read;
	 snd_cmipci_put_volume -> snd_cmipci_mixer_write;
	 snd_cmipci_read -> inl;
	 snd_cmipci_read_b -> inb;
	 snd_cmipci_read_w -> inw;
	 snd_cmipci_remove -> pci_get_drvdata;
	 snd_cmipci_remove -> pci_set_drvdata;
	 snd_cmipci_resume -> pci_get_drvdata;
	 snd_cmipci_resume -> snd_cmipci_ch_reset;
	 snd_cmipci_resume -> snd_cmipci_mixer_write;
	 snd_cmipci_resume -> snd_cmipci_write;
	 snd_cmipci_resume -> snd_power_change_state;
	 snd_cmipci_set_bit -> inl;
	 snd_cmipci_set_bit -> outl;
	 snd_cmipci_set_bit_b -> inb;
	 snd_cmipci_set_bit_b -> outb;
	 snd_cmipci_silence_hack -> __raw_spin_unlock;
	 snd_cmipci_silence_hack -> raw_local_irq_enable;
	 snd_cmipci_silence_hack -> set_dac_channels;
	 snd_cmipci_silence_hack -> snd_cmipci_read;
	 snd_cmipci_silence_hack -> snd_cmipci_write;
	 snd_cmipci_spdif_default_get -> __raw_spin_unlock;
	 snd_cmipci_spdif_default_get -> raw_local_irq_enable;
	 snd_cmipci_spdif_default_put -> __raw_spin_unlock;
	 snd_cmipci_spdif_default_put -> raw_local_irq_enable;
	 snd_cmipci_spdif_stream_get -> __raw_spin_unlock;
	 snd_cmipci_spdif_stream_get -> raw_local_irq_enable;
	 snd_cmipci_spdif_stream_put -> __raw_spin_unlock;
	 snd_cmipci_spdif_stream_put -> raw_local_irq_enable;
	 snd_cmipci_spdout_enable_get -> _snd_cmipci_uswitch_get;
	 snd_cmipci_spdout_enable_put -> _snd_cmipci_uswitch_put;
	 snd_cmipci_spdout_enable_put -> snd_cmipci_clear_bit;
	 snd_cmipci_spdout_enable_put -> snd_cmipci_set_bit;
	 snd_cmipci_suspend -> pci_get_drvdata;
	 snd_cmipci_suspend -> snd_cmipci_mixer_read;
	 snd_cmipci_suspend -> snd_cmipci_read;
	 snd_cmipci_suspend -> snd_cmipci_write;
	 snd_cmipci_suspend -> snd_power_change_state;
	 snd_cmipci_uswitch_get -> __snd_bug_on;
	 snd_cmipci_uswitch_get -> _snd_cmipci_uswitch_get;
	 snd_cmipci_uswitch_put -> __snd_bug_on;
	 snd_cmipci_uswitch_put -> _snd_cmipci_uswitch_put;
	 snd_cmipci_write -> outl;
	 snd_cmipci_write_b -> outb;
	 snd_cmipci_write_w -> outw;
label = <<table border="0" cellborder="1">
<tr><td>STATS - total functions: 0</td></tr>
<tr><td>STATS - total_LOC: 0</td></tr>
<tr><td bgcolor="gray">STATS - no_annotation: -1</td></tr>
<tr><td bgcolor="gray">STATS - no_annotation_LOC: -1</td></tr>
<tr><td>STATS - kern_funcs: 62</td></tr>
<tr><td>STATS - kern_funcs_LOC: -1</td></tr>
</table>>
}