## Slide 1: Presto: Edge-based Load Balancing for Fast Datacenter Networks
Keqiang He, Eric Rozner, Kanak Agarwal, Wes Felter, John Carter, Aditya Akella

## Slide 2: Background
Datacenter networks support a wide variety of traffic
Elephants: throughput sensitive
Data Ingestion, VM Migration, Backups
Mice: latency sensitive
Search, Gaming, Web, RPCs

## Slide 3: The Problem
Network congestion: flows of both types suffer
Example
  Elephant throughput is cut by half
  TCP RTT is increased by 100X per hop (Rasley, SIGCOMM’14)
SLA is violated, revenue is impacted

## Slide 4: Traffic Load Balancing Schemes
Scheme | Hardware changes | Transport changes | Granularity | Pro-/reactive

## Slide 5: Traffic Load Balancing Schemes
Scheme | Hardware changes | Transport changes | Granularity | Pro-/reactive
ECMP | No | No | Coarse-grained | Proactive
Proactive: try to avoid network congestion in the first place

## Slide 6: Traffic Load Balancing Schemes
Scheme | Hardware changes | Transport changes | Granularity | Pro-/reactive
ECMP | No | No | Coarse-grained | Proactive
Centralized | No | No | Coarse-grained | Reactive (control loop)
Reactive: mitigate congestion after it already happens

## Slide 7: Traffic Load Balancing Schemes
Scheme | Hardware changes | Transport changes | Granularity | Pro-/reactive
ECMP | No | No | Coarse-grained | Proactive
Centralized | No | No | Coarse-grained | Reactive (control loop)
MPTCP | No | Yes | Fine-grained | Reactive

## Slide 8: Traffic Load Balancing Schemes
Scheme | Hardware changes | Transport changes | Granularity | Pro-/reactive
ECMP | No | No | Coarse-grained | Proactive
Centralized | No | No | Coarse-grained | Reactive (control loop)
MPTCP | No | Yes | Fine-grained | Reactive
CONGA/ Juniper VCF | Yes | No | Fine-grained | Proactive

## Slide 9: Traffic Load Balancing Schemes
Scheme | Hardware changes | Transport changes | Granularity | Pro-/reactive
ECMP | No | No | Coarse-grained | Proactive
Centralized | No | No | Coarse-grained | Reactive (control loop)
MPTCP | No | Yes | Fine-grained | Reactive
CONGA/ Juniper VCF | Yes | No | Fine-grained | Proactive
Presto | No | No | Fine-grained | Proactive

## Slide 10: Presto
Near perfect load balancing without changing hardware or transport
  Utilize the software edge (vSwitch)
  Leverage TCP offloading features below transport layer
  Work at 10 Gbps and beyond
Goal: near optimally load balance the network at fast speeds

## Slide 11: Presto at a High Level
vSwitch
NIC
NIC
vSwitch
TCP/IP
Spine
Leaf
TCP/IP
Near uniform-sized data units

## Slide 12: Presto at a High Level
vSwitch
NIC
NIC
vSwitch
TCP/IP
Spine
Leaf
TCP/IP
Proactively distributed evenly over symmetric network by vSwitch sender
Near uniform-sized data units

## Slide 13: Presto at a High Level
vSwitch
NIC
NIC
vSwitch
TCP/IP
Spine
Leaf
TCP/IP
Proactively distributed evenly over symmetric network by vSwitch sender
Near uniform-sized data units

## Slide 14: Presto at a High Level
vSwitch
NIC
NIC
vSwitch
TCP/IP
Spine
Leaf
TCP/IP
Receiver masks packet reordering due to multipathing below transport layer
Proactively distributed evenly over symmetric network by vSwitch sender
Near uniform-sized data units

## Slide 15: Outline
Sender
Receiver
Evaluation

## Slide 16: What Granularity to do Load-balancing on?
Per-flow
  Elephant collisions
Per-packet
  High computational overhead
  Heavy reordering including mice flows
Flowlets
  Burst of packets separated by inactivity timer
  Effectiveness depends on workloads
inactivity timer
A lot of reordering
Mice flows fragmented
small
large
Large flowlets
(hash collisions)

## Slide 17: Presto LB Granularity
Presto: load-balance on flowcells
What is flowcell?
  A set of TCP segments with bounded byte count
  Bound is maximal TCP Segmentation Offload (TSO) size
    Maximize the benefit of TSO for high speed
    64KB in implementation
What’s TSO?
TCP/IP
NIC
Segmentation & Checksum Offload
MTU-sized Ethernet Frames
Large Segment

## Slide 18: Presto LB Granularity
Presto: load-balance on flowcells
What is flowcell?
  A set of TCP segments with bounded byte count
  Bound is maximal TCP Segmentation Offload (TSO) size
    Maximize the benefit of TSO for high speed
    64KB in implementation
Examples
25KB
30KB
30KB
Flowcell: 55KB
TCP segments
Start

## Slide 19: Presto LB Granularity
Presto: load-balance on flowcells
What is flowcell?
  A set of TCP segments with bounded byte count
  Bound is maximal TCP Segmentation Offload (TSO) size
    Maximize the benefit of TSO for high speed
    64KB in implementation
Examples
1KB
5KB
1KB
Flowcell: 7KB (the whole flow is 1 flowcell)
TCP segments
Start

## Slide 20: Presto Sender
vSwitch
NIC
NIC
vSwitch
TCP/IP
Spine
Leaf
TCP/IP
Host A
Host B
Controller installs label-switched paths

## Slide 21: Presto Sender
vSwitch
NIC
NIC
vSwitch
TCP/IP
Spine
Leaf
TCP/IP
Host A
Host B
Controller installs label-switched paths

## Slide 22: Presto Sender
vSwitch
NIC
NIC
vSwitch
TCP/IP
Spine
Leaf
TCP/IP
vSwitch receives TCP segment #1
Host A
Host B
50KB
id,label
flowcell #1: vSwitch encodes flowcell ID, rewrites label
NIC uses TSO and chunks segment #1 into MTU-sized packets

## Slide 23: Presto Sender
vSwitch
NIC
NIC
vSwitch
TCP/IP
Spine
Leaf
TCP/IP
vSwitch receives TCP segment #2
Host A
Host B
60KB
id,label
flowcell #2: vSwitch encodes flowcell ID, rewrites label
NIC uses TSO and chunks segment #2 into MTU-sized packets

## Slide 24: Benefits
Most flows smaller than 64KB [Benson, IMC’11]
  the majority of mice are not exposed to reordering
Most bytes from elephants [Alizadeh, SIGCOMM’10]
  traffic routed on uniform sizes
Fine-grained and deterministic scheduling over disjoint paths
  near optimal load balancing

## Slide 25: Presto Receiver
Major challenges
  Packet reordering for large flows due to multipath
  Distinguish loss from reordering
  Fast (10G and beyond)
  Light-weight

## Slide 26: Intro to GRO
Generic Receive Offload (GRO)
  The reverse process of TSO

## Slide 27: Intro to GRO
TCP/IP
GRO
NIC
OS
Hardware

## Slide 28: Intro to GRO
TCP/IP
GRO
NIC
MTU-sized
Packets
P2
P3
P4
P5
P1
Queue head

## Slide 29: Intro to GRO
TCP/IP
GRO
NIC
MTU-sized
Packets
P2
P3
P4
P5
P1
Merge
Queue head

## Slide 30: Intro to GRO
TCP/IP
GRO
NIC
MTU-sized
Packets
P2
P3
P4
P5
P1
Merge
Queue head

## Slide 31: Intro to GRO
TCP/IP
GRO
NIC
MTU-sized
Packets
P3
P4
P5
P1 – P2
Merge
Queue head

## Slide 32: Intro to GRO
TCP/IP
GRO
NIC
MTU-sized
Packets
P4
P5
P1 – P3
Merge
Queue head

## Slide 33: Intro to GRO
TCP/IP
GRO
NIC
MTU-sized
Packets
P5
P1 – P4
Merge
Queue head

## Slide 34: Intro to GRO
TCP/IP
GRO
NIC
MTU-sized
Packets
P1 – P5
Push-up
Large TCP segments are pushed-up at the end of a batched IO event
(i.e., a polling event)

## Slide 35: Intro to GRO
TCP/IP
GRO
NIC
MTU-sized
Packets
P1 – P5
Push-up
Merging pkts in GRO creates less segments & avoids using substantially more cycles at TCP/IP and above [Menon, ATC’08]
If GRO is disabled, ~6Gbps with 100% CPU usage of one core

## Slide 36: Reordering Challenges
P1
P2
P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC
Out of order packets

## Slide 37: Reordering Challenges
P1
P2
P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC

## Slide 38: Reordering Challenges
P1 – P2
P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC

## Slide 39: Reordering Challenges
P1 – P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC

## Slide 40: Reordering Challenges
P1 – P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC
GRO is designed to be fast and simple; it pushes-up the existing segment immediately when 1) there is a gap in sequence number, 2) MSS reached or 3) timeout fired

## Slide 41: Reordering Challenges
P1 – P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC

## Slide 42: Reordering Challenges
P1 – P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC

## Slide 43: Reordering Challenges
P1 – P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC

## Slide 44: Reordering Challenges
P1 – P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC

## Slide 45: Reordering Challenges
P1 – P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC

## Slide 46: Reordering Challenges
P1 – P3
P6
P4
P7
P5
P8 – P9
TCP/IP
GRO
NIC

## Slide 47: Reordering Challenges
P1 – P3
P6
P4
P7
P5
P8 – P9
TCP/IP
GRO
NIC

## Slide 48: Reordering Challenges
GRO is effectively disabled
Lots of small packets are pushed up to TCP/IP
Huge CPU processing overhead
Poor TCP performance due to massive reordering

## Slide 49: Improved GRO to Mask Reordering for TCP
P1
P2
P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC
Flowcell #1
Flowcell #2

## Slide 50: Improved GRO to Mask Reordering for TCP
P1
P2
P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC
Flowcell #1
Flowcell #2

## Slide 51: Improved GRO to Mask Reordering for TCP
P1 – P2
P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC
Flowcell #1
Flowcell #2

## Slide 52: Improved GRO to Mask Reordering for TCP
P1 – P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC
Flowcell #1
Flowcell #2

## Slide 53: Improved GRO to Mask Reordering for TCP
P1 – P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC
Flowcell #1
Flowcell #2
Idea: we merge packets in the same flowcell into one TCP segment, then we check whether the segments are in order

## Slide 54: Improved GRO to Mask Reordering for TCP
P1 – P4
P6
P7
P5
P8
P9
TCP/IP
GRO
NIC
Flowcell #1
Flowcell #2

## Slide 55: Improved GRO to Mask Reordering for TCP
P1 – P4
P6 – P7
P5
P8
P9
TCP/IP
GRO
NIC
Flowcell #1
Flowcell #2

## Slide 56: Improved GRO to Mask Reordering for TCP
P1 – P5
P6 – P7
P8
P9
TCP/IP
GRO
NIC
Flowcell #1
Flowcell #2

## Slide 57: Improved GRO to Mask Reordering for TCP
P1 – P5
P6 – P8
P9
TCP/IP
GRO
NIC
Flowcell #1
Flowcell #2

## Slide 58: Improved GRO to Mask Reordering for TCP
P1 – P5
P6 – P9
TCP/IP
GRO
NIC
Flowcell #1
Flowcell #2

## Slide 59: Improved GRO to Mask Reordering for TCP
P1 – P5
P6 – P9
TCP/IP
GRO
NIC
Flowcell #1
Flowcell #2

## Slide 60: Improved GRO to Mask Reordering for TCP
Benefits:
1)Large TCP segments pushed up, CPU efficient
2)Mask packet reordering for TCP below transport
Issue:
How we can tell loss from reordering?
Both create gaps in sequence numbers
  Loss should be pushed up immediately
  Reordered packets held and put in order

## Slide 61: Loss vs Reordering
Heuristic: sequence number gap within a flowcell is assumed to be loss
Action: no need to wait, push-up immediately
Presto Sender: packets in one flowcell are sent on the same path (64KB flowcell ~ 51 us on 10G networks)

## Slide 62: Loss vs Reordering
P1
P2
P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC
✗
Flowcell #1
Flowcell #2

## Slide 63: Loss vs Reordering
P1
P6 – P9
TCP/IP
GRO
NIC
P3 – P5
Flowcell #1
Flowcell #2
P2
✗

## Slide 64: Loss vs Reordering
P1
P6 – P9
TCP/IP
GRO
NIC
P3 – P5
No wait
Flowcell #1
Flowcell #2
P2
✗

## Slide 65: Loss vs Reordering
Benefits:
Most of losses happen within a flowcell and are captured by this heuristic
TCP can react quickly to losses
Corner Case:
Losses at the flowcell boundaries

## Slide 66: Loss vs Reordering
P1
P2
P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC
✗
Flowcell #1
Flowcell #2

## Slide 67: Loss vs Reordering
P1 – P5
P6
P7 – P9
TCP/IP
GRO
NIC
✗
Flowcell #1
Flowcell #2

## Slide 68: Loss vs Reordering
P1 – P5
P6
P7 – P9
TCP/IP
GRO
NIC
✗
Wait based on
adaptive timeout
(an estimation of the extent of reordering)
Flowcell #1
Flowcell #2

## Slide 69: Loss vs Reordering
P1 – P5
P6
P7 – P9
TCP/IP
GRO
NIC
✗
Flowcell #1
Flowcell #2

## Slide 70: Evaluation
Implemented in OVS 2.1.2 & Linux Kernel 3.11.0
  1500 LoC in kernel
  8 IBM RackSwitch G8246 10G switches, 16 hosts
Performance evaluation
  Compared with ECMP, MPTCP and Optimal
  TCP RTT, Throughput, Loss, Fairness and FCT
Leaf
Spine

## Slide 71: Microbenchmark
Presto’s effectiveness on handling reordering
Segment Size (KB)
CDF
Chart: 
Stride-like workload. Sender runs Presto. Vary receiver (unmodified GRO vs Presto GRO).
9.3G with 69% CPU
of one core (6% additional CPU overhead compared with the 0 packet reordering case)
4.6G with 100% CPU
of one core

## Slide 72: Evaluation
Chart: 
| Shuffle | Random | Stride | Bijection
ECMP | 2872.2175 | 4525.2567 | 5324.1979 | 5275.5302
MPTCP | 2921.4021 | 5335.9952 | 7396.2355 | 7095.1567
Presto | 2956.7857 | 6232.2405 | 9121.4621 | 9051.8426
Optimal | 3097.1641 | 6358.3881 | 9265.3628 | 9160.0432
Workloads
Throughput (Mbps)
Presto’s throughput is within 1 – 4% of Optimal, even when the network utilization is near 100%; In non-shuffle workloads, Presto improves upon ECMP by 38-72% and improves upon MPTCP by 17-28%.
Optimal: all the hosts are attached to one single non-blocking switch

## Slide 73: Evaluation
Chart: 
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0 | 1.1 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9 | 2.0 | 2.2 | 2.4 | 2.6 | 2.8 | 3.0 | 3.5 | 4.0 | 4.5 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0
ECMP | 0.00017143 | 0.1912 | 0.4989 | 0.54381 | 0.54473 | 0.545 | 0.54561 | 0.54671 | 0.54906 | 0.55381 | 0.56201 | 0.57236 | 0.58591 | 0.60227 | 0.62153 | 0.64393 | 0.67171 | 0.70154 | 0.73473 | 0.7678 | 0.82693 | 0.8705 | 0.90129 | 0.92917 | 0.95583 | 0.9942 | 0.99991 | 0.99999
MPTCP | 0.0015429 | 0.090729 | 0.37311 | 0.56704 | 0.68887 | 0.77134 | 0.82753 | 0.86701 | 0.89674 | 0.9195 | 0.93714 | 0.94957 | 0.96019 | 0.9678 | 0.9743 | 0.97906 | 0.98271 | 0.98589 | 0.98813 | 0.98984 | 0.9928 | 0.99496 | 0.99634 | 0.99703 | 0.99737 | 0.99766 | 0.99777 | 0.99781 | 0.9979 | 0.99799 | 0.99811 | 0.99816 | 0.99817 | 0.99819
Presto | 0.00018571 | 0.18464 | 0.64464 | 0.95466 | 0.99796 | 1
Optimal | 0.00022923 | 0.34006 | 0.90374 | 0.99924 | 1
TCP Round Trip Time (msec) [Stride Workload]
CDF
Presto’s 99.9% TCP RTT is within 100us of Optimal
8X smaller than ECMP

## Slide 74: Additional Evaluation
Presto scales to multiple paths
Presto handles congestion gracefully
  Loss rate, fairness index
Comparison to flowlet switching
Comparison to local, per-hop load balancing
Trace-driven evaluation
Impact of north-south traffic
Impact of link failures

## Slide 75: Conclusion
Presto: moving network function, Load Balancing, out of datacenter network hardware into software edge
No changes to hardware or transport
Performance is close to a giant switch
Notes: In conclusion, Presto moves the network function, load balancing, out of datacenter network hardware into the software defined edge.
The results are promising. We believe that other network functions can also be implemented at the software edge.
Presto requires no change to…

## Slide 76: Thanks!