## Slide 1: On Transactional Memory, Spinlocks and Database Transactions
Khai Q. Tran
Spyros Blanas
Jeffrey F. Naughton
(University of Wisconsin Madison)

## Slide 2: Motivation
Growing need for extremely high transaction (xact) processing rates.
  Potential markets: financial trading (Wall Street), airlines, and retailers .
  Focusing on extremely short xacts (no I/O, read and update a few records, a few hundreds of instructions).
DBMS industry recognizes this need:
  Some current startups: VoltDB and other.
  Major DBMS vendors also considering this market.
Notes: The motivation for this talk is well-known to this audience. The computer industry has transitioned from an era where microprocessor clock speeds doubled every two years, automatically delivering software performance improvement, to an era where microprocessor speeds are only incrementally improving. Computer designers have turned to integrating multiple cores on a processor, offering parallel execution as a new avenue for software performance improvement.
Today, the prevalent model for programming multicore processors is multithreading. But multithreading has significant drawbacks that threaten to hamper its widespread adoption. Dependences in a multithreaded program are typically encoded statically, which makes it hard to apply to client applications with irregular data accesses that will now need to achieve parallel execution. Multithreading introduces many new types of errors, such as data races and deadlock, that are not present in sequential programs. Furthermore, execution of multithreaded programs is nondeterministic, making it very difficult and costly to write, test, and debug these programs. It may also result in significant degradation in application reliability.
In order for the information technology industry to continue its past success, we need new parallel execution models to leverage the performance potential of multicore processors.

## Slide 3: Concurrency Control problem
Need a lightweight CC for such short xacts. Historical approaches:
Traditional db locks:
  High overhead of acquiring and releasing locks: at least 200-500 ins/lock, ≈ CPU time of a short xact.
Run xacts serially, with no CC:
  Garcia-Molina and Salem, 1984: Great for uniprocessor systems, but what about multi-cores?
Is there a way to run short xacts on multiple cores at close to their no CC rates?
Notes: The motivation for this talk is well-known to this audience. The computer industry has transitioned from an era where microprocessor clock speeds doubled every two years, automatically delivering software performance improvement, to an era where microprocessor speeds are only incrementally improving. Computer designers have turned to integrating multiple cores on a processor, offering parallel execution as a new avenue for software performance improvement.
Today, the prevalent model for programming multicore processors is multithreading. But multithreading has significant drawbacks that threaten to hamper its widespread adoption. Dependences in a multithreaded program are typically encoded statically, which makes it hard to apply to client applications with irregular data accesses that will now need to achieve parallel execution. Multithreading introduces many new types of errors, such as data races and deadlock, that are not present in sequential programs. Furthermore, execution of multithreaded programs is nondeterministic, making it very difficult and costly to write, test, and debug these programs. It may also result in significant degradation in application reliability.
In order for the information technology industry to continue its past success, we need new parallel execution models to leverage the performance potential of multicore processors.

## Slide 4: Can hardware help?
The community has long investigated hardware support for DB performance:
  Flash and SCM to mitigate slow disks
  Multi-cores and GPUs for parallelism
  FPGAs to implement basic DB query operations
  But has not explored hardware assist for xact isolation.
Can we also use hardware support to speed up short-xact workloads?

## Slide 5: Our work
Explore hardware primitives to support xact isolation.
Perhaps raises more questions than it answers, due to:
  Limitations of prototype hardware upon which to test
  Simple workloads because of the limitations
  Lack of consideration of many issues required for a complete solution.
Still, results suggest this is worth exploring.

## Slide 6: Hardware TM
  Idea: let pieces of code run atomically and in isolation on each core.
  Similar to optimistic CC in DBMS:
    Keep track of xact’s read set and write set
    Use a cache coherence protocol to detect conflicts (RW, WR, WW)
    Abort xact if a conflict happens (restart the xact later.)
Notes: The motivation for this talk is well-known to this audience. The computer industry has transitioned from an era where microprocessor clock speeds doubled every two years, automatically delivering software performance improvement, to an era where microprocessor speeds are only incrementally improving. Computer designers have turned to integrating multiple cores on a processor, offering parallel execution as a new avenue for software performance improvement.
Today, the prevalent model for programming multicore processors is multithreading. But multithreading has significant drawbacks that threaten to hamper its widespread adoption. Dependences in a multithreaded program are typically encoded statically, which makes it hard to apply to client applications with irregular data accesses that will now need to achieve parallel execution. Multithreading introduces many new types of errors, such as data races and deadlock, that are not present in sequential programs. Furthermore, execution of multithreaded programs is nondeterministic, making it very difficult and costly to write, test, and debug these programs. It may also result in significant degradation in application reliability.
In order for the information technology industry to continue its past success, we need new parallel execution models to leverage the performance potential of multicore processors.

## Slide 7: HTM – a simple example
T2
T3
A
B
C
D
T1
Core 1
Core 2
E
R
W
C’
A
B
R
W
D
E’
commit
W
conflict!
cache coherence protocol
abort
E’
D’
commit
C’
Xact | 
Read set | 
Write set | 
Xact | 
Read set | 
Write set | 
T1
{A, B}
{C}
T2
{B, D}
{E}
T3
{A, D}
Notes: The motivation for this talk is well-known to this audience. The computer industry has transitioned from an era where microprocessor clock speeds doubled every two years, automatically delivering software performance improvement, to an era where microprocessor speeds are only incrementally improving. Computer designers have turned to integrating multiple cores on a processor, offering parallel execution as a new avenue for software performance improvement.
Today, the prevalent model for programming multicore processors is multithreading. But multithreading has significant drawbacks that threaten to hamper its widespread adoption. Dependences in a multithreaded program are typically encoded statically, which makes it hard to apply to client applications with irregular data accesses that will now need to achieve parallel execution. Multithreading introduces many new types of errors, such as data races and deadlock, that are not present in sequential programs. Furthermore, execution of multithreaded programs is nondeterministic, making it very difficult and costly to write, test, and debug these programs. It may also result in significant degradation in application reliability.
In order for the information technology industry to continue its past success, we need new parallel execution models to leverage the performance potential of multicore processors.

## Slide 8: HTM: pros and cons
Pros: very low overhead.
Cons: trouble with high contention.
Chart: # threads
TM | 0.96247 | 1.677 | 2.2498 | 2.7915 | 2.7864 | 2.7002 | 2.4148 | 2.0806 | 1.8137 | 1.5515 | 1.4375 | 1.325 | 1.2333 | 1.1887 | 1.1582
Scalability of HTM

## Slide 9: Alternative: Spinlocks
Spinlock: a lock where the thread simply waits and repeatedly checks until the lock becomes available.
  Can be implemented with atomic instructions: test-and-set, compare-and-swap.
Spinlocks as a CC method:
  Associate each database object with a spinlock.
  Acquire and release locks following 2PL protocol.
  No lock manager, no lock table → problem with deadlock detection.

## Slide 10: Spinlocks: deadlock detection/prevention
No data structure to build the “waits-for” graph => hard to detect deadlocks.
Solutions:
  Approach 1: if objects accessed by xacts are known in advance, sort to prevent deadlocks.
  Approach 2: if not, use time-out mechanism.

## Slide 11: Experiments: HTM, spinlock and database lock
Workload:
  Database:
    Collections of objects, each object: (key, value)
    Database size = 1000.
  Xacts:
    Read and update numbers of objects
    Less than 1000 instructions.
  Workload contention:
    Vary degree to which the workload can be partitioned among cores (Perfect partitioning means no contention.)

## Slide 12: Experiments: HTM, spinlock and database lock (2)
Environment:
  Hardware prototype of HTM (TM0): 16 cores, real hardware, fun and challenging!
  TM Simulator: LogTM from Wisconsin GEMS project.

## Slide 13: Implementation of database lock
Simple implementation of the lock manager with out deadlock detection
Sort objects in advance to prevent deadlocks
Our purpose: get the lower bound of the lock manager performance.

## Slide 14: Experiment 1: Overhead
(a) on TM0
(b) on LogTM
Chart: # Objects
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20
TM | 0.158 | 0.1714 | 0.1752 | 0.1792 | 0.1802 | 0.1818 | 0.1848 | 0.2112 | 0.2142 | 0.2386
spinlock | 0.289 | 0.55 | 0.846 | 1.106 | 1.364 | 1.586 | 1.882 | 2.153 | 2.365 | 2.604
DB lock | 1.7766 | 3.3286 | 5.0766 | 6.299 | 7.8674 | 10.2056 | 12.6072 | 14.2512 | 16.1136 | 17.613
Chart: # Objects
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20
TM | 0.048761 | 0.067708 | 0.043251 | 0.080307 | 0.082215 | 0.18952 | 0.19829 | 0.083093 | 0.082308 | 0.085731
spinlock | 0.17128 | 0.58264 | 0.78382 | 1.0007 | 1.2229 | 1.2631 | 1.3819 | 1.4914 | 1.724 | 1.9265
DB lock | 2.0054 | 4.2687 | 6.1739 | 7.8503 | 9.7142 | 11.5157 | 13.8915 | 15.7507 | 17.3474 | 19.7515

## Slide 15: Experiment 2: Scalability – low contention
On LogTM, 10 reads + 10 writes/xact, 95% partitioned
Chart: # threads
TM | 0.96228 | 1.9381 | 2.932 | 3.7105 | 4.3929 | 5.1367 | 6.0147 | 6.6084 | 7.3195 | 7.801 | 8.1983 | 8.7698 | 9.2984 | 9.6826 | 9.9637 | 10.4319
spinlock | 0.30046 | 0.59817 | 0.92327 | 1.217 | 1.5408 | 1.8505 | 2.157 | 2.4326 | 2.7472 | 3.0483 | 3.3655 | 3.6483 | 3.97 | 4.2527 | 4.5772 | 4.8563
DB lock | 0.19107 | 0.3193 | 0.43488 | 0.5857 | 0.66094 | 0.70864 | 0.80585 | 0.8903 | 0.9392 | 0.96714 | 0.44335 | 0.42847 | 0.39211 | 0.32636 | 0.33234 | 0.27766
1 thread with no CC | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 16: Experiment 3: Scalability – high contention
On LogTM, 10 reads + 10 writes/xact, 0% partitioned
Chart: # threads
TM | 0.96247 | 1.677 | 2.2498 | 2.7915 | 2.7864 | 2.7002 | 2.4148 | 2.0806 | 1.8137 | 1.5515 | 1.4375 | 1.325 | 1.2333 | 1.1887 | 1.1582
spinlock | 0.29531 | 0.5639 | 0.84263 | 1.1066 | 1.36 | 1.6078 | 1.8527 | 2.0811 | 2.297 | 2.5076 | 2.7032 | 2.9087 | 3.0814 | 3.2633 | 3.4163 | 3.6161
DB lock | 0.1911 | 0.29828 | 0.38901 | 0.49344 | 0.57489 | 0.59605 | 0.57661 | 0.42904 | 0.33236 | 0.31329 | 0.28928 | 0.27444 | 0.25692 | 0.23967 | 0.22811 | 0.23334
1 thread with no CC | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 17: Summary
Hardware support for very short transactions on multi-cores is intriguing and promising.
  HTM works well under low contention.
  Spinlocks work well under higher contention.
  Both hardware support approaches completely dominate traditional db locks.
A great deal of work remains to fully explore this area.
Notes: The motivation for this talk is well-known to this audience. The computer industry has transitioned from an era where microprocessor clock speeds doubled every two years, automatically delivering software performance improvement, to an era where microprocessor speeds are only incrementally improving. Computer designers have turned to integrating multiple cores on a processor, offering parallel execution as a new avenue for software performance improvement.
Today, the prevalent model for programming multicore processors is multithreading. But multithreading has significant drawbacks that threaten to hamper its widespread adoption. Dependences in a multithreaded program are typically encoded statically, which makes it hard to apply to client applications with irregular data accesses that will now need to achieve parallel execution. Multithreading introduces many new types of errors, such as data races and deadlock, that are not present in sequential programs. Furthermore, execution of multithreaded programs is nondeterministic, making it very difficult and costly to write, test, and debug these programs. It may also result in significant degradation in application reliability.
In order for the information technology industry to continue its past success, we need new parallel execution models to leverage the performance potential of multicore processors.