## Slide 1: Bypassing Last-Level Caches for Energy Efficiency
“Half the money I spend on advertising is wasted; the trouble is I don't know which half.”
Attributed to John Wanamaker
Lena E. Olson and Mark D. Hill

## Slide 2: Bypassing Last-Level Caches for Energy Efficiency
“Half the energy I spend on caching is wasted; the trouble is I don't know which half.”
Lena E. Olson and Mark D. Hill

## Slide 3: Executive Summary
Memory growing faster than cache
  In-memory workloads don’t fit in cache
L2/L3 caches have inefficiencies
  High miss percentage
  High percentage of blocks evicted before use
Bypassing can
  save dynamic energy
  reduce cache pollution
  improve performance

## Slide 4: Outline
Motivation and Opportunity
Hardware Approach
Software Approach
Conclusion

## Slide 5: But first… Caveats
Preliminary work
Focusing on exclusive caches

## Slide 6: Caches Save Energy
Static Energy
  Reduced load/store latency -> reduced execution time
Dynamic Energy
  Avoid memory accesses

## Slide 7: However… L2 and L3 are inefficient
Takeaway: many accesses miss!
Chart: Miss % for Exclusive 512KB L2
| astar | bwaves | bzip2 | cactusADM | calculix | gamess | gcc | GemsFDTD | gobmk | gormacs | h264ref | hmmer | lbm | leslie3d | libquantum | mcf | milc | namd | omnetpp | perlbench | povray | soplex | AVERAGE
miss % | 41.612 | 74.7621 | 28.1373 | 43.1764 | 7.3228 | 1.6564 | 19.6914 | 91.3819 | 14.2237 | 8.0586 | 4.2197 | 52.5268 | 60.4355 | 66.8459 | 99.0328 | 51.1772 | 98.1034 | 1.291 | 13.1104 | 12.9588 | 0.82753 | 69.5404 | 47.9722

## Slide 8: However… L2 and L3 are inefficient
Takeaway: many writes to LLC are avoidable; bypassing would not increase misses
Chart: % of Writes to L2 which are Avoidable
| astar | bwaves | bzip2 | cactusADM | calculix | gamess | gcc | GemsFDTD | gobmk | gormacs | h264ref | hmmer | lbm | leslie3d | libquantum | mcf | milc | namd | omnetpp | perlbench | povray | soplex | AVERAGE
avoidable writes | 93.5155 | 96.4362 | 52.2378 | 65.641 | 42.2403 | 51.1599 | 77.9354 | 95.3586 | 74.2082 | 69.6889 | 40.8629 | 90.4247 | 55.0569 | 86.5658 | 99.7281 | 87.0931 | 98.7426 | 68.4715 | 63.1841 | 74.7136 | 58.3171 | 82.9266 | 82.6327

## Slide 9: Breakdown of L2 Dynamic Energy
Chart: 
| astar | bwaves | bzip2 | cactusADM | calculix | gamess | gcc | GemsFDTD | gobmk | gormacs | h264ref | hmmer | lbm | leslie3d | libquantum | mcf | milc | namd | omnetpp | perlbench | povray | soplex | AVERAGE
hit | 546902.1691 | 231986.5385 | 1279374.7585 | 930860.8308 | 577227.2376 | 1433942.2047 | 2289972.5565 | 241466.9775 | 1429810.9703 | 1034490.5901 | 382982.1196 | 311728.4496 | 2401629.4775 | 1071879.8151 | 8965.4472 | 7819553.9813 | 37783.5616 | 1083716.1501 | 721658.469 | 1750101.1137 | 1628999.4205 | 1198654.8928 | 28413687.7317
miss | 29380.038 | 51801.1596 | 37759.3975 | 53315.1774 | 3437.9681 | 1820.5533 | 42324.5206 | 192997.7499 | 17871.9611 | 6834.7211 | 1271.8381 | 25999.0435 | 276529.3076 | 162903.9145 | 69196.0461 | 617850.9826 | 147316.8662 | 1068.3979 | 8207.8001 | 19640.4831 | 1024.6185 | 206279.5927 | 1974832.1375
unavoidable write | 46610.6907 | 45218.6348 | 441522.0459 | 448732.0032 | 47606.3536 | 20888.893 | 228662.2192 | 219667.5135 | 112597.6245 | 50250.7156 | 17362.0611 | 60883.8896 | 3048084.8378 | 536632.6617 | 4610.8723 | 1956124.606 | 45418.2463 | 7667.3004 | 73428.7189 | 121366.5973 | 9707.8214 | 863672.6378 | 8406716.9445
avoidable write | 672190.393 | 1223630.8727 | 482895.6024 | 857277.2346 | 34815.1119 | 21881.073 | 807668.0184 | 4513086.018 | 323965.263 | 115532.5877 | 11996.9317 | 574960.0211 | 3734016.205 | 3457902.8372 | 1690964.4 | 13199500.8471 | 3566666.0496 | 16651.3398 | 126019.917 | 358601.443 | 13581.851 | 4194927.1193 | 39998731.1367

## Slide 10: Breakdown of L2 Dynamic Energy
Takeaway: A lot of L2 dynamic energy goes to doing avoidable writes
Chart: 
| astar | bwaves | bzip2 | cactusADM | calculix | gamess | gcc | GemsFDTD | gobmk | gormacs | h264ref | hmmer | lbm | leslie3d | libquantum | mcf | milc | namd | omnetpp | perlbench | povray | soplex | AVERAGE
hit | 546902.1691 | 231986.5385 | 1279374.7585 | 930860.8308 | 577227.2376 | 1433942.2047 | 2289972.5565 | 241466.9775 | 1429810.9703 | 1034490.5901 | 382982.1196 | 311728.4496 | 2401629.4775 | 1071879.8151 | 8965.4472 | 7819553.9813 | 37783.5616 | 1083716.1501 | 721658.469 | 1750101.1137 | 1628999.4205 | 1198654.8928 | 28413687.7317
miss | 29380.038 | 51801.1596 | 37759.3975 | 53315.1774 | 3437.9681 | 1820.5533 | 42324.5206 | 192997.7499 | 17871.9611 | 6834.7211 | 1271.8381 | 25999.0435 | 276529.3076 | 162903.9145 | 69196.0461 | 617850.9826 | 147316.8662 | 1068.3979 | 8207.8001 | 19640.4831 | 1024.6185 | 206279.5927 | 1974832.1375
unavoidable write | 46610.6907 | 45218.6348 | 441522.0459 | 448732.0032 | 47606.3536 | 20888.893 | 228662.2192 | 219667.5135 | 112597.6245 | 50250.7156 | 17362.0611 | 60883.8896 | 3048084.8378 | 536632.6617 | 4610.8723 | 1956124.606 | 45418.2463 | 7667.3004 | 73428.7189 | 121366.5973 | 9707.8214 | 863672.6378 | 8406716.9445
avoidable write | 672190.393 | 1223630.8727 | 482895.6024 | 857277.2346 | 34815.1119 | 21881.073 | 807668.0184 | 4513086.018 | 323965.263 | 115532.5877 | 11996.9317 | 574960.0211 | 3734016.205 | 3457902.8372 | 1690964.4 | 13199500.8471 | 3566666.0496 | 16651.3398 | 126019.917 | 358601.443 | 13581.851 | 4194927.1193 | 39998731.1367

## Slide 11: Potential Benefits of Bypassing
Benefits of eliminating avoidable writes:
  Reduce dynamic energy
  Reduce cache pollution  increase effective cache capacity
  Smaller effect on other applications
  Reduce contention on L2/L3

## Slide 12: Predicting Avoidable Writes
“Half the energy I spend on caching blocks is wasted; the trouble is I don't know which half.”
Avoidable write characteristics?
Can we predict?
  Challenge: L2/L3 misses are expensive
  Need to avoid false positives!

## Slide 13: Why are some writes avoidable?
What kinds of blocks should we avoid writing to L2/L3?
  Random accesses into a hash table
  Streaming accesses
  Accesses to leaves of a tree (the nodes closer to the root are useful to cache)

## Slide 14: Why Not Bypass at L1?
Hard to have time for predictions
Many blocks have short-term reuse in L1, but not longer-term reuse in LLC
  for (i = 0; i < 100000000; i++){
  tmp = a[i];
  tmp = foo(tmp);
  a[i] = tmp;
  }
L1 hit rate >> LLC hit rate

## Slide 15: No-Reuse Blocks by PC
Chart: % of Accesses from PCs that Generate Avoidable Writes > X% of the time
| astar | bwaves | bzip2 | cactusADM | calculix | gamess | gcc | GemsFTDT | gobmk | gromacs | h264 | hmmer | lbm | leslie3d | libquantum | mcf | milc | namd | omnetppp | perlbench | povray | soplex | AVG
100 | 4.733 | 1.6876 | 3.5066 | 18.1835 | 2.929 | 2.656 | 20.9766 | 3.1185 | 41.1278 | 23.2579 | 1.3901 | 0 | 0.43467 | 30.9423 | 0 | 1.6619 | 8.755 | 37.1414 | 0 | 0.24711 | 0 | 6.2846 | 9.5015
99 | 5.9448 | 82.9841 | 5.4463 | 21.3987 | 1.9696 | 9.2586 | 17.1272 | 89.5884 | 10.5662 | 8.2513 | 1.4451 | 0 | 54.7309 | 28.1302 | 97.5004 | 23.3532 | 79.2426 | 18.5936 | 0.093801 | 24.0622 | 2.1085 | 40.2567 | 28.2751
98 | 2.0185 | 2.6162 | 3.6855 | 1.356 | 0 | 4.5339 | 10.9749 | 0.10119 | 0.10134 | 0.8728 | 0 | 0.18788 | 0.0034382 | 21.7004 | 0.11688 | 48.1963 | 0 | 0 | 0 | 8.9118 | 0 | 4.1027 | 4.9764
95 | 74.5407 | 0 | 0.22437 | 3.6481 | 2.1714 | 5.0427 | 4.244 | 0.016392 | 0 | 1.1637 | 0.59919 | 28.5513 | 0.018096 | 0.83566 | 0.062225 | 0.076823 | 0.0062943 | 0 | 0 | 2.9813 | 6.273 | 1.9386 | 6.0179
all no-reuse blocks | 3.1779 | 6.1927 | 37.5637 | 18.8601 | 29.0079 | 12.779 | 20.2865 | 2.3216 | 18.4178 | 23.3995 | 20.5573 | 56.8399 | 0.2552 | 4.6375 | 0.46138 | 13.8883 | 10.248 | 3.0754 | 60.7963 | 31.6206 | 26.5977 | 29.8569 | 19.5837
Takeaway: PC is predictive of reuse behavior

## Slide 16: Outline
Motivation and Opportunity
Hardware Approach
Software Approach
Conclusion

## Slide 17: Prediction Strategies: Hardware
The PC of an access is a strong predictor of reuse behavior
  However, tracking no-reuse blocks in hardware is difficult
  PC is not kept in the cache
  One possibility: make predictions using only the PC and address streams

## Slide 18: Case Study: Hardware Filter
One potential strategy: use a bitmap to keep track of PCs that access a wide range of addresses
PCs that access many addresses:
  Have poor locality
  Should bypass the LLC

## Slide 19: Hardware Filter Results
Chart: 
| astar | bwaves | bzip2 | cactusADM | calculix | gamess | gcc | GemsFDTD | gobmk | gormacs | h264ref | hmmer | lbm | leslie3d | libquantum | mcf | milc | namd | omnetpp | perlbench | povray | soplex
% writebacks avoided | 97.7718 | 93.0137 | 19.465 | 43.5 | 13.6016 | 40.6036 | 75.6967 | 93.9947 | 66.6667 | 58.7234 | 18.6227 | 86.383 | 29.9789 | 87.6709 | 99.5182 | 52.5732 | 99.5336 | 38.7233 | 19.3944 | 47.0745 | 18.5455 | 72.9736
Chart: 
| astar | bwaves | bzip2 | cactusADM | calculix | gamess | gcc | GemsFDTD | gobmk | gormacs | h264ref | hmmer | lbm | leslie3d | libquantum | mcf | milc | namd | omnetpp | perlbench | povray | soplex
normalized execution time | 1.0018 | 1.0006 | 0.99736 | 1.0038 | 1.0008 | 0.99983 | 1.0083 | 1.003 | 0.99955 | 0.99963 | 1 | 0.99505 | 1.0133 | 0.99708 | 0.99925 | 1.0053 | 1.0008 | 1.0001 | 1.0013 | 1.0032 | 1 | 1.0467
Takeaway: Insufficiently accurate so far

## Slide 20: Outline
Motivation and Opportunity
Hardware Approach
Software Approach
Conclusion

## Slide 21: Prediction Strategies: Cross-Layer
Exploit programmer knowledge of data access patterns
Most avoidable writes are from a few PCs
  Modifying a few lines of source code may be sufficient
Case study: insert prefetchnta
  On AMD machines, prefetchnta blocks are evicted from L1 directly to memory

## Slide 22: Speedup with added instructions
Chart: 
| baseline | baseline + prefetch | baseline + prefetchnta
graph500 | 1 | 0.97877 | 1.3725
CG | 1 | 0 | 1.0063
Takeaway: No performance degradation, actually a speedup

## Slide 23: L2 Writebacks
Chart: 
| baseline | baseline + prefetch | baseline + prefetchnta
graph500 | 1 | 1.0021 | 0.42586
CG | 1 | 0 | 0.25146
Takeaway: Eliminate many writes to L2

## Slide 24: Conclusion
Significant potential energy benefit to eliminating avoidable writes to LLC
Many avoidable writes come from a small number of PCs
  Hardware mechanisms may be able to predict
  Programmers may be able to annotate

## Slide 25: Questions?

## Slide 26: 512 KB vs. 4 MB L2
Chart: % of Accesses that Miss
| astar | bwaves | bzip2 | cactusADM | calculix | gamess | gcc | GemsFTDT | gobmk | gromacs | h264 | hmmer | lbm | leslie3d | libquantum | mcf | milc | namd | omnetpp | perlbench | povray | soplex
512KB | 45.0587 | 93.7225 | 33.3932 | 43.341 | 14.3484 | 1.6158 | 48.3989 | 91.3939 | 32.0362 | 8.0433 | 4.9366 | 52.6208 | 60.434 | 66.8459 | 99.0807 | 51.1762 | 98.1329 | 1.2783 | 16.9357 | 24.9476 | 0.87977 | 71.294
4MB | 42.8296 | 91.0173 | 1.5069 | 37.5637 | 5.3945 | 0.34878 | 41.9131 | 72.3969 | 21.536 | 3.7868 | 1.7375 | 3.9693 | 60.2495 | 56.8889 | 98.3578 | 42.1908 | 97.0276 | 1.2248 | 6.1388 | 18.191 | 0.47191 | 51.4197
Takeaway: A bigger cache doesn’t solve the problem

## Slide 27: Graph500 L2 Hit Rate
Takeaway: Benefits of bypassing for graph500 are not due to more efficient cache use
Chart: Hit Percentage
| baseline | baseline + prefetch | baseline + prefetchnta
graph500 | 7.1402 | 7.192 | 3.8124
CG | 1 | 0 | 0.1582