## Slide 1
ECE 1755
Lecture 17
Interconnects: Topology
Winter 2018
Prof. Natalie Enright Jerger

## Slide 2: Topics to be covered
Interfaces
Topology
Routing
Flow Control
Router Microarchitecture

## Slide 3: Topology Overview
Definition: determines arrangement of channels and nodes in network
  Analogous to road map
Often first step in network design
Significant impact on network cost-performance
  Determines number of hops
    Latency
    Network energy consumption
  Implementation complexity
    Node degree
    Ease of layout

## Slide 4: Abstract Metrics

## Slide 5: Abstract Metrics
Use metrics to evaluate performance and cost of topology
Also influenced by routing/flow control
  At this stage
    Assume ideal routing (perfect load balancing)
    Assume ideal flow control (no idle cycles on any channel)

## Slide 6: Abstract Metrics: Degree
Switch Degree: number of links at a node
  Proxy for estimating cost
    Higher degree requires more links and port counts at each router
A
B
A
B
A
B
2
4
2,3,4

## Slide 7: Abstract Metrics: Hop Count
Path: ordered set of channels between source and destination
Hop Count: number of hops a message takes from source to destination
  Simple, useful proxy for network latency
    Every node, link incurs some propagation delay even when no contention
Minimal hop count: smallest hop count connecting two nodes

## Slide 8: Hop Count
Network diameter: large min hop count in network
Average minimum hop count: average across all src/dst pairs
  Implementation may incorporate non-minimal paths
    Increases average hop count

## Slide 9: Hop Count
Uniform random traffic
  Ring > Mesh > Torus
Derivations later
A
B
A
B
A
B
Max = 4
Avg = 2.2
Max = 2
1.33
Max = 4
1.77

## Slide 10: Latency
Time for packet to traverse network
  Start: head arrives at input port
  End: tail departs output port
Latency = Head latency + serialization latency
  Serialization latency: time for packet with Length L to cross channel with bandwidth b (L/b)
Approximate with hop count
  Other design choices (routing, flow control) impact latency
    Unknown at this stage

## Slide 11: Abstract Metrics: Maximum Channel Load
Estimate max bandwidth the network can support
  Max bits per second (bps) that can be injected by every node before it saturates
    Saturation: network cannot accept any more traffic
  Determine most congested link
    For given traffic pattern
    Will limit overall network bandwidth
    Estimate load on this channel

## Slide 12: Maximum Channel Load
Preliminary
  Don’t know specifics of link yet
  Define relative to injection load
Channel load of 2
  Channel is loaded with twice injection bandwidth
  If each node injects a flit every cycle
    2 flits will want to traverse bottleneck channel every cycle
    If bottleneck channel can only handle 1 flit per cycle
      Max network bandwidth is ½ link bandwidth
      A flit can be injected every other cycle

## Slide 13: Maximum Channel Load Example
Uniform random
  Every node has equal probability of sending to every node
Identify bottleneck channel
Half of traffic from every node will cross bottleneck channel
  4 x ½ = 2
Network saturates at ½ injection bandwidth
A
C
D
B
E
G
H
F

## Slide 14: Bisection Bandwidth
Common off-chip metric
  Proxy for cost
  Amount of global wiring that will be necessary
  Less useful for on-chip
    Global on-chip wiring considered abundant
Cuts: partition all the nodes into two disjoint sets
  Bandwidth of a cut
Bisection
  A cut which divides all nodes into (nearly) half
  Channel bisection  min. channel count over all bisections
  Bisection bandwidth  min. bandwidth over all bisections
With uniform traffic
  ½ of traffic crosses bisection

## Slide 15: Throughput Example
Bisection = 4 (2 in each direction)
0
1
2
3
4
5
6
7
With uniform random traffic
  3 sends 1/8 of its traffic to 4,5,6
  3 sends 1/16 of its traffic to 7 (2 possible shortest paths)
  2 sends 1/8 of its traffic to 4,5
  Etc
Channel load = 1
Notes: Start here.

## Slide 16: Path Diversity
A
B
Multiple shortest paths between source/destination pair (R)
Fault tolerance
Better load balancing in network
Routing algorithm should be able to exploit path diversity
A
B
A
B
RA-B = 1
RA-B = 2
RA-B = 6

## Slide 17: Types of Topologies

## Slide 18: Types of Topologies
Focus on switched topologies
  Alternatives: bus and crossbar
  Bus
    Connects a set of components to a single shared channel
    Effective broadcast medium
  Crossbar
    Directly connects n inputs to m outputs without intermediate stages
    Fully connected, single hop network
    Component of routers

## Slide 19: Types of Topologies
Direct
  Each router is associated with a terminal node
  All routers are sources and destinations of traffic
Indirect
  Routers are distinct from terminal nodes
  Terminal nodes can source/sink traffic
  Intermediate nodes switch traffic between terminal nodes
Most on-chip network use direct topologies

## Slide 20: Torus (1)
K-ary n-cube: kn network nodes
N-Dimensional grid with k nodes in each dimension
3-ary 2-cube
3-ary 2-mesh
2,3,4-ary 3-mesh

## Slide 21: Torus (2)
1D or 2D torus map well to planar substrate for on-chip
Topologies in Torus Family
  Ex: Ring -- k-ary 1-cube
Edge Symmetric
  Good for load balancing
  Removing wrap-around links for mesh loses edge symmetry
    More traffic concentrated on center channels
Good path diversity
Exploit locality for near-neighbor traffic

## Slide 22: Torus (3): Hop Count
Average shortest distance over all pairs of nodes
Torus:
  For uniform random traffic
    Packet travels k/4 hops in each of n dimensions
Mesh:

## Slide 23: Torus (4)
Degree = 2n, 2 channels per dimension
  All nodes have same degree
Total channels = 2nN
  N is total number of nodes

## Slide 24: Channel Load for Torus
Even number of k-ary (n-1)-cubes in outer dimension
Dividing these k-ary (n-1)-cubes gives a 2 sets of kn-1 bidirectional channels or 4kn-1
½ traffic from each node crosses bisection
Mesh has ½ the bisection bandwidth of torus
Notes: 4k^(n-1) = 4*k^n*k^-1 = 4N/k
N/2 traffic is going to be distributed over 4N/k channels so the load is (N/2)/(4N/k) = N/2 * k/4N
Mention adversarial traffic pattern for torus… some kind of permutation…

## Slide 25: Deriving Channel Load: 4-ary 2-cube
Divide network in half
Number of bisection channels
  8 links, bidirectional = 16 channels
½ traffic crosses bisection
N/2 traffic distributed over 16 links
Channel load = ½
  Loaded at twice injection bandwidth
Notes: Channel load of 2
  Channel is loaded with twice injection bandwidth
  If each node injects a flit every cycle
    2 flits will want to traverse bottleneck channel every cycle
    If bottleneck channel can only handle 1 flit per cycle
      Max network bandwidth is ½ link bandwidth
      A flit can be injected every other cycle

## Slide 26: Torus Path Diversity
2 edge and node disjoint minimum paths
2 dimensions*
*assume single direction for x and y
NW, NE, SW, SE combos
Notes: Assumes one-way routes (choose starting direction for X and Y, 6 routes with X east and Y south). 6 more routes for X west and Y south),

## Slide 27: Mesh
A torus with end-around connection removed
Same node degree
Higher demand for central channels
  Load imbalance

## Slide 28: Butterfly
Indirect network
K-ary n-fly: kn network nodes
Routing from 000 to 010
  Dest address used to directly route packet
  Bit n used to select output port at stage n
0
00
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
01
02
03
10
11
12
13
20
21
22
23
0
1
0
2-ary 3-fly
2 input switch, 3 stages

## Slide 29: Butterfly (2)
No path diversity
  Can add extra stages for diversity
    Increase network diameter
0
x0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
x1
x2
x3
10
11
12
13
20
21
22
23
00
01
02
03

## Slide 30: Butterfly (3)
Hop Count
  LogkN + 1
  Does not exploit locality
    Hop count same regardless of location
Switch Degree = 2k
Requires long wires to implement

## Slide 31: Butterfly: Channel Load
Hmin x N: Channel demand
  Number of channel traversals required to deliver one round of packets
Channel Load  uniform traffic
  Equally loads channels
  Increases for adversarial traffic
Notes: Hmin = n+1

## Slide 32: Butterfly: Deriving Channel Load
Divide network in half
Number of bisection channels: 4
4 nodes (top half) send ½ traffic to lower half
Distributed across 2 channels (C)
Channel load = 1
0
00
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
01
02
03
10
11
12
13
20
21
22
23

## Slide 33: Butterfly: Channel Load
Adversarial traffic
  All traffic from top half sent to bottom half
  E.g. 0 sends to 4, 1 sends to 5
Channel load: 2
  Loaded at ½ injection bandwidth
0
00
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
01
02
03
10
11
12
13
20
21
22
23

## Slide 34: Clos network
3-stage networks where all input/output nodes are connected to all middle routers
Key attribute: path diversity
  Input node can select any middle router
  Can enable non-blocking routing algorithms
(5,3,4) Clos network

## Slide 35: Fat Tree
Bandwidth remains constant at each level
Regular Tree: Bandwidth decreases closer to root

## Slide 36: Fat Tree (2)
Provides path diversity

## Slide 37: Application of Topologies to On-Chip Networks
FBFly
  Convert butterfly to direct network
Swizzle switch
  Circuit-optimized crossbar
Rings
  Simple, low hardware cost
Mesh networks
  Several products/prototypes
MECS and bus-based networks
  Broadcast and multicast capabilities

## Slide 38: Topology Implementation

## Slide 39: Implementation
Folding
  Equalize path lengths
    Reduces max link length
    Increases length of other links
0
1
2
3
0
1
2
3

## Slide 40: Concentration
Don’t need 1:1 ratio of routers to cores
  Ex: 4 cores concentrated to 1 router
Can save area and power
Increases network complexity
  Concentrator must implement policy for sharing injection bandwidth
  During bursty communication
    Can bottleneck

## Slide 41: Implication of Abstract Metrics on Implementation
Degree: useful proxy for router complexity
  Increasing ports requires additional buffer queues, requestors to allocators, ports to crossbar
  All contribute to critical path delay, area and power
  Link complexity does not correlate with degree
    Link complexity depends on link width
    Fixed number of wires, link complexity for 2-port vs 3-port is same

## Slide 42: Implications (2)
Hop Count: useful proxy for overall latency and power
  Does not always correlate with latency
    Depends heavily on router pipeline and link propagation
  Example:
    Network A with 2 hops, 5 stage pipeline, 4 cycle link traversal vs.
    Network B with 3 hops, 1 stage pipeline, 1 cycle link traversal
Hop Count says A is better than B
But A has 18 cycle latency vs 6 cycle latency for B

## Slide 43: Topology Summary
First network design decision
Critical impact on network latency and throughput
  Hop count provides first order approximation of message latency
  Bottleneck channels determine saturation throughput