## Slide 1
ECE 1755
Lecture 18
Interconnects: Routing
Winter 2018
Prof. Natalie Enright Jerger

## Slide 2: Topics to be covered
Interfaces
Topology
Routing
Flow Control
Router Microarchitecture

## Slide 3: Routing

## Slide 4: Routing Overview
Discussion of topologies assumed ideal routing
In practice…
  Routing algorithms are not ideal
Goal: distribute traffic evenly among paths
  Avoid hot spots, contention
  More balanced  closer throughput is to ideal
Keep complexity in mind

## Slide 5: Routing Basics
Once topology is fixed
Routing algorithm determines path(s) from source to destination

## Slide 6: Routing Example
Some routing options:
  Greedy: shortest path
  Uniform random: randomly pick direction
  Adaptive: send packet in direction with lowest local channel load
Which gives best worst-case throughput?
0
1
2
3
4
5
6
7

## Slide 7: Routing Example (2)
Consider tornado traffic
  node i sends to i+3 mod 8
0
1
2
3
4
5
6
7

## Slide 8: Routing Example (3)
Greedy:
  All traffic moves counterclockwise
    Loads counterclockwise with 3 units of traffic
      Each node gets 1/3 throughput
    Clockwise channels are idle
Random:
  Clockwise channels become bottleneck
    Load of 5/2
      Half of traffic traverses 5 links in clockwise direction
      Gives throughput of 2/5

## Slide 9: Routing Example (4)
Adaptive:
  Perfect load balancing (some assumptions about implementation)
  Sends 5/8 of traffic over 3 links, sends 3/8 over 5 links
    Channel load is 15/8, throughput of 8/15
Note: worst case throughput just 1 metric designer might optimize

## Slide 10: Routing Algorithm Attributes
Types
  Deterministic, Oblivious, Adaptive
Number of destinations
  Unicast, Multicast, Broadcast?
Adaptivity
  Oblivious or Adaptive? Local or Global knowledge?
  Minimal or non-minimal?
Implementation
  Source or node routing?
  Table or circuit?

## Slide 11: Routing Deadlock
Each packet is occupying a link and waiting for a link
Without routing restrictions, a resource cycle can occur
  Leads to deadlock
A
B
D
C

## Slide 12: Types of Routing Algorithms

## Slide 13: Deterministic
All messages from Source to Destination traverse the same path
Common example: Dimension Order Routing (DOR)
  Message traverses network dimension by dimension
  Aka XY routing
Cons:
  Eliminates any path diversity provided by topology
  Poor load balancing
Pros:
  Simple and inexpensive to implement
  Deadlock-free

## Slide 14: Dimension Order Routing
a.k.a X-Y Routing
  Traverse network dimension by dimension
  Can only turn to Y dimension after finished X

## Slide 15: Destination-Tag Routing: Butterfly Networks
Destination address
  Interpreted as an n-digit radix-k number
  Directly routes packet
Each digit selects the output port at each step
0
00
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
01
02
03
10
11
12
13
20
21
22
23
1
0
1
2-ary 3-fly

## Slide 16: Destination-Tag Routing (2)
Routing from 7 to 11
11 = 10112 = 234
Source does not play role in routing
Previous example
  To route from any node to 5 use ports:
    101
This example
  To route to 11 use port 2 then 3
0
3
4
7
8
11
12
15
00
01
02
03
10
11
12
13
0
3
4
7
8
11
12
15
4-ary 2-fly

## Slide 17: Oblivious
Routing decisions are made without regard to network state
  Keeps algorithms simple
  Unable to adapt
Deterministic algorithms are a subset of oblivious

## Slide 18: Valiant’s Routing Algorithm
To route from s to d
  Randomly choose intermediate node d’
  Route from s to d’ and from d’ to d.
Randomizes any traffic pattern
  All patterns appear uniform random
  Balances network load
Non-minimal
Destroys locality
d’
d
s

## Slide 19: Valiant’s Algorithm: Indirect Networks
Applying Valiant’s can eliminate bottlenecks caused by certain traffic patterns
Two-pass Valiant routing
  Equivalent to logically duplicating butterfly network

## Slide 20: Valiant’s: Indirect Networks
0
00
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
01
02
03
10
11
12
13
20
21
22
23
0
00
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
01
02
03
10
11
12
13
20
21
22
23
2 sends to 7
3 sends to 5
Bottleneck link from 01
With Valiant:
2 routes to intermediate node 0 then to 7
3 routes to intermediate node 4 then to 5
Distributes traffic

## Slide 21: Minimal Oblivious
Valiant’s: Load balancing but significant increase in hop count
Minimal Oblivious: some load balancing, but use shortest paths
  d’ must lie within min quadrant
  6 options for d’
  Only 3 different paths
d
s

## Slide 22: Minimal Oblivious Routing on Fat Tree
Node labels (addr template)
  All nodes reachable from left terminals
Route from s to d
  Randomly selected, nearest common ancestor x of s and d
Route s to x then x to d
Example s = 1, d = 6
Construct route incrementally
  Randomly select output port
  Until addr template matches d
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
000X
001X
010X
011X
100X
101X
110X
111X
00XX
01XX
0XXX
A
0XXX
B
10XX
11XX
1XXX
A
1XXX
B
XXXX
A
XXXX
B
XXXX
C
XXXX
D
Notes: Start here…

## Slide 23: Oblivious Routing
Valiant’s and Minimal Adaptive
  Deadlock free
    When used in conjunction with X-Y routing
Randomly choose between X-Y and Y-X routes
  Oblivious but not deadlock free!

## Slide 24: Adaptive
Exploits path diversity
Uses network state to make routing decisions
  Buffer occupancies often used
  Coupled with flow control mechanism
Local information readily available
  Global information more costly to obtain
  Network state can change rapidly
  Use of local information can lead to non-optimal choices
Can be minimal or non-minimal

## Slide 25: Minimal Adaptive Routing
Local info can result in sub-optimal choices
d
s

## Slide 26: Non-minimal adaptive
Fully adaptive
Not restricted to take shortest path
  Generally undesirable to increase path length
  Necessary for fault tolerance
Misrouting: directing packet along non-productive channel
  Priority given to productive output
  Some algorithms forbid U-turns
Livelock potential: traversing network without ever reaching destination
  Mechanism to guarantee forward progress
    Limit number of misroutings
Notes: Fbfly is an on-chip example with non-minimal routing

## Slide 27: Non-minimal routing example
Longer path with potentially lower latency
d
s
d
s
Livelock: continue routing in cycle

## Slide 28: Adaptive Routing Example
Should 3 route clockwise or counterclockwise to 7?
  5 is using all the capacity of link 5  6
Queue at node 5 will sense contention but not at node 3
Backpressure: allows nodes to indirectly sense congestion
  Queue in one node fills up, it will stop receiving flits
  Previous queue will fill up
If each queue holds 4 packets
  3 will send 8 packets before sensing congestion
0
1
2
3
4
5
6
7

## Slide 29: Congestion Information
Local
  Information about my neighbors only
  Implicitly available – I know how many downstream buffers are available (from flow control)
Global
  Information about all nodes
  Explicitly send status information
  Usually based on VC utilization or buffer occupancy
Timeliness

## Slide 30: Sending Congestion Information
Piggybacking
  Send congestion information along with packets
Extra side network
  More affordable in on-chip networks
  Broadcast
  Packetize
Aggregate or individual node

## Slide 31: Adaptive Routing: Turn Model
DOR eliminates 4 turns
  N to E, N to W, S to E, S to W
  No adaptivity
Some adaptivity by removing 2 of 8 turns
  Remains deadlock free (like DOR)
West first
  Eliminates S to W and N to W
West first
Notes: All eliminate the North to West turn and then each eliminates one other turn to remove deadlock.

## Slide 32: Turn Model Routing
Negative first
  Eliminates E to S and N to W
North last
  Eliminates N to E and N to W
Odd-Even
  Eliminates 2 turns depending on if current node is in odd or even col.
    Even column: E to N and N to W
    Odd column: E to S and S to W
  Deadlock free (disallow 180 turns)
  Better adaptivity
North last
Negative first

## Slide 33: Negative-First Routing Example
Limited or no adaptivity for certain source-destination pairs
(0,0)
(2,3)
(0,3)
(2,0)

## Slide 34: Turn Model Routing Deadlock
What about eliminating turns NW and WN?
Not a valid turn elimination
  Resource cycle results

## Slide 35: Adaptive Routing and Deadlock
Option 1: Eliminate turns that lead to deadlock
  Limits flexibility
Option 2: Allow all turns
  Give more flexibility
  Must use other mechanism to prevent deadlock
  Rely on flow control (later)
    Escape virtual channels

## Slide 36: Adaptive Routing: Other Topologies
Butterfly: no path diversity
  Can add extra stages for path diversity, adaptive routing
Fat tree (folded Clos)
  Similar to minimal oblivious
    But instead of randomly selecting path to least common ancestor
      Select adaptively (upstream)
      Message routed deterministically (downstream)

## Slide 37: Routing in a Clos Network
Strictly non-blocking when m ≥ 2n-1
All inputs are connected except for 1 input (a.i) and 1 output (b.j)
  Previous routes already setup
    Middle switches used by a are disjoint from middle switched used to connect to b
    Middle switch to route from a.i to b.j found by intersecting switches not used by a with those not used by b

## Slide 38: Routing in a Clos Network
Strictly non-blocking: m ≥ 2n-1
nxm input switch
nxm input switch
nxm input switch
nxm input switch
rxr input switch
rxr input switch
rxr input switch
rxr input switch
rxr input switch
mxn output switch
mxn output switch
mxn output switch
mxn output switch
1.1
3.3

## Slide 39: Routing in a Clos Network
Strictly non-blocking is expensive
Rearrangeable network
  m ≥ n
  Rearranges paths if no middle switch found

## Slide 40: Routing Algorithm Implementation

## Slide 41: Routing Implementation
Source tables
  Entire route specified at source
  Avoids per-hop routing latency
  Unable to adapt dynamically to network conditions
  Can specify multiple routes per destination
    Give fault tolerance and load balance
  Support reconfiguration (not specific to topology)

## Slide 42: Source Table Routing
Destination | Route 1 | Route 2
00 | X | X
10 | EX | EX
20 | EEX | EEX
01 | NX | NX
11 | NEX | ENX
21 | NEEX | ENEX
02 | NNX | NNX
12 | ENNX | NNEX
22 | EENNX | NNEEX
03 | NNNX | NNNX
13 | NENNX | ENNNX
23 | EENNNX | NNNEEX
(0,0)
Arbitrary length paths: storage overhead and packet overhead

## Slide 43: Node Tables
Store only next direction at each node
Smaller tables than source routing
Adds per-hop routing latency
Can adapt to network conditions
  Specify multiple possible outputs per destination
  Select randomly to improve load balancing

## Slide 44: Node Table Routing
Implements West-First Routing
Each node would have 1 row of table
  Max two possible output ports
To |  |  |  |  |  |  |  |  | 
From | 00 | 01 | 02 | 10 | 11 | 12 | 20 | 21 | 22
00 | X ¦- | N ¦ - | N ¦ - | E ¦ - | E ¦ N | E ¦ N | E ¦ - | E ¦ N | E ¦ N
01 | S ¦ - | X ¦ - | N ¦ - | E ¦ S | E ¦ - | E ¦ N | E ¦ S | E ¦ - | E ¦ N
02 | S ¦ - | S¦ - | X ¦ - | E ¦ S | E ¦ S | E ¦ - | E ¦ S | E ¦ S | E ¦ -
10 | W¦- | W¦- | W¦- | X ¦ - | N ¦ - | N ¦ - | E ¦ - | E ¦ N | E ¦ N
11 | W¦- | W¦- | W¦- | S ¦ - | X ¦ - | N ¦ - | E ¦ S | E ¦ - | E ¦ N
12 | W¦- | W¦- | W¦- | S ¦ - | S ¦ - | X ¦ - | E ¦ S | E ¦ S | E ¦ -
20 | W¦- | W¦- | W¦- | W¦- | W¦- | W¦- | X ¦ - | N ¦ - | N ¦ -
21 | W¦- | W¦- | W¦- | W¦- | W¦- | W¦- | S ¦ - | X ¦ - | N ¦ -
22 | W¦- | W¦- | W¦- | W¦- | W¦- | W¦- | S ¦ - | S ¦ - | X ¦ -
(1,0)
Notes: Illustrating both node table routing and an example of the turn model
(1,0) to (0,1) is N and W but can only go W because its west first.

## Slide 45: Implementation
Combinational circuits can be used
  Simple (e.g. DOR): low router overhead
  Specific to one topology and one routing algorithm
    Limits fault tolerance
Tables can be updated to reflect new configuration, network faults, etc

## Slide 46: Circuit Based
Next hop based on buffer occupancies
Or could implement simple DOR
Fixed w.r.t. topology
sx
x
sy
y
=0
=0
Route selection
Productive Direction Vector
+x
-x
+y
-y
exit
Queue lengths
Selected Direction Vector
+x
-x
+y
-y
exit
Notes: have the x and y deltas – check sign bit – positive or negative direction and check for zero.
loss of generality – specific to topology and routing algorithm

## Slide 47: Routing Algorithms: Implementation
Routing Algorithm | Source Routing | Combinational | Node Table
Deterministic |  |  | 
DOR | Yes | Yes | Yes
Oblivious |  |  | 
Valiant’s | Yes | Yes | Yes
Minimal | Yes | Yes | Yes
Adaptive | No | Yes | Yes

## Slide 48: Routing Summary
Latency paramount concern
  Minimal routing most common for NoC
  Non-minimal can avoid congestion and deliver low latency
To date: NoC research favors DOR for simplicity and deadlock freedom
  On-chip networks often lightly loaded
Only covered unicast routing
  Recent work on extending on-chip routing to support multicast