## Slide 1
ECE 1755
Lecture 20
Interconnects: Router Microarchitecture
Winter 2018
Prof. Natalie Enright Jerger

## Slide 2: Overview
Topology: connectivity
Routing: paths
Flow control: resource allocation
Router Microarchitecture
  Implementation of routing, flow control and router pipeline
  Impacts per-hop delay and energy

## Slide 3: Router Microarchitecture Overview
Focus on microarchitecture of Virtual Channel router
  Router complexity increase with bandwidth demands
  Simple routers built when high throughput is not needed
    Wormhole flow control, unpipelined, limited buffer

## Slide 4: Virtual Channel Router
Route Computation
VC Allocator
Switch Allocator
Input buffers
VC 1
VC 2
VC 3
VC 4
Input buffers
VC 1
VC 2
VC 3
VC 4
Crossbar switch
Input 5
Input 1
Output 5
Output 1
Credits In
Credits Out

## Slide 5: Router Components
Input buffers, route computation logic, virtual channel allocator, switch allocator, crossbar switch
Most OCN routers are input buffered
  Use single-ported memories
Buffer store flits for duration in router

## Slide 6: Baseline Router Pipeline
Logical stages
  Fit into physical stages depending on frequency
Canonical 5-stage pipeline
  BW: Buffer Write
  RC: Routing computation
  VA: Virtual Channel Allocation
  SA: Switch Allocation
  ST: Switch Traversal
  LT: Link Traversal
BW
RC
VA
SA
ST
LT

## Slide 7: Baseline Router Pipeline (2)
Routing computation performed once per packet
Virtual channel allocated once per packet
Body and tail flits inherit this info from head flit
BW
RC
ST
LT
Head
VA
SA
1
2
3
4
5
6
7
BW
ST
LT
Body 1
SA
BW
ST
Body 2
SA
BW
Tail
LT
ST
SA
LT
8
9
Cycle

## Slide 8: Atomic Modules and Dependencies in Router
Dependence between output of one module and input of another
  Determine critical path through router
  Cannot bid for switch port until routing performed
Decode + Routing
Switch Arbitration
Crossbar Traversal
Wormhole Router
Decode + Routing
Switch Arbitration
Crossbar Traversal
Virtual Channel Router
VC Allocation
Decode + Routing
Speculative Switch Arbitration
Crossbar Traversal
Speculative Virtual Channel Router
VC Allocation

## Slide 9: Router Pipeline Performance
Baseline (no load) delay
Ideally, only pay link delay
Techniques to reduce pipeline stages

## Slide 10: Pipeline Optimizations: Lookahead Routing
At current router perform routing computation for next router
  Overlap with Buffer Write (BW)
  Precomputing route allows flits to compete for VCs immediately after BW
BW
RC
VA
SA
ST
LT

## Slide 11: Pipeline Optimizations: Speculation
Assume that Virtual Channel Allocation stage will be successful
  Valid under low to moderate loads
Entire VA and SA in parallel
If VA unsuccessful (no virtual channel returned)
  Must repeat VA/SA in next cycle
Prioritize non-speculative requests
BW
RC
VA
SA
ST
LT

## Slide 12: Pipeline Optimizations: Bypassing
When no flits in input buffer
  Speculatively enter ST
  On port conflict, speculation aborted
  In the first stage, a free VC is allocated, next routing is performed and the crossbar is setup
VA
RC
Setup
ST
LT

## Slide 13: Pipeline Bypassing
No buffered flits when A arrives
Inject
N
S
E
W
Eject
N
S
E
W
1b
1a
Lookahead Routing Computation
1
2
A
Virtual Channel Allocation

## Slide 14: Speculation
Inject
N
S
E
W
Eject
N
S
E
W
1b
1a
Lookahead Routing Computation
1
1c
1
1b
1c
Virtual Channel Allocation
Switch Allocation
2a
2b
3
4
Port conflict detected
3
A succeeds in VA but fails in SA, retry SA
B
A

## Slide 15: Buffer Organization
Single buffer per input
Multiple fixed length queues per physical channel
Physical channels
Virtual channels

## Slide 16: Buffer Organization
Multiple variable length queues
  Multiple VCs share a large buffer
  Each VC must have minimum 1 flit buffer
    Prevent deadlock
  More complex circuitry
VC 0
tail
head
VC 1
tail
head

## Slide 17: Buffer Organization
Many shallow VCs?
Few deep VCs?
More VCs ease HOL blocking
  More complex VC allocator
Light traffic
  Many shallow VCs – underutilized
Heavy traffic
  Few deep VCs – less efficient, packets blocked due to lack of VCs

## Slide 18: Switch Organization
Heart of datapath
  Switches bits from input to output
High frequency crossbar designs challenging
Crossbar composed for many multiplexers
  Common in low-frequency router designs
i00
i10
i20
i30
i40
o0
sel0
o1
sel1
o2
sel2
o3
sel3
o4
sel4

## Slide 19: Switch Organization: Crosspoint
Area and power scale at O((pw)2)
  p: number of ports (function of topology)
  w: port width in bits (determines phit/flit size and impacts packet energy and delay)
Inject
N
S
E
W
Eject
N
S
E
W
w columns
w rows

## Slide 20: Crossbar speedup
Increase internal switch bandwidth
Simplifies allocation or gives better performance with a simple allocator
  More inputs to select from  higher probability each output port will be matched (used) each cycle
Output speedup requires output buffers
  Multiplex onto physical link
10:5 crossbar
5:10 crossbar
10:10 crossbar

## Slide 21: Arbiters and Allocators

## Slide 22: Arbiters and Allocators
Allocator matches N requests to M resources
Arbiter matches N requests to 1 resource
Resources are VCs (for virtual channel routers) and crossbar switch ports.

## Slide 23: Arbiters and Allocators (2)
Virtual-channel allocator (VA)
  Resolves contention for output virtual channels
  Grants them to input virtual channels
Switch allocator (SA) that grants crossbar switch ports to input virtual channels
Allocator/arbiter that delivers high matching probability translates to higher network throughput.
  Must also be fast and/or able to be pipelined

## Slide 24: Round Robin Arbiter
Last request serviced given lowest priority
Generate the next priority vector from current grant vector
Exhibits fairness

## Slide 25: Round Robin (2)
Gi granted, next cycle Pi+1 high
Grant 0
Grant 1
Grant 2
Next priority 0
Next priority 1
Next priority 2
Priority 0
Priority 1
Priority 2

## Slide 26: Wavefront Allocator
Arbitrates among requests for inputs and outputs simultaneously
Row and column tokens granted to diagonal group of cells
If a cell is requesting a resource, it will consume row and column tokens
  Request is granted
Cells that cannot use tokens pass row tokens to right and column tokens down

## Slide 27: Wavefront Allocator Example
p0
p1
p2
p3
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33
A requesting Resources 0, 1 ,2
B requesting Resources 0, 1
C requesting Resource 0
D requesting Resources 0, 2
Tokens inserted at P0
Entry [0,0] receives grant, consumes token
Remaining tokens pass down and right
[3,2] receives 2 tokens and is granted

## Slide 28: Wavefront Allocator Example
p0
p1
p2
p3
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33
[1,1] receives 2 tokens and granted
All wavefronts propagated

## Slide 29: Separable Allocator
Need for pipelineable allocators
Allocator composed of arbiters
  Arbiter chooses one out of N requests to a single resource
Separable switch allocator
  First stage: select single request at each input port
  Second stage: selects single request for each output port

## Slide 30: Separable Allocator
A 3:4 allocator
First stage: 3:1 – ensures only one grant for each input
Second stage: 4:1 – only one grant asserted for each output
3:1 arbiter
3:1 arbiter
3:1 arbiter
3:1 arbiter
4:1 arbiter
4:1 arbiter
4:1 arbiter
Requestor 1 requesting resource A
Requestor 1 requesting resource C
Requestor 4 requesting resource A
Resource A granted to Requestor 1
Resource A granted to Requestor 2
Resource A granted to Requestor 3
Resource A granted to Requestor 4
Resource C granted to Requestor 1
Resource C granted to Requestor 4
Resource C granted to Requestor 2
Resource C granted to Requestor 3

## Slide 31: Separable Allocator Example
4 requestors, 3 resources
Arbitrate locally among requests
  Local winners passed to second stage
3:1 arbiter
3:1 arbiter
3:1 arbiter
3:1 arbiter
4:1 arbiter
4:1 arbiter
4:1 arbiter
A
B
C
A
B
A
A
C
Requestor 1 wins A
Requestor 4 wins C

## Slide 32: Virtual Channel Allocator Organization
Depends on routing function
  If routing function returns single VC
    VCA need to arbitrate between input VCs contending for same output VC
  Returns multiple candidate VCs (for same physical channel)
    Needs to arbitrate among v first stage requests before forwarding winning request to second stage)

## Slide 33: Adaptive Routing & Allocator Design
Deterministic routing
  Single output port
  Switch allocator bids for output port
Adaptive routing
  Returns multiple candidate output ports
    Switch allocator can bid for all ports
    Granted port must match VC granted
  Return single output port
    Reroute if packet fails VC allocation

## Slide 34: Speculative VC Router
Non-speculative switch requests must have higher priority than speculative ones
  Two parallel switch allocators
    1 for speculative
    1 for non-speculative
    From output, choose non-speculative over speculative
  Possible for flit to succeed in speculative switch allocation but fail in virtual channel allocation
    Done in parallel
    Speculation incorrect
      Switch reservation is wasted
  Body and Tail flits: non-speculative switch requests
    Do not perform VC allocation  inherit VC from head flit

## Slide 35: On-Chip Network Summary

## Slide 36: Interconnection Network Summary
Latency vs. Offered Traffic
Latency
Offered Traffic (bits/sec)
Min latency given by topology
Min latency given by routing algorithm
Zero load latency
(topology+routing+flow control)
Throughput given by topology
Throughput given by routing
Throughput given by flow control

## Slide 37: Towards the Ideal Interconnect
Ideal latency
  Solely due to wire delay between source and destination
  D = Manhattan distance
  L = packet size
  b = channel bandwidth
  v = propagation velocity

## Slide 38: State of the Art
Dedicated wiring impractical
  Long wires segmented with insertion of routers

## Slide 39: Latency Throughput Gap
Aggressive speculation and bypassing
8 VCs/port
Chart: Injected load (fraction of capacity)
| 0.01 | 0.02 | 0.05 | 0.1 | 0.12 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55 | 0.6 | 0.65 | 0.7 | 0.75 | 0.76 | 0.85 | 0.9 | 0.95 | 1.0
Ideal | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13
On-chip Network | 20 | 20 | 20 | 20 | 20.1 | 20.3 | 20.4 | 20.7 | 21 | 21.6 | 22.5 | 23.8 | 25 | 27 | 29 | 33 | 39 | 50 | 60 | 100 | 100 | 100 | 100
Throughput gap
Latency gap

## Slide 40: Towards the Ideal Interconnect
Ideal Energy
  Only energy of interconnect wires
  D = Distance
  Pwire = transmission power per unit length

## Slide 41: State of the Art
No longer just wires
  Prouter = buffer read/write power, arbitration power, crossbar traversal

## Slide 42: Energy Gap
Chart: Injected load (fraction of capacity)
| 0.05 | 0.12 | 0.2 | 0.28 | 0.36 | 0.4 | 0.43 | 0.46 | 0.51 | 0.54 | 0.6 | 0.64 | 0.72 | 0.8
baseline | 0.375 | 0.9 | 1.5 | 2.1 | 2.7 | 3 | 3.225 | 3.45 | 3.825 | 4.05 | 4.5 | 4.65 | 4.7 | 4.75
ideal | 0.125 | 0.3 | 0.5 | 0.7 | 0.9 | 1 | 1.075 | 1.15 | 1.275 | 1.35 | 1.5 | 1.6 | 1.8 | 2

## Slide 43: Key Research Challenges
Low power on-chip networks
  Power consumed largely dependent on bandwidth it has to support
  Bandwidth requirement depends on several factors
Beyond conventional interconnects
  Power efficient link designs
  3D stacking
  Optics
Resilient on-chip networks
  Manufacturing defects and variability
  Soft errors and wearout