## Slide 1: Persistency Programming 101 Understanding memory persistency
Aasheesh Kolli* Steven Pelley† Ali Saidi^
Peter M. Chen* Thomas F. Wenisch*
* University of Michigan
† Snowflake Computing
^ ARM
Notes: :

## Slide 2: Executive summary
NVMs -> in-memory, recoverable data structs
Require ordering of NVM writes (persists)
Consistency models do not order persists
Memory persistency [ISCA ‘14]
  Consistency models for NVM
This talk:
  Motivate memory persistency
  Summarize persistency models

## Slide 3: Background - Memory consistency
Consistency spectrum
Contract b/w hardware and software on store visibility (implementation independent)
May be strict (SC) or relaxed (RMO)
Does not apply to persists
Need persistency models to order persists

## Slide 4: Future system abstraction
Time
Memory events (stores/loads/barriers)
Core0
Core1
1
2
3
4
5
6
Volatile memory order
(consistency model)
No Failures
Core0
Core1
1
2
3
4
5
6
Persist memory order
(persistency model)
Failures
Recovery
Persistency model governs store visibility in the presence of failures

## Slide 5: Types of persistency models
Memory events (stores/loads/barriers)
Core0
Core1
1
2
3
4
5
6
Consistency
Core0
Core1
1
2
3
4
5
6
Strict
persistency
Core0
Core1
1
2
3
4
5
6
Relaxed
persistency

## Slide 6: Strict vs relaxed persistency
Strict persistency
  Consistency model = persistency model
  Expensive (cost of persist > cost of store)
Relaxed persistency
  Separate consistency and persistency models
  Reduces persist memory order constraints
  Might require more robust recovery software
  Failures are infrequent  recovery overhead OK
Relaxed persistency models  performance

## Slide 7: How do persists affect performance?
Persists form a directed acyclic graph (DAG)
  Critical path limits overall performance
1: persist Qe.data[0] = x
2: persist Qe.data[1] = y
3: persist Qe.valid = true
Models should allow expression of minimal constraints
D[0]
D[1]
V
D[0]
D[1]
V

## Slide 8: Strict persistency
Consistency model = persistency model
Two sources of persist concurrency:
  Use a relaxed memory consistency model
  Multi-threading

## Slide 9: Strict persistency with SC
Program order => persist order
No annotations required
Suboptimal persist critical paths
1. lock (volatile mutex)
2. persist Qe.data[0] = x
3. persist Qe.data[1] = y
4. persist Qe.valid = true
5. unlock
D[0]
D[1]
V

## Slide 10: Strict persistency with RMO
Barriers for synchronization and recovery
Annotation burden on the programmer
Affects volatile perf
lock (volatile mutex)
barrier
persist Qe.data[0] = x
persist Qe.data[1] = y
barrier
persist Qe.valid = true
barrier
unlock
D[0]
D[1]
V

## Slide 11: Relaxed persistency models
Decouple consistency and persistency models
Expose additional persist concurrency
  Important for conservative consistency models
Will use SC as underlying consistency model

## Slide 12: Epoch persistency
Persist barriers divide program into epochs
  Persists within epoch concurrent
  Persists from successive epochs ordered
  Store visibility still dictated by program order
lock (volatile mutex)
persist Qe.data[0] = x
persist Qe.data[1] = y
persist barrier
persist Qe.valid = true
unlock
D[0]
D[1]
V
Epoch 1
Epoch 2

## Slide 13: Epoch persistency drawback
A
B
C
A
B
C
A
B
C
persist A
persist B
persist C
DAG-1
DAG-2
Cannot express minimal constraints
persist A
persist barrier
persist B
persist C
persist A
persist barrier
persist C
persist B
persist A
persist C
persist barrier
persist B
persist C
persist A
persist barrier
persist B
Ideal

## Slide 14: Strand persistency
Divide thread’s execution into strands
  A strand can be abstracted as a logical thread
Persists on different strands are concurrent
New memory event newStrand
  Persist barriers order persists within a strand
Can enforce only the necessary constraints
A
B
C
persist A
persist barrier
persist B
newStrand
persist C

## Slide 15: Ordering persists across threads
Conflicting accesses establish persist order
  Two accesses to same address, at least one store
  Persist order must match volatile order
  Could be to volatile/non-volatile addresses
  Strong persist atomicity

## Slide 16: Strong persist atomicity example
Thread - 1
lock X (volatile mutex)
persist barrier
persist A
persist barrier
unlock X
Thread - 2
lock X
persist barrier
persist B
persist barrier
unlock X
Conflicting
accesses
Time
Persist order

## Slide 17: Conclusions
Strict persistency
  Unifies consistency and persistency model
Epoch persistency
  Persists within epoch concurrent, epochs ordered
Strand persistency
  Allows enforcing only minimal constraints
Strong persist atomicity
  Allows ordering persists across threads

## Slide 18: Thank You!
Questions?

## Slide 19: Persistency terminology
Memory events: Stores/loads/barriers
Failure abstracted as recovery observer
  Atomically loads all of memory at failure
Volatile memory order
  Partial order of memory events
  Governs visibility of stores to all processors
Persist memory order
  Governs visibility of persists w.r.t recovery observer

## Slide 20: Persist ordering constraints
Persists form a directed acyclic graph (DAG)
Critical path limits overall performance
  Remove unnecessary ordering constraints
  Requires an interface to describe constraints
1: Persist data[0]
2: Persist data[1]
3: Persist flag
3
2
1
Program order implies unnecessary constraints

## Slide 21: Background – Memory consistency
Contract b/w hardware & software regarding visibility of stores
Implementation independent
Relaxed models improve store/load concurrency (performance)
However, do not extend to memory
  Cache evictions
  Memory controller optimizations

## Slide 22: Strict persistency
Persist memory order = volatile memory order
  Order of persists matches store visibility
Strict persistency with SC/TSO
  Program order => persist order
  No annotations necessary
  Restrictive, suboptimal performance
Strict persistency with RMO
  Program order + memory barriers => persist order
  Need barriers to ensure correct store visibility and recovery correctness

## Slide 23: Strict persistency
SC
lock (volatile mutex)
persist data[0]
persist data[1]
persist flag
unlock
RMO
lock (volatile mutex)
barrier
persist data[0]
persist data[1]
…
persist data[N]
barrier
persist flag
barrier
unlock (volatile mutex)
Task: persist data then persist flag

## Slide 24: Epoch persistency
lock (volatile mutex)
persist data[0]
persist data[1]
…
persist data[N]
persist barrier
persist flag
Unlock
Persist barriers divide program into epochs
Persists within epoch concurrent
Program order => Store visibility
Program order + persist barriers
=> Persist order
Epoch persistency improves persist concurrency

## Slide 25: Nonvolatile memory (NVM) recovery
Future systems will have NVM on memory bus
In-memory, recoverable data structures
Recovery needs NVM write (persist) ordering
Writes unordered
Need a mechanism to express order of persists

## Slide 26: Memory persistency: consistency models for NVRAM
Framework to reason about persist order while maximizing concurrency [ISCA ‘14]
Persistency models may be strict or relaxed
This talk:
  Primer on persistency models
  Discussion on achieving desired order of persists

## Slide 27: Outline
Background
Strict persistency
Epoch persistency
Strand persistency
Multi-threaded persist ordering

## Slide 28: Executive summary
NVMs -> in-memory, recoverable data structs
  Require ordering of NVM writes (persists))
Consistency models govern visibility of stores
  Do not extend guarantees to persists
  Might want order of stores and persists to differ
Memory persistency [ISCA ‘14]
  Consistency models for NVM
This talk:
  Summary of persistency models
  Example illustrating use of persistency models

## Slide 29: Epoch persistency drawback
Persist barriers some times cause unnecessary persist order constraints
Task: persist A, then persist B, persist C not ordered
persist A
persist barrier
persist B
persist C
Unnecessary constraint: A->C
persist A
persist C
persist barrier
persist B
Unnecessary constraint: C->B

## Slide 30: Future system abstraction
3
Caches (unordered)
2
1
2
1
3
Processors
Memory events
(stores/loads/barriers)
NVM
Recovery observer
(atomically loads Mem
@Failure)
Volatile memory order
(consistency model)
Persist memory order
(persistency model)
Notes: Animate failure and recovery observer

## Slide 31: Why two different models?
Consistency and persistency time scales differ
  Cache access (10s ns) vs NVM write (100s ns)
Used for different purposes
  Consistency -> synchronization correctness
  Persistency -> recovery correctness
Unified model works (strict persistency), but
  Must ensure correct synchronization & recovery
  Suboptimal performance
Separate consistency and persistency models improve performance

## Slide 32: Future system abstraction
3
2
1
2
1
3
Memory events
(stores/loads/barriers)
NVM
Volatile memory order
(consistency model)
Persist memory order
(persistency model)
Core0
Core1
Memory cntrl
Pre-failure
Post-failure
Recovery processor
(can only access
contents of NVM)
Notes: Animate failure and recovery observer

## Slide 33: Future system abstraction
Core0
Core1
Time
1
2
3
4
5
Memory event on volatile address
Memory event on non-volatile (persistent) address
6
Pre-failure
Post-failure
1
2
3
6
Store visibility
(consistency model)
Persist order
(persistency model)

## Slide 34: Future system abstraction
Core0
Core1
Time
1
2
3
4
5
Memory events (stores/loads/barriers)
6
Store visibility
(consistency model)
No Failures
Core0
Core1
1
2
3
4
5
6
Persist order
(persistency model)
Failures

## Slide 35: Future system abstraction
Core0
Core1
Time
1
2
3
4
5
Memory events (stores/loads/barriers)
6
Store visibility
(consistency model)
Persist order
(persistency model)
Core0
Core1
1
2
3
4
5
6
No Failures
Failures

## Slide 36: Future system abstraction
Core0
Core1
Time
1
2
3
4
5
Memory events (stores/loads/barriers)
6
Store visibility
(consistency model)
Persist order
(persistency model)
Core0
Core1
1
2
3
4
5
6
No Failures
Failures
Persistency model governs store visibility across failures