## Slide 1: Memory Persistency
Steven Pelley, Peter M. Chen, Thomas F. Wenisch
University of Michigan

## Slide 2: Nonvolatile memory (NVRAM) recovery
Writes unordered!
Constrain persist order for correctness, but reorder for performance
Writes to memory unordered (cache eviction)
But, recovery depends on write ordering
Enforcing order for all writes too slow!

## Slide 3: Persist performance
Persist ordering constraints form a directed acyclic graph (DAG)
Critical path limits overall performance
  Remove unnecessary ordering constraints
  Requires an interface to describe constraints
1: Persist data[0]
2: Persist data[1]
3: Persist flag
3
2
1
Program order implies unnecessary constraints

## Slide 4: Persist performance
Persist ordering constraints form a directed acyclic graph (DAG)
Critical path limits overall performance
  Remove unnecessary ordering constraints
  Requires an interface to describe constraints
Expose persist concurrency; sounds like consistency!
3
1
2
1: Persist data[0]
2: Persist data[1]
3: Persist flag
Need interface to specify necessary constraints

## Slide 5: Memory persistency: consistency models for NVRAM
Framework to reason about persist order while maximizing concurrency
Just as in consistency, may be strict or relaxed
  Strict: persist order matches store visibility order
  Relaxed: persist order need not match store order
Our contribution:
  Define memory persistency; explore design space
Relaxed persistency enables native instruction execution rate (30x speedup over strict persistency) while preserving data integrity across failure

## Slide 6: Outline
Define memory persistency
Strict persistency and models
Relaxed persistency and models
Methodology and evaluation

## Slide 7: Outline
Define memory persistency
Strict persistency and models
Relaxed persistency and models
Methodology and evaluation

## Slide 8: Memory consistency models
Consistency spectrum
Enable performance via memory concurrency
  Provide ordering guarantees when needed
Model separate from implementation
May be strict or relaxed
Persistency similarly decouples implementation from model, and allows both strict and relaxed models

## Slide 9: Abstracting failure: recovery observer
Memory consistency:
Constrain order of loads and stores between processors
Memory persistency:
Imagine failure as recovery observer
Atomically loads all memory at failure following consistency model
Use recovery observer to reason about recovery semantics
Persistency = Consistency + Recovery observer

## Slide 10: Persistency design space
Strict persistency: single memory order
Relaxed persistency: separate volatile and
(new) persistent memory orders
Volatile memory order
Persistent memory order
Happens before:

## Slide 11: Outline
Define memory persistency
Strict persistency and models
Relaxed persistency and models
Methodology and evaluation

## Slide 12: Strict persistency
Enforce persist order to match store order
  Thus, consistency model also orders persists
  Store and persist are the same event
Persists to different addresses from different threads can still be concurrent
Implementation free to optimize
  In-hardware speculation? Logging/indirection?

## Slide 13: Strict persistency under Sequential Consistency (SC)
Lock(volatile mutex)
Persist data[0]
Persist data[1]
…
Persist data[N]
Persist flag
Unlock(volatile mutex)
No annotation required
Persists serialize according to program order
Volatile accesses synchronize persists from different threads
Must rely on multi-threading for persist concurrency

## Slide 14: Strict persistency under Relaxed Memory Order (RMO)
Lock(volatile mutex)
Barrier
Persist data[0]
Persist data[1]
…
Persist data[N]
Barrier
Persist flag
Barrier
Unlock(volatile mutex)
Barriers constrain visible order of loads/stores
These same barriers order persists
Persists within a single thread may be concurrent

## Slide 15: Outline
Define memory persistency
Strict persistency and models
Relaxed persistency and models
Methodology and evaluation

## Slide 16: Relaxed persistency
Decouple thread and persist synchronization
  Persist order may deviate from store order
  Separate volatile and persistent memory orders
Persist barriers order persists
Consistency and persistency time scales differ
Expose additional concurrency only where necessary

## Slide 17: Relaxed persistency models
Epoch persistency [similar to BPFS cache]
  Persist barriers separate execution into epochs
  Persists within same epoch are concurrent
  Complex behavior when stores synchronized, but persists are not synchronized (see paper)
Strand persistency
  New model to minimally constrain persists
  Precisely defines DAG of ordering constraints

## Slide 18: Epoch persistency example
Lock/Mutex synchronizes threads
No need to enforce persist order
Flag must not persist before data
Already locked, no need to synchronize threads
Relaxed persistency appropriately orders memory events
Stores reorder around persist barriers Persists reorder around store barriers Complicates store atomicity (see paper)
Lock(volatile mutex)
Memory barrier
Persist data[0]
Persist data[1]
…
Persist data[N]
Persist barrier
Persist flag
Memory barrier
Unlock(volatile mutex)

## Slide 19: Strand persistency
Divide execution into strands
Each strand is an independent set of persists
  All strands initially unordered
  Conflicting accesses (i.e., 2 accesses to address, at least 1 is store) establish persist order
NewStrand label begins each strand
Barriers continue to order persists within each strand as in epoch persistency
Strand persistency precisely labels constraints

## Slide 20: Strand persistency example
Strands remove unnecessary ordering constraints
A
B
C
...
Epoch
A
Barrier
B
C
A
B
Barrier
C
B must be ordered with A and/or C
or
Strand
NewStrand
A
Barrier
C
NewStrand
B
...

## Slide 21: Outline
Define memory persistency
Strict persistency and models
Relaxed persistency and models
Methodology and evaluation

## Slide 22: Methodology
µ-benchmark: concurrent, persistent queue
  See paper for pseudocode
Implementations under strict, epoch, and strand persistency models (under SC)
Measure native performance on real server (2.4Ghz Xeon) for 1 and 8 threads
Measure persist concurrency via memory trace simulation
Compare persist critical path against instruction execution rate

## Slide 23: Relaxed persistency
30x
Relaxed persistency removes constraints, regains throughput
Line = instruction execution rate
Assumes 500ns persists

## Slide 24: Conclusion
Must order persists, but over-constraining hurts performance (resembles consistency)
Memory persistency builds on consistency to enforce persist order
Persistency may be relaxed, de-coupling store and persist order constraints
Relaxed persistency enables instruction execution rate with recovery correctness
  30x speedup over strict persistency/SC

## Slide 25: Thank You!
Questions?

## Slide 26: Persist latency sensitivity
Relaxed persistency tolerates greater persist latency
17ns
119ns
6.2µs
1 Thread

## Slide 27: Byte-addressable File System (BPFS) cache
BPFS persistency model:
  Only order according to persistent conflicts
    Accesses to vol. address space do not order persists
  No load-before-store conflict order (TSO ordering)
Newly introduced semantics:
  Consequences of simultaneously relaxing consistency and persistency
  Persist epoch races
    Volatile accesses synchronized; persists are not
  Atomic persists/persist coalescing

## Slide 28: Memory Persistency
Steven Pelley, Peter M. Chen, Thomas F. Wenisch
University of Michigan

## Slide 29: Memory Persistency: Consistency Models for NVRAM
Writes unordered!
Writes to memory unordered (cache eviction)
But, recovery depends on write ordering
Enforcing order for all writes too slow!
Persistency models provide framework to reason about NVRAM write order while maximizing concurrency

## Slide 30: Nonvolatile memory (NVRAM)
DRAM and flash scaling slowing down
New NVRAMs provide fast, scalable storage (phase change, memristor, STT-RAM)
Performance of DRAM, durability of disk
Storage technology | Random read latency | Durable?
Disk | 10ms | 
Flash | 90µs | 
DRAM | 100ns | 
NVRAM | 50-1000ns [IBM] | 