## Slide 1: AirTrack: Locating Non-WiFi Interferers using Commodity WiFi Hardware
Ashish Patro, Shravan Rayanchu, Suman Banerjee
University of Wisconsin-Madison

## Slide 2: Talk Outline
How non-WiFi devices affect WiFi traffic?
How to detect non-WiFi transmissions using “commodity” WiFi cards?
How to physically locate these non-WiFi devices?
Evaluation
Notes: I’ll start off by presenting an overview of the various non-WiFi devices that co-exist with WiFi deployments and why are they an issue to the wireless deployments?

## Slide 3: Some Non-WiFi devices
Analog Cordless Phone
Video Camera
Microwave Oven
ZigBee
FHSS Cordless Phone
Bluetooth
SCO/ACL
Game Controllers
Audio
Transmitter
Narrowband/High-duty devices
Broadband devices
Frequency-hopping devices

## Slide 4: Problem
Non-WiFi devices exist in 2.4GHz/5.8GHz spectrum and impact WiFi performance

## Slide 5: Scenario
Access Point
GOALS
How do we detect and locate these non-WiFi devices?
How to do this in real time using commodity WiFi cards?
Notes: If we just create a software based solution, it can be easily deployed in enterprise WLANs.

## Slide 6: Why use commodity WiFi cards?
Software-only solution that works on top of the cards
Can easily deploy this software solution in current WLANs
No additional expensive hardware needed
  e.g. spectrum analyzers

## Slide 7: What do commodity WiFi cards provide?
Wireless Card
WiFi Packets
Packet Capture
FFT Samples
Non-WiFi devices
Sub-carrier energy samples
-73, -65, -72, …

## Slide 8: Challenges?
Less resolution of FFT samples compared to specialized hardware
  4 us for Bandspeed AirMaestro vs 116us for Atheros
Missing FFT Samples in presence of WiFi transmissions
  We can miss some non-WiFi device transmissions
Narrowband mode of operation
  Atheros card scans only 20Mhz band at a time
Notes: Not guaranteed to capture all WiFi samples. Thus, we can occasionally miss non-WiFi device transmissions.

## Slide 9: Talk Outline
How non-WiFi devices affect WiFi traffic?
How to detect non-WiFi transmissions using “commodity” WiFi cards?
How to physically locate these non-WiFi devices?
Evaluation
Notes: I’ll start off by presenting an overview of the various non-WiFi devices that co-exist with WiFi deployments and why are they an issue to the wireless deployments?

## Slide 10: How to detect non-WiFi devices?
Capture energy samples
Power
Frequency
Timing
Properties
Duration
Bandwidth
“Tagged Pulses”
e.g., Bluetooth
“Classify”
Pulses
Extract ``Features’’
Identify ``Pulses”
Sniffer

## Slide 11: Talk Outline
How non-WiFi devices affect WiFi traffic?
How to detect non-WiFi transmissions using “commodity” WiFi cards?
How to physically locate these non-WiFi devices?
Evaluation
Notes: I’ll start off by presenting an overview of the various non-WiFi devices that co-exist with WiFi deployments and why are they an issue to the wireless deployments?

## Slide 12: AirTrack Overview
Access Point
(with Sniffer)
Culprit Device Locations:
Analogphone @ Room 104
Analogphone @ Room 110
FHSS Phone @ Room 105
ZigBee @ Room 108

## Slide 13: Device Localization
S1
S2
S3
S1: -40db
S2: -70db
S3: -75db
Use RSSI vector to localize each device

## Slide 14: How to create RSSI vectors?
Same pulse caught by multiple sniffers
FHSS Pulse
S1
S2
S3
S1: -70db
S2: -60db
S3: -45db
S1: -70db
S2: -60db
S1: -45db
“Merge”
Merge pulses using matching start/end times and center frequency + bandwidth
Synchronize the APs

## Slide 15: How to synchronize APs?
+5 µs
-9 µs
Reference AP
Common Packets
Common Packets
Transitive sync
Use Breadth First Search over clock offsets to synchronize APs

## Slide 16: A problem…
FHSS
Device 1
FHSS
Device 2
We can’t decode non-WiFi pulses
How many devices?
Which pulse belongs to what device?
Notes: We can’t decode pulses unlike WiFi pulses, where we can easily figure out the packet source and destination. Pulses are just time-energy blocks of transmissions….
Suppose there is one phone at one end of the room and a another phone at another end of the room… How do the controller segregate these pulses? This is a pre-requisite for localization. We need to know the number of active devices operating simultaneously, so that we can locate each one of them.

## Slide 17: Some challenges need to be solved…
Airshark only identifies pulse types
Access Point (with Airshark sniffer)
FHSS Phone
Bluetooth
How can we create the RSSI vector?

## Slide 18: How to segregate pulses?
FHSS phone
Merged Pulses
FHSS Pulse Cluster 2
FHSS Pulse Cluster 1
Cluster using
    RSSI vector
  Timing properties
Algorithms
  DBSCAN
  EM + k-Means
Clustering process segregates pulses belonging to different device instances
Notes: - Timing based properties work really well…
- RSSI based properties work well unless the two devices are very to each other…

## Slide 19: Each “Pulse Cluster” is a device
FHSS Pulse Cluster 2
FHSS Pulse Cluster 1
S1: -40db
S2: -70db
S3: -75db
S1: -70db
S2: -60db
S3: -45db
FHSS Device 1
FHSS Device 2
Each cluster is represented by an RSSI Vector

## Slide 20: Can we perform localization now?
The answer is ‘Yes’. But, few challenges in localizing non-WiFi devices….

## Slide 21: Putting it together…
Synchronize access points
“Tagged
Pulses”
Access Point (with Sniffer)
AirTrack
Locate non-WiFi devices using multiple Sniffers
Localize each device
(Pulse Cluster)
Merge + Cluster pulses

## Slide 22: Putting it together…
Synchronize access points
“Tagged
Pulses”
Access Point (with Sniffer)
AirTrack
Locate non-WiFi devices using multiple sniffers
Localize each device
(Pulse Cluster)
Merge + Cluster pulses

## Slide 23: Localization algorithms
AP locations are known
Tested various algorithms with different requirements
Algorithm | Input Parameters
Fingerprint | Known Fingerprints

## Slide 24: Localization algorithms
AP locations are known
Tested various algorithms with different requirements
Algorithm | Input Parameters
Fingerprint | Known Fingerprints
RSS Triangulation | Device Transmit Power + Propagation Model

## Slide 25: Localization algorithms
AP locations are known
Tested various algorithms with different requirements
Algorithm | Input Parameters
Fingerprint | Known Fingerprints
RSS Triangulation | Device Transmit Power + Propagation Model
Pairwise AP | Propagation Model

## Slide 26: Pairwise AP algorithm
Pairwise AP: S0,S2
Pairwise AP: S3,S5
We can localize without knowing device transmit power
FHSS Cordless Phone

## Slide 27: Talk Outline
How non-WiFi devices affect WiFi traffic?
How to detect non-WiFi transmissions using “commodity” WiFi cards?
How to physically locate these non-WiFi devices?
Evaluation
Notes: I’ll start off by presenting an overview of the various non-WiFi devices that co-exist with WiFi deployments and why are they an issue to the wireless deployments?

## Slide 28: Clustering results
FHSS Phones
Microwave Oven
FHSS Phones
Time domain clustering
RSS domain clustering
Each cluster is a unique active device
AirTrack can differentiate between multiple devices

## Slide 29: Localization Accuracy
Localization error < 6 metres for 80% of the locations

## Slide 30: Summary
Presented a system for real-time localization of non-WiFi devices using commodity WiFi cards.
Localization works in the presence of multiple device instances.
Don’t require to know the device transmit power for localization.

## Slide 31: Demo

## Slide 32
Thank You!!