## Slide 1: BitWarp
Energy Efficient Analytic Data Processing on Next Generation General Purpose GPUs
Jason Power || Yinan Li || Mark D. Hill || Jignesh M. Patel || David A. Wood
Computer architecture affiliates meeting 10/10/2014
Notes: Todo:
- Put in overhead data (time per number of columns)
- Might be interesting to show seconds per column entry instead of seconds per scan
- Talk about 1 TPC-H query (Q 12?)

## Slide 2: Problem
Data is growing rapidly
Analytic DBs increasingly important
Want: High performance
Need: Low energy
Notes: High perf in terms of both low-latency (i.e. near real time) and high throughput (e.g. concurrency)
Datacenters use 1-2% of all energy, depending on how you look at it

## Slide 3: GPUs to the Rescue
GPUs are becoming more general
  Easier to program
  Pervasive
GPUs show great promise
  Higher performance than CPUs
  Better energy efficiency
Analytic DBs look like GPU workloads
Notes: Percent of all processors shipping with GPUs?

## Slide 4: BitWarp
WideTable and BitWeaving [Li and Patel ‘13 & ‘14]
  Denormalized and coded column-store
  State of the art scan algorithm
Evaluate current and future GPGPUs
  Discrete, integrated, HSA, 3D-stacked
Today: 1.4–2.9x energy savings
Future: >50x less energy

## Slide 5: Outline
Motivation
GPGPU Analytic DB System
  Analytic DBs
  BitWeaving & BitWarp
  GPGPU generations
Results
Conclusion
Notes: Why GPGPU generations?

## Slide 6: Analytic DBs
In-memory
Column-based layout
WideTable
  Denormalize: Pre-join most tables
  Convert queries to mostly scans
BitWeaving
  Very fast scan
  Sub-word parallelism
Similar to industry proposals
Notes: I’m just going to discuss a couple of these details important to the GPU
Be clear this is on CPU

## Slide 7: WideTable—Pre-join
S-ID | Type | Color
0 | Tee | Red
1 | Tee | Blue
2 | Tee | Green
3 | Tee | Yellow
4 | Sweat | Red
5 | Sweat | Green
O-ID | S-ID | Amt
0 | 2 | 1
0 | 5 | 3
0 | 1 | 1
1 | 2 | 5
1 | 3 | 8
2 | 0 | 2
2 | 3 | 1
2 | 1 | 4
3 | 3 | 2
O-ID | S-ID | Type | Color | Amt
0 | 2 | Tee | Green | 1
0 | 5 | Sweat | Green | 3
0 | 1 | Tee | Blue | 1
1 | 2 | Tee | Green | 5
1 | 3 | Tee | Yellow | 8
2 | 0 | Tee | Red | 2
2 | 3 | Tee | Yellow | 1
2 | 1 | Tee | Blue | 4
3 | 3 | Tee | Yellow | 2
NULL | 4 | Sweat | Red | NULL
⋈

## Slide 8: Encoding Data
O-ID | S-ID | Type | Color | Amt
0 | 2 | Tee | Green | 1
0 | 5 | Sweat | Green | 3
0 | 1 | Tee | Blue | 1
1 | 2 | Tee | Green | 5
1 | 3 | Tee | Yellow | 8
2 | 0 | Tee | Red | 2
2 | 3 | Tee | Yellow | 1
2 | 1 | Tee | Blue | 4
3 | 3 | Tee | Yellow | 2
NULL | 4 | Sweat | Red | NULL
Type
0
1
0
0
0
0
0
0
0
1
Color
10
10
01
10
11
00
11
01
11
00
Type | Code
Tee | 0
Sweat | 1
Color | Code
Red | 00
Blue | 01
Green | 10
Yellow | 11

## Slide 9: BitWeaving—Layout (Horizontal)
 | Color
c0 | 2 (10)
c1 | 2 (10)
c2 | 1 (01)
c3 | 2 (10)
c4 | 3 (11)
c5 | 0 (00)
c6 | 3 (11)
c7 | 1 (01)
c8 | 3 (11)
c9 | 0 (00)
word |  | c0 |  | c1 | 
w0 | X | 10 | X | 10 | 
 |  | c2 |  | c3 | 
w1 | X | 01 | X | 10 | 
 |  | c4 |  | c5 | 
w2 | X | 11 | X | 00 | 
 |  | c6 |  | c7 | 
w3 | X | 11 | X | 01 | 
 |  | c8 |  | c9 | 
w4 | X | 11 | X | 00 | 
01001000 00101000 01100000 01100100 01100000
word |  | c0
w0 | X | 10
word |  | c0 |  | c1 | 
w0 | X | 10 | X | 10 | 

## Slide 10: Naïve Scan
10100110 11001101 1100…
Data:
Compare code:
10
Result bitvector:
Find all green shirt orders amount
1
11
110
10
10
Notes: Find all the green shirts
Or all the time > 5 of some shirt is ordered

## Slide 11: BitWeaving—Layout (Vertical)
 | Color
c0 | 10
c1 | 10
c2 | 01
c3 | 10
c4 | 11
c5 | 00
c6 | 11
c7 | 01
c8 | 11
c9 | 00
word | c0 | c1 | c2 | c3 | c4 | c5 | c6 | c7
w0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0
w1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1
 | c8 | c9 |  |  |  |  |  | 
w2 | 1 | 0 |  |  |  |  |  | 
w3 | 1 | 0 |  |  |  |  |  | 
word | c0
w0 | 1
w1 | 0
word | c0 | c1
w0 | 1 | 1
w1 | 0 | 0

## Slide 12: BitWeaving
11011010
00101011
Data:
Compare code:
1
0
Result bitvector:
Find all green shirt orders amount
11001000
Notes: Find all the green shirts
Or all the time > 5 of some shirt is ordered

## Slide 13: BitWeaving Algorithm
Compute on codes
  No need to decode
  Multiple codes per operation
Horizontal
  Better for retrieving data
Vertical
  More compact
  Can use “early pruning”
See Li and Patel SIGMOD ‘13 for details

## Slide 14: BitWarp
Scan: data parallel
CPU: 10’s of parallel execution units
GPUs: 1000’s of parallel execution units
Low computational intensity
  Bandwidth-bound on CPU at 2+ cores
  GPUs high memory bandwidth

## Slide 15: BitWarp
11011010
00101011
Data:
Compare code:
1
0
Result bitvector:
11001000 0000100 11000010 …
Find all green shirt orders amount
11011010
00101011
11011010
00101011
Notes: Find all the green shirts
Or all the time > 5 of some shirt is ordered

## Slide 16: GPGPU Generations
Discrete (Gen 1)
Integrated (Gen 2)
  Logically integrated (Gen 2.1)
Integrated+3D-stacked (Gen 3)
Notes: “Now I’m going to discuss some of the characteristics of the 3 GPGPU generations we evaluated BitWarp with.”

## Slide 17: Generation 1 & 2 GPGPUs
Memory Bus
chip
Memory Bus
Heterogeneous
chip
Discrete (Gen 1)
  High mem. B/W
  Low comm. B/W
  Low mem. capacity
Integrated (Gen 2)
  Low mem. B/W
  High comm. B/W
  High mem. capacity
Discrete GPU (Gen 1)
32 CUs
CPU
4 cores
GPU (Gen 2)
8 CUs
PCI-e

## Slide 18: GPGPU Trends
Tight physical & logical integration
  High memory capacity for GPU
  Lower GPU overheads
  Lower compute capability
  Lower memory bandwidth
3D die-stacking (soon)
  Increased compute capability (GPU on CPU)
  Increased memory bandwidth

## Slide 19: Gen 2.1 GPGPUs
HSA: Heterogeneous system architecture
Tightly logically integrated
  Shared virtual address space
  Cache coherent
  “Pointer-is-a-pointer”
Very low communication overhead

## Slide 20: Future GPGPUs
Gen 2.2
Increased bandwidth to DRAM
Physical and logical integration
Gen 3
Increased compute capability
High bandwidth to DRAM
Physical and logical integration
CPU
GPU
DRAM
Board
CPU
GPU
DRAM

## Slide 21: Future GPGPUs (Gen 3)
Increased bandwidth to DRAM
Physical and logical integration
Increased compute capability
Board
CPU
GPU
DRAM

## Slide 22: Outline
Motivation
Background
Results
  Scan performance
  Scan energy
  TPC-H performance
Conclusion

## Slide 23: Test System
AMD HD7970 Discrete GPU (Gen 1)
  32 CU @ 1125 MHz
  3 GB memory, 264 GB/s peak B/W
  225 W TDP (including memory)
AMD Kaveri A10-7850K (Gen 2 and Gen 2.1)
  4-Core CPU @ 3.7 GHz
  8-CU GPU @ 720 MHz
  16 GB memory, 21 GB/s peak B/W
  95 W TDP
Energy measured with WattsUp meter

## Slide 24: Scan Time
Notes: 1 billion codes (~ 1 GB)
Ignores the cost to migrate data to/from the GPU

## Slide 25: Scan Energy

## Slide 26: Scan Energy
Notes: 1000 scans of 10-bit codes

## Slide 27: TPC-H
Analytic DB benchmark
Evaluated @ 10 GB
16/22 queries
Two main components
  Scan time
  Other: aggregate, group-by

## Slide 28: TPC-H Performance
Query 12 (scan bottom, other top)
Query 7 (scan bottom, other top)

## Slide 29: TPC-H Averages
Total query time (scan bottom, other top)
Scan-only time

## Slide 30: Gen 3 Energy
Compute capability
Memory bandwidth
Overheads
Memory capacity
Performance
Energy

## Slide 31: Current Directions
Working with new HSA support
  Quite cool
  Very early software
Implementing non-scan portion of queries
  GPU group-by
  GPU aggregation

## Slide 32: Conclusions
Analytic DBs important
  High performance
  Low energy
GPU good for scan-mostly workloads
Future systems make GPGPUs compelling

## Slide 33
?