## Slide 1: Bandwidth Optimized DRAM Caches
Jason Lowe-Power Mark D. Hill David A. Wood

## Slide 2: Problem
More compute resources Same number of pins
Die stacking to the rescue?
Limited capacity 
High bandwidth
Low capacity
Low bandwidth
High capacity
Notes: For instance, knight’s landing peak FP rate: 3.46 TFLOPS
Bandwidth can’t keep up

## Slide 3: Summary
Die-stacked cache: transparent high-bandwidth memory
Caches have “extra” DRAM accesses
Call this: Access Amplification. How Reduce?
  Writes: Not writeback  Writethrough  selective writethrough
  Insert: Not on miss  on LLC-writeback  on some LLC-writebacks
New mechanism: Laundry list
  Tracks and constrains dirty blocks in the cache
  Minimizes access amplification without hurting performance
Notes: Talk about how this compares to using it as a scratchpad

## Slide 4: Outline
Background
  SRAM cache vs. DRAM cache
  Sources of access amplification
Mitigating access amplification
Bandwidth Optimized Design
Results
Conclusion

## Slide 5
Bank 0
Bank 1
Bank 2
Bank 3
SRAM Cache
DRAM Cache
Addr
Channel 0
Controller
Channel 1
Controller
Channel 2
Controller
Bank 0
Bank 0
Bank 0
Bank 0
Channel 3
Controller
Addr
Many more sub-banks for max bandwidth
Extra layer of controllers
DRAM
Controller
DRAM
Controller
DRAM
Controller
DRAM
Controller
Notes: DRAM commands

## Slide 6
SRAM Cache Bank
DRAM Cache Channel
Bank 0
Addr
Addr
Addr
Channel 0
Controller
DRAM Controller
Tag
Data
DRAM Bank
Addr
Tag
Tag
Tag array higher bandwidth
Extra tag accesses interfere with demand
Tag
Data

## Slide 7: DRAM Cache Design
Reduce latency by storing tags with data [Alloy Cache: Qureshi & Loh]
Non-inclusive, memory-side cache

## Slide 8: Read: Cache hit
LLC-read
DRAM-cache read
Tag check
Response
❶
❷
❹
Cache controller
From on-chip LLC
❸
Notes: Add tag check

## Slide 9: Read: Cache miss
LLC-read
DRAM-cache read
Tag check
Main-memory write (if needed)
DRAM-cache write for busy
Main-memory read
DRAM-cache write for fill
Response
❶
❷
❸
❹
❺
❻
❼
❽
From on-chip LLC
Cache controller
Access amplification
Notes: Add pop-ups to explain each red arrow

## Slide 10: Write: Cache hit or miss
LLC-write
DRAM-cache read
Tag check
DRAM-cache write
Main-memory write (if needed)
❶
❷
❸
❹
❺
From on-chip LLC
Cache controller
Must turn around bus from read to write

## Slide 11: Access Amplification Effects
Traffic generation with 50-50 read-write ratio and 50% miss ratio
Notes: Explain how I did this.
Assumes 50% reads 50% dirty and 50% misses
This baseline is like an SRAM cache. Fill on miss and writeback.
Key idea: Remove all of this extra access amplification. We can remove all but the fill requests.

## Slide 12: Outline
Background
Mitigating access amplification
  Writes: Not writeback  Writethrough  selective writethrough
  Insert: Not on miss  on LLC-writeback  on some LLC-writebacks
Design details
Results
Conclusion
❶
❷
❸
❹

## Slide 13: ❶Writes: Not writeback  Writethrough
LLC-write
DRAM-cache read
Tag check
DRAM-cache write
Main-memory write (if needed)
❶
❷
❸
❹
❺
From on-chip LLC
Cache controller

## Slide 14: ❶Write: Not writeback  Writethrough
Traffic generation with 25-75 read-write ratio and 50% miss ratio
Removes “Tag read on write” and “writeback read” amplification
Notes: Mostly writes to make the data more pronounced.
Key thing: This assumes an infinite backing store bandwidth. Not practical!

## Slide 15: ❷Write: Not writethrough  selective writethrough
Writethrough
  Reduces write amplification (no check for dirty cache data)
  Pressure on main-memory bandwidth
Best of both writethrough and writeback
  Track dirty cache frames in SRAM (no check for dirty data)
  Proactively clean the cache when main-memory not busy
How? Laundry list

## Slide 16: ❸Insert: Not on miss  on LLC-writeback
LLC-read
DRAM-cache read
Tag check
Main-memory write (if needed)
DRAM-cache write for busy
Main-memory read/response
DRAM-cache write for fill
Response
❶
❷
❸
❹
❺
❻
❼
❽
From on-chip LLC
Cache controller
Notes: Targets tag write for busy and write for fill @ miss time.

## Slide 17: ❸Insert: Not on miss  on LLC-writeback
Traffic generation with 75-25 read-write ratio and 100% miss ratio
Removes “Tag write busy” amplification
Increases “fill write” amplification

## Slide 18: Fill on LLC-write problem
Traffic generation with 75-25 read-write ratio and 10% miss ratio
Most “fill writes” are clean WBs to data that is already in the cache.

## Slide 19: ❹Insert: Not on LLC-writebacks  on some LLC-writebacks
Fill on miss -> Access amplification (Write busy state to tag)
Fill on LLC-writeback -> Useless clean writebacks
Best of both:
  Fill on LLC-writeback, only if data not from cache
  Track origin of data in on-chip caches
  Detect “likely inclusive” data (it’s OK if we’re wrong)

## Slide 20: Outline
Background
Mitigating access amplification
Bandwidth-optimized design
  Fill on LLC-Write
  Laundry List
  Selective writeback
Results
Conclusion

## Slide 21: Bandwidth optimized design
Key idea: Only read the tag when reading data Only write the tag when writing data
Fill on LLC-write with likely inclusion detection
Laundry List to track dirty frames in cache
Selective writeback to limit dirty frames in cache

## Slide 22: 1. Fill on LLC-write
No allocate on miss
Fill on LLC-write like a victim cache
Likely inclusion detection
  When DRAM cache responds, set cached bit
  Track cached bit in the LLC
  On LLC eviction: only send LLC-write if dirty or no cached bit

## Slide 23: 2. Laundry List
Goal: Remove all tag reads on LLC-write
  Store some data in SRAM
Requires: Know when it is safe to write
  If the cache frame is clean
  If the tag matches
Invariant: Entry in laundry list for every dirty cache frame
Naïve design 1: Dirty bits in SRAM
  Area overhead (2 MB for 1 GB)
  Still some access amplification
    Assumes tag miss-match
Naïve design 2: Full Laundry list
  Same as SRAM tags
  Large area overhead (36 MB)

## Slide 24: 2. Laundry List
Goal: Remove all tag reads on LLC-write
  Store some data in SRAM
Requires: Know when it is safe to write
  If the cache frame is clean
  If the tag matches
Invariant: Entry in laundry list for every dirty cache frame
Subset of cache allowed dirty
  Workloads are mostly-clean
  ¼ of the cache in our design
Track “super frames”
  Workloads show high locality
  16 KB frames in our design
Set associative structure
  Any part of the cache can be dirty
930 KB area overhead (< 6% LLC)
Laundry list design

## Slide 25: 3. Selective writeback
Selectively clean lines
  Every time a cache frame is read or written, try to clean the frame
  On dirty writeback, try writethrough
Only write through if main-memory not saturated
Reduces number of dirty lines and size of laundry list

## Slide 26: Outline
Background
Mitigating access amplification
Bandwidth Optimized Design
Results
  Microbenchmark
  NAS Parallel benchmarks
Conclusion

## Slide 27: Methodology
DRAM caches only make sense for large bandwidth-bound workloads
gem5 used for detailed memory system
1. Traffic generation microbenchmark
2. NAS parallel benchmarks (HPC)
  These would take years to simulate: Sampling
System parameters: 32 core, 16 MB LLC, 128 GB/s HBM, 25 GB/s DDR3

## Slide 28: Microbenchmark results
Many writes (50/50 split)
Mostly read (90/10 split)
Writethrough better than writeback designs
Bandwidth Opt. design equal to writethrough
Writethrough hurts performance: main-memory bandwidth
Bandwidth Opt. Better than writeback and writethrough

## Slide 29: Access amplification reduction
29
Writethrough: No access amplification
Bandwidth Opt.: Slightly more than SRAM tags
Notes: Start with just workloads. Go through each color of fill on miss, then all of fill on WB, all of WT, then the final two.

## Slide 30: NPB Workloads
Bandwidth Opt. design reduces access amplification increasing performance
Notes: Note: I can’t really show the average speedup. This would be some insane distribution that I couldn’t even fathom a guess at
Show first three, then BW-opt and SRAM Tags

## Slide 31: Conclusions
Optimizing DRAM cache solely for latency leads to poor designs
  Access amplification for fills and writebacks
Bandwidth optimized DRAM cache
  Fill on write (save busy write)
  Track dirty blocks (save read before write)
  Adaptive writethrough (keeps cache mostly clean)
Reduces access amplification
Modest performance increase in simulation

## Slide 32: Backup slides

## Slide 33: 2. Laundry list
DRAM Cache
Cache frame
Super frame
Laundry List
Super frame
number
Physical tag
Super frame tag
Dirty count
¼ Laundry list 928 KB for 1 GB cache

## Slide 34: All workloads

## Slide 35: Most workloads show high locality

## Slide 36: Workloads mostly clean

## Slide 37: Miss ratio
Distinct phases in applications
Mixture of high and low miss ratios

## Slide 38: Traffic-gen results
All designs about the same at low hit rate
High hit rate: writethrough and adaptive best
Mostly reads (75/25 split)

## Slide 39: DRAM Cache Operation
Shared LLC (SRAM)
DRAM-cache controller
Cache storage controller
LLC-read
LLC-write
DRAM-cache read
DRAM-cache write
Main-memory
read
Main-memory
write

## Slide 40: But what about bandwidth?
Let’s look at a real system!
  Note: 100% hit rate!
30% reduction in peak bandwidth for transparency
Theoretical overhead of tags: 12.5%

## Slide 41: DRAM vs. SRAM caches
Tags
Data