## Slide 1: Announcements
2nd Exam: Congratulations on finishing!
    More than half-way through course material
P3: Due tomorrow at 9:00 pm
    Only turn in code in one project partner’s handin directory
  P4: Threads (Part a and b) available near end of week
    Can choose or be matched with new partner
Read as we go along!
  Chapter 36 + 37

## Slide 2: Persistence: I/O devices
Questions answered in this lecture:
How does the OS interact with I/O devices (check status, send data+control)?
What is a device driver?
What are the components of a hard disk drive?
How can you calculate sequential and random throughput of a disk?
What algorithms are used to schedule I/O requests?
UNIVERSITY of WISCONSIN-MADISON Computer Sciences Department
CS 537 Introduction to Operating Systems
Andrea C. Arpaci-Dusseau Remzi H. Arpaci-Dusseau

## Slide 3: Motivation
What good is a computer without any I/O devices?
- keyboard, display, disks
We want:
- H/W that will let us plug in different devices
- OS that can interact with different combinations

## Slide 4: Hardware support for I/O
CPU
RAM
Graphics
Memory Bus
General I/O Bus
(e.g., PCI)
Peripheral I/O Bus
(e.g., SCSI, SATA, USB)
Why use hierarchical buses?

## Slide 5: Canonical Device
Status
COMMAND
DATA
OS reads/writes to these
  Device Registers:

## Slide 6: Canonical Device
Status
COMMAND
DATA
  Device Registers:
OS reads/writes to these
  Hidden Internals:
???

## Slide 7: Canonical Device
Status
COMMAND
DATA
  Device Registers:
OS reads/writes to these
  Hidden Internals:
Microcontroller (CPU+RAM)
Extra RAM
Other special-purpose chips

## Slide 8: Example Write Protocol
while (STATUS == BUSY)
; // spin
Write data to DATA register
Write command to COMMAND register
while (STATUS == BUSY)
; // spin
Status
COMMAND
DATA
Microcontroller (CPU+RAM)
Extra RAM
Other special-purpose chips

## Slide 9
while (STATUS == BUSY) // 1
;
Write data to DATA register // 2
Write command to COMMAND register // 3
while (STATUS == BUSY) // 4
;
CPU:
Disk:

## Slide 10
A
CPU:
Disk:
C
while (STATUS == BUSY) // 1
;
Write data to DATA register // 2
Write command to COMMAND register // 3
while (STATUS == BUSY) // 4
;

## Slide 11
A
CPU:
Disk:
C
A wants to do I/O
while (STATUS == BUSY) // 1
;
Write data to DATA register // 2
Write command to COMMAND register // 3
while (STATUS == BUSY) // 4
;

## Slide 12
1
A
CPU:
Disk:
C
while (STATUS == BUSY) // 1
;
Write data to DATA register // 2
Write command to COMMAND register // 3
while (STATUS == BUSY) // 4
;

## Slide 13
1
2
A
CPU:
Disk:
A
C
while (STATUS == BUSY) // 1
;
Write data to DATA register // 2
Write command to COMMAND register // 3
while (STATUS == BUSY) // 4
;

## Slide 14
1
2
A
CPU:
Disk:
A
C
3
while (STATUS == BUSY) // 1
;
Write data to DATA register // 2
Write command to COMMAND register // 3
while (STATUS == BUSY) // 4
;

## Slide 15
1
2
4
3
A
CPU:
Disk:
C
A
while (STATUS == BUSY) // 1
;
Write data to DATA register // 2
Write command to COMMAND register // 3
while (STATUS == BUSY) // 4
;

## Slide 16
1
2
4
3
A
CPU:
Disk:
C
A
while (STATUS == BUSY) // 1
;
Write data to DATA register // 2
Write command to COMMAND register // 3
while (STATUS == BUSY) // 4
;

## Slide 17
1
2
4
3
A
B
CPU:
Disk:
C
A
while (STATUS == BUSY) // 1
;
Write data to DATA register // 2
Write command to COMMAND register // 3
while (STATUS == BUSY) // 4
;
how to avoid spinning?
interrupts!

## Slide 18
1
2
4
3
A
B
CPU:
Disk:
C
A
how to avoid spinning?
interrupts!
while (STATUS == BUSY) // 1
wait for interrupt;
Write data to DATA register // 2
Write command to COMMAND register // 3
while (STATUS == BUSY) // 4
wait for interrupt;

## Slide 19
2
3,4
A
B
CPU:
Disk:
C
A
how to avoid spinning?
interrupts!
B
B
A
A
1
while (STATUS == BUSY) // 1
wait for interrupt;
Write data to DATA register // 2
Write command to COMMAND register // 3
while (STATUS == BUSY) // 4
wait for interrupt;

## Slide 20: Interrupts vs. Polling
Are interrupts ever worse than polling?
Fast device: Better to spin than take interrupt overhead
  Device time unknown? Hybrid approach (spin then use interrupts)
Flood of interrupts arrive
  Can lead to livelock (always handling interrupts)
  Better to ignore interrupts while make some progress handling them
Other improvement
  Interrupt coalescing (batch together several interrupts)

## Slide 21: Protocol Variants
Status checks: polling vs. interrupts
Data: PIO vs. DMA
Control: special instructions vs. memory-mapped I/O
Status
COMMAND
DATA
Microcontroller (CPU+RAM)
Extra RAM
Other special-purpose chips

## Slide 22
2
3,4
A
B
CPU:
Disk:
C
A
what else can we optimize?
B
B
A
A
1
while (STATUS == BUSY) // 1
wait for interrupt;
Write data to DATA register // 2
Write command to COMMAND register // 3
while (STATUS == BUSY) // 4
wait for interrupt;
data transfer!

## Slide 23: Programmed I/O vs. Direct Memory Access
PIO (Programmed I/O):
  CPU directly tells device what the data is
DMA (Direct Memory Access):
  CPU leaves data in memory
  Device reads data directly from memory

## Slide 24
2
3,4
A
B
CPU:
Disk:
C
A
B
B
A
A
1
while (STATUS == BUSY) // 1
wait for interrupt;
Write data to DATA register // 2
Write command to COMMAND register // 3
while (STATUS == BUSY) // 4
wait for interrupt;

## Slide 25
2
3,4
A
B
CPU:
Disk:
C
A
B
B
A
A
1
while (STATUS == BUSY) // 1
wait for interrupt;
Write data to DATA register // 2
Write command to COMMAND register // 3
while (STATUS == BUSY) // 4
wait for interrupt;

## Slide 26
A
CPU:
Disk:
C
A
B
B
A
1
3,4
while (STATUS == BUSY) // 1
wait for interrupt;
Write data to DATA register // 2
Write command to COMMAND register // 3
while (STATUS == BUSY) // 4
wait for interrupt;

## Slide 27: Protocol Variants
Status checks: polling vs. interrupts
Data: PIO vs. DMA
Control: special instructions vs. memory-mapped I/O
Status
COMMAND
DATA
Microcontroller (CPU+RAM)
Extra RAM
Other special-purpose chips

## Slide 28
A
CPU:
Disk:
C
A
B
B
A
1
3,4
how does OS read and write registers?
while (STATUS == BUSY) // 1
wait for interrupt;
Write data to DATA register // 2
Write command to COMMAND register // 3
while (STATUS == BUSY) // 4
wait for interrupt;

## Slide 29: Special Instructions vs. Mem-Mapped I/O
Special instructions
  each device has a port
  in/out instructions (x86) communicate with device
Memory-Mapped I/O
  H/W maps registers into address space
  loads/stores sent to device
Doesn’t matter much (both are used)

## Slide 30: Protocol Variants
Status checks: polling vs. interrupts
Data: PIO vs. DMA
Control: special instructions vs. memory-mapped I/O
Status
COMMAND
DATA
Microcontroller (CPU+RAM)
Extra RAM
Other special-purpose chips

## Slide 31: Variety is a Challenge
Problem:
  many, many devices
  each has its own protocol
How can we avoid writing a slightly different OS for each H/W combination?
Write device driver for each device
Drivers are 70% of Linux source code

## Slide 32: Storage Stack
application
file system
scheduler
driver
hard drive
build common interface
on top of all HDDs

## Slide 33: Hard Disks

## Slide 34: Basic Interface
Disk has a sector-addressable address space
  Appears as an array of sectors
Sectors are typically 512 bytes or 4096 bytes.
Main operations: reads + writes to sectors
Mechanical (slow) nature makes management “interesting”

## Slide 35
Platter
Disk Internals

## Slide 36
Platter is covered with a magnetic film.

## Slide 37
Spindle

## Slide 38
Surface
Surface

## Slide 39
Many platters may be bound to the spindle.

## Slide 40
Each surface is divided into rings called tracks.
A stack of tracks (across platters) is called a cylinder.

## Slide 41
The tracks are divided into numbered sectors.
1
2
3
0
6
5
4
7
8
9
10
11
15
14
13
12
16
17
18
19
23
22
21
20

## Slide 42
Heads on a moving arm can read from each surface.
1
2
3
0
6
5
4
7
8
9
10
11
15
14
13
12
16
17
18
19
23
22
21
20

## Slide 43
1
2
3
0
6
5
4
7
8
9
10
11
15
14
13
12
16
17
18
19
23
22
21
20
spin
Spindle/platters rapidly spin.

## Slide 44: Disk Terminology
spindle
platter
surface
track
cylinder
sector
read/write head

## Slide 45: Hard Drive Demo
http://youtu.be/9eMWG3fwiEU?t=30s
https://www.youtube.com/watch?v=L0nbo1VOF4M

## Slide 46: Let’s Read 12!
1
2
3
0
6
5
4
7
8
9
10
11
15
14
13
12
16
17
18
19
23
22
21
20

## Slide 47: Positioning
Drive servo system keeps head on track
  How does the disk head know where it is?
  Platters not perfectly aligned, tracks not perfectly concentric (runout) -- difficult to stay on track
  More difficult as density of disk increase
    More bits per inch (BPI), more tracks per inch (TPI)
Use servo burst:
  Record placement information every few (3-5) sectors
  When head cross servo burst, figure out location and adjust as needed

## Slide 48: Let’s Read 12!
1
2
3
0
6
5
4
7
8
9
10
11
15
14
13
12
16
17
18
19
23
22
21
20

## Slide 49: Seek to right track.
1
2
3
0
6
5
4
7
8
9
10
11
15
14
13
12
16
17
18
19
23
22
21
20

## Slide 50: Seek to right track.
1
2
3
0
6
5
4
7
8
9
10
11
15
14
13
12
16
17
18
19
23
22
21
20

## Slide 51: Seek to right track.
1
2
3
0
6
5
4
7
8
9
10
11
15
14
13
12
16
17
18
19
23
22
21
20

## Slide 52: Wait for rotation.
1
2
3
0
6
5
4
7
8
9
10
11
15
14
13
12
16
17
18
19
23
22
21
20

## Slide 53: Wait for rotation.
1
2
3
0
6
5
4
7
8
9
10
11
15
14
13
12
16
17
18
19
23
22
21
20

## Slide 54: Wait for rotation.
1
2
3
0
6
5
4
7
8
9
10
11
15
14
13
12
16
17
18
19
23
22
21
20

## Slide 55: Wait for rotation.
1
2
3
0
6
5
4
7
8
9
10
11
15
14
13
12
16
17
18
19
23
22
21
20

## Slide 56: Wait for rotation.
1
2
3
0
6
5
4
7
8
9
10
11
15
14
13
12
16
17
18
19
23
22
21
20

## Slide 57: Wait for rotation.
1
2
3
0
6
5
4
7
8
9
10
11
15
14
13
12
16
17
18
19
23
22
21
20

## Slide 58: Transfer data.
1
2
3
0
6
5
4
7
8
9
10
11
15
14
13
12
16
17
18
19
23
22
21
20

## Slide 59: Transfer data.
1
2
3
0
6
5
4
7
8
9
10
11
15
14
13
12
16
17
18
19
23
22
21
20

## Slide 60: Transfer data.
1
2
3
0
6
5
4
7
8
9
10
11
15
14
13
12
16
17
18
19
23
22
21
20

## Slide 61: Yay!
1
2
3
0
6
5
4
7
8
9
10
11
15
14
13
12
16
17
18
19
23
22
21
20

## Slide 62: Time to Read/write
Three components:
Time = seek + rotation + transfer time

## Slide 63: Seek, Rotate, Transfer
Seek cost: Function of cylinder distance
  Not purely linear cost
Must accelerate, coast, decelerate, settle
Settling alone can take 0.5 - 2 ms
Entire seeks often takes several milliseconds
  4 - 10 ms
Approximate average seek distance = 1/3 max seek distance

## Slide 64: Seek, Rotate, Transfer
Depends on rotations per minute (RPM)
  7200 RPM is common, 15000 RPM is high end.
With 7200 RPM, how long to rotate around?
  1 / 7200 RPM =
  1 minute / 7200 rotations =
  1 second / 120 rotations =
  8.3 ms / rotation
Average rotation?
  8.3 ms / 2 = 4.15 ms

## Slide 65: Seek, Rotate, Transfer
Pretty fast — depends on RPM and sector density.
100+ MB/s is typical for maximum transfer rate
How long to transfer 512-bytes?
512 bytes * (1s / 100 MB) = 5 us

## Slide 66: Workload Performance
So…
- seeks are slow
- rotations are slow
- transfers are fast
What kind of workload is fastest for disks?
Sequential: access sectors in order (transfer dominated)
Random: access sectors arbitrarily (seek+rotation dominated)

## Slide 67: Disk Spec
 | Cheetah | Barracuda
Capacity | 300 GB | 1 TB
RPM | 15,000 | 7,200
Avg Seek | 4 ms | 9 ms
Max Transfer | 125 MB/s | 105 MB/s
Platters | 4 | 4
Cache | 16 MB | 32 MB
Sequential workload: what is throughput for each?
Cheeta: 125 MB/s.
Barracuda: 105 MB/s.

## Slide 68: Disk Spec
Random workload: what is throughput for each?
(what else do you need to know?)
 | Cheetah | Barracuda
Capacity | 300 GB | 1 TB
RPM | 15,000 | 7,200
Avg Seek | 4 ms | 9 ms
Max Transfer | 125 MB/s | 105 MB/s
Platters | 4 | 4
Cache | 16 MB | 32 MB
What is size of each random read?
Assume 16-KB reads

## Slide 69
 | Cheetah | Barracuda
RPM | 15,000 | 7,200
Avg Seek | 4 ms | 9 ms
Max Transfer | 125 MB/s | 105 MB/s
How long does an average random 16-KB read take w/ Cheetah?
Seek + rotation + transfer
Seek = 4 ms

## Slide 70
 | Cheetah | Barracuda
RPM | 15,000 | 7,200
Avg Seek | 4 ms | 9 ms
Max Transfer | 125 MB/s | 105 MB/s
How long does an average random 16-KB read take w/ Cheetah?
avg rotation =
1
2
1 min
15000
60 sec
1 min
1000 ms
1 sec
= 2 ms
Average rotation in ms?

## Slide 71
 | Cheetah | Barracuda
RPM | 15,000 | 7,200
Avg Seek | 4 ms | 9 ms
Max Transfer | 125 MB/s | 105 MB/s
How long does an average random 16-KB read take w/ Cheetah?
transfer =
1 sec
125 MB
16 KB
1,000,000 us
1 sec
= 125 us
Transfer of 16 KB?

## Slide 72
 | Cheetah | Barracuda
RPM | 15,000 | 7,200
Avg Seek | 4 ms | 9 ms
Max Transfer | 125 MB/s | 105 MB/s
How long does an average random 16-KB read take w/ Cheetah?
Cheetah time = 4ms + 2ms + 125us = 6.1ms
Throughput?

## Slide 73
 | Cheetah | Barracuda
RPM | 15,000 | 7,200
Avg Seek | 4 ms | 9 ms
Max Transfer | 125 MB/s | 105 MB/s
How long does an average random 16-KB read take w/ Cheetah?
Cheetah time = 4ms + 2ms + 125us = 6.1ms
throughput =
16 KB
6.1ms
1 MB
1024 KB
100 ms
1 sec
= 2.5 MB/s

## Slide 74
 | Cheetah | Barracuda
RPM | 15,000 | 7,200
Avg Seek | 4 ms | 9 ms
Max Transfer | 125 MB/s | 105 MB/s
How long does an average random 16-KB read take w/ Barracuda?
Time = seek + rotation + transfer
Seek = 9ms

## Slide 75
 | Cheetah | Barracuda
RPM | 15,000 | 7,200
Avg Seek | 4 ms | 9 ms
Max Transfer | 125 MB/s | 105 MB/s
How long does an average random 16-KB read take w/ Barracuda?
avg rotation =
1
2
1 min
7200
60 sec
1 min
1000 ms
1 sec
= 4.1 ms

## Slide 76
 | Cheetah | Barracuda
RPM | 15,000 | 7,200
Avg Seek | 4 ms | 9 ms
Max Transfer | 125 MB/s | 105 MB/s
How long does an average random 16-KB read take w/ Barracuda?
transfer =
1 sec
105 MB
16 KB
1,000,000 us
1 sec
= 149 us

## Slide 77
 | Cheetah | Barracuda
RPM | 15,000 | 7,200
Avg Seek | 4 ms | 9 ms
Max Transfer | 125 MB/s | 105 MB/s
How long does an average random 16-KB read take w/ Barracuda?
Barracuda time = 9ms + 4.1ms + 149us = 13.2ms

## Slide 78
 | Cheetah | Barracuda
RPM | 15,000 | 7,200
Avg Seek | 4 ms | 9 ms
Max Transfer | 125 MB/s | 105 MB/s
How long does an average random 16-KB read take w/ Barracuda?
throughput =
16 KB
13.2ms
Barracuda time = 9ms + 4.1ms + 149us = 13.2ms
1 MB
1024 KB
1000 ms
1 sec
= 1.2 MB/s

## Slide 79
 | Cheetah | Barracuda
Sequential | 125 MB/s | 105 MB/s
Random | 2.5 MB/s | 1.2 MB/s
 | Cheetah | Barracuda
Capacity | 300 GB | 1 TB
RPM | 15,000 | 7,200
Avg Seek | 4 ms | 9 ms
Max Transfer | 125 MB/s | 105 MB/s
Platters | 4 | 4
Cache | 16 MB | 32 MB

## Slide 80: Other Improvements
Track Skew
Zones
Cache

## Slide 81
8
9
10
11
15
14
13
12
16
17
18
19
23
22
21
20
Imagine sequential reading, how should sectors numbers be laid out on disk?

## Slide 82
8
9
10
11
15
14
13
12
16
17
18
19
23
22
21
20
When reading 16 after 15, the head won’t settle
quick enough, so we need to do a rotation.

## Slide 83
8
9
10
11
15
14
13
12
23
23
16
17
21
20
19
18

## Slide 84
8
9
10
11
15
14
13
12
23
23
16
17
21
20
19
18
enough time to settle now

## Slide 85: Other Improvements
Track Skew
Zones
Cache

## Slide 89
ZBR (Zoned bit recording): More sectors on outer tracks

## Slide 90: Other Improvements
Track Skew
Zones
Cache

## Slide 91: Drive Cache
Drives may cache both reads and writes.
  OS caches data too
What advantage does caching in drive have for reads?
What advantage does caching in drive have for writes?
8
9
10
11
15
14
13
12
16
17
18
19
23
22
21
20

## Slide 92: Buffering
Disks contain internal memory (2MB-16MB) used as cache
Read-ahead: “Track buffer”
  Read contents of entire track into memory during rotational delay
Write caching with volatile memory
  Immediate reporting: Claim written to disk when not
  Data could be lost on power failure
Tagged command queueing
  Have multiple outstanding requests to the disk
  Disk can reorder (schedule) requests for better performance

## Slide 93: I/O Schedulers

## Slide 94: I/O Schedulers
Given a stream of I/O requests, in what order should they be served?
Much different than CPU scheduling
Position of disk head relative to request position matters more than length of job

## Slide 95: FCFS (First-Come-First-Serve)
Assume seek+rotate = 10 ms for random request
How long (roughly) does the below workload take?
  Requests are given in sector numbers
300001, 700001, 300002, 700002, 300003, 700003
~60ms

## Slide 96: FCFS (First-Come-First-Serve)
Assume seek+rotate = 10 ms for random request
How long (roughly) does the below workload take?
  Requests are given in sector numbers
300001, 700001, 300002, 700002, 300003, 700003
300001, 300002, 300003, 700001, 700002, 700003
~60ms
~20ms

## Slide 97: Schedulers
OS
Disk
Scheduler
Scheduler
Where should the
scheduler go?

## Slide 98: SPTF (Shortest Positioning Time First)
Strategy: always choose request that requires least positioning time (time for seeking and rotating)
  Greedy algorithm (just looks for best NEXT decision)
How to implement in disk?
How to implement in OS?
Use Shortest Seek Time First (SSTF) instead
Disadvantages?
Easy for far away requests to starve

## Slide 99: SCAN
Elevator Algorithm:
  Sweep back and forth, from one end of disk other, serving requests as pass that cylinder
  Sorts by cylinder number; ignores rotation delays
Pros/Cons?
Better: C-SCAN (circular scan)
  Only sweep in one direction

## Slide 100: What happens?
void reader(int fd) {
char buf[1024];
int rv;
while((rv = read(buf)) != 0) {
assert(rv);
// takes short time, e.g., 1ms
process(buf, rv);
}
}
Assume 2 processes each calling read() with C-SCAN

## Slide 101: Work Conservation
Work conserving schedulers always try to do work if there’s work to be done
Sometimes, it’s better to wait instead if system anticipates another request will arrive
Such non-work-conserving schedulers are called anticipatory schedulers

## Slide 102: CFQ (Linux Default)
Completely Fair Queueing
  Queue for each process
  Weighted round-robin between queues, with slice time proportional to priority
  Yield slice only if idle for a given time (anticipation)
Optimize order within queue

## Slide 103: I/O Device Summary
Overlap I/O and CPU whenever possible!
- use interrupts, DMA
Storage devices provide common block interface
On a disk: Never do random I/O unless you must!
- e.g., Quicksort is a terrible algorithm on disk
Spend time to schedule on slow, stateful devices