## Slide 1
38. RAID
Operating System: Three Easy Pieces

## Slide 2: RAID (Redundant Array of Inexpensive Disks)
Use multiple disks in concert to build a faster, bigger, and more reliable disk system.
  RAID just looks like a big disk to the host system.
Advantage
  Performance & Capacity: Using multiple disks in parallel
  Reliability: RAID can tolerate the loss of a disk.
RAIDs provide these advantages transparently
to systems that use them.

## Slide 3: RAID Interface
When a RAID receives I/O request,
  The RAID calculates which disk to access.
  The RAID issue one or more physical I/Os to do so.
RAID example: A mirrored RAID system
  Keep two copies of each block (each one on a separate disk)
  Perform two physical I/Os for every one logical I/O it is issued.

## Slide 4: RAID Internals
A microcontroller
  Run firmware to direct the operation of the RAID
Volatile memory (such as DRAM)
  Buffer data blocks
Non-volatile memory
  Buffer writes safely
Specialized logic to perform parity calculation

## Slide 5: Fault Model
RAIDs are designed to detect and recover from certain kinds of disk faults.
Fail-stop fault model
  A disk can be in one of two states: Working or Failed.
    Working: all blocks can be read or written.
    Failed: the disk is permanently lost.
  RAID controller can immediately observe when a disk has failed.

## Slide 6: How to evaluate a RAID
Capacity
  How much useful capacity is available to systems?
Reliability
  How many disk faults can the given design tolerate?
Performance

## Slide 7: RAID Level 0: Striping
RAID Level 0 is the simplest form as striping blocks.
  Spread the blocks across the disks in a round-robin fashion.
  No redundancy
  Excellent performance and capacity
Disk 0 | Disk 1 | Disk 2 | Disk 3
0 | 1 | 2 | 3
4 | 5 | 6 | 7
8 | 9 | 10 | 11
12 | 13 | 14 | 15
RAID-0: Simple Striping
(Assume here a 4-disk array)
Stripe
(The blocks in the same row)

## Slide 8: RAID Level 0 (Cont.)
Example) RAID-0 with a bigger chunk size
  Chunk size : 2 blocks (8 KB)
  A Stripe: 4 chunks (32 KB)
Disk 0 | Disk 1 | Disk 2 | Disk 3
0 | 2 | 4 | 6
1 | 3 | 5 | 7
8 | 10 | 12 | 14
9 | 11 | 13 | 15
Striping with a Bigger Chunk Size
chunk size:
2blocks

## Slide 9: Chunk Sizes
Chunk size mostly affects performance of the array
  Small chunk size
    Increasing the parallelism
    Increasing positioning time to access blocks
  Big chunk size
    Reducing intra-file parallelism
    Reducing positioning time
Determining the “best” chunk size is hard to do.
Most arrays use larger chunk sizes (e.g., 64 KB)

## Slide 10: RAID Level 0 Analysis
Capacity  RAID-0 is perfect.
  Striping delivers N disks worth of useful capacity.
Performance of striping  RAID-0 is excellent.
  All disks are utilized often in parallel.
Reliability  RAID-0 is bad.
  Any disk failure will lead to data loss.
: the number of disks

## Slide 11: Evaluating RAID Performance
Consider two performance metrics
  Single request latency
  Steady-state throughput
Workload
  Sequential: access 1MB of data (block (B) ~ block (B + 1MB))
  Random: access 4KB at random logical address
A disk can transfer data at
  S MB/s under a sequential workload
  R MB/s under a random workload

## Slide 12: Evaluating RAID Performance Example
sequential (S) vs random (R)
  Sequential : transfer 10 MB on average as continuous data.
  Random : transfer 10 KB on average.
  Average seek time: 7 ms
  Average rotational delay: 3 ms
  Transfer rate of disk: 50 MB/s
Results:
  S = = = 47.62 MB /s
  R = = = 0.981 MB /s

## Slide 13: Evaluating RAID-0 Performance
Single request latency
  Identical to that of a single disk.
Steady-state throughput
  Sequential workload : MB/s
  Random workload : MB /s
: the number of disks

## Slide 14: RAID Level 1 : Mirroring
RAID Level 1 tolerates disk failures.
  Copy more than one of each block in the system.
  Copy block places on a separate disk.
    RAID-10 (RAID 1+0) : mirrored pairs and then stripe
    RAID-01 (RAID 0+1) : contain two large striping arrays, and then mirrors
Simple RAID-1: Mirroring (Keep two physical copies)
Disk 0 | Disk 1 | Disk 2 | Disk 3
0 | 0 | 1 | 1
2 | 2 | 3 | 3
4 | 4 | 5 | 5
6 | 6 | 7 | 7

## Slide 15: RAID-1 Analysis
Capacity: RAID-1 is Expensive
  The useful capacity of RAID-1 is N/2.
Reliability: RAID-1 does well.
  It can tolerate the failure of any one disk (up to N/2 failures depending on which disk fail).
: the number of disks

## Slide 16: Performance of RAID-1
Two physical writes to complete
  It suffers the worst-case seek and rotational delay of the two request.
  Steady-state throughput
    Sequential Write : MB/s
      Each logical write must result in two physical writes.
    Sequential Read : MB/s
      Each disk will only deliver half its peak bandwidth.
    Random Write : MB/s
      Each logical write must turn into two physical writes.
    Random Read : MB/s
      Distribute the reads across all the disks.

## Slide 17: RAID Level 4 : Saving Space With Parity
Add a single parity block
  A Parity block stores the redundant information for that stripe of blocks.
Five-disk RAID-4 system layout
Disk 0 | Disk 1 | Disk 2 | Disk 3 | Disk 4
0 | 0 | 1 | 1 | P0
2 | 2 | 3 | 3 | P1
4 | 4 | 5 | 5 | P2
6 | 6 | 7 | 7 | P3
* P: Parity

## Slide 18: RAID Level 4 (Cont.)
Compute parity : the XOR of all of bits
Recover from parity
  Imagine the bit of the C2 in the first row is lost.
    Reading the other values in that row : 0, 0, 1
    The parity bit is 0  even number of 1’s in the row
    What the missing data must be: a 1.
C0 | C1 | C2 | C3 | P
0 | 0 | 1 | 1 | XOR(0,0,1,1)=0
0 | 1 | 0 | 0 | XOR(0,1,0,0)=1

## Slide 19: RAID-4 Analysis
Capacity
  The useful capacity is .
Reliability
  RAID-4 tolerates 1 disk failure and no more.
: the number of disks

## Slide 20: RAID-4 Analysis (Cont.)
Performance
  Steady-state throughput
    Sequential read: MB/s
    Sequential write: MB/s
    Random read: MB/s
Full-stripe Writes In RAID-4
Disk 0 | Disk 1 | Disk 2 | Disk 3 | Disk 4
0 | 1 | 2 | 3 | P0
4 | 5 | 6 | 7 | P1
8 | 9 | 10 | 11 | P2
12 | 13 | 14 | 15 | P3

## Slide 21: Random write performance for RAID-4
Overwrite a block + update the parity
Method 1: additive parity
  Read in all of the other data blocks in the stripe
  XOR those blocks with the new block (1)
  Problem: the performance scales with the number of disks

## Slide 22: Random write performance for RAID-4 (Cont.)
Method 2: subtractive parity
  Update C2(old)  C2(new)
    Read in the old data at C2 (C2(old)=1) and the old parity (P(old)=0)
    Calculate P(new):
      If C2(new)==C2(old)  P(new)==P(old)
      If C2(new)!=C2(old)  Flip the old parity bit
C0 | C1 | C2 | C3 | P
0 | 0 | 1 | 1 | XOR(0,0,1,1)=0

## Slide 23: Small-write problem
The parity disk can be a bottleneck.
  Example: update blocks 4 and 13 (marked with *)
    Disk 0 and Disk 1 can be accessed in parallel.
    Disk 4 prevents any parallelism.
Writes To 4, 13 And Respective Parity Blocks.
Disk 0 | Disk 1 | Disk 2 | Disk 3 | Disk 4
0 | 1 | 2 | 3 | P0
*4 | 5 | 6 | 7 | +P1
8 | 9 | 10 | 11 | P2
12 | *13 | 14 | 15 | +P3
RAID-4 throughput under random small writes is MB/s (terrible).

## Slide 24: A I/O latency in RAID-4
A single read
  Equivalent to the latency of a single disk request.
A single write
  Two reads and then two writes
    Data block + Parity block
    The reads and writes can happen in parallel.
  Total latency is about twice that of a single disk.

## Slide 25: RAID Level 5: Rotating Parity
RAID-5 is solution of small write problem.
  Rotate the parity blocks across drives.
  Remove the parity-disk bottleneck for RAID-4
RAID-5 With Rotated Parity
Disk 0 | Disk 1 | Disk 2 | Disk 3 | Disk 4
0 | 1 | 2 | 3 | P0
5 | 6 | 7 | P1 | 4
10 | 11 | P2 | 8 | 9
15 | P3 | 12 | 13 | 14
P4 | 16 | 17 | 18 | 19

## Slide 26: RAID-5 Analysis
Capacity
  The useful capacity for a RAID group is .
Reliability
  RAID-5 tolerates 1 disk failure and no more.
: the number of disks

## Slide 27: RAID-5 Analysis (Cont.)
Performance
  Sequential read and write
  A single read and write request
  Random read : a little better than RAID-4
    RAID-5 can utilize all of the disks.
  Random write : MB/s
    The factor of four loss is cost of using parity-based RAID.
Same as RAID-4
: the number of disks

## Slide 28: RAID Comparison: A Summary
RAID Capacity, Reliability, and Performance
 |  |  | RAID-0 | RAID-1 | RAID-4 | RAID-5
Capacity |  |  | N | N/1 | N-1 | N-1
Reliability |  |  | 0 | 1 (for sure) (if lucky) | 1 | 1
Throughput |  |  |  |  |  | 
 | Sequential Read |  | NㆍS | (N/2) ㆍS | (N-1) ㆍS | (N-1) ㆍS
 | Sequential Write |  | NㆍS | (N/2) ㆍS | (N-1) ㆍS | (N-1) ㆍS
 | Random Read |  | NㆍR | NㆍR | (N-1) ㆍR | NㆍR
 | Random Write |  | NㆍR | (N/2) ㆍR | R | R
Latency |  |  |  |  |  | 
 |  | Read | D | D | D | D
 |  | Write | D | D | 2D | 2D
 |  |  | RAID-0 | RAID-1 | RAID-4 | RAID-5
Capacity |  |  | N | N/1 | N-1 | N-1
Reliability |  |  | 0 |  | 1 | 1
Throughput |  |  |  |  |  | 
 | Sequential Read |  | NㆍS | (N/2) ㆍS | (N-1) ㆍS | (N-1) ㆍS
 | Sequential Write |  | NㆍS | (N/2) ㆍS | (N-1) ㆍS | (N-1) ㆍS
 | Random Read |  | NㆍR | NㆍR | (N-1) ㆍR | NㆍR
 | Random Write |  | NㆍR | (N/2) ㆍR |  | 
Latency |  |  |  |  |  | 
 |  | Read | D | D | D | D
 |  | Write | D | D | 2D | 2D
: the number of disks
: the time that a request to a single disk take

## Slide 29: RAID Comparison: A Summary
Performance and do not care about reliability  RAID-0 (Striping)
Random I/O performance and Reliability  RAID-1 (Mirroring)
Capacity and Reliability  RAID-5
Sequential I/O and Maximize Capacity  RAID-5

## Slide 30
Disclaimer: This lecture slide set was initially developed for Operating System course in Computer Science Dept. at Hanyang University. This lecture slide set is for OSTEP book written by Remzi and Andrea at University of Wisconsin.