## Slide 1: Reliable Multicast Routing for Software-Defined Networks

## Slide 2: Introduction (1/7) Unicast
Video services via unicast suffer from high server and network load
Keep one connection for each client  high server load
Each stream occupy bandwidth high network load

## Slide 3: Introduction (2/7) Multicast
Multicast reduces the load of both servers and networks
Support more clients with the same resources
The load of the server is reduced
The load of the network is reduced
More clients can be served

## Slide 4: Introduction (3/7) Reliable Multicast
Reliable transmission is desired by some applications
Video services such as MPEG DASH
Sender handles recovery  high recovery cost
Middle nodes handle recovery  where to place the recovery nodes
Recovery Packets
Recovery Packets
Acks
Recovery Packets
Acks
Acks
Save BW and latency
Place a recovery node

## Slide 5: Introduction (4/7) Multicast with SDN
Multicast traffic engineering for SDN?
  Shortest-Path Tree (SPT) in Internet
    Employ OSPF unicast routing, no traffic engineering
    Minimize an end-to-end cost
    Difficult to efficiently reduce the total bandwidth consumption
  Steiner Tree (ST) in Graph Theory
    Minimum resource consumption (# of edges in T)
    Does not consider the selection of the recovery node
    Difficult to facilitate local loss recovery

## Slide 6: Introduction (5/7) Recover-Aware Steiner Tree
Reliable multicast
  Each destination is assigned a recovery node to recover loss packets
  Recovery nodes cache packets and monitor transmission for destinations
  The total costs include tree and recovery cost
Proposed Recover-Aware Steiner tree (RST)
  Reduce both tree and recovery costs
  Objective: minimize (tree cost + α× recovery cost)
    α: weighting factor for recovery cost

## Slide 7: Introduction (6/7) Tree and Recovery Costs
D = {1, 2, 3, 4, 5, 6, 7}, C = V, r = 2, R = {7, v}
Then c(T) = 36
w(P1) = 2 w(P3) = 1 w(P4) = 5 w(P5) = 3 w(P6) = 5 w(P7) = 9
par(2) = v w(P2) = 1 + 2 = 3
w(P2) = 3
par(v) = s w(Pv) = 3 + 8 = 11
w(Pv) = 11
, w(T) = 39

## Slide 8: Introduction (7/7) Comparison
(a) Original Network
(b) Shortest-path tree
Tree cost = 40
Recovery = 58
(c) Steiner tree
Tree cost = 22
Recovery = 66
(d) Recover-aware Steiner tree
Tree cost = 25
Recovery = 32

## Slide 9: Related Works
Few current works in SDN community address multicast traffic engineering
Current reliable multicast approaches (RMTP-II, PGM, NORM) focus on minimizing the number of ACK and NAK messages
None of them consider the selection of recovery nodes
Can not minimize recovery costs

## Slide 10: Main Contributions
Observe that both SPT and ST are not suitable for reliable multicast
  Traffic engineering
  Can not reduce both tree and recovery costs
Propose Recover-Aware Steiner Tree (RST)
  Integer Programming (IP) formulation
Prove that RST is NP-hard and not approximable within k
  k: terminal node number
Propose k-approximation algorithm RAERA for RST
  RAERA: Recover-Aware Edge Reduction Algorithm
  Achieve the best approximation ratio

## Slide 11: Hardness Result
RST is NP-Hard
Steiner tree (ST) approximable within ratio 1.55
RST not approximable within |D|1-ε for everyε＞0
  Gap-introducing reduction from the Set Cover (SC) problem
Transform an instance in SC to G in RST, such that
  If SC returns TRUE, OPT(G)≦(α + 1)(k + 1)|D|
  If SC returns FALSE, OPT(G)＞(α + 1)(k + 1)|D|2-ε
  k:
  D: the destination set
  L: the cost of each edge from s to X in G

## Slide 12: Gap-Introducing Reduction
L
L
1
1
Transform to G in RST
An instance in SC
x3
x5
x4
x1
x2
y1
y1
y3
y2
ym
Y
X
…
s
x3
x5
x4
x1
x2
y1
y3
y2
y1
y3
y2
ym
…
|Y|p copies of Y
X
…
…
ym

## Slide 13: If (X, Y, E) has a k-node subset A of X covering all nodes in Y, then there exists a tree T rooted at s which contains A and D. And recovery set R is set as A. R = {x1, x2, x5} c(T) = k * L + |D| , w(T) = k * L + |D|
k-node subset A
T
x3
x5
x4
x1
x2
y1
y1
y3
y2
ym
Y
X
…
s
x3
x5
x4
x1
x2
y1
y3
y2
y1
y3
y2
ym
…
|Y|p copies of Y
X
…
…
ym

## Slide 14: If (X, Y, E) does not have a k-node subset A of X covering all nodes in Y,| then w(T) > L * |Y|p
For each copy of Y, at least one node connects to a non-recovery node, leading to a much higher recovery cost .
s
x3
x5
x4
x1
x2
y1
y3
y2
y1
y3
y2
ym
…
|Y|p copies of Y
X
…
…
ym

## Slide 15: Recover Aware Edge Reduction Algorithm (1/8)
Tree Routing Phase
  The first phase starts from the shortest-path tree with root s and iteratively improves the tree to reduce the tree cost.
  RAERA iteratively re-routes a destination node on the solution tree T(VT, ET ) to reduce the tree cost.
  More importantly, the re-routing path needs to include at least one candidate recovery node in C and the cost of the depth in the new tree cannot exceed the depth of the original shortest-path tree.
Recovery Selection Phase
  Recovery Selection Phase is a dynamic programming algorithm to select the recovery nodes to minimize the recovery cost.

## Slide 16: Recover Aware Edge Reduction Algorithm (2/8)
Shortest-path tree with root s
Original network
An example of Tree Routing Phase:
s
1
6
3
5
11
12
2
9
2
3
3
5
5
2
8
7
2
u
5
2
2
w
2
1
8
1
4
b
v
d
6
1
10
c
1
8
6
e
Calculate a shortest-path tree for each destination
2
1
8
1
2
8
6
5
2
2
1
2
u
5
1
6
1
2
3
5
3
s
11
12
8
2
4
9
3
5
10
6
7
w
b
v
d
c
e
x
3
1
3
1
1
2
1
2
3
9
2
9
1
1
9

## Slide 17: Recover Aware Edge Reduction Algorithm (3/8)
Tree Routing Phase
Shortest-path tree with root s
An example of Tree Routing Phase:
s
1
6
3
5
11
12
2
9
2
3
3
5
5
2
8
7
2
u
5
2
2
w
2
1
8
1
4
b
v
d
6
1
10
c
1
8
6
e
s
1
3
5
6
11
12
2
9
2
3
3
5
5
2
8
7
2
u
5
2
2
w
1
8
1
2
4
b
v
d
6
1
10
c
1
8
6
e
3
2
1
3
1
1
2
Re-route destinations

## Slide 18: Recover Aware Edge Reduction Algorithm (4/8)
Recovery Selection Phase:
  For each node v in VT, let Tv be the subtree of T rooted at v. Let Rv be a recovery set on Tv. The dynamic programming algorithm finds the optimal recovery sets for two cases.
  A recovery set Rv on Tv is type I if v not in Rv.
  Rv belongs to type II if v in Rv.
  σx,k(Tv): the minimum recovery cost on Tv over all type I recovery set Rv with |Rv| ≦ x, such that v exactly dominates k nodes in RvD.
  τx(Tv): the minimum recovery cost on Tv over all type II recovery set Rv with |Rv| ≦ x .
Bottom up

## Slide 19: Recover Aware Edge Reduction Algorithm (5/8)
uδv
u1
v
u2
v
v
…
Lemma 1: For each node and its child nodes in , the following equations hold for , , and .
If , then
If , then
Similar discussions to 2)
When is NOT a recovery node
When is a recovery node
When , can not be a recovery node
Since ,
dominates nodes in

## Slide 20: Recover Aware Edge Reduction Algorithm (6/8)
u1
v
u2
…
# R & #D | Cost
(0,0) | c1
(0,1) | c2
(1,0) | c3
： | ：
# R & #D | Cost
(0,0) | c1
(0,1) | c2
(1,0) | c3
： | ：
# R & #D | Cost
(0,0) | c1
(0,1) | c2
(1,0) | c3
： | ：
Lemma 2: Suppose are the child nodes of . For , the following equality holds.
Use DP,
for to ,
to calculate for every

## Slide 21: Recover Aware Edge Reduction Algorithm (7/8）
x | k = 1 | k = 2
0 1 2 | ∞ 10 9 | 15 12 7
x | k = 1 | k = 2
0 1 2 | ∞ ∞ 8 | 20 16 11
τ1(Tu) = 15
τ2(Tu) = 10
τ1(Tw) = 20
τ2(Tw) = 16
x | k = 1 | k = 2 | k = 3
0 1 2 | ∞ | ∞ ∞ ∞ | 
21
σ0,3(Tv1) = σ0,2(Tu) + 3 * 2 = 15 + 6
σx,k(Tv1)
σ1,1(Tv1) = τ1(Tu) + 2 = 15 + 2
17
σ1,3(Tv1) = σ1,2(Tu) + 3 * 2 = 12 + 6
18
σ2,1(Tv1) = τ2(Tu) + 2 = 10 + 2
12
σ2,3(Tv1) = σ2,2(Tu) + 3 * 2 = 7 + 6
13

## Slide 22: Recover Aware Edge Reduction Algorithm (8/8）
σx,k(Tv1)
x | k = 1 | k = 2 | k = 3
0 1 2 | ∞ 17 12 | ∞ ∞ ∞ | 21 18 13
σx,k(Tv2)
x | k = 1 | k = 2
0 1 2 | ∞ ∞ 10 | 26 22 17
σ1,3(Tv) =
min{σ0,1(Tv1) +σ1,2(Tv2), σ0,2(Tv1) +σ1,1(Tv2), σ1,1(Tv1) +σ0,2(Tv2), σ1,2(Tv1) +σ0,1(Tv2)}
= min{∞, ∞, 17+26 ,∞} = 43

## Slide 23: Simulation Setup
Estinet network simulator
A real topology
  Biznet with 29 nodes and 33 links
  #destinations = 6 ~ 12
  #recovery nodes = 2
Synthetic topologies
  Generated by Inet
  #nodes = 4000 ~ 10000
  #destinations = 100 ~ 500
  #recovery nodes = 15 ~ 55

## Slide 24: Simulation Setup
Algorithms
  The shortest-path tree algorithm (SPT)
  The Steiner tree (ST) algorithm
  The optimal solution by CPLEX
  RAERA
Performance metrics
  Total cost (tree + recovery costs)
  Total retransmitted bytes
  Average latency

## Slide 25: The Real Topology
Chart: k
| 6.0 | 8.0 | 10.0 | 12.0
CPLEX | 13 | 19 | 18 | 18
RAERA | 14 | 19 | 18 | 19
ST | 13 | 17 | 17 | 17
SPT | 16 | 21 | 21 | 21
Chart: k
| 6.0 | 8.0 | 10.0 | 12.0
CPLEX | 17 | 24 | 27 | 31
RAERA | 17 | 25 | 27 | 31
ST | 28 | 33 | 43 | 48
SPT | 23 | 34 | 35 | 41
Tree Cost
Recovery Cost
ST minimizes tree cost, and provides the lowest tree cost
The tree cost provided by RAERA is similar to optimized solution
ST does not consider recovery cost and results in the highest recovery cost
REARA also consider recovery cost, so the cost is the lowest
SPT also provides higher recovery cost
SPT minimizes end-to-end hops, and it results in the highest tree cost

## Slide 26: The Real Topology
Chart: k
| 6.0 | 8.0 | 10.0 | 12.0
CPLEX | 3.2 | 30 | 38.0975 | 38.0975
RAERA | 4.3257 | 38.0975 | 38.0975 | 38.0975
ST | 80.6261 | 106.7139 | 234.0466 | 234.0466
SPT | 48.2485 | 115.3979 | 115.3979 | 115.3979
Retransmission
Latency
Chart: k
| 6.0 | 8.0 | 10.0 | 12.0
CPLEX | 1.0322 | 1.7039 | 1.9005 | 2.1217
RAERA | 1.0322 | 1.7039 | 1.9005 | 2.1217
ST | 1.9251 | 2.2118 | 3.0226 | 3.3503
SPT | 1.622 | 2.3429 | 2.4412 | 2.8017
REARA similar to optimized solution generates the fewest retransmission bytes
SPT is in between
Because of the highest recovery cost, ST generates the most retransmission bytes
Longer end-to-end hops make longer latency when k is larger
REARA shows the lowest latency with lower total costs
SPT reduces the end-to-end hops, so its latency does not grow with k critically

## Slide 27: Synthetic Topology
Chart: k
| 100.0 | 200.0 | 300.0 | 400.0 | 500.0
RAERA | 278 | 522 | 763 | 1009 | 1260
ST | 323 | 666 | 989 | 1291 | 1613
SPT | 349 | 672 | 991 | 1323 | 1614
Chart: r
| 15.0 | 25.0 | 35.0 | 45.0 | 55.0
RAERA | 814 | 782 | 763 | 763 | 763
ST | 1011 | 989 | 990 | 989 | 979
SPT | 1008 | 992 | 991 | 989 | 989
Cost with Different k
Cost with Different r
The cost increase with k, because of larger tree for more destinations.
The cost slightly decreases with more recovery nodes
ST and SPT work similar with higher cost.
REARA successfully reduces the cost

## Slide 28: Synthetic Topology
Chart: |V|
| 4000.0 | 6000.0 | 8000.0 | 10000.0
RAERA | 762 | 793 | 766 | 763
ST | 1005 | 1000 | 983 | 989
SPT | 956 | 1005 | 943 | 991
Cost with Different |V|
Chart: k
| 100.0 | 200.0 | 300.0 | 400.0 | 500.0
RAERA | 8.5402 | 20.3004 | 33.6442 | 46.0067 | 56.7756
ST | 13.8674 | 27.2784 | 41.0242 | 54.6985 | 67.7948
SPT | 13.5684 | 26.6204 | 40.9327 | 54.0934 | 66.3414
Retransmission bytes with different k
The cost does not increase with |V|, because the size of tree is similar.
More destinations generate more retransmission Bytes.
ST and SPT work similar.
RAERA provides lower cost and generate less transmission bytes

## Slide 29: Synthetic Topology
Chart: k
| 100.0 | 200.0 | 300.0 | 400.0 | 500.0
RAERA | 9.8 | 9.34 | 9.16 | 9.29 | 9.36
ST | 80.6261 | 94.022 | 94.1472 | 92.8327 | 93.2458
SPT | 48.2485 | 48.0535 | 48.0318 | 49.3865 | 47.8064
Chart: r
| 15.0 | 25.0 | 35.0 | 45.0 | 55.0
RAERA | 10.52 | 9.6667 | 9.16 | 9.16 | 9.16
ST | 80.6261 | 77.467 | 77.6043 | 77.467 | 75.8187
SPT | 48.2485 | 46.7342 | 46.608 | 46.3556 | 46.2715
Latency with different k
Latency with different r
Latency does not change obviously with k and r
Latency is the highest in ST cast, because of longer end-to-end hops
RAERA provides the lowest latency
SPT shows higher latency than REARA, because of higher recovery latency

## Slide 30: Running Time of RAERA
Intel Xeon E7-4870 2.4 GHz CPUs and 128GB RAM
｜v｜ | k = 100 | k = 200 | k = 300 | k = 400 | k = 500
4000 | 0.7 | 1.37 | 2.87 | 5.29 | 9.56
6000 | 1.5 | 2.23 | 3.9 | 6.93 | 11.48
8000 | 2.61 | 3.39 | 5.09 | 7.91 | 12
10000 | 4.08 | 4.9 | 6.6 | 10.14 | 13.99
Running time increases with k
Also increases with
|V|
When scale is small, the running time is less than 1 second
Even in a large scale, the running is still acceptable.

## Slide 31: Implementation
We evaluate RAERA in our experimental SDN network
Use Floodlight as our controller
Implement recovery nodes in Click software router
Topology includes 14 nodes and 20 links with 8 destinations and 2 recovery nodes
Test video is 136 seconds in length

## Slide 32: Evaluation in Our Testbed
Algorithm | Bandwidth Consumption | Re-buffering
RAERA | 13.18 Mbytes | 0.4 s
ST | 16.39 Mbytes | 33.5 s
SPT | 17.83 Mbytes | 7.8 s
ST and SPT generate similar retransmission bytes
ST provides longer average end-to-end hops that causes longer video re-buffering
RAERA provides better video quality

## Slide 33: Conclusion
Traffic engineering and recovery node selection in SDN have not been carefully addressed for reliable multicast
Propose Recover-aware Steiner Tree (RST)
Prove that RST
  NP-Hard and not able be approximated within k.
Design algorithm RAERA
  k–approximation algorithm – tightest bound
  Acquire a solution in seconds in massive networks
Notes: 1. 我們設計了在multi-view 3D 影片network下 價格based的DIBR觀看視野管理機制
2.3. 將network中的 server 與 觀看者之間的階層關係model成Stackelberg game 並且設計演算法得到他們的最佳策略
4. 考慮到傳統的uniform pricing, 公平分配以及提出一個滿意度最大化問題. NUP有效的控制視野範圍且可以避免資源被少數觀看者所佔領 並且得到的平衡點滿意度總和接近滿意度最大化問題的解。

## Slide 34
Backup Slides

## Slide 35: Reliable Multicast
Sender handles recovery  high recovery cost
Middle nodes handle recovery  where to place the recovery nodes
Recovery Packets
Recovery Packets
Acks
Acks
High recovery costs

## Slide 36: Reliable Multicast
Sender handles recovery  high recovery cost
Middle nodes handle recovery  where to place the recovery nodes
Recovery Packets
Recovery Packets
Acks
Place a recovery node
Recovery Packets
Acks
Acks
Save BW and latency

## Slide 37: Recover Aware Edge Reduction Algorithm (7/8)
An example for recovery node selection
Use lemma 2 to calculate σx,k(Tu)
x | k = 1 | k = 2 | k = 3 | k = 4
0 1 2 | ∞ ∞ ∞ | ∞ ∞ ∞ | 9 9 9 | ∞ ∞ ∞
u can help only tree special nodes for recovery, so there is no solution when k = 1, 2, 4
τ1(Tu) = τ2(Tu) = 9
σx,k(Tu)

## Slide 38: Recover Aware Edge Reduction Algorithm (8/8)
Use Lemma1.(ii) to calculate σx,k(T11)
x | k = 1 | k = 2 | k = 3 | k = 4
0 1 2 | ∞ 14 14 | ∞ ∞ ∞ | 24 24 24 | ∞ ∞ ∞
σx,k(T11)
σ2,3(T111) = σ2,3(Tu) + 3 * 5 = 9 + 15
σ1,1(T111) = min {σ1,1(Tu) + 5, τ1(Tu) + 5} = min {∞, 9 + 5}