## Slide 1: Pushing the Limits of Accelerator Efficiency While Retaining Programmability
Tony Nowatzki*, Vinay Gangadhar*, Karu Sankaralingam*, Greg Wright+
*Vertical Research Group
University of Wisconsin – Madison
+Qualcomm
Notes: Which explores how far the efficiency limits of accelerators can be pushed while still having the programmability feature

## Slide 2: Executive Summary
5 common principles of architectural specialization
A programmable architecture (LSSD) embodying the specialization principles
LSSD compared to single domain specific accelerator (DSA)
  Performance: Matches DSA
  Area: Overhead of at most 4x
  Power: Overhead of at most 4x
LSSD power overhead inconsequential with system-level energy efficiency tradeoffs
Notes: We mainly propose 5 important principles of specialization common to many DSAs and how they are exploited
A programmable arch. LSSD composed of uarch mechanisms embodying the common specialization principles.
I will show that LSSD can be provisioned to match the performance of DSAs with little overheads
Economic and energy tradeoffs of DSAs compared to LSSD

## Slide 3: Outline
Introduction and Motivation
Principles of architectural specialization
  Embodiment of principles in DSAs
Architecture for programmable specialization (LSSD)
Evaluation of LSSD with 4 DSAs (Performance, power & area)
System-level energy efficiency tradeoffs with LSSD and DSA
Speedup
Energy
Computation
Data Reuse
Concurrency
Coordination
Communication
Core
System Bus
$
Memory
Accel.

## Slide 4: Era of Specialization
Performance and/or energy gains from multicore chips is challenging
Specialization of application domains with custom hardware units
Domain Specific Acceleration
Domain Specific Accelerators (DSAs):
  + High Efficiency
Traditional Multicore
Linear Algebra
Neural Approx.
Graph Traversal
AI
Scan
Sort
Reg Expr.
Deep Neural
Stencil
DSAs
Cache
Core
Core
Core
Application domain specialization
Cache
Core
Core
Core
10 – 100x
Performance/Power
or
Performance/Area
Not general purpose programmable
  - No Generality
  - Obsoletion Prone
Notes: With no benefits from device scaling, extracting performance and energy efficiency from multicore chips has become challenging in last few years
Industry and academia is relying on specializing each individual application domain using custom hardware engines to do the domain specific logic
And getting 10-1000x performance
- DSAs – hardware engines capable of performing computations in one domain with high perf and energy efficiency

## Slide 5: Our Goal: Programmable Specialization
Specialization benefits of DSAs in a Programmable Architecture
Programmable architecture
matching the efficiency of DSAs

## Slide 6: Key Insight: Commonality in DSAs’ Specialization Principles
+
S
S
FU
S
S
FU
Computation
Data Reuse
Concurrency
Coordination
Communication
Most DSAs employ 5 common Specialization Principles
Linear Algebra
Neural Approx.
Graph Traversal
AI
Scan
Sort
Reg Expr.
Deep Neural
Stencil
Cache
Core
Core
Core
DSAs
Host System
Notes: To understand the sources of efficiency and specialization benefits in DSAs,
We mainly investigated 4 relevant application domains and their recent DSA proposals
Key insight we derived out of this study was  Most of the DSAs employ 5 common spec. principles.

## Slide 7: Solution: Architecture for Programmable Specialization
Idea 1: Specialization principles can be exploited in a general way
Idea 2: Composition of known uArch. mechanisms embodying the specialization principles
Low power core
Spatial fabric
Scratchpad
DMA
Programmable Architecture (LSSD)
LSSD as a programmable hardware template
to map one or many application domains
Stencil, Sort, Scan, AI
Balanced LSSD
Deep Neural
Domain provisioned LSSD
*Figures not to scale
Notes: Using that insight, the key solution we propose in this work are:
  Programmable specialization can be achieved In a general way instead of domain specific way
- As architects we can come up with a programmable arch with known simple uarch. Mechanisms embodying these principles
- we call this arch as LSSD named after --
LSSD can be used as a programmable hardware template employing the specialization principles to map one of many appl. Domains and get the beneifts of specialziation.
Composition of known programmable and configurable uarch mechanisms
And also show that this power overhead becomes insignificant when considering energy efficiency tradeoffs in a system level implementation involving LSSD

## Slide 8: Outline
Introduction and Motivation
Principles of architectural specialization
  Embodiment of principles in DSAs
Architecture for programmable specialization (LSSD)
Evaluation of LSSD with 4 DSAs (Performance, power & area)
System-level energy efficiency tradeoffs with LSSD and DSA
Speedup
Energy
Computation
Data Reuse
Concurrency
Coordination
Communication
Core
System Bus
$
Memory
Accel.

## Slide 9: Principles of Architectural Specialization
Match hardware concurrency to that of algorithm
Problem-specific computation units
Explicit communication as opposed to implicit communication
Customized structures for data reuse
Hardware coordination using simple low-power control logic
+
Computation
FU
Data Reuse
Concurrency
Coordination
S
S
FU
S
S
Communication
Notes: We mainly propose 5 important principles of specialization common to many DSAs and how they are exploited
A programmable arch. LSSD composed of uarch mechanisms embodying the common specialization principles.
I will show that LSSD can be provisioned to match the performance of DSAs with little overheads
Economic and energy tradeoffs of DSAs compared to LSSD

## Slide 10
+
S
S
FU
S
S
FU
Computation
Data Reuse
Concurrency
Coordination
Communication
5 Specialization Principles
Linear Algebra
Neural Approx.
Graph Traversal
AI
Scan
Sort
Reg Expr.
Deep Neural
Stencil
NPU
Convolution
Engine
DianNao
Q100
Deep Neural
Stencil
Neural Approx.
Database
How do DSAs embody these principles in a domain specific way ?

## Slide 11: Principles in DSAs
Computation
Data Reuse
Concurrency
Coordination
Communication
High Level
Organization
Processing Engine
PE
PE
PE
PE
PE
PE
PE
PE
In Fifo
Bus Sched
Out Fifo
General Purpose Processor
Weight Buf.
Fifo
Out Buf.
Cont-roller
Acc Reg.
Sigmoid
NPU – Neural Proc. Unit
Mult-Add
Match hardware concurrency to that of algorithm
Problem-specific computation units
Explicit communication as opposed to implicit communication
Customized structures for data reuse
Hardware coordination using simple low-power control logic

## Slide 12: Principles in DSAs
High Level
Organization
Processing Units
Most DSAs employ 5 common
Specialization Principles
Computation
Data Reuse
Concurrency
Coordination
Communication

## Slide 13: Outline
Introduction and Motivation
Principles of architectural specialization
  Embodiment of principles in DSAs
Architecture for programmable specialization (LSSD)
Evaluation of LSSD with 4 DSAs (Performance, power & area)
System-level energy efficiency tradeoffs with LSSD and DSA
Speedup
Energy
Computation
Data Reuse
Concurrency
Coordination
Communication
Core
System Bus
$
Memory
Accel.

## Slide 14
Concurrency: Multiple tiles (Tile – hardware for coarse grain unit of work)
Computation: Special FUs in spatial fabric
Communication: Dataflow + spatial fabric
Data Reuse: Scratchpad (SRAMs)
Coordination: Low power simple core
Computation
Data Reuse
Concurrency
Coordination
Communication
Composition of simple micro-architectural mechanisms
Each Tile
Implementation of Principles in a General Way

## Slide 15: LSSD Programmable Architecture
Spatial Fabric
Output Interface
Input Interface
. . .
Scratchpad
DMA
Memory
Low-power Core
(LX3)
D$
Spatial Fabric
Output Interface
Input Interface
. . .
Scratchpad
DMA
Memory
Low-power Core
(LX3)
D$
Spatial Fabric
Output Interface
Input Interface
. . .
Scratchpad
DMA
Memory
Low-power Core
(LX3)
D$
. . .
Memory
FU
S
FU
FU
FU
S – Switch
Low power core | Spatial fabric | Scratchpad | DMA  LSSD
Computation
Data Reuse
Concurrency
Coordination
Communication

## Slide 16: Instantiating LSSD
LSSDC
LSSD
Provisioned for
one single application domain
Programmable hardware template for specialization
Neural Approx.
Deep Neural
Stencil
Neural Approx.
Database
Provisioned for
multiple application domains
Stencil
Deep Neural
Database
*Figures not to scale
LSSDD
LSSDQ
LSSDN
LSSDBalanced
or
LSSDB
Design point selection, Synthesis & Programming: More details in the paper…..

## Slide 17: Outline
Introduction and Motivation
Principles of architectural specialization
  Embodiment of principles in DSAs
Architecture for programmable specialization (LSSD)
Evaluation of LSSD with 4 DSAs (Performance, power & area)
System-level energy efficiency tradeoffs with LSSD and DSA
Speedup
Energy
Computation
Data Reuse
Concurrency
Coordination
Communication
Core
System Bus
$
Memory
Accel.

## Slide 18: Methodology
Modeling framework for LSSD
  Perf: Trace driven simulator + application specific modeling
  Power & Area: Synthesized modules, CACTI and McPAT
Compared to four DSAs (published perf., area & power)
Four parameterized LSSDs
Provisioned to match performance of DSAs
  Other tradeoffs possible (power, area, energy etc. )
LSSDN
LSSDC
LSSDD
LSSDQ
1 Tile 1 Tile 8 Tiles 4 Tiles
NPU
Conv.
DianNao
Q100
LSSDB
NPU
Conv.
DianNao
Q100
8 Tiles
One combined balanced LSSD
Notes: An analytical model  trace driven simulator with application specific modeling to capture compiler and LSSD program role
Framework has multiple execution stages depending on application
We contacted authors to get detailed cycle level counts and area/power information
LSSDn and LSSDc required one tile of LSSD

## Slide 19: Performance Analysis (1)
Chart: Speedup
| fft (1-4-4-2) | inversek2j (2-8-2) | jmeint (18-32-8-2) | jpeg (64-16-64) | kmeans (6-8-4-1) | sobel (9-8-1) | Geometric Mean
LP Core + Sig. (+comp.) | 2.3932 | 2.3717 | 1.1563 | 1.1553 | 1.9857 | 1.5917 | 1.698
SIMD (+concur.) | 3.2068 | 4.1649 | 6.5484 | 7.21 | 5.1393 | 4.8342 | 5.2031
Spatial (+comm.) | 1.4 | 1.5846 | 3.3072 | 4.7067 | 0.95 | 1.6438 | 2.104
LSSD (+reuse.) | 1.4848 | 1.8047 | 4.1473 | 3.533 | 2.4576 | 3.1238 | 2.6444
blank2
blank1
NPU (DSA) | 8.75 | 10.3077 | 17.2926 | 16.5554 | 12.1125 | 10.8438 | 12.2574
LSSDN vs. NPU
Baseline – 4 wide OOO core (Intel 3770K)
N
Notes: Core + Sig  1.7x
SIMD  7x
CGRA  9x
Reuse  11.5x

## Slide 20
Performance Analysis (2)
Chart: Speedup
| IME | DOG | EXTR. | FME | Geometric Mean
LP core + FUs (+comp.) | 0.1199 | 0.09409 | 0.0849 | 0.1009 | 0.099149
SIMD (+concur.) | 3.7171 | 2.8049 | 2.4313 | 3.1288 | 2.9843
Spatial (+comm.) | 32.245 | 13.0047 | 19.6707 | 17.5664 | 19.6004
LSSD (+reuse.) | 11.6445 | 1.3522 | 10.4318 | 4.9808 | 6.163
blank1
blank2
blank3
Conv. (domain-acccel) | 38.254 | 20.9771 | 35.3521 | 22.3275 | 28.2111
C
LSSDc vs. Conv.
(1 Tile)
Chart: Speedup
| conv1 | pool1 | class1 | conv2 | conv3 | pool3 | class3 | conv4 | conv5 | pool5 | GeoMean
LP core + Sig. (+comp.) | 0.22734 | 1.1044 | 0.20586 | 0.39404 | 0.41349 | 1.3529 | 0.49191 | 0.40973 | 0.24285 | 1.0795 | 0.47639
8-Tile (+concur.) | 1.5914 | 7.731 | 1.441 | 2.7583 | 2.8944 | 9.4706 | 3.4434 | 2.8681 | 1.7 | 7.5562 | 3.3347
SIMD (+concur.) | 56.3798 | 8.8355 | 51.0531 | 47.2849 | 102.5449 | 53.1764 | 121.9933 | 101.6129 | 60.2274 | 8.6356 | 51.3888
Spatial (+comm.) | 26.4539 | 0 | 23.8 | 22.926 | 48.1149 | 0 | 57.2403 | 47.6776 | 28.2592 | 0 | 16.5398
LSSD (+reuse.) | 79.6728 | 0 | 45.9 | 57.4358 | 144.9108 | 0 | 110.6645 | 139.7338 | 54.5476 | 0 | 34.9587
blank1
blank2
blabnk3
blank4
DianNao (domain-acccel) | 174.5955 | 18.7754 | 158.1 | 151.3117 | 317.5585 | 23 | 377.7857 | 314.6723 | 186.5106 | 18.3507 | 108.8288
D
LSSDD vs. DianNao
(8 Tiles)
Chart: Speedup
| q1 | q2 | q3 | q4 | q5 | q6 | q17 | q10 | q15 | q16 | q17 | GM
LP core + SFUs (+comp.) | 15.1464 | 85.1409 | 13.4594 | 19.2165 | 4.4296 | 15.3257 | 4.1783 | 4.6616 | 24.5196 | 58.1734 | 11.1292 | 14.7144
4-Tile (+concur.) | 45.411 | 194.0066 | 35.494 | 45.7601 | 11.602 | 45.9413 | 10.9398 | 10.3447 | 72.1946 | 122.1649 | 33.1729 | 38.2799
SIMD (+concur.) | 135.6535 | 615.6754 | 92.3035 | 81.5204 | 27.0759 | 168.3682 | 27.8345 | 22.2086 | 178.7332 | 60.4818 | 39.3581 | 84.0034
LSSD (+comm.) | 62.4929 | 0.4974 | 90.7516 | 37.328 | 3.095 | 176.7822 | 7.1854 | 0.28304 | 112.6348 | 0.68423 | 5.9585 | 30.593
blank1
blank2
blank3
basl
ads
Q100 (domain-acccel) | 190.62 | 471.281 | 125.907 | 159.6399 | 99.9728 | 161.07 | 122.2967 | 168.0406 | 179.1163 | 334.132 | 107.3691 | 171.7656
Q
LSSDQ vs. Q100
(4 Tiles)
Baseline – 4 wide OOO core (Intel 3770K)
Domain Provisioned LSSDs
Performance: LSSD able to match DSA
Main contributor to speedup: Concurrency

## Slide 21
Domain Provisioned LSSDs
LSSD area & power compared to a single DSA ?

## Slide 22
Area Analysis
Chart: Normalized Area
| LSSDN | NPU | LSSDC | Conv. | LSSDD | DianNao | LSSDQ | Q100
 | 1.2 | 1 | 1.7 | 1 | 3.8 | 1 | 0.5 | 1
1.2x
1.7x
3.8x
0.5x
Domain Provisioned LSSDs
LSSDN
NPU
LSSDC
Conv.
LSSDD
DianNao
LSSDQ
Q100
Domain provisioned LSSD overhead
1x – 4x worse in Area
*Detailed area breakdown in paper
Notes: For NPU, same area as DSA. 1.6x more power
For Conv, 1.3x more area and 4.1x more power (Conv – 10bit datapath width)
LSSD alone is around 40x lower area/power than OOO

## Slide 23
Power Analysis
Chart: Normalized Power
| LSSDN | NPU | LSSDC | Conv. | LSSDD | DianNao | LSSDQ | Q100
 | 2 | 1 | 3.6 | 1 | 4.1 | 1 | 0.6 | 1
2x
3.6x
4.1x
0.6x
Domain Provisioned LSSDs
LSSDN
NPU
LSSDC
Conv.
LSSDD
DianNao
LSSDQ
Q100
Domain provisioned LSSD overhead
2x – 4x worse in Power
*Detailed power breakdown in paper

## Slide 24
Balance LSSD design
Area and power of LSSDBalanced design, when multiple domains mapped ?

## Slide 25
Chart: 
| LSSDB | Multi-DSA
 | 2.5 | 1
Chart: Normalized Area
| LSSDB | Multi-DSA
 | 0.6 | 1
0.6x
2.5x
LSSDBalanced Analysis
LSSDB
Multi-DSA
LSSDB
Multi-DSA
Area
Power
Balance LSSD design overheads
Area efficient than multiple DSAs
2.5x worse in Power than multiple DSAs

## Slide 26: Outline
Introduction and Motivation
Principles of architectural specialization
  Embodiment of principles in DSAs
Architecture for programmable specialization (LSSD)
Evaluation of LSSD with 4 DSAs (Performance, power & area)
System-level energy efficiency tradeoffs with LSSD and DSA
Speedup
Energy
Computation
Data Reuse
Concurrency
Coordination
Communication
Core
System Bus
$
Memory
Accel.

## Slide 27
LSSD’s power overhead of
2x - 4x matter in a system with accelerator?
In what scenarios you want to build
DSA over LSSD?

## Slide 28: Energy Efficiency Tradeoffs
Accel. energy
System energy
Core energy
Pacc * (U/S) * t
Pcore * (1 - U) * t
Psys * (1 – U + U/S) * t
E =
+
+
S: accelerator’s speedup
U: accelerator utilization
Overall energy of the computation executed on system
*Power numbers are example representation
t: execution time
OOO Core
System with accelerator
System Bus
Pcore: 5W
Psys: 5W
Pacc: 0.1 – 5W
System power
Core power
Accel. power
Caches
Memory
Accel.
(LSSD or DSA)

## Slide 29
Speeduplssd = Speedupdsa (Speedup w.r.t OOO)
Energy Efficiency Gains of
LSSD & DSA over OOO core
Chart: Accelerator Speedup w.r.t OOO core
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50
U = 1 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40 | 42 | 44 | 46 | 48 | 50 | 52 | 54 | 56 | 58 | 60 | 62 | 64 | 66 | 68 | 70 | 72 | 74 | 76 | 78 | 80 | 82 | 84 | 86 | 88 | 90 | 92 | 94 | 96 | 98 | 100
U = 0.95 | 1.9048 | 3.4783 | 4.8 | 5.9259 | 6.8966 | 7.7419 | 8.4848 | 9.1429 | 9.7297 | 10.2564 | 10.7317 | 11.1628 | 11.5556 | 11.9149 | 12.2449 | 12.549 | 12.8302 | 13.0909 | 13.3333 | 13.5593 | 13.7705 | 13.9683 | 14.1538 | 14.3284 | 14.4928 | 14.6479 | 14.7945 | 14.9333 | 15.0649 | 15.1899 | 15.3086 | 15.4217 | 15.5294 | 15.6322 | 15.7303 | 15.8242 | 15.914 | 16 | 16.0825 | 16.1616 | 16.2376 | 16.3107 | 16.381 | 16.4486 | 16.5138 | 16.5766 | 16.6372 | 16.6957 | 16.7521 | 16.8067
U = 0.9 | 1.8182 | 3.0769 | 4 | 4.7059 | 5.2632 | 5.7143 | 6.087 | 6.4 | 6.6667 | 6.8966 | 7.0968 | 7.2727 | 7.4286 | 7.5676 | 7.6923 | 7.8049 | 7.907 | 8 | 8.0851 | 8.1633 | 8.2353 | 8.3019 | 8.3636 | 8.4211 | 8.4746 | 8.5246 | 8.5714 | 8.6154 | 8.6567 | 8.6957 | 8.7324 | 8.7671 | 8.8 | 8.8312 | 8.8608 | 8.8889 | 8.9157 | 8.9412 | 8.9655 | 8.9888 | 9.011 | 9.0323 | 9.0526 | 9.0722 | 9.0909 | 9.1089 | 9.1262 | 9.1429 | 9.1589 | 9.1743
U = 0.75 | 1.6 | 2.2857 | 2.6667 | 2.9091 | 3.0769 | 3.2 | 3.2941 | 3.3684 | 3.4286 | 3.4783 | 3.52 | 3.5556 | 3.5862 | 3.6129 | 3.6364 | 3.6571 | 3.6757 | 3.6923 | 3.7073 | 3.7209 | 3.7333 | 3.7447 | 3.7551 | 3.7647 | 3.7736 | 3.7818 | 3.7895 | 3.7966 | 3.8033 | 3.8095 | 3.8154 | 3.8209 | 3.8261 | 3.831 | 3.8356 | 3.84 | 3.8442 | 3.8481 | 3.8519 | 3.8554 | 3.8588 | 3.8621 | 3.8652 | 3.8681 | 3.871 | 3.8737 | 3.8763 | 3.8788 | 3.8812 | 3.8835
Pdsa ≈ 0.0W
Chart: Accelerator Speedup w.r.t OOO core
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50
U = 1 | 1.8182 | 3.6364 | 5.4545 | 7.2727 | 9.0909 | 10.9091 | 12.7273 | 14.5455 | 16.3636 | 18.1818 | 20 | 21.8182 | 23.6364 | 25.4545 | 27.2727 | 29.0909 | 30.9091 | 32.7273 | 34.5455 | 36.3636 | 38.1818 | 40 | 41.8182 | 43.6364 | 45.4545 | 47.2727 | 49.0909 | 50.9091 | 52.7273 | 54.5455 | 56.3636 | 58.1818 | 60 | 61.8182 | 63.6364 | 65.4545 | 67.2727 | 69.0909 | 70.9091 | 72.7273 | 74.5455 | 76.3636 | 78.1818 | 80 | 81.8182 | 83.6364 | 85.4545 | 87.2727 | 89.0909 | 90.9091
U = 0.95 | 1.7467 | 3.2129 | 4.461 | 5.5363 | 6.4725 | 7.2948 | 8.0229 | 8.6721 | 9.2545 | 9.78 | 10.2564 | 10.6904 | 11.0874 | 11.4519 | 11.7878 | 12.0983 | 12.3862 | 12.6538 | 12.9032 | 13.1363 | 13.3545 | 13.5593 | 13.7519 | 13.9332 | 14.1044 | 14.2661 | 14.4192 | 14.5644 | 14.7022 | 14.8331 | 14.9578 | 15.0766 | 15.1899 | 15.2981 | 15.4015 | 15.5005 | 15.5954 | 15.6863 | 15.7735 | 15.8573 | 15.9378 | 16.0153 | 16.0898 | 16.1616 | 16.2308 | 16.2976 | 16.3621 | 16.4243 | 16.4844 | 16.5426
U = 0.9 | 1.6807 | 2.8777 | 3.7736 | 4.4693 | 5.0251 | 5.4795 | 5.8577 | 6.1776 | 6.4516 | 6.689 | 6.8966 | 7.0796 | 7.2423 | 7.3879 | 7.5188 | 7.6372 | 7.7449 | 7.8431 | 7.9332 | 8.016 | 8.0925 | 8.1633 | 8.229 | 8.2902 | 8.3472 | 8.4006 | 8.4507 | 8.4977 | 8.542 | 8.5837 | 8.6231 | 8.6604 | 8.6957 | 8.7291 | 8.761 | 8.7912 | 8.82 | 8.8475 | 8.8737 | 8.8988 | 8.9227 | 8.9457 | 8.9677 | 8.9888 | 9.009 | 9.0285 | 9.0472 | 9.0652 | 9.0825 | 9.0992
U = 0.75 | 1.5094 | 2.1918 | 2.5806 | 2.8319 | 3.0075 | 3.1373 | 3.237 | 3.3161 | 3.3803 | 3.4335 | 3.4783 | 3.5165 | 3.5495 | 3.5783 | 3.6036 | 3.6261 | 3.6461 | 3.6641 | 3.6804 | 3.6952 | 3.7086 | 3.7209 | 3.7323 | 3.7427 | 3.7523 | 3.7613 | 3.7696 | 3.7774 | 3.7847 | 3.7915 | 3.7979 | 3.8039 | 3.8095 | 3.8149 | 3.8199 | 3.8247 | 3.8292 | 3.8335 | 3.8376 | 3.8415 | 3.8453 | 3.8488 | 3.8522 | 3.8554 | 3.8585 | 3.8615 | 3.8643 | 3.8671 | 3.8697 | 3.8722
Plssd = 0.5W
500mW Power overhead
Baseline – 4 wide OOO core
At higher speedups (S  ∞), energy efficiency gains ‘capped’ due to large system power

## Slide 30
LSSD’s power overhead of
2x - 4x matter in a system with accelerator?
When Psys >> Plssd, 2x - 4x power overheads of LSSD become inconsequential

## Slide 31
Energy Efficiency Gains of
DSA over LSSD
Chart: Accelerator Speedup w.r.t OOO core
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50
U = 1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1
U = 0.95 | 1.0905 | 1.0826 | 1.076 | 1.0704 | 1.0655 | 1.0613 | 1.0576 | 1.0543 | 1.0514 | 1.0487 | 1.0463 | 1.0442 | 1.0422 | 1.0404 | 1.0388 | 1.0373 | 1.0358 | 1.0345 | 1.0333 | 1.0322 | 1.0311 | 1.0302 | 1.0292 | 1.0284 | 1.0275 | 1.0268 | 1.026 | 1.0253 | 1.0247 | 1.0241 | 1.0235 | 1.0229 | 1.0224 | 1.0218 | 1.0213 | 1.0209 | 1.0204 | 1.02 | 1.0196 | 1.0192 | 1.0188 | 1.0184 | 1.0181 | 1.0178 | 1.0174 | 1.0171 | 1.0168 | 1.0165 | 1.0162 | 1.016
U = 0.9 | 1.0818 | 1.0692 | 1.06 | 1.0529 | 1.0474 | 1.0429 | 1.0391 | 1.036 | 1.0333 | 1.031 | 1.029 | 1.0273 | 1.0257 | 1.0243 | 1.0231 | 1.022 | 1.0209 | 1.02 | 1.0191 | 1.0184 | 1.0176 | 1.017 | 1.0164 | 1.0158 | 1.0153 | 1.0148 | 1.0143 | 1.0138 | 1.0134 | 1.013 | 1.0127 | 1.0123 | 1.012 | 1.0117 | 1.0114 | 1.0111 | 1.0108 | 1.0106 | 1.0103 | 1.0101 | 1.0099 | 1.0097 | 1.0095 | 1.0093 | 1.0091 | 1.0089 | 1.0087 | 1.0086 | 1.0084 | 1.0083
U = 0.75 | 1.06 | 1.0429 | 1.0333 | 1.0273 | 1.0231 | 1.02 | 1.0176 | 1.0158 | 1.0143 | 1.013 | 1.012 | 1.0111 | 1.0103 | 1.0097 | 1.0091 | 1.0086 | 1.0081 | 1.0077 | 1.0073 | 1.007 | 1.0067 | 1.0064 | 1.0061 | 1.0059 | 1.0057 | 1.0055 | 1.0053 | 1.0051 | 1.0049 | 1.0048 | 1.0046 | 1.0045 | 1.0043 | 1.0042 | 1.0041 | 1.004 | 1.0039 | 1.0038 | 1.0037 | 1.0036 | 1.0035 | 1.0034 | 1.0034 | 1.0033 | 1.0032 | 1.0032 | 1.0031 | 1.003 | 1.003 | 1.0029
Speeduplssd = Speedupdsa (Speedup w.r.t OOO)
Baseline – LSSD
is no more than 10% even at 100% utilization
At lower speedups, DSA’s energy efficiency gains 6 - 10% over LSSD
At higher speedups, benefits of DSA less than 5% on energy efficiency
= (1 / DSA energy) / (1 / LSSD energy)
= LSSD energy / DSA energy

## Slide 32
In what scenarios you want to build
DSA over LSSD?
Only when application speedups are small &
small energy efficiency gains too important

## Slide 33: Conclusion
5 common principles for architectural specialization
Programmable architecture (LSSD) composed of simple uArch. mechanisms embodying the principles
LSSD competitive with DSA performance and overheads of only up to 4x in area and power
Power overhead inconsequential when system-level energy tradeoffs considered
LSSD as a baseline for future accelerator research
5 stage pipelined processor (ISCA’ 87)
Programmable Architecture

## Slide 34: Back Up Slides

## Slide 35
 | Synthesis – Time | Run – Time
Concurrency | No. of LSSD Units | Power-gating unused LSSD Units
Computation | Spatial fabric FU mix | Scheduling of spatial fabric and core
Communication | Enabling spatial datapath elements, & SRAM interface widths | Config. of spatial datapath, switches and ports, memory access pattern
Data Reuse | Scratchpad (SRAM) size | Scratchpad used as DMA/reuse buffer
Design-Time vs. Runtime Decisions
Notes: Implement the principles in general way

## Slide 36: LSSD Design Point Selection
Design | Concurrency | Computation | Comm. | Data Reuse | No. of LSSD Units
LSSDN | 24-tile CGRA (8 Mul, 8 Add, 1 Sigmoid) | 2k x 32b sigmoid lookup table | 32b CGRA; 256b SRAM interface | 2k x 32b weight buffer | 1
LSSDC | 64-tile CGRA (32 Mul/Shift, 32 Add/logic) | Standard 16b FUs | 16b CGRA; 512b SRAM interface | 512 x 16b SRAM for inputs | 1
LSSDD | 64-tile CGRA (32 Mul, 32 Add, 2 Sigmoid) | Piecewise linear sigmoid unit | 32b CGRA; 512b SRAM interface | 2k x 16b SRAMs for inputs | 8
LSSDQ | 32-tile CGRA (16 ALU, 4 Agg, 4 Join) | Join + Filter units | 64b CGRA; 256b SRAM interface | SRAMs for buffering | 4
LSSDB | 32-tile CGRA (Combination of above) | Combination of above FUs | 64b CGRA; 512b SRAM interface | 4KB SRAM | 8

## Slide 37
Accelerator Workloads
DNN
Database Streaming
Neural Approx.
Convolution
1. Ample Parallelism 2. Regular Memory
3. Large Datapath 4. Computation Heavy

## Slide 38: LSSD in Practice
Perf.
App. 1: ...
App. 2: ...
App. 3: ...
Area goal: ...
Power goal: ...
Synthesis
Performance
Requirements
Design Synthesis
FU Types
No. of FUs
Spatial fabric size
No. of LSSD tiles
Programming
For each application:
Write Control Program
(C Prog. + Annotations)
Write Datapath Program
(spatial scheduling compiler framework)
1.
2.
LSSD
H/W
Constraints
Design
decisions
Designer

## Slide 39: Programming LSSD
#pragma lssd cores 2
#pragma reuse-scratchpad weights
void nn_layer(int num_in, int num_out,
const float* weights,
const float* in,
const float* out )
{
for (int j = 0; j < num_out; ++j)
{
for (int i = 0; i < num_in; ++i)
{
out[j] += weights[j][i] *in[i];
}
out[j] = sigmoid(out[j]);
}
}
Pragmas
Spatial Fabric
Output Interface
Input Interface
Scratchpad
DMA
Memory
Low-power Core
D$
x
x
x
x
x
x
+
+
+
x
x
+
+
+
+
Ʃ
Loop Parallelize, Insert Communication,
Modulo Schedule
Resize Computation (Unroll), Extract Computation Subgraph, Spatial Schedule
LSSD
Insert data transfer

## Slide 40: Power & Area Analysis (1)
LSSDN
1.2x more Area than DSA
2x more Power than DSA
1.7x more Area than DSA
3.6x more Power than DSA
LSSDC
Notes: For NPU, same area as DSA. 1.6x more power
For Conv, 1.3x more area and 4.1x more power (Conv – 10bit datapath width)
LSSD alone is around 40x lower area/power than OOO

## Slide 41: Power & Area Analysis (2)
LSSDD
3.8x more Area than DSA
4.1x more Power than DSA
0.5x more Area than DSA
0.6x more Power than DSA
LSSDQ
Notes: For Q100, we are better in area by 0.2x and 0.3x better in power
For DianNao, we are 2.6x worse in area and 2.4x in power
LSSD is around 6x to 90x lower area and 5x to 40x lower power than OOO

## Slide 42
LSSD Area & Power Numbers
 |  | Area (mm2) | Power (mW)
Neural Approx. | LSSDN | 0.37 | 149
 | NPU | 0.30 | 74
Stencil | LSSDC | 0.15 | 108
 | Conv. Engine | 0.08 | 30
Deep Neural. | LSSDD | 2.11 | 867
 | DianNao | 0.56 | 213
Database Streaming | LSSDQ | 1.78 | 519
 | Q100 | 3.69 | 870
 | LSSDBalanced | 2.74 | 352
*Intel Ivybridge 3770K CPU 1 core Area – 12.9mm2 | Power – 4.95W
*Source: http://www.anandtech.com/show/5771/the-intel-ivy-bridge-core-i7-3770k-review/3
+Estimate from die-photo analysis and block diagrams from wccftech.com
*Intel Ivybridge 3770K iGPU 1 execution lane Area – 5.75mm2
+AMD Kaveri APU Tahiti based GPU 1CU Area – 5.02mm2

## Slide 43: Power & Area Analysis (3)
2.7x more Area than DSAs
2.4x more Power than DSAs
0.6x more Area than DSA
2.5x more Power than DSA
LSSDB  Balanced LSSD design

## Slide 44
Energy Efficiency Gains of
DianNao over LSSD
SpeedupLSSD = SpeedupDianNao (Speedup w.r.t OOO)
Chart: Accelerator Speedup w.r.t OOO
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50
U = 1 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255 | 1.1255
U = 0.95 | 1.114 | 1.1044 | 1.0963 | 1.0894 | 1.0834 | 1.0781 | 1.0735 | 1.0694 | 1.0657 | 1.0624 | 1.0594 | 1.0567 | 1.0543 | 1.052 | 1.0499 | 1.048 | 1.0462 | 1.0445 | 1.043 | 1.0416 | 1.0402 | 1.0389 | 1.0378 | 1.0366 | 1.0356 | 1.0346 | 1.0337 | 1.0328 | 1.0319 | 1.0311 | 1.0304 | 1.0297 | 1.029 | 1.0283 | 1.0277 | 1.0271 | 1.0265 | 1.0259 | 1.0254 | 1.0249 | 1.0244 | 1.0239 | 1.0235 | 1.0231 | 1.0226 | 1.0222 | 1.0218 | 1.0215 | 1.0211 | 1.0207
U = 0.9 | 1.1034 | 1.088 | 1.0765 | 1.0677 | 1.0607 | 1.0551 | 1.0503 | 1.0464 | 1.043 | 1.0401 | 1.0375 | 1.0353 | 1.0333 | 1.0315 | 1.0299 | 1.0284 | 1.0271 | 1.0259 | 1.0248 | 1.0238 | 1.0229 | 1.0221 | 1.0213 | 1.0205 | 1.0198 | 1.0192 | 1.0186 | 1.018 | 1.0175 | 1.017 | 1.0165 | 1.016 | 1.0156 | 1.0152 | 1.0148 | 1.0145 | 1.0141 | 1.0138 | 1.0135 | 1.0132 | 1.0129 | 1.0126 | 1.0123 | 1.0121 | 1.0118 | 1.0116 | 1.0114 | 1.0112 | 1.011 | 1.0108
U = 0.75 | 1.0765 | 1.0551 | 1.043 | 1.0353 | 1.0299 | 1.0259 | 1.0229 | 1.0205 | 1.0186 | 1.017 | 1.0156 | 1.0145 | 1.0135 | 1.0126 | 1.0118 | 1.0112 | 1.0106 | 1.01 | 1.0095 | 1.0091 | 1.0087 | 1.0083 | 1.008 | 1.0077 | 1.0074 | 1.0071 | 1.0069 | 1.0066 | 1.0064 | 1.0062 | 1.006 | 1.0058 | 1.0057 | 1.0055 | 1.0054 | 1.0052 | 1.0051 | 1.005 | 1.0048 | 1.0047 | 1.0046 | 1.0045 | 1.0044 | 1.0043 | 1.0042 | 1.0041 | 1.004 | 1.004 | 1.0039 | 1.0038

## Slide 45: Does Accelerator power matter?
At Speedups > 10x, DSA eff. is around 5%, when accelerator power == core power
At smaller speedups, makes a bigger difference, up to 35%