## Slide 1: MIAOW: An Open Source RTL Implementation of a GPGPU
Vinay Gangadhar, Raghu Balasubramaniam, Mario Drumond, Ziliang Guo, Jai Menon, Cherin Joseph, Robin Prakash, Sharath Prasad, Pradip Vallathol, Karu Sankaralingam
www.miaowgpu.org
Vertical Research Group
University of Wisconsin - Madison

## Slide 2: MIAOW Open Source GPGPU
AMD Southern Islands ISA-based GPGPU
Transformative for Academic GPU research
Contribution to Industry
MIAOW as a Research tool –
  RTL codebase, Verification and Simulation toolchain
  Support for workloads
MIAOW - Many-core Integrated Accelerator Of Wisconsin
Notes: First publicly available open source GPGPU - MIAOW
Embodies its principles that it can be transformative for GPU research in Academia with RTL implementation
We also envision that this research tool could be of help to industry in applying new research ideas and exploring the uarch impact

## Slide 3: Outline
Open Source GPGPU
Micro-Architecture
Realism
Research Flexibility
Conclusion

## Slide 4
MIAOW Overview
MIAOW has 32 Compute Units (CUs)

## Slide 5
Hardware Organization
In-order + Vector core
Single Issue
40
16-wide vector ALUs
LSU – Memory operations
Wavefronts
Compute Unit
Notes: -- Hybrid of an in-order + vector core all fed by single instruction supply with MT support

## Slide 6
ISA Summary
95 instructions – AMD Southern Islands ISA
No Graphics support
support
Notes: The instructions selected are based on application profiling , operations in datapath and practically implementable by a small design team
Program control – predication and branch instructions
32 bit data support

## Slide 7: MIAOW Design Approach
(a) Full ASIC Design
Low Flexibility,
High Cost,
High Realism
Medium Flexibility,
Low Cost,
Long Design Time,
Medium Realism
High Flexibility,
Low Cost,
Short Design Time,
Flexible Realism
(b) Mapped to FPGA
(c) Hybrid Design
Notes: Spectrum of Implementation strategizies and tradeoffs MIAOW follows
Shaded portion indicates Register file and SRAM storage
FPGA has resource constraints

## Slide 8: Outline
Open Source GPGPU
Micro-Architecture
Realism
Research Flexibility
Conclusion

## Slide 9
MIAOW Realism
MIAOW
Kaveri
No graphics and
texture support
in MIAOW
Notes: -- MIAOW should be a realistic implementation of a GPU resembling principles and implementation of industry GPU
-- Area and Power estimation done to assure that our design decisions reflect that

## Slide 10
Realism – Software Compatibility
Runs unmodified OpenCL programs
All OpenCL benchmarks
Many Rodinia benchmarks
Easily extendable to add any missing instruction from ISA

## Slide 11
Realism – FPGA Synthesis
Xilinx Virtex 7 based
Maps 1 CU
Explores feasibility of Design
Benchmark prototyping – Ongoing work
Notes: - ASIC Chip not built yet, but we do have a synthesized version of FPGA
Has embedded microblaze soft core processor connected to Compute unit via AXI interface
300K LUTs and 1K Block RAMs

## Slide 12: Outline
Open Source GPGPU
Micro-Architecture
Realism
Research Flexibility
Conclusion

## Slide 13
Research Flexibility
Direction | Research Idea | MIAOW enabled findings
Traditional µarch | Thread-block compaction (TBC) | Implemented TBC in RTL Significant design complexity Increase in Critical Path length
Ultra-threaded Dispatcher modified
Micro-architecture impacted
Direction | Research Idea | MIAOW enabled findings
New Directions | Circuit-Failure Prediction (Aged SDMR) | Implemented entirely in µarch Works elegantly in GPUs Small area, power overheads
 | Timing Speculation (TS) | Quantifies error-rate on GPU
Compute Units modified
Micro-architectural Gates + Delay elements impacted
Compute Units + Storage modified
Delay elements impacted
Direction | Research Idea | MIAOW enabled findings
Validation of Simulator studies | Transient Fault Injection | RTL Level Fault Injection More Gray area than CPUs Silent data corruption seen
Notes: Physical design perspective to traditional uarch
It should be flexible enough to accommodate research studies of various types
Compare the implementation to simulator studies

## Slide 14
Research Flexibility
Direction | Research Idea | MIAOW enabled findings
Traditional µarch | Thread-block compaction (TBC) | Implemented TBC in RTL Significant design complexity Increase in Critical Path length
New Directions | Circuit-Failure Prediction (Aged SDMR) | Implemented entirely in µarch Works elegantly in GPUs Small area, power overheads
 | Timing Speculation (TS) | Quantifies error-rate on GPU
Validation of Simulator studies | Transient Fault Injection | RTL Level Fault Injection Silent data corruption seen
Notes: Physical design perspective to traditional uarch
It should be flexible enough to accommodate research studies of various types
Compare the implementation to simulator studies

## Slide 15
Conclusion
MIAOW provides transformative capability for GPU research
More community support  First Open Source Silicon GPU Chip
Can it help kick-start an Open Source hardware movement?
Are Open Source hardware chips feasible?
www.miaowgpu.org
Notes: -- It should be flexible enough to accommodate research studies of various types

## Slide 16
Back Up Slides
Notes: -- It should be flexible enough to accommodate research studies of various types

## Slide 17
Area Estimates
Total Area: 15 mm2
SRAM based RF: 9mm2

## Slide 18
Power Estimates
Total Power: 1.1 W

## Slide 19
Performance Estimates
Compared to NVIDIA Fermi 1-SM GPU
CPI close on 3 benchmarks
CPI | DMin | DMax | BinS | BSort | MatT | PSum | Red | SLA
Scalar | 1 | 3 | 3 | 3 | 3 | 3 | 3 | 3
Vector | 1 | 6 | 5.4 | 2.1 | 3.1 | 5.5 | 5.4 | 5.5
Memory | 1 | 100 | 14.1 | 3.8 | 4.6 | 6.0 | 6.8 | 5.5
Overall | 1 | 100 | 5.1 | 1.2 | 1.7 | 3.6 | 4.4 | 3.0
NVIDIA | 1 | - | 20.5 | 1.9 | 2.1 | 8 | 4.7 | 7.5

## Slide 20
Verification Methodology
Emulator – Multi2sim Heterogeneous Simulator