## Slide 1: PENN: Programmable Engine for Neural Networks
Vinay Gangadhar, Sharmila Shridhar,
Anilkumar Ranganagoudra, Chandana Hosamane
ECE 751 Project Presentation
Fall 2015
University of Wisconsin - Madison

## Slide 2: Executive Summary
Design of a Programmable Accelerator/Engine for Neural Networks (NNs)
A flexible programming software interface to map NNs like DNN, CNN or any ML network
A 2 level configurability:
  Synthesis
  Runtime
End-to-End implementation with RISCV Toolchain (Ongoing)
Comparison with a Domain Specific Accelerator (DSA) -- DianNao with preliminary performance, area and power results

## Slide 3: Introduction
Neural networks – A new computing paradigm
Deep neural, Convolutional, Recurring and other Neural networks
High computational throughput and energy efficiency requirements
Domain/Application Specific Accelerators and ASIC for the help
  Ex: DianNao Bros., NPU, Custom ASICs, Microsoft Catapult for CNN etc.
DNN  Focus of the project
Source: DaDianNao
Notes: Neural networks is an emerging computing paradigm in last decade with resurgence of back-propogation and efficient perceptron based designs.
It is no longer the case the desktop and servers or even GPUs drive the computing needs of future NN based applications

## Slide 4: Outline
Introduction
Motivation/Problem
Insights – Principles of Specialization
PENN Overview
Programmable Software Interface
PENN Architecture
Implementation & Preliminary Modeling Results
Conclusion
Notes: Now with that introduction, we will now see what is the problem with DNN DSAs and why there is a need for programmability

## Slide 5
Programs
General Language
General ISA
Compiler
General Hardware
Domain-Specific
Programs
Specialized
Hardware
Traditional
Accelerator
(DSA)
(tiny HW/SW
Interface)
10-1000X Performance/Power or Performance/Area
(completely lose generality/programmability)

## Slide 6
Programs
Configurable
Hardware
Traditional
Specialization
Programs
General Language
General ISA
Compiler
(customizable + flexible
HW/SW Interface)
Synthesis Interface
General Hardware
Can we get 10-1000x?
Is it still general purpose enough?
(“specialized”)
DNN
Goal: To achieve efficiency of DSA with Programmability
Notes: What you need is some sort of specialized program with a customizable and flexible interface exposed to programmers
We also add an extra level of interface called synthesis interface here for more reconfigurability

## Slide 7: Outline
Introduction
Motivation/Problem
Insights – Principles of Specialization
PENN Overview
Programmable Software Interface
PENN Architecture
Implementation & Preliminary Modeling Results
Conclusion
Notes: Now with that introduction, we will now see what is the problem with DNN DSAs and why there is a need for programmability

## Slide 8: How to design a Specialized Architecture for DNNs?
DNN Programs
Regular Memory
Large Datapath
Ample Parallelism
Specialization Principles:
Communication
Concurrency
Compute
Data Reuse
Coordination

## Slide 9: PENN Overview
Communication
Concurrency
Compute
Data Reuse
Coordination
CGRA
(Timing based)
Scratchpad
DMA
Output Controller
Tiny Core
(RISC V SODOR)
D$
Input Controller
× N Tiles
CGRA
CGRA
Cycle 7
FU
Cycle 7
…
FU
FU
FU

## Slide 10: Configuring PENN
Synthesis Time
  Functional Unit Mix
  Datapath Width
  Scratchpad Line Size
  Number of PENN units
Run-Time
  Datapath Configuration
  Memory Access Pattern
  Scratchpad Storage
[fu-model]
FU_TYPE FU_ADD: Add16:0
FU_TYPE FU_MUL: Mul16:0
FU_TYPE FU_SPC: Sig16:0, Div16:1
OUT_DIRECTIONS: SE:0
[switch-model]
OUT_DIRECTIONS: N:0 NE:1 E:2 SE:3
S:4 SW:5 W:6 NW:7
[sub-model]
outs_per_switch: 3
ins_per_switch: 6
[dpath-model]
FU_MUL FU_ADD FU_MUL FU_ADD
FU_ADD FU_MUL FU_ADD FU_MUL
FU_MUL FU_ADD FU_MUL FU_ADD
FU_ADD FU_MUL FU_ADD FU_MUL
FU_MUL FU_ADD FU_MUL FU_SPC
[io-model]
VPORT_IN 0: 1:<3 5> 3:<5 7 9 11>
VPORT_IN 2: 4:<17 18>
SPORT_IN 0: 6:<19>
…

## Slide 11
1. Design Synthesis
Analyze DNN workloads
Define HW/SW interface and Synthesis Config.
2. Programming
Fit applications into HW/SW interface
Get the scheduler program for DFG
3. Runtime
Runtime configuration
Switch dynamically per DNN kernel
DNN 1
DNN 2
DNN 3
PENN
Config.
Programming Interface
Arch. Constraints
Using PENN Infrastructure
Configure for DNN Kernel 1
Scheduler program
DNN Kernels (modified)
Run
Kernel 1
Configure for DNN Kernel 2
Run
Kernel 2
Notes: FU Type, Spatial Array size, datapath width

## Slide 12: Outline
Introduction
Motivation/Problem
Insights – Principles of Specialization
PENN Overview
Programmable Software Interface
PENN Architecture
Implementation & Preliminary Modeling Results
Conclusion
Notes: Now with that introduction, we will now see what is the problem with DNN DSAs and why there is a need for programmability

## Slide 13: Programming Interface Definitions
mem_addr: starting address to access (can be GPP register that
holds address)
stride: memory stride [Ni x Nx]
access_size: length of stride access [Ni x Kx]
num_strides: Number of strides [Ky]
scratch_offset: offset value of scratchpad to load to/from
mem_addr
access_size
memory stride
num_strides

## Slide 14: PENN Program Macros
CGRA
(Timing based)
Scratchpad
DMA
Output Controller
Input Controller
CGRA
CGRA
Main Memory
IC_DMA_SCRATCH_LOAD
IC_SCRATCH_READ
IC_DMA_READ
OC_PENN_WRITE
OC_PENN_SCRATCH_WRITE
OC_BUF_DMA_WRITE
Other Misc. Macros for synchronization and Constant buffering not shown here
Notes: IC_DMA_SCRATCH_LOAD [access_size] [num_strides] [scratch_addr][word_offset]
IC_SCRATCH_READ [scratch_addr] [word_offset][port_type] [port_num]
IC_DMA_READ [mem_addr] [access_size] [num_strides] [port_type] [port_num]
OC_SB_WRITE [port_type] [port_num] [port_type] [port_num][num_strides]
OC_SB_SCRATCH_WRITE [port_type] [port_num][scratch_addr] [word_offset] [num_strides]
OC_BUF_DMA_WRITE [mem_addr] [access_size] [num-strides]

## Slide 15: PENN Example Workload
Example Classifier Program
Source: DianNao

## Slide 16: PENN Instructions
Extended RISCV Base 32bit ISA to encode PENN instructions
Major Operations Encoding
Example Instructions

## Slide 17: Outline
Introduction
Motivation/Problem
Insights – Principles of Specialization
PENN Overview
Programmable Software Interface
PENN Architecture Details
Implementation & Preliminary Modeling Results
Conclusion
Notes: Now with that introduction, we will now see what is the problem with DNN DSAs and why there is a need for programmability

## Slide 18: PENN Detailed Architecture

## Slide 19: PENN Architecture
Output Controller
SODOR
Core
D$
CGRA
(Timing based)
Input
FIFO
Output
FIFO
Wide Port
Interface
Input Controller
Scratchpad (4KB)
DMA
1 2 3 4 5 6 7 8
5
1
Input Elements Vector
62
73
84
To Data Fifos
Ready
Fifo
Ready
Logic
Ready
Full
Consume
CQ

## Slide 20: CGRA Fabric
Functional Unit can be: ALU, Multiplier, Sigmoid
FU mix can be configured at Synthesis time
Datapath schedule is configured at run-time
6x5 CGRA Fabric
CGRA Tile

## Slide 21: CGRA Run-time Configuration
Configuration streamed down from top rows of switches – 40bits for each CGRA tile
Command to DMA to stream the configuration (40b x 6 switches each cycle):
IC_DMA_CFG_READ [mem_addr] [access_size] [num_strides] [port_type] [port_num]
5 cycle config.
(30B/cycle)
cfg_mode=1
IC_DMA_CFG_READ

## Slide 22: Outline
Introduction
Motivation/Problem
Insights – Principles of Specialization
PENN Overview
Programmable Software Interface
PENN Architecture Details
Implementation & Preliminary Modeling Results
Conclusion
Notes: Now with that introduction, we will now see what is the problem with DNN DSAs and why there is a need for programmability

## Slide 23: PENN Implementation
Hardware in Chisel (Scala based)
Interface/Parameters exposed for Synthesis level configuration
Generates Verilog and C++ cycle acurate Simulator
Extended the scheduler framework of Nowatzki. et.al [*]
Timing based scheduling for CGRA
*Nowatzki et. Al, “A general constraint-centric scheduling framework for spatial architectures,” in PLDI 2013
Modified the RISCV GNU Assembler to handle the intrinsic functions
Macros are pre-processed as inline assembly
RISCV ISA Simulator (Spike) was extended to include new PENN instructions
Functionality of scheduled dataflow graph is checked here

## Slide 24: Evaluation & DNN Workloads
Same kernels as
in DianNao* paper
Performance results based on an Analytical Model (PENN Infrastructure still ongoing work)
Area and Power from Chisel generated Synthesized Verilog @32nm node
Compared with the DNN accelerator  DianNao
DianNao Perf. , area and power estimates from the paper [*] normalized to 32nm, 1GHz Freq.
*Chen et. al, DianNao: A SmallFootprint High-Throughput Accelerator for Ubiquitous Machine-Learning. In International Conference on
Architectural Support for Programming Languages and Operating Systems. ASPLOS’14.
Notes: In remaining classifier and convolutional workloads, PENN has slight overhead on managing DMA (instructions overhead)
8x from multi-tile, 32x SIMD
CGRA provides some additional benefit by reducing instruction management and a reuse buffer reduces cache contention

## Slide 25: Performance Results
Baseline  4-Wide OOO processor
Pooling Kernels max out on memory bandwidth
Maximum benefit from the Concurrency (SIMD + Multi-tile  ~49x)
Notes: In remaining classifier and convolutional workloads, PENN has slight overhead on managing DMA (instructions overhead)
8x from multi-tile, 32x SIMD
CGRA provides some additional benefit by reducing instruction management and a reuse buffer reduces cache contention  CGRA + SPM = 35%

## Slide 26: Area Results
Chart: 
| PENN-1 Tile Area (mm2)
Core + Cache | 0.09
CGRA Fabric | 0.114
IC + OC + Port Interface | 0.00058
Scratchpad (4KB) | 0.04
1 PENN Tile Area  0.24 mm2
@32nm & 1GHz Freq.
8 Tile –PENN | DianNao
1.95 | 0.56
Overall Area Comparison (mm2)
~3.5x Area Overhead
DianNao area normalized to 32nm @ 1GHz Frequency
Switches | FUs
0.109 | 0.0048
CGRA Fabric Breakdown (mm2)
36 Switches and 25 FUs

## Slide 27: Power Results
1 Tile Power  65.03mW
@32nm & 1GHz Freq.
8 Tile –PENN | DianNao
526.64 | 213
Overall Power Comparison (mW)
~2.5x Area Overhead
DianNao power normalized to 32nm @ 1GHz Frequency
Switches | FUs
10.2 | 7.6
CGRA Fabric Breakdown (mW)
36 Switches and 25 FUs
Chart: 
| PENN-1 Tile Power (mW)
Core + Cache | 41
CGRA Fabric | 17.8
IC + OC + Port Interface | 1.63
Scratchpad (4KB) | 5.4

## Slide 28: Challenges & Lessons Learned
H/W-S/W Co-design is challenging but Fun !!
  Future specialization engines will follow this technique
  Experience gained with assembler, static scheduler and simulator
CHISEL enables a nice parameterizable interface for exploring different design points
Scope for different acceleratable domains using PENN like H/W-S/W interface
  File compression, Regex matching, Database processing etc.
  Combined Area and Power overhead is amortized when multiple domains are mapped to PENN
A good study to push the limits of efficiency and still have programmability

## Slide 29: Conclusion
A flexible programmable engine for Neural Networks
  Configurable at 2 levels  Enabling wider design space exploration
Different types of NNs can be mapped with same H/W-S/W interface
DSA like performance with 2.5x Power and 3.5x Area overhead
  Overhead becomes smaller when multiple domains are mapped to this engine
Scope for other domains  Database processing, File compression, Regex all can have similar programming interface

## Slide 30: Back Up Slides

## Slide 31: Example Program

## Slide 32: Diannao – Machine Learning Accelerator
Diannao: accelerator for deep/convolutional neural networks.
Mapping of DNN/CNN to PENN:
  Two or four 16 16-bit elements reduction tree fed into CGRA.
  Scratchpad with input neurons can be re-used across multiple output neurons.
  Partial output sums buffered into scratchpad or output buffers
  CGRA is pipelined to compute 2 or 4 neuron-weight reduction tree per cycle.
Presumed Results: The design can match the performance of Diannao, though at somewhat larger area and power.
Diannao

## Slide 33: DianNao Example
Tn = 16, Ti = 16
Synapse stride_size: 16 x 16 x 2B
Neuron size: 16 X 2B
Scratchpad load: All neurons
DMA stream: All synapses
Partial Sums stored in Output buffers before being fed to sigmoid units

## Slide 34: RISCV Core (3 Stage SODOR)
SODOR Core commands:
To DMA (Stream Configuration bits directly)
To Input Controller (For loading Scratchpad and Input FIFOs)
TO Output Controller (For handling Output values)

## Slide 35: Workload Sizes
Benchmark | Accel. Blocks (in K Neurons) | Synapse Size (KB) | In Neuron Size (KB) | Out Neuron Size (KB)
conv1 | 30380 | 40 | 1491.25 | 2861.25
pool1 | 45.26 | 0 | 697.5 | 691.25
class1 | 0.12 | 7.5 | 1.88 | 64
conv2 | 3240 | 192500 | 181.25 | 152.5
conv3 | 460 | 110 | 40 | 55
pool3 | 8.19 | 0 | 40 | 31.25
class3 | 0.11 | 56 | 0.44 | 0.25
conv4 | 400 | 96.25 | 47.53 | 125
conv5 | 761270 | 2836 | 4351.25 | 6000
pool5 | 260 | 0 | 4062.5 | 4000