## Slide 1: Exploring the Potential of Heterogeneous Von Neumann / Dataflow Execution Models
Tony Nowatzki
Vinay Gangadhar
Karthikeyan Sankaralingam
University of Wisconsin - Madison

## Slide 2
Low ILP
High ILP
Low ILP
High ILP
Time
Program Execution
Due to Speculation
Very high/non-local parallelism
Von
Neumann
Explicit-
Dataflow
Explicit-Dataflow
Von Neumann
Best Suited Architecture:
Reason for high ILP:
Helpful Arch. Features:
Branch Prediction, speculative scheduling, fast recovery
Very-high issue width,
Very-large instruction window
Our Proposal:
Highly Speculative,
Modest ILP
High ILP,
Little Speculation

## Slide 3
Von
Neumann
Von
Neumann
Dual Issue OOO + 4 Others:
(Beret, CCores, bigLITTLE, In-place Loop)
5% Speedup,
20% Energy Efficiency
Von
Neumann
Explicit
Dataflow
Dual Issue OOO + SEED
-
30% Speedup,
70% Energy Efficiency
Related Work
Our Proposal

## Slide 4: Outline
Control
Memory
Describing why VonNeumann can complement Dataflow architectures
Leveraging program properties for efficient heterogeneous design
Performing a Design-Space Exploration
Across (Small, Medium, Big) VN Cores
Designing SEED: Specialization
Engine for Explicit-Dataflow
Speedup
Energy
Nested Loops
Von-
Neumann
Explicit
Dataflow
(General Purpose)
(Offload Engine)

## Slide 5
Explicit-Dataflow
Von Neumann (Out-of-Order)
Instruction Stream
Instruction
Window
Dependence Graph
Instruction-by-instruction execution of Control Flow Graph
Dependence-graph execution,
Control deps becomes data deps
+Speculation
+Local/Non Local ILP
+Lower Overheads
No Fetch, Decode, Rename – No dynamic dependence graph construction

## Slide 6
×
ld
×
ld
×
ld
+
+
+
+
+
+
-
-
-
Explicit-Dataflow Wins
Von Neumann Wins
+
>
br
ld
+
>
br
(Speculation)
(Higher ILP)
Loop 1:
Data Dependent
Control
Loop 2:
High ILP,
Non-Critical Control

## Slide 7
Control Regularity
Memory Regularity
General Code
(Out-of-Order)
Higher ILP
Data-Parallel
(SIMD/GPU)
Memory Latency Bound (Dataflow?)
Unpredictable (Dataflow?)
High ILP
(Data-
flow?)

## Slide 8: Outline
Control
Memory
Describing why VonNeumann can complement Dataflow architectures.
Leveraging program properties for efficient heterogeneous design
Performing a Design-Space Exploration
Across (Small, Medium, Big) VN Cores
Designing SEED: Specialization
Engine for Explicit-Dataflow
Speedup
Energy
Nested Loops
Von-
Neumann
Explicit
Dataflow
  24 Irregular Workloads from SpecINT/MediaBench

## Slide 9: Property 1: Affinity Phase Behavior
App. 1
App. 2
App. 3
Hundreds to Millions of Instructions
Architecture affinity over Time
Out-of-Order
SIMD
Explicit-
Dataflow
Cache Hierarchy
fast-switching
VonNeumann
Data-Parallel
Dataflow
Chart: 
| Quad-Issue OOO Only | Ideal Dataflow Only | Heterogeneous Execution
 | 3 | 6 | 15
13%
25%
63%
Workload Architecture Affinity

## Slide 10: Property 2: Benefits of Restricted Scope
Scope:
(must support arbitrary procedure calls, recursion, instruction misses)
Arbitrary Code
Inner Loops
Traces
Area/Power:
High
Low
Low
Coverage:
(any duration)
Coverage:
(long duration)
100%
100%
Fine Print: Static Region Size 1024 Instructions; Long Duration (lasting Longer than 1000 Cycles)
61%
46%
41%
27%
(call)

## Slide 11
Scope:
Arbitrary Code
Inner Loops
Traces
Area/Power:
High
Low
Low
Coverage:
(any duration)
Coverage:
(long duration)
100%
100%
Fine Print: Static Region Size 1024 Instructions; Long Duration (lasting Longer than 1000 Instructions)
61%
46%
41%
27%
Nested Loops
Low
74%
67%
Property 2: Benefits of Restricted Scope
(call)

## Slide 12: Outline
Control
Memory
Describing why VonNeumann can complement Dataflow architectures.
Leveraging program properties for efficient heterogeneous design
Performing a Design-Space Exploration
Across (Small, Medium, Big) VN Cores
Designing SEED: Specialization
Engine for Explicit-Dataflow
Speedup
Energy
Nested Loops
Von-
Neumann
Explicit
Dataflow
  System Overview
  Architecture Inspiration
  Architecture Overview
  Fine-Grain Switching => Phased Dataflow Affinity
  Simplify Dataflow Arch. => Nested-Loop Scope

## Slide 13: System Overview
Compiler finds and inlines profitable nested loop regions, and generates the dataflow representation for SEED.
Invoking SEED:
  SEED_CONFIG: Begins streaming configuration (20-250 cycles)
  SEED_BEGIN: Transfers execution, powers down non-stateful host core components
Resuming OOO:
  Core is powered on
  Live values transferred to OOO core registers.
Time
SEED_CONFIG
SEED_BEGIN
Resume OOO
Program Execution
Time
Nested Loop
OOO
Core
SEED
L1 Cache
System Architecture
Compiler
Runs on
Program
Binary

## Slide 14: Leveraging Decades of Dataflow Research
Criteria: 1. Low Area/Power
    2. High Performance
3. Complement Capabilities of VonNeumann
Design Decisions | TRIPS | WaveScalar | DySER | BERET
Scope | Whole Program | Whole Program | Inner Loop Compute | Hot Loop Trace
Integration to Host |  |  | Behind L1 Cache | Behind L1 Cache
Control Flow | VN/Predicat. | Switch Insts. | Predication | Trace-only
Control Speculation | Block-based | None | Block-based | Trace-only
Dataflow Firing | Position-based | Tag-based | Static | Not applicable
Execution Units | Homog. FU | Heterog. FU | Heterog. FU | Compound FU
Design Decisions
Scope
Integration to Host
Control Flow
Control Speculation
Dataflow Firing
Execution Units

## Slide 15: SEED Architecture
L1 Cache
OOO
CPU
Config & Init.
CPU
XFER
Store
Buffer
IMU
ODU
Bus
Arbiter
Seed Unit 1
Seed Unit 8
IMU
(Instruction
Mgmt. Unit)
CFU8
…
CFU1
ODU
IMU: Keeps instruction definitions and unrolled operand storage (32 comp. insts). Issues one instruction per cycle to CFU.
CFU: SEED Units are organized around a set of compound functional units (CFUs). 2-5 Instructions each.
ODU+Bus: Multi-bus distribution network for communicating between SEED Units.
Store Buffer: Interface to memory system.
ICache
DCache
Entering & Exiting SEED Regions
SEED
Compile-time scheduler assigns instructions to compound FUs and SEED units, using an integer linear program [see Paper]

## Slide 16: Capability Comparison
L1 Cache
OOO
CPU
Config & Init.
CPU
XFER
Store
Buffer
IMU
ODU
Bus
Arbiter
Seed Unit 1
Seed Unit 8
IMU
(Instruction
Mgmt. Unit)
CFU8
…
CFU1
ODU
ICache
DCache
 | Quad-Issue OOO | SEED
Max. Effective IPC | 3-3.5 (4) | 6-7 (16)
Max. Instruction Window | 48 (48) | 200-300 (1024)
Speculative Control | Yes | No
Speculative Scheduling | Yes | No
(parens:
theoretical max)

## Slide 17: Outline
Control
Memory
Describing why VonNeumann can complement Dataflow architectures.
Leveraging program properties for efficient heterogeneous design
Performing a Design-Space Exploration
Across (Small, Medium, Big) VN Cores
Designing SEED: Specialization
Engine for Explicit-Dataflow
Speedup
Energy
Nested Loops
Von-
Neumann
Explicit
Dataflow

## Slide 18: Experimental Setup
Methodology
  Simulator: Modified Gem5 + McPAT/Cacti
  Power: Core + L1 + L2 + Static (@2Ghz and 22nm)
Comparison to State-of-the-art VonNeuman-Based Heterogeneous Execution Models:
  “Accelerators”: BERET, Conservation-Cores
  Micro-arch: bigLITTLE, In-place Loop Execution
  Oracle scheduler: choose best arch. per-region (others have demonstrated solutions [Padmanabha et al., MICRO 2013])
Design Space Exploration:
  IO2: Dual-Issue Inorder
  OOO2: Dual-Issue, 32-entry IW
  OOO4: Quad-Issue, 48-entry IW

## Slide 19: Architecture Comparison
1.3× Perf.
1.7× En.
1.14× Perf.
1.54× En.
State-of-the-art
ThisWork
This Way Better

## Slide 20: Dataflow Heterogeneity Analysis
Slowdown Regions
  Vectorizable on OOO Core
  Control on Critical Path
  Short Regions
Similar Regions
  No speculative scheduling
  Fewer Branch-Mispredicts
  Less Stack Spilling
Speedup Regions
  High Instruction Parallelism
  High Memory Parallelism
Chart: SEED Speedup over Quad-Issue OOO
| gsmencode | jpg2000enc | vpr | mcf
 | 0.07 | 0.1 | 0.12 | 0.15 | 0.17 | 0.17 | 0.17 | 0.18 | 0.2 | 0.75 | 0.88 | 1.13 | 1.16 | 1.17 | 0.08 | 0.13 | 0.31 | 0.42 | 0.79 | 0.82 | 0.88 | 1.32 | 1.37 | 0.45 | 0.51 | 0.54 | 0.65 | 0.84 | 1.93 | 0.51 | 0.83 | 1.01 | 2.12 | 3.06

## Slide 21: Dataflow Heterogeneity Analysis
Slowdown Regions
  Vectorizable on OOO Core
  Control on Critical Path
  Short Regions
Similar Regions
  No speculative scheduling
  Fewer Branch-Mispredicts
  Less Stack Spilling
Speedup Regions
  High Instruction Parallelism
  High Memory Parallelism
Chart: SEED Speedup over Quad-Issue OOO
| gsmencode | jpg2000enc | vpr | mcf
 | 0.07 | 0.1 | 0.12 | 0.15 | 0.17 | 0.17 | 0.17 | 0.18 | 0.2 | 0.75 | 0.88 | 1.13 | 1.16 | 1.17 | 0.08 | 0.13 | 0.31 | 0.42 | 0.79 | 0.82 | 0.88 | 1.32 | 1.37 | 0.45 | 0.51 | 0.54 | 0.65 | 0.84 | 1.93 | 0.51 | 0.83 | 1.01 | 2.12 | 3.06

## Slide 22: Dataflow Heterogeneity Analysis
Slowdown Regions
  Vectorizable on OOO Core
  Control on Critical Path
  Short Regions
Similar Regions
  No speculative scheduling
  Fewer Branch-Mispredicts
  Less Stack Spilling
Speedup Regions
  High Instruction Parallelism
  High Memory Parallelism
Chart: SEED Speedup over Quad-Issue OOO
| gsmencode | jpg2000enc | vpr | mcf
 | 0.07 | 0.1 | 0.12 | 0.15 | 0.17 | 0.17 | 0.17 | 0.18 | 0.2 | 0.75 | 0.88 | 1.13 | 1.16 | 1.17 | 0.08 | 0.13 | 0.31 | 0.42 | 0.79 | 0.82 | 0.88 | 1.32 | 1.37 | 0.45 | 0.51 | 0.54 | 0.65 | 0.84 | 1.93 | 0.51 | 0.83 | 1.01 | 2.12 | 3.06

## Slide 23: Dataflow Heterogeneity Analysis
Slowdown Regions
  Vectorizable on OOO Core
  Control on Critical Path
  Short Regions
Similar Regions
  No speculative scheduling
  Fewer Branch-Mispredicts
  Less Stack Spilling
Speedup Regions
  High Instruction Parallelism
  High Memory Parallelism
Chart: SEED Speedup over Quad-Issue OOO
| gsmencode | jpg2000enc | vpr | mcf
 | 0.07 | 0.1 | 0.12 | 0.15 | 0.17 | 0.17 | 0.17 | 0.18 | 0.2 | 0.75 | 0.88 | 1.13 | 1.16 | 1.17 | 0.08 | 0.13 | 0.31 | 0.42 | 0.79 | 0.82 | 0.88 | 1.32 | 1.37 | 0.45 | 0.51 | 0.54 | 0.65 | 0.84 | 1.93 | 0.51 | 0.83 | 1.01 | 2.12 | 3.06

## Slide 24: Dataflow Heterogeneity Analysis
Slowdown Regions
  Vectorizable on OOO Core
  Control on Critical Path
  Short Regions
Similar Regions
  No speculative scheduling
  Fewer Branch-Mispredicts
  Less Stack Spilling
Speedup Regions
  High Instruction Parallelism
  High Memory Parallelism
Chart: SEED Speedup over Quad-Issue OOO
| gsmencode | jpg2000enc | vpr | mcf
 | 0.07 | 0.1 | 0.12 | 0.15 | 0.17 | 0.17 | 0.17 | 0.18 | 0.2 | 0.75 | 0.88 | 1.13 | 1.16 | 1.17 | 0.08 | 0.13 | 0.31 | 0.42 | 0.79 | 0.82 | 0.88 | 1.32 | 1.37 | 0.45 | 0.51 | 0.54 | 0.65 | 0.84 | 1.93 | 0.51 | 0.83 | 1.01 | 2.12 | 3.06

## Slide 25: Dataflow Heterogeneity Analysis
Slowdown Regions
  Vectorizable on OOO Core
  Control on Critical Path
  Short Regions
Similar Regions
  No speculative scheduling
  Fewer Branch-Mispredicts
  Less Stack Spilling
Speedup Regions
  High Instruction Parallelism
  High Memory Parallelism
Chart: SEED Speedup over Quad-Issue OOO
| gsmencode | jpg2000enc | vpr | mcf
 | 0.07 | 0.1 | 0.12 | 0.15 | 0.17 | 0.17 | 0.17 | 0.18 | 0.2 | 0.75 | 0.88 | 1.13 | 1.16 | 1.17 | 0.08 | 0.13 | 0.31 | 0.42 | 0.79 | 0.82 | 0.88 | 1.32 | 1.37 | 0.45 | 0.51 | 0.54 | 0.65 | 0.84 | 1.93 | 0.51 | 0.83 | 1.01 | 2.12 | 3.06

## Slide 26: Dataflow Heterogeneity Analysis
Slowdown Regions
  Vectorizable on OOO Core
  Control on Critical Path
  Short Regions
Similar Regions
  No speculative scheduling
  Fewer Branch-Mispredicts
  Less Stack Spilling
Speedup Regions
  High Instruction Parallelism
  High Memory Parallelism
Chart: SEED Speedup over Quad-Issue OOO
| gsmencode | jpg2000enc | vpr | mcf
 | 0.07 | 0.1 | 0.12 | 0.15 | 0.17 | 0.17 | 0.17 | 0.18 | 0.2 | 0.75 | 0.88 | 1.13 | 1.16 | 1.17 | 0.08 | 0.13 | 0.31 | 0.42 | 0.79 | 0.82 | 0.88 | 1.32 | 1.37 | 0.45 | 0.51 | 0.54 | 0.65 | 0.84 | 1.93 | 0.51 | 0.83 | 1.01 | 2.12 | 3.06

## Slide 27: Heterogeneity Analysis Summary
Slowdown Regions
  Vectorizable on OOO Core
  Control on Critical Path
  Short Regions
Similar Regions
  No speculative scheduling
  Fewer Branch-Mispredicts
  Less Stack Spilling
Speedup Regions
  High Instruction Parallelism
  High Memory Parallelism
Chart: SEED Speedup over Quad-Issue OOO
| gsmencode | jpg2000enc | vpr | mcf
 | 0.07 | 0.1 | 0.12 | 0.15 | 0.17 | 0.17 | 0.17 | 0.18 | 0.2 | 0.75 | 0.88 | 1.13 | 1.16 | 1.17 | 0.08 | 0.13 | 0.31 | 0.42 | 0.79 | 0.82 | 0.88 | 1.32 | 1.37 | 0.45 | 0.51 | 0.54 | 0.65 | 0.84 | 1.93 | 0.51 | 0.83 | 1.01 | 2.12 | 3.06

## Slide 28: Conclusions
Heterogeneous Von Neumann + Dataflow has a high potential
  Especially for modest sized OOO Cores
  Delay need for application-specific accelerators?
Looking Forward
  Augment dataflow-architecture with data-parallel capabilities?
  Alternative heterogeneous models (what other program properties to leverage?)
  Can micro-architecture modifications achieve the same benefits?
VN
?
Thank you!
DF
DF